GT POWER - 15.00
                 Copyright (c) 1985, 1989: by P & M Software Co.
                            All rights are reserved.



                             Host Mode Documentation


                                  June 20, 1989




                             P & M Software Company
                             3104 E. Camelback Rd. #503
                             Phoenix, AZ      85016
                             U. S. A.



                             Voice Phone: (602) 285-9914
                             Modem Phone: (602) 285-1146
                             Modem Phone: (713) 772-2090






















                                    - 1 -



                                Table of Contents
                    -----------------------------------------
     A Brief Summary . . . . . . . . . . . . . . . . . . . . . . .  4
     The Installation Of Host Mode . . . . . . . . . . . . . . . .  4
         The Modem Init String . . . . . . . . . . . . . . . . . .  4
         The Host Mode: Modem Init String  . . . . . . . . . . . .  4
         The Modem Answer String . . . . . . . . . . . . . . . . .  5
         The Modem Result Codes  . . . . . . . . . . . . . . . . .  5
         Logging Status During Host Mode . . . . . . . . . . . . .  5
         Hang-up During Host Mode  . . . . . . . . . . . . . . . .  5
         The Default Message Base Path . . . . . . . . . . . . . .  6
         The Default File Section  . . . . . . . . . . . . . . . .  6
         File Reception Directory  . . . . . . . . . . . . . . . .  6
         The Sysop Message Base  . . . . . . . . . . . . . . . . .  6
     Security Considerations . . . . . . . . . . . . . . . . . . .  6
         DSZ.EXE, PCKERMIT.EXE and Other Externals . . . . . . . .  8
     Host Mode Text Files  . . . . . . . . . . . . . . . . . . . . 11
         Forcing a "More?" Prompt  . . . . . . . . . . . . . . . . 11
         Disable the "More?" Prompt  . . . . . . . . . . . . . . . 11
         Nest the Display of Bulletins . . . . . . . . . . . . . . 11
         Disable the ^K/^C Break . . . . . . . . . . . . . . . . . 11
         The Variable Substitution Line  . . . . . . . . . . . . . 11
         ANSI Graphics (.BBS vs .CBS)  . . . . . . . . . . . . . . 11
     File Descriptions . . . . . . . . . . . . . . . . . . . . . . 12
         GTSYSID.BBS . . . . . . . . . . . . . . . . . . . . . . . 12
         GTWELCOM.BBS  . . . . . . . . . . . . . . . . . . . . . . 12
         GTPASSWD.BBS  . . . . . . . . . . . . . . . . . . . . . . 12
             Field Descriptions  . . . . . . . . . . . . . . . . . 13
         GTBULLET.BBS  . . . . . . . . . . . . . . . . . . . . . . 16
         BULLETx.BBS . . . . . . . . . . . . . . . . . . . . . . . 16
         GTMENU.BBS  . . . . . . . . . . . . . . . . . . . . . . . 16
         GTHELP.BBS  . . . . . . . . . . . . . . . . . . . . . . . 16
         GTBYE.BBS . . . . . . . . . . . . . . . . . . . . . . . . 16
         GTBYEx.BBS  . . . . . . . . . . . . . . . . . . . . . . . 16
         GTUSER.BBS  . . . . . . . . . . . . . . . . . . . . . . . 16
         GTDIR.BBS . . . . . . . . . . . . . . . . . . . . . . . . 17
             Comment Lines . . . . . . . . . . . . . . . . . . . . 17
             Directory Lines . . . . . . . . . . . . . . . . . . . 17
         GTDDIR.BBS  . . . . . . . . . . . . . . . . . . . . . . . 18
         GTBMENU.BBS . . . . . . . . . . . . . . . . . . . . . . . 19
         GTMDIR.BBS  . . . . . . . . . . . . . . . . . . . . . . . 19
         GTDOORS.BBS . . . . . . . . . . . . . . . . . . . . . . . 20
             GTDOORnn.BAT and GTDORnnn.BAT . . . . . . . . . . . . 21
         ANSWERn.BBS . . . . . . . . . . . . . . . . . . . . . . . 21
         QUESTn.BBS  . . . . . . . . . . . . . . . . . . . . . . . 22
         PQUESTn.BBS . . . . . . . . . . . . . . . . . . . . . . . 23
         GTQMENU.BBS . . . . . . . . . . . . . . . . . . . . . . . 23
         PROTOCOL.BBS  . . . . . . . . . . . . . . . . . . . . . . 23
         WELCOME.BBS . . . . . . . . . . . . . . . . . . . . . . . 24
         MBULLETx.BBS  . . . . . . . . . . . . . . . . . . . . . . 24
         SYSOP.BBS . . . . . . . . . . . . . . . . . . . . . . . . 24
         SCHEDULE.BBS  . . . . . . . . . . . . . . . . . . . . . . 24
         TRASHCAN.BBS  . . . . . . . . . . . . . . . . . . . . . . 26
         FILES.BBS . . . . . . . . . . . . . . . . . . . . . . . . 26


                                    - 2 -



     Host Mode Control Files and Directories . . . . . . . . . . . 27
     Running Host Mode . . . . . . . . . . . . . . . . . . . . . . 28
         SYSOP Commands  . . . . . . . . . . . . . . . . . . . . . 28
         Command Line Usage  . . . . . . . . . . . . . . . . . . . 28
         The HOST.BAT File . . . . . . . . . . . . . . . . . . . . 30
         The HOST.SCR File . . . . . . . . . . . . . . . . . . . . 30
         Using a LAN with GT . . . . . . . . . . . . . . . . . . . 30
     The Host Mode LOG . . . . . . . . . . . . . . . . . . . . . . 32
     The Shell to DOS  . . . . . . . . . . . . . . . . . . . . . . 32
         COMMAND.COM . . . . . . . . . . . . . . . . . . . . . . . 32
         DOS 2.xx  . . . . . . . . . . . . . . . . . . . . . . . . 32
     Using the Shell to DOS  . . . . . . . . . . . . . . . . . . . 33
     The Generic Tool Interface  . . . . . . . . . . . . . . . . . 34
     The Remote Sysop Interface  . . . . . . . . . . . . . . . . . 34
     The Usage of Color  . . . . . . . . . . . . . . . . . . . . . 35
     The Logon Doors . . . . . . . . . . . . . . . . . . . . . . . 35
     The Logoff Doors  . . . . . . . . . . . . . . . . . . . . . . 36
     Appendix  . . . . . . . . . . . . . . . . . . . . . . . . . . 37
         Extended ASCII Codes  . . . . . . . . . . . . . . . . . . 37
         Sample ANSI Sequences . . . . . . . . . . . . . . . . . . 37
         Power-Loss Protected Operation  . . . . . . . . . . . . . 38
         Sample Files For Power-Loss Protected Operation . . . . . 39
         GT POWER under DESQview . . . . . . . . . . . . . . . . . 40

     (tm) DESQview is the trademark of QuarterDeck Office Systems.































                                    - 3 -



     Brief Summary
     -------------
     The host mode provided within GT POWER allows you to run an unattended 
     session with your system.  That is,  if you expect  to  receive  calls 
     from  other  computer systems (say from clients or a set of authorized 
     remote users) then you can tell GT POWER that it should  automatically 
     answer the telephone for you,  verify the caller's credentials, and if 
     found to be valid,  to provide that user with a menu of functions that 
     can   be  performed.   All  of  that,   of  course,   without  further 
     intervention on your part.  

     Security is of paramount importance when  running  in  host  mode  for 
     obvious   reasons.   Please   read   the  section  entitled  'Security 
     Considerations' before attempting to operate this system.  



     Installation of Host Mode
     -------------------------
     The most important thing about host mode is proper installation of the 
     modem control strings and result codes.  These strings and codes  must 
     not just control the modem,  they MUST WORK TOGETHER.  For example, if 
     the modem init strings specify "verbose" result codes, then the result 
     code table better have the "verbose" codes  in  it,  not  the  "terse" 
     codes.  There  are 11 specific areas that *must* be installed;  all of 
     these options and strings are accessible via the ALT-I command.  Let's 
     discuss each of these items in turn: 

     1.   The "Modem Init String".  The default value is:

                           AT V1 Q0 E0 X1 S0=0 S2=43|

          Assuming that one wants to  use  the  default  string,  there  is 
          really  only one thing that one SHOULD DO to this string:  change 
          the Xn command.  The most powerful Xn command available  on  your 
          modem  is  the  one  to  choose.  With  a USRobotics Courier 2400 
          modem,  use either X5 or X6.  With a normal Hayes-compatible 1200 
          baud modem, use X1.  X4 would be normal for most Hayes-compatible 
          2400 baud modems.  For other modems consult the modem manual.  

          NOTE:
               Many  so  called  "Hayes-compatibles" are compatible in name 
               only.  We get many calls for support from  individuals  with 
               non-Hayes  modems.  Please  read your modem manual carefully 
               because it is very hard to support all the different modems.  

     2.   The "Host Mode:  Modem Init String".  This string is found  under 
          item #30 of the configuration screen.  The default value is: 

                           AT V1 Q0 E0 M0 X1 S0=1 S2=255|

          There are several things one could do to this string.  First, one 
          must modify the X1 command to match the value added to the  Modem 
          Init  String  above.  Secondly,  if one desires the speaker to be 


                                    - 4 -



          heard during host mode,  remove the M0 from the string.  Thirdly, 
          the  S0=1  may  be changed to S0=0,  THIS IS THE ONLY OTHER VALID 
          VALUE!  If S0=0 is used, the modem will not answer automatically, 
          GT will count the rings and command the modem to answer after the 
          2nd ring (or if the /Rn command line switch is  used,  after  the 
          Nth  ring).  This  is  why S0=1 and S0=0 are the only permissible 
          values!  Refer  to  the  main  GT1500.DOC  file  for  a  complete 
          discussion of the available command line switches.  

     3.   The  "Modem Answer String".  This string is located with the Host 
          Modem Init String under item #30  of  the  configuration  screen.  
          The default value is: 

                           ATA|

          GT  will  issue  this string to the modem whenever the ring count 
          reaches 2 (or the number  indicated  by  the  /Rn  switch).  This 
          string should not be changed,  unless GT should not be allowed to 
          answer the modem.  For example,  one could erase this string  and 
          set S0=5,  so that the modem would answer on the 5th ring,  but I 
          don't advise anyone do this.  

     4.   The "Result Codes".  Because the modem init strings above contain 
          V1,  "verbose" result codes should be  programmed.  They  can  be 
          found  under  item #29 of the configuration screen.  There are 16 
          possible results.  If the modem does not support  all  of  these, 
          simply  leave  the  extra  strings  in  their default state.  The 
          program comes with the default result codes set for  use  with  a 
          USRobotics  Courier HST modem.  Please consult the manual for the 
          modem in use and modify this table to match.  Remember,  use  the 
          "verbose" (word codes), not the "terse" codes.  It IS POSSIBLE to 
          use  the "terse" codes,  but they are not as compatible with such 
          services as PC Pursuit.  It  is  especially  important  that  the 
          result  codes for the CONNECT results are correct.  GT uses these 
          to determine the baud rate of the  incoming  call.  If  they  are 
          wrong,  then  GT will not be able to talk to the incoming caller, 
          because the modem and GT will not be at the same baud rate;  they 
          will be out-of-sync.  

     5.   It  is  highly recommended that logging be TRUE during host mode.  
          Otherwise,  all records of  the  host  mode  activities  will  be 
          discarded.  

     6.   How  to  allow GT to hang-up during host mode.  Since the "escape 
          code" must be disabled during host mode,  otherwise  some  caller 
          may  crash  your system,  the normal hang-up string,  "~+++~ATH", 
          will not work!  Therefore,  GT cannot hang-up the  modem,  unless 
          you set the modem to normal DTR operation.  During host mode,  GT 
          will drop the DTR signal whenever he wants the modem to  hang-up.  
          Most modems come from the factory set so that they ignore the DTR 
          signal  -  you  must reset a switch or,  in the case of the Hayes 
          2400 modem, you must make an entry in the Modem init string to do 
          this.  In any case, if the modem ignores DTR, it will not hang up 
          during host mode operations.  Some modems which must be setup via 


                                    - 5 -



          the init strings to handle DTR properly use either  &D2  or  &D3, 
          please  consult  the manual for the modem in use to determine the 
          correct setting.  

     7.   How does GT determine when a connection  is  lost?  The  GT  host 
          monitors  the  carrier  detect  signal from the modem,  when this 
          signal goes low,  then GT assumes that the  connection  has  been 
          lost.  Most  modems  come  from the manufacturer with the carrier 
          detect signal forced high.  "This is like having a telephone with 
          no  ringer."  Quote  by  Tom  Jennings.  Obviously,  this must be 
          changed.  Some modems have a switch that must be reset to  enable 
          a true carrier detect,  others require setup via the init string.  
          Many of the modems that require init string setup use &C1, please 
          consult the manual for the modem in use to determine the  correct 
          setting.  

     8.   Another option available under the Alt-I, #26, the pathname setup 
          section,  is the "Default Message Base PATH".  This option is  to 
          be  used to indicate to GT where the main or default message base 
          is located.  This is the message  base  that  the  user  will  be 
          initially  given  access to upon calling the system.  This should 
          be an open message base since all callers to the system that pass 
          the logon procedure will have access to this area.  

     9.   Another option available under the Alt-I, #26, the pathname setup 
          section, it the "Default File Section".  This option indicates to 
          GT where the main or default file section  is  located.  This  is 
          the file section that callers will see initially when they access 
          your  system.  This  should  be  an area with the lowest security 
          access level, as everyone will be able to use it.  

     10.  To designate the directory where the host  mode  receives  files, 
          you  should  specify the DOWNLOAD directory path.  This option is 
          specified under Alt-I, #26, the pathname setup section.  The user 
          may be confused by the terminology here,  so let me  stress  that 
          the  DOWNLOAD  directory  is  where  GT  POWER  *receives* files, 
          whether in host or terminal modes.  Further, the UPLOAD directory 
          path only pertains to Terminal Mode,  as the host mode file areas 
          are  otherwise  controlled  via  entries  in  the GTDIR.BBS file, 
          described below.  

     11.  To specify the directory where the host mode will  save  messages 
          to  the  sysop.  These  messages are entered with the 'M' command 
          from the main menu.  This option is specified under  Alt-I,  #26, 
          the pathname setup section.  


     PLEASE NOTE:
          The pathnames mentioned above are all found on the pathname setup 
          section, #26 of the Alt-I menu.  


     Security Considerations
     -----------------------


                                    - 6 -



     Many  of  GT  POWER's  design  considerations  were  directed  towards 
     providing  absolute system integrity while in host mode.  This section 
     is designed  to  highlight  some  of  those  considerations  with  the 
     intention  of making the System operator of a host mode fully aware of 
     both his protection and his responsibilities in that regard.  

     The fundamental truth about security is that essentially  it  is  YOUR 
     responsibility.  GT  POWER's  first  line of defense in your behalf is 
     its password  function.  Without  a  preassigned  password,  a  remote 
     caller  cannot  gain  access  to  the  functions provided by GT POWER!  
     Thus,  it stands to reason that your first responsibility is to assign 
     those  passwords and TO GUARD THEM.  Because there are several sets of 
     facilities that you will wish to control and to allow various users to 
     be provided selectively, GT provides several 'levels' of authorization 
     that may be assigned to each password.  In this way, all users who log 
     on with the same password will have identical (and only those that are 
     assigned) access to GT facilities.  For example,  GT POWER provides to 
     users  who  have  a  sufficiently  high 'level' of authorization,  the 
     ability to shell into DOS and,  thus,  have the ability to execute ANY 
     DOS  COMMAND  from  their  remote location!  Obviously,  you would not 
     casually distribute that password amongst your  user  community.  Most 
     users  should  NEVER be allowed to Shell to your DOS!  (While in DOS a 
     user could,  for example,  format your hard  disk  -  that  would,  of 
     course,  result  in  the end of subsequent functionality of the entire 
     system).   To  these  users  you  would  assign  a  lower  'level'  of 
     authority.  To do so you would simply change their access level to the 
     new level with the Sysop Tools program.  

     One of the nicest features of the host mode provided by GT  POWER  are 
     its  message  bases.  With  this  feature  the users of the system may 
     leave 'mail' for other users and receive mail for themselves.  Indeed, 
     there are two kinds of mail:  Public and Private.  Public mail may  be 
     read by any user of the system.  Private mail,  on the other hand, may 
     be read only by the person sending  it  or  by  the  recipient.  Here, 
     then,  is  another  area  of security that you need to be aware of and 
     control.  For example,  say that you allow your system to be called by 
     clients of your firm and that they are encouraged to leave messages to 
     you  in your absence.  It is possible that several of your clients are 
     competitors of each other.  Thus,  it would be improper to allow  them 
     to read messages sent by others.  This is the reason for Private mail.  
     At  this point,  I would like to point out that there is no such thing 
     as 'Private' from the Sysop!  That is,  the System operator  may  read 
     any  message,  whether  addressed  to  him or not and whether they are 
     marked Private or not.  Finally, lest the earlier remarks did not sink 
     in,  any user who has access to the DOS via the Shell command (because 
     of  his  assigned  extremely high 'level' of authorization) can easily 
     read any messages while he is in the DOS Shell!  

     As  far  as  sending  PRIVATE  messages  to  the  System  operator  is 
     concerned,  any user may do that!  There is an 'M' command on the Main 
     Menu that results in messages that only  the  Sysop  may  view.  These 
     messages  are  automatically  addressed  to  the  Sysop  and marked as 
     private.  They are placed in the  message  base  specified  for  sysop 
     messages,   they   may   be  read  only  by  someone  with  the  Sysop 


                                    - 7 -



     authorization level.  This message base needs to be accessed at  least 
     once by the sysop during setup, to insure that a message is entered to 
     create  all control files.  Otherwise,  the system will not be able to 
     process 'M' messages to the sysop.  

     The hierarchy of access 'levels' based on password enables  the  Sysop 
     to  control  which  directories on the disk those users have access to 
     for purposes of downloading files.  However, each caller to the system 
     will be granted access to the  "Default  file  section",  which  is  a 
     config  option.  So please be sure that this file section contains the 
     least sensitive material on your system.  

     For ease of use,  it is recommended that the user  construct  a  batch 
     file  to invoke GT POWER,  especially host mode users.  It should look 
     like this: 

            C:                          To specify a default drive of C
            set GTPATH=C:\GT            Remember to set GTPATH!
            GT1500 !xxxx host.scr       To invoke GT POWER

     If the above batch file were called GT.BAT and placed in your system's 
     PATH then you could safely invoke GT  by  simply  typing:  GT.  It  is 
     important  to  note,  that one of the most frequent errors reported to 
     the GT support staff is the incorrect setting of GTPATH.  

     As you will see when you read the next section  (about  the  GTDIR.BBS 
     file), you can allow your users to have access to all directories that 
     have  a  matching  authorization  level  OR  LOWER.  Further,  you can 
     specify that particular directories are  only  available  to  specific 
     authorization levels.  

     Where  is  all this authorization level information kept within the GT 
     POWER system?  In  a  file  called  GTPASSWD.BBS.  That  file,  it  is 
     unnecessary to say, is the key to the security of your system.  One of 
     the  subtle  security  features  of GT POWER is that it will not allow 
     that file,  even if it is contained in a directory that the  user  has 
     been  authorized  to  Download  from,   to  be  transmitted  over  the 
     telephone!  

     NOTE:  That  the  external protocols can transfer prohibited files and 
            for this reason, extreme care should be taken when using either 
            DSZ.EXE or PCKERMIT.EXE.  

     Similarly,  because the Log file that is optionally maintained  by  GT 
     contains  the  user  names and passwords of those who have logged onto 
     the system, it may not be transmitted over the telephone either.  

     When  running  in  host  mode  the screen on the host system shows all 
     keystrokes entered by the remote user (except while he is in  the  DOS 
     Shell  or using a DOOR,  should that be allowed).  In other words,  if 
     the remote user,  for example,  entered a Private message  to  another 
     user, or to the Sysop, the text is showing on the host screen as it is 
     typed.  If  the  user  were  to log off immediately after entering the 
     message then it would  be  possible  that  the  text  of  the  message 


                                    - 8 -



     remained  on  the screen.  GT POWER erases the screen after the caller 
     hangs up to prevent such a lapse in security.  If you  are  running  a 
     host  mode  system  in  an  environment  where others might be able to 
     observe the screen then it is recommended that you turn  your  monitor 
     off while you are not in attendance.  

     If  others may be in the area as you are communicating (chatting) with 
     users and you wish to control the information on the screen you  would 
     do  well  to  remember that the Alt-W keystroke will erase your screen 
     instantly.  

     A user-name may be BANned from accessing the  system.  Note,  however, 
     that  doing so merely encourages an undesirable to log on with another 
     user name.  With the advent of personalized passwords,  this provision 
     has  become more effective,  since one could setup the system password 
     to have  a  low  access  level,  which  would  be  raised  only  after 
     validation.  

     Computer  time  is  a resource that you can also control in host mode.  
     Each password may have a designated time limit beyond which the caller 
     will be automatically logged off.  The number of calls per day made to 
     your system by an individual caller is also subject to control.  

     One  of  the  more  subtle  security  measures  need  in  a  host mode 
     ennvironment is called a 'Watchdog'.  In the  GT  POWER  system,  this 
     function  is  provided  by a program called DOORMAN.  DOORMAN is a TSR 
     program that should be loaded in your AUTOEXEC.BAT  file,  it  has  no 
     command  line  options,  and  is  loaded simply by its name,  DOORMAN.  
     Should an authorized user be in the DOS Shell or out a DOOR,  and  for 
     any  reason  he  were to drop his carrier (hang-up),  the system would 
     then be vulnerable to the next caller as that caller  could  find  the 
     system "in" DOS and he would then have uncontrolled access to do as he 
     pleased to your system.  In the situation mentioned,  loss of carrier, 
     GT will force your system to reboot and if you setup the  AUTOEXEC.BAT 
     file  properly,  when the system completes rebooting it will invoke GT 
     and put it back in  host  mode!  The  same  thing  would  happen,  for 
     example,  if  power  were  to be lost during host mode.  When power is 
     restored the system will automatically return to the host mode  of  GT 
     POWER.  Note, however, that for those systems that do not have a built 
     in clock, the time and date of the system would no longer be correct.  

     As  a  Sysop of a host mode GT system you must be aware that there are 
     some legal considerations that you may face.  For example,  should you 
     allow users to place copyrighted programs onto your system and to then 
     allow  other  users  to  download  those  same programs,  then you are 
     participating in an illegal activity!  Naturally there is  no  way  to 
     prevent a user from sending you copyrighted material,  provided he has 
     upload capability.  There are many things that you can do, however, to 
     stop others from having access  to  that  material.  For  example,  GT 
     POWER  allows  you to cause all files that are uploaded to your system 
     to be placed into a special receiving directories,  rather  than  into 
     the  directory  the  user  is currently using.  It makes good sense to 
     make a receiving directory PRIVATE, in the sense that it is NOT listed 
     as available in the GTDIR.BBS to your remote users.  In this way,  you 


                                    - 9 -



     may  review  the files received at your convenience and move them over 
     to the public directories if you are satisfied that  they  are  either 
     public domain or Shareware programs and files.  

     Another  reason that you will want to do the above is that there are a 
     few people out in the world that like to send what are  called  Trojan 
     Horses to BBS's.  A Trojan Horse is a program that causes some form of 
     damage  when  it is run.  It would not be at all fair to your users to 
     expose them to such programs.  So,  when it is safe for you to do  so, 
     either  run  the  programs  you  receive  (using BOMBSQAD or a similar 
     program to prevent a problem for you).  When you  are  satisfied  that 
     the programs received are safe then you can move them to public areas.  

     And  in  the  event  that  a  user  does  send  you  a Trojan Horse or 
     copyrighted code,  it is in your best interest to know who did so.  GT 
     POWER  provides  an  optional  log file function.  If that is enabled, 
     which is highly recommended,  then the log contains the  name  of  the 
     person who logged on and sent you the file.  

     This section of the document is substantially larger than you may have 
     expected it to be.  The reason should now be obvious.  

     YOU are the person responsible for security.  It is necessary that you 
     know the previous information and take appropriate actions.  
































                                   - 10 -



     Host Mode Text Files
     --------------------
     The following text files must be created  and/or  maintained  with  an 
     editor  that  can  produce plain ASCII files.  Any of the display type 
     BBS files may have a DC2, Ctrl-R,  character inserted into column 1 of 
     line 1 to disable the "More?" prompt during display of the file, and a 
     DC4, Ctrl-T, character inserted into column 1 of line 1 to disable the 
     Ctrl-K and/or Ctrl-C user break,  or a ENQ, Ctrl-E, character inserted 
     into column 1 of any line to force a "More?" pause  at  that  line.  A 
     NAK,  Ctrl-U,  can  be inserted in column 1 of any line to introduce a 
     variable substitution line.  The ACK, Ctrl-F,  can be used in column 1 
     of a bulletin file to nest the display of other text files.  

     +--------------------------------------------------------------------+
     |                                                                    |
     |     Ctrl-E ... ENQ ... Insert a "More?" at current location.       |
     |     Ctrl-F ... ACK ... Nest the display of bulletin files.         |
     |     Ctrl-R ... DC2 ... Disable "More?" during file display.        |
     |     Ctrl-T ... DC4 ... Disable ^K/^C break during file display.    |
     |     Ctrl-U ... NAK ... Introduce variable substitution line.       |
     |                                                                    |
     +--------------------------------------------------------------------+

     Using the Ctrl-R to disable the "More?" prompt is useful when the file 
     contains such graphic or annimation techniques that would  be  spoiled 
     by  such  interruption.  Except  for the GT?DIR.BBS files,  every .BBS 
     file can have two versions:  (a) a color graphics  version  or  (b)  a 
     plain  text  version.  This  is  coordinated  with  the  ANSI graphics 
     question asked of callers before  they  logon  the  system.  The  .BBS 
     extension  is  the default used if only one version of the file can be 
     found by GT,  the .CBS extension is used to  indicate  to  GT  that  a 
     graphics  version  is available.  If both versions are available,  the 
     .CBS version will be shown to callers who elect graphics,  if graphics 
     are not elected by the caller, the .BBS version will be displayed.  

     The variable substitution line is interpreted by GT, and certain 
     substitutions can be made.  The following are supported:

          C ... The caller's number (i.e. the 100th caller).
          D ... The current calendar date.
          F ... The caller's first name.
          H ... The caller's home - city and state.
          L ... Time left for current session in minutes.
          M ... The current message base description.
          N ... The caller's full name.
          R ... The caller's upload amount in kilobytes.
          RF .. The caller's upload amount in number of files.
          S ... The current file section description.
          T ... The current time of day.
          Wn .. Set width of the parameter that follows to 'n' columns.
          X ... The caller's download amount in kilobytes.
          XF .. The caller's download amount in number of files.
          n ... 'n' number of blank columns.



                                   - 11 -



     In addition to these items, plain text may also appear on the variable 
     substitution line, it must be quoted however, like this:
     
                "plain text between quotation marks"
     
          For example:

                ^U"          Name: "N
                ^U"         First: "F
                ^U"          Home: "H
                ^U"Time remaining: "L
                ^U"  Current time: "T
                ^U" Blank Columns: "30"30 of them."
                ^U"   Fixed width: "W30N"30 characters in width"

     The nesting of bulletin files with the Ctrl-F character  is  extremely 
     useful,  but also hazzardous, if the nesting is done to a great level.  
     For best results,  the nesting should be kept to a  single  level.  An 
     example of usage is: 

                                 ^FC:\GT\FOO.BAR

     Please note that there is no space between the Ctrl-F and the filename 
     and that the full pathname must be given for the file.  

     
     File Descriptions
     -----------------
     GTSYSID.BBS     This  file is displayed as soon as the GT host detects 
                     a connection has been  established  with  an  incoming 
                     call.  After  displaying  this  file,  GT will ask the 
                     user if the terminal program he is using supports ANSI 
                     graphics.  

     GTWELCOM.BBS    This file is displayed to a caller just before  he  is 
                     asked for his name by the GT host.  It should identify 
                     the system to callers.  

     GTPASSWD.BBS    This  file  contains the list of passwords that people 
                     must know to access the system.  The entries  in  this 
                     file  are composed of one line per password,  and each 
                     line contains the following information,  beginning in 
                     column 1: 

     Lvlx ([xx:xx(,n,hh:mm,path)]) Pwd Auth (1st-Name Last-Name Phone-Number)

                     These  items  can  have  a  variable  number of blanks 
                     between them,  but the "Lvl" must begin in  column  1.  
                     EACH  PASSWORD,  "Pwd",  MUST  BE UNIQUE and from 1-20 
                     characters in length.  

                     The () which have been  shown  around  the  call  time 
                     limit, the daily call limit, the daily time limit, the 
                     name,  and  phone  number fields,  indicate that these 


                                   - 12 -



                     items are optional and need not  be  included  in  the 
                     file.  

                     Field descriptions:
                     -------------------
                     Lvlx ... The Access Level assigned to this entry.  May 
                              be any character from the following sets:  0-
                              9,  A-Z,  or a-z.  NOTE:  "0" is the  highest 
                              level   and  "z"  is  the  lowest.   The  'x' 
                              following 'Lvl' is  the  bullet  number  that 
                              this  caller  will  be  shown.  Valid  bullet 
                              numbers  are  0-9,   A-Z.   Read   additional 
                              instructions bellow under BULLETx.BBS.  

                     xx:xx .. The  Call Time Limit.  This field is optional 
                              and is enclosed within [...].  If omitted, it 
                              defaults to approximately 24 hours.  

                     n ...... The Daily Call Limit.  This field is  a  sub-
                              field within the [...] of the Call Time Limit 
                              field.  It  cannot  be  specified without the 
                              Call  Time  Limit   being   specified   also.  
                              Example:  [1:30,2]  would grant two calls per 
                              day of 1:30 duration each.  

                     hh:mm .. The Daily Time Limit.  This field is  a  sub-
                              field within the [...] of the Call Time Limit 
                              field.  It  cannot  be  specified without the 
                              Call Time Limit  and  the  Daily  Call  Limit 
                              being specified also.  Example: [1:00,5,2:00] 
                              would grant five calls per day, each of up to 
                              1 hour each, but a maximum of 2 hours per day 
                              total usage.  

                     path ... The  upload  pathname.  This  specifies where 
                              files uploaded by a particular class of  user 
                              are to be stored.  

                     pwd .... The  Password.  As  said above,  the password 
                              may be from 1-20  characters  in  length  and 
                              must  be  unique.  If  this  line  is a class 
                              entry the "pwd" field should contain the word 
                              CLASS in capital letters.  

                     auth ... The Authorizations given to this entry.  They 
                              come from the following list: 

                              UP : Upload authorized.
                              DN : Download authorized.
                              PR : Private mail authorized.
                              KL : Allow the killing of messages,  the same 
                                   as the Sysop.  
                              SY : Sysop priveledges authorized.
                              CH : Manual directory  change  is  authorized 


                                   - 13 -



                                   (in absence of the GTDIR.BBS file).  
                              SH : Shell to DOS is authorized.
                              DR : Use of DOORS is authorized.
                              MS : Allows message reading.
                              FA : Allows   file   attach  when  using  the 
                                   netmail programs.  
                              FR : Allows  file  request  when  using   the 
                                   netmail programs.  
                              NL : Disable  the  L)ist directory command at 
                                   the main menu.  
                              NE : Disable the E)nter message command.

                              These  authorizations are listed seperated by 
                              commas,   following  the  "pwd"  field.   See 
                              examples  below.  The  CH  authorization is a 
                              "do nothing"  authorization  in  most  cases, 
                              because  most  systems  use a GTDIR.BBS file.  
                              On these systems the CH option may be used as 
                              a way to grant no  authorization,  because  a 
                              total   lack   of  authorization  yields  the 
                              default authorization set: DN,UP,PR,MS.  

                     1st-Name Last-Name Phone-Number
                              These  three  fields  are  present when it is 
                              desired  to  allow  the   caller   "callback" 
                              priveledges.  In effect, if the caller's name 
                              matches the name listed here and he gives the 
                              correct  password,  the  system will offer to 
                              call him at the listed  number.  This  allows 
                              the  host  to  assume  the  cost of the phone 
                              charges for the session.  The caller must  be 
                              prepared  to  accept  the  call,  that is his 
                              modem must be  in  "auto-answer"  mode.  Send 
                              "ATS0=1|"  to  most  Hayes type modems to set 
                              auto-answer  mode.   The  "|"  represents   a 
                              "carriage return".  If the conditions are met 
                              GT  will  return  the call within 15 seconds, 
                              and will retry 3 times before giving-up  hope 
                              of  establishing  the connection.  NOTE:  the 
                              password assigned here for the callback, must 
                              *not* be the same as  the  caller's  personal 
                              password  --  the callback password *MUST* be 
                              unique.  

              NOTE:  It is possible to append a  single  character  to  the 
                     level  indicator.  Thus  "A1"  would be a valid level.  
                     This extra character is  used  to  identify  a  custom 
                     bulletin  file  for this caller.  This extra character 
                     is optional,  but if present MUST BE a character  that 
                     is  legal within a file name.  Read about BULLET files 
                     below.  

                Examples:
                     A  [2:00,100,5:00,c:\goodies] MASTER  SY


                                   - 14 -



                     B1 [1:00] FRIEND  DN,PR
                     B1 [1:00,4,2:00,c:\up] CLASS DN,UP,PR
                     C  [1:30] JOGGER  DN,UP,PR,DR MARY ADAMS 1-213-555-1234
                     A  [2:00,10,4:00] CLASS SY
                     C2 [2:00,3,3:00] CLASS DN,UP,PR,DR

                     In  version 12.10 of GT POWER,  personalized passwords 
                     were introduced.  When  a  caller  gets  his  personal 
                     password it is stored in the GTMAIL.CTL file, with the 
                     other  user information.  The access level assigned to 
                     the password used by the  caller  on  the  first  call 
                     (before  a personal password was assigned) will be the 
                     access level assigned to the caller until changed  via 
                     the  Sysop  Tools  program.  To  provide a time limit, 
                     daily call limit,  and bullet #,  a cross reference of 
                     the  access  level  stored  in  the  users  record  in 
                     GTMAIL.CTL file and the GTPASSWD.BBS file is required.  
                     This is accomplished by placing CLASS cards  for  each 
                     access  level  your  system uses into the GTPASSWD.BBS 
                     file.  The format of the CLASS card is the same  as  a 
                     normal  password  entry,  except  the  word CLASS must 
                     appear in uppercase letters.  In addition,  the  CLASS 
                     entries  cannot  be used to provide callbacks,  normal 
                     password entries must be provided  for  that  purpose.  
                     Here are some example CLASS entries: 

                Examples:
                     A1  [2:00,5,3:00]  CLASS  DN,UP,PR,DR,SH,MS
                     B3  [1:30,2,2:00]  CLASS  DN,PR,MS
                     K2  [:45,1,:45]    CLASS  DN,UP,PR,DR,MS

                     The  first CLASS entry establishes a class for callers 
                     with an 'A' access  level,  grants  them  2  hours  of 
                     session  time,  and  a daily call limit of 5 calls,  3 
                     hours  of  time  per   day,   and   gives   them   the 
                     authorizations:  Download,  Upload,  Private mail, use 
                     DOORS,  Shell to DOS,  and read  messages.  The  other 
                     entries  grant  lesser time amounts to the 'B' and 'K' 
                     classes.  The 'B' class  is  given  Download,  Private 
                     mail, and read messages authorizations.  The 'K' class 
                     is given Download,  Upload,  Private mail,  use DOORS, 
                     and  read  messages  authorizations.   Note:   if  you 
                     neglect  to setup CLASS entries then once your callers 
                     have been assigned their own personal passwords,  this 
                     is  automatically  done  by  GT,  then  they will have 
                     unlimited time access  to  your  system,  the  default 
                     authorizations, and they will not be given a bullet #.  

               +----------------------------------------------------------+
               |                                                          |
               |      Remember to give callers the MS authorization       |
               |      so they can "read messages".  And setup a CLASS     |
               |      entry for each different access level in use.       |
               |                                                          |


                                   - 15 -



               +----------------------------------------------------------+

     GTBULLET.BBS    This  file  is  displayed  for the caller after he/she 
                     completes logon.  It is useful to leave notes here for 
                     expected callers.  

     BULLETx.BBS     The "x" may be any character that can be a legal  part 
                     of   a   filename.   This  character  must  match  the 
                     character which is found after the level indicator  in 
                     the password file,  to enable custom bulletin files to 
                     be displayed for callers.  For example:  if a caller's 
                     level  was  "BZ",  then the program would search for a 
                     file named BULLETZ.BBS to display whenever the  caller 
                     logged onto the program.  

              NOTE:  Custom  bulletin  files  are  OPTIONAL.  If you do not 
                     wish to use them, simply use single letters for access 
                     level indicators.  

     GTMENU.BBS      This file is displayed for callers as the  main  menu.  
                     It  may  be suppressed by a caller by selecting X)pert 
                     mode.  

     GTHELP.BBS      This file  is  displayed  for  the  caller  if  he/she 
                     requests help with the main menu.  

     GTBYE.BBS       This file is displayed for the caller when he/she logs 
                     off,  i.e.  selects the G)oodbye command from the main 
                     menu.  

     GTBYEx.BBS      This is  a  custom  bye  file.  The  'x'  may  be  any 
                     character  that can be a legal part of a filename.  It 
                     comes  from  the  GTPASSWD.BBS  file,  as  the  letter 
                     following   the  level  indicator.   Most  commonly  a 
                     number.  See custom BULLETx.BBS files above.  

     GTUSER.BBS      This file is created whenever a call  comes  into  the 
                     system.  It  will contain the access level and name of 
                     the current caller, or if no call is in progress,  the 
                     previous caller to the system.  The file contains just 
                     this 1 line of text.  The exact format is: 

     Lvl 1st-Name Last-Name auth baud ANSI-opt last-on limit event time

                     The line is free format with spaces delimiting fields.  
                     The "auth" field will contain the authorizations given 
                     this caller from the GTPASSWD.BBS file when he  logged 
                     onto  the system.  The "baud" field will be one of the 
                     following numbers:  300, 1200, 2400,  9600 or the word 
                     LOCAL,  if  the  sysop  is  logged-on.  The "ANSI-opt" 
                     field will contain "NOANSI" if the caller doesn't want 
                     ANSI graphics, or "ANSI" if he does want the graphics.  
                     The "last-on" field contains the date  the  user  last 
                     called  the  system.  The  "limit"  field contains the 


                                   - 16 -



                     remaining time the caller has  left  for  the  current 
                     call.  The  "event"  field contains the time remaining 
                     until the next event is scheduled.  The  "time"  field 
                     contains the current time in "xx:xx" format.  The time 
                     remaining  fields  are  integer  showing  time left in 
                     minutes.  

                     The  purpose  of  this information is to supply needed 
                     control information  to  external  programs  that  run 
                     either in the Shell to DOS or DOOR environment.  

     GTDIR.BBS       This  file  contains a list of directories that may be 
                     accessed by callers.  There are two types of lines  in 
                     this  file:  the  actual  directory  lines and comment 
                     lines.  The comment lines are displayed to the  caller 
                     when he asks to see the list of directories.  The list 
                     displayed  will  contain  only  those  directories the 
                     caller is authorized to access.  The formats: 

                Comment Lines:
                     Contain a blank in the 1st column,  the  remainder  of 
                     the line is displayed for the caller.  

                Directory Lines:
                     Column  1  - access Level.  The minimum level required 
                     to access the directory.  If this column  contains  an 
                     "="  then  the  actual  line is shifted to the right 1 
                     column and the "=" acts to reserve the  directory  for 
                     the  indicated  access  level  - which would now be in 
                     column 2. (See example.) 

                     One or  more blank  columns follows  the level, then the
                     complete DOS name  of  the  directory,  including  all 
                     drive and PATH information.  One or more blank columns 
                     follows the directory name,  then a description of the 
                     directory is given.  When a caller selects the C)hange 
                     directory command,  the list of choices  will  display 
                     the  descriptions  you  provide  here,  so  try  to be 
                     helpful.  

                Examples:

                       This is a comment.  (Since column 1 is blank)
                     A   C:\DOS\TEST    The description goes here.
                     =B  C:\LOTUS\DATA  This is for "B" level callers only.
                     C   A:\            The description again goes here.

                     This example shows three directories,  one with an "A" 
                     access level,  one with a "C" access level.  These are 
                     the minimum levels that callers  must  have  to  "see" 
                     these  directories.  The  "=B"  directory  may only be 
                     accessed by a caller with the "B" access level.  

              NOTE:  When host mode is started,  the then default directory 


                                   - 17 -



                     will  be made available to all callers,  regardless of 
                     the contents of GTDIR.BBS.  So it is advised that this 
                     directory require the least security and  that  it  be 
                     the 1st entry in the GTDIR.BBS file.  

     GTDDIR.BBS      This  file controls access to the GT DOOR system.  Its 
                     function  is  much  like   GTDIR.BBS   is   for   file 
                     directories.  It  serves  as  a way to add security to 
                     doors,  document them and  pass  parameters  to  them.  
                     Each  door must have an entry in this file,  there are 
                     no comment lines in this file.  Each line in this file 
                     follows the this syntax: 

           Lvl  ([comment_here_with_no_spaces])  (Prompt message here:)

                     The () indicate which fields are optional and need not 
                     be included in the file.  

                     As  with  the  GTDIR.BBS file,  the "Lvl" controls the 
                     minimum access level required to open  the  door.  The 
                     [comment]  is  optional,  but  must be enclosed within 
                     [...] if it appears and no blanks are  allowed  within 
                     the  comment  field.  If a parameter must be passed to 
                     the DOOR,  then the  optional  prompt  field  must  be 
                     added.  The  answer given to this prompt by the caller 
                     will be passed to the DOOR as  command  line  argument 
                     %3.  

                     Examples:
                         B  [this-is-door-1]
                         Z  [this-is-door-2]  Enter filename:
                         S  [this-is-door-3]

                     In the example above, the 2nd door has a prompt listed 
                     that  indicates  that this door requires a filename be 
                     passed.  This could be for example to implement an ARC 
                     view type door,  where the  name  of  the  ARC  to  be 
                     processed  might  need  to  be supplied.  The caller's 
                     response will be passed as command line argument %3 to 
                     the GTDOOR2.BAT file in this case.  

                     If you are  using  the  overlaid  doors  command  line 
                     option,  /V:D,  it is possible to selectively override 
                     the feature and have some doors that are not overlaid.  
                     This may be done by putting an '&'  character  as  the 
                     first  character  of the prompt (callers won't see it, 
                     don't worry).  If you have no prompt for a door,  then 
                     just end the line with the '&'.  For example: 

                         E [EDLIN_Door_#1] &Enter Filename:
                         E [EDLIN_Door_#2] &

                     Either  method  would  serve  to insure that this door 
                     does not overlay GT when it is activated.  


                                   - 18 -



                     
               +----------------------------------------------------------+
               |                                                          |
               |     Please note, the order of the lines in this file     |
               |     must be 1st door on 1st line, 2nd door on 2nd line,  |
               |     etc.  The lines must be in 1, 2, 3... order.         |
               |                                                          |
               +----------------------------------------------------------+

     GTBMENU.BBS     This file is the bulletin menu file.  It  should  list 
                     the  numbered  bulletin  files.  The numbered bulletin 
                     files should  be  located  in  the  "Default  Download 
                     Area",  and  their  file names should simply be 1,  2, 
                     etc.  This menu file will be displayed as users  logon 
                     your  system  and  besides the numeric bulletins,  two 
                     alpha options should be listed:  L)ist  logon  bullets 
                     and  Q)uit bulletin menu.  An example of a GTBMENU.BBS 
                     file: 

                              1.  Bullet #1 description here.
                              2.  Bullet #2 description here.
                              .
                              .  etc.
                              .
                              L)ist logon bullets
                              Q)uit bulletin menu.

                     It  is  possible that these bulletin files can contain 
                     ANSI graphics.  If so, they should be named with a CBS 
                     extension.  For example: 

                           1          Bullet #1, no extension, no graphics.
                           1.CBS      Bullet  #1,   with  .CBS   extension, 
                                      contains graphics.  
                           2          Bullet #2, no extension, no graphics.
                           2.CBS      Bullet #2,    with  .CBS   extension,
                                      contains graphics.

                     Remember:  These bullet files must be placed into  the 
                                "Default  Download Area",  as defined under 
                                the Alt-I pathname setup.  


     GTMDIR.BBS      This  file controls the multiple message bases that GT 
                     can support.  The format of this file is the  same  as 
                     the  format  for  the GTDIR.BBS file,  except that you 
                     have 1 additional option for column 1, you may place a 
                     '*' in column 1 of an line in this file and then  that 
                     message  area  will  become  a  'by  application only' 
                     message base.  The  caller  applies  for  entrance  by 
                     trying to select the message area via the A)rea change 
                     command.  GT  will  inform the caller that application 
                     has been accepted and  the  Sysop  must  approve.  The 
                     users  name  will  be  placed into the GTMAIL.CTL file 


                                   - 19 -



                     associated with the message base, but the BAN bit will 
                     be set,  the Sysop must use Sysop Tools to  reset  the 
                     BAN bit so that the caller can be admitted.  

                     When setting up, the Sysop should insure that all sub-
                     directories  listed  in GTMDIR.BBS exist,  but GT will 
                     automatically  provide  all  the  control  files   and 
                     message directories, as needed.  

                     All  message  areas  must  have an entry in this file.  
                     The main default message area  must  be  open  to  all 
                     callers  and must use the same pathname as the message 
                     base  pathname  in  GT's   configuration   file.   The 
                     GTMDIR.BBS  file  must  be located with the other .BBS 
                     files in GT's home directory.  

           +--------------------------------------------------------------+
           |                                                              |
           |    The PATH name portion of the lines in the GTMDIR.BBS      |
           |    file may be prefixed with either '^', '~', '<' or '$'.    |
           |                                                              |
           |       ^ ... Designates a message area that can support       |
           |             public messages only.                            |
           |       ~ ... Designates a message area that is used as a      |
           |             netmail area (see netmail docs).                 |
           |       < ... Designates a message area that is Read-Only.     |
           |             Only the Sysop can enter messages.               |
           |       $ ... Designates a message area that can support       |
           |             private messages only.                           |
           |                                                              |
           +--------------------------------------------------------------+

                     Examples:

                     Z   ^C:\GTBBS\OPEN       Public Message Base
                     E    C:\GTBBS\GENERAL    General Message Base
                     F    C:\GTBBS\SPECIAL    Special Message Base
                     Z   ~C:\GTBBS\PUBLIC     Public Netmail Area

     GTDOORS.BBS     This file is displayed for the caller when he  selects 
                     the  O)pen  DOORS  option from the main menu.  It is a 
                     pure text file,  which should contain your DOOR  menu.  
                     Each DOOR is assigned a number,  1-999,  and should be 
                     listed on this menu by the number needed to select the 
                     door.  

                     It is possible to have sub-menus,  which work  off  of 
                     the  GTDOORS.BBS menu.  If the GTDOORS.BBS file looked 
                     like this: 

                                   Main Door Menu
                                   --------------
                                   A.  Game Doors
                                   B.  Database Doors


                                   - 20 -



                                   C.  Utility Doors

                     Then   if  the  caller  selected  'A',   the  sub-menu 
                     GTDOORöA.BBS would shown.  Or  if  'B'  were  selected 
                     then  GTDOORöB.BBS  would  be  shown.  Then whenever a 
                     numeric entry was made,  the caller would be put  into 
                     the  selected  door.  A  simple  carriage return would 
                     take  the  caller  back  to  the   main   door   menu, 
                     GTDOORS.BBS.  

     GTDOORnn.BAT    These are the DOOR files themselves.  These are  batch 
     GTDORnnn.BAT    files,  much  like  the  Shell to DOS batch file,  but 
                     instead of executing another copy of  COMMAND.COM,  it 
                     executes your DOOR program.  The mechanism of the DOOR 
                     is  actually the CTTY commands at the start and end of 
                     the file.  The CTTY redirects the console to  the  COM 
                     port  at  the start of the DOOR file,  and back to the 
                     console at the end.  Sample DOOR  files  are  included 
                     with the package.  Here is a short example: 

                                    %1 com%2
                                    edlin %3
                                    %1 con

                     The  %1  will become "ctty" or "rem",  and the %2 will 
                     become the port number,  through substitution by  DOS.  
                     The  "REM" substitution is used when the DOOR is being 
                     run locally by the Sysop to check it out.  A DOOR that 
                     works in the local mode may  not  work  for  a  remote 
                     caller,  because  the DOOR program may not use the DOS 
                     functions to perform I/O with the console.  

                     Remember  that the 3rd command line argument is passed 
                     from the GT host to the DOOR containing  the  response 
                     from  the  caller to a prompt you have placed into the 
                     GTDDIR.BBS file.  In this case,  it would  have  asked 
                     the caller which file he wanted to edit.  

                     Please  note  the  two  forms  of  the   door   names.  
                     GTDOORnn.BAT  is  used  for door numbers 1 through 99.  
                     For  doors  numbered  from  100   through   999,   use 
                     GTDORnnn.BAT.  For example: 

                               Door #5 ..... GTDOOR5.BAT
                               Door #45 .... GTDOOR45.BAT
                               Door #125 ... GTDOR125.BAT
                               Door #999 ... GTDOR999.BAT

     ANSWERn.BBS     This file contains the answers supplied by the callers 
                     to  the 'n' questionaire,  that you have stored in the 
                     QUESTn.BBS  file.  The  format  of  this  file  is  as 
                     follows:  each  answer given by a user is written on a 
                     separate line to this file, the answers are grouped by 
                     placing the users name,  from logon,  onto  the  first 


                                   - 21 -



                     line  of  the  group,  enclosed  within  <<  ...   >>, 
                     following this each answer appears on a separate  line 
                     and  each group is terminated with a line containing a 
                     single period.  Here is an example: 

                               << Paul Meiners >>
                               9350 Country Creek #30
                               Houston, TX 77036
                               713-772-2090
                               .
                               << Susie Meiners >>
                               1245 Sunnyside Dr.
                               Houston, TX 77081
                               713-894-3465
                               .

                     The  example  shown  above  contains  two  groups   of 
                     answers.  As  GT  accumulates answers it will continue 
                     to append them to the end of this file.  If this  file 
                     does  not exist,  GT will create it.  The Sysop should 
                     avoid editing this file,  because any attempt to do so 
                     may render GT incapable of adding answers to it.  

     QUESTn.BBS      This  file  contains  the  questionaire for callers to 
                     fill out.  This feature is optional.  The file  is  in 
                     template  format,  using  the  [------]  construct  to 
                     indicate where GT should gather answers to  questions.  
                     For example: 

                                                  [------------]
                               Enter Phone Number:

                     Would  direct GT to collect the phone number,  showing 
                     GT where to collect the answer and the  maximum  width 
                     answer  to  accept.  Each  answer  can  be  up  to  80 
                     characters long and there may be up  to  50  questions 
                     per questionaire.  

                     After  having filled out the questionaire,  the caller 
                     will be asked if he wishes his answers to be recorded.  
                     If he indicates in the negative,  GT will discard  the 
                     answers.  

                     The questionaire is optional, and if the user tries to 
                     fill out a questionaire that cannot be found,  GT will 
                     indicate to the caller that there is  no  questionaire 
                     currently available.  

                     Date/time   stamping  can  be  done  automatically  by 
                     including a special code in  the  questionnaire  file.  
                     For example: 

                          [%DT]



                                   - 22 -



                     Would  cause  the current date and time to be recorded 
                     in the answer file (no question would be asked  here), 
                     of  course  the  balance of the questionnaire would be 
                     processed in a normal manner.  

                     There can be up to 99 different questionnaires for the 
                     caller  to  choose  from.   The  GTQMENU.BBS  file  is 
                     displayed with a list of all available questionnaires.  

     PQUESTn.BBS     This  file  is  displayed  for  the caller immediately 
                     after he selects the  questionaire  he/she  wishes  to 
                     complete  from  the  questionnaire  menu.   It  should 
                     explain  to  the  caller  the  basic  purpose  of  the 
                     questionaire and allow him to consider if he wishes to 
                     continue  to  fill  out the questionaire.  Immediately 
                     after this file is displayed,  the caller will receive 
                     a prompt, asking if he wishes to continue and fill out 
                     the questionaire.  

                     The PQUESTn.BBS file is optional.

     GTQMENU.BBS     This file is listed for the caller when he selects the 
                     Q  option  from the main menu.  It is a menu file that 
                     should contain a list (in text format) for the user to 
                     choose which questionnaire he wishes to complete.  For 
                     example: 

                         1.  Order form for GT POWER.
                         2.  Order form for Turbo CALC.
                         3.  User poll.

                     This  shows  only  three  options,   as  many  as   99 
                     questionnaires may be supported by the system.  

     PROTOCOL.BBS    This  file  contains  the  protocol  menu that will be 
                     displayed for  the  caller  if  he  initiates  a  file 
                     transfer.  It  is  provided  so  that  the  Sysop  can 
                     customize this menu to his own taste.  It is pure text 
                     format, except for the first line,  which contains the 
                     list of protocols the Sysop wishes to activate for his 
                     system.  The  format  of  this  activation  line is as 
                     follows: 

                                  ;XYZB1TWKMSG

                     Where the ";" appears in column 1 of  the  line.  Each 
                     letter activates a specific protocol, as follows: 

                               X ... Xmodem
                               Y ... Ymodem
                               Z ... Zmodem
                               B ... Ymodem Batch
                               1 ... 1k Telink
                               T ... Telink


                                   - 23 -



                               W ... WXmodem
                               K ... Kermit
                               M ... MegaLink
                               S ... SEAlink
                               G ... Ymodem-G

                     By omitting the activation letter from this line,  the 
                     Sysop may  disable  the  corresponding  protocol.  For 
                     example: 

                                      ;XYZT

                     Would activate and allow on the Xmodem, Ymodem, Zmodem 
                     and  Telink  protocols.  The other protocols would not 
                     be allowed.  

                     The PROTOCOL.BBS file is optional,  if omitted GT will 
                     display a canned protocol menu.  

     WELCOME.BBS     Each  message  base  may  have  a  welcome screen.  It 
                     present,  it resides in the directory with the message 
                     CTL files and is displayed for the caller as he enters 
                     the message base.  It is in the nature of a conference 
                     welcome screen.  The WELCOME.BBS file is optional.  

     MBULLETx.BBS    Each  message  base may have bulletins associated with 
                     it.  These bulletin files will reside in the directory 
                     with the message .CTL files and will be displayed  for 
                     the   caller  after  the  WELCOME.BBS  file  has  been 
                     displayed.  The bulletin numbers are coordinated  with 
                     the regular bulletin numbers in the main GT directory, 
                     which come from the bulletin numbers on the entries in 
                     the GTPASSWD.BBS file.  

                     The MBULLETx.BBS files are optional.

     SYSOP.BBS       This file contains  the  welcome  to  Chat  Mode,  the 
                     prompt  for  City/State given to new callers,  and the 
                     name of the Sysop.  Here is a sample:

                          , here is the SYSOP.
                          What city %& state are you calling from[?]
                          Sysop

                     The intention is that you are able to customize  these 
                     strings to suit your own needs.  

     SCHEDULE.BBS    The  "scheduler" is code within the GT host mode which 
                     allows the sysop to schedule  events.  The  format  of 
                     the  SCHEDULE.BBS  file  is  very simple.  The file is 
                     composed of lines that begin with a time or  range  of 
                     times,   then  the  command  to  be  executed  at  the 
                     specified time.  



                                   - 24 -



                     Examples:

                     03:00       copy file1 file2
                     03:30       QUIT 5
                     04:00-05:00 QUIT 6
                     06:00       maint

                     Based on the above example, at 3 a.m. the GT host will 
                     copy file1 to file2 (any DOS command can  be  executed 
                     like  this).  Then at 3:30 a.m.  the GT host will quit 
                     execution and set an ERRORLEVEL of  5,  the  runstream 
                     that  is  controlling GT must be prepared to deal with 
                     this ERRORLEVEL,  else nothing will be done.  Also the 
                     user  must  insure  that the GT host is restarted.  At 
                     any time between 4 a.m.  and 5 a.m.  the GT host  will 
                     quit  execution  and an ERRORLEVEL of 6 -- this one is 
                     meant to illustrate a quit to  the  netmail  function, 
                     which  should always be started with a range of times, 
                     so that in case it cannot start exactly on the  button 
                     of  4  a.m.  the GT host will start it,  even if it is 
                     late   starting.   Again   the   runstream   that   is 
                     controlling  GT  must  be  prepared  to  deal with the 
                     indicated ERRORLEVEL, 6 in this case, and must restart 
                     the GT host after 5 a.m.  Then at 6 a.m.  the GT  host 
                     will  execute the 'maint' batch file.  NOTE:  when the 
                     GT host starts a command like this, it is done via the 
                     SHELL mechanism,  this requires alot of memory and  it 
                     is  not  recommended  if  you  are using multi-tasking 
                     software.  The netmail documentation includes examples 
                     of how this can be setup.  

                     A  sysop  may  also  add  a  special   line   to   the 
                     SCHEDULE.BBS  file  which  will  allow  control of the 
                     P)age function from the main menu.  The OFFICE command 
                     allows the sysop to  specify  when  a  P)age  will  be 
                     acceptable.  If  a  P)age  is attempted outside of the 
                     specified time range, then the caller will be notified 
                     about the sysop's OFFICE HOURS.  

                     Here is the format:  OFFICE=08:00-21:00

                     The hours must be given in 24:00 notation,  and please 
                     notice that leading zeros, must be supplied.  08:00 is 
                     correct,  8:00  is  wrong!   No  embedded  spaces  are 
                     allowed in this format.  It must be as shown above.  

               +----------------------------------------------------------+
               |                                                          |
               |                          NOTE                            |
               |                                                          |
               |    Five minutes prior to a external event, GT POWER      |
               |    will cease accepting calls and wait for the event     |
               |    start time.  Callers who call in the vicinity of      |
               |    an event will have their time on the system cutback   |


                                   - 25 -



               |    so that the caller will be off the system before      |
               |    the event is to start.                                |
               |                                                          |
               |                                                          |
               +----------------------------------------------------------+

     TRASHCAN.BBS    This file will test your creativity  <GRIN>.  All  the 
                     dirty words go in here,  and then anyone, who uses one 
                     of them in their name,  will not be allowed  to  enter 
                     your system.  The words in the TRASHCAN.BBS must be in 
                     _lowercase_,  otherwise  they  won't be recognized.  A 
                     special wildcard character can  be  used  in  TRASHCAN 
                     words,  the  '?'  character can be used to match *any* 
                     character other than a blank.  The blank is treated as 
                     a delimiter between first and  last  names,  and  each 
                     name  is  checked  against  the trashcan individually.  
                     The check is only performed on  new  callers  to  your 
                     system, so it doesn't slow the regular logon.  And use 
                     of  the  trashcan is optional.  Just leave it out,  if 
                     you don't want to  use  it.  An  example  TRASHCAN.BBS 
                     file: 

                                      d?mn
                                      h?ll
                                      sc??w
                                      f?ck
                                      sh?t

     FILES.BBS       When  you create a directory to contain files,  either 
                     for upload or download,  you should include within the 
                     directory  a  file named FILES.BBS.  It should contain 
                     the descriptions of the  files  contained  within  the 
                     directory.  When  the  caller  selects  the "F" option 
                     from the main menu,  the content of this file will  be 
                     displayed.  

                     The  FILES.BBS  that  is  located  in  the appropriate 
                     upload directory will be  updated  automatically  with 
                     information supplied by the uploader as follows: 

                     Position     Description
                     --------     -----------
                     1-12         Filename
                     13           Blank
                     14-16        File size in kilobytes
                     17           Blank
                     18-25        Upload date
                     26           Blank
                     27-79        File description







                                   - 26 -



     Host Mode Control Files and Directories
     ---------------------------------------
     During  the  operation  of  the  GT  host  mode,   several  files  and 
     directories will be created automatically.  The  Sysop  Tools  program 
     must  be used to maintain these files,  when the need arises.  Here is 
     an overview of the purpose of these files: 

     MESSAGE.CTL     This  file  contains  the  header  information for all 
                     messages maintained by the GT host.  Such  information 
                     as  sender  name,  addressee  name,  date of entry and 
                     whether or not the message has been received, are kept 
                     here.  

     USER_MSG.CTL    This file  contains  information  about  the  messages 
                     which  have  been read by each caller who has joined a 
                     message base.  

     USER_MSG.IDX    The index  file  for  the  USER_MSG.CTL  file.  Speeds 
                     access to individual caller records.  

     USER.CTL        This file contains information about  the  callers  to 
                     your  GT  host.  Such  as  their name,  where they are 
                     calling from and their personal passwords and access 
                     level.

     USER.IDX        The index file for the USER.CTL  file.  Speeds  access 
                     to individual caller records.  

     GTMSGS          This is a sub-directory where the text of the messages 
                     is  stored.  Each message is stored in a separate file 
                     without the header information, which is stored in the 
                     MESSAGE.CTL file.  The messages  are  named  with  the 
                     message  number  as the main filename and extension of 
                     MSG.  

     These  files will be created as necessary by the GT host.  The program 
     Sysop Tools will  perform  needed  maintenance  of  these  files:  for 
     example renumbering the messages,  deleting obsolete users,  providing 
     reports and listings.  HOWEVER,  do  not  run  Sysop  Tools  prior  to 
     establishing these files.  
















                                   - 27 -



     Running Host Mode
     -----------------
     Once installed,  host mode is fairly self-explanatory,  but here is  a 
     quick once over.  

     Host mode is started by pressing "ALT -".  GT will automatically enter 
     "Half  duplex"  mode.  This  is  so  that  anything  typed on the host 
     console will echo so that it can be seen.  Then GT will send the  host 
     mode  Modem Init String to the modem and wait for a call.  While GT is 
     waiting for a call, there are 4 commands available:  [Esc], which will 
     terminate host mode,  carriage return, which allows the Sysop to logon 
     to GT's host mode from the local console, [Ctrl-L], which turns on the 
     system printer for logging,  and [Ctrl-S] to load a fresh copy of  the 
     schedule from disk.  Note that you must have logging enabled in the GT 
     configuration,  via  Alt-I,  the  [Ctrl-L]  command merely enables the 
     printer,  so that whatever is logged will also appear  on  the  system 
     printer.  There  also  is  a  command  line  option to turn on the log 
     printer.  If you place "/p" on the GT command line,  the  printing  of 
     the  log  will  automatically  be turned on from the very start of the 
     program.  

     Once GT has answered an incoming  call,  there  are  several  commands 
     available to the operator, as follows: 

     +--------------------------------------------------------------------+
     |                                                                    |
     |                          SYSOP COMMANDS                            |
     |                                                                    |
     |      Alt-H      List available sysop commands.                     |
     |                                                                    |
     |      Ctrl-D     List current schedule on the screen.               |
     |      Ctrl-L     Toggle log printer on/off.                         |
     |      Ctrl-N     Raise caller's access level while on-line.         |
     |      Ctrl-P     Sysop initiated chat mode.                         |
     |      Ctrl-R     Reset time limit, gives caller more time.          |
     |      Ctrl-S     Load new schedule from disk.                       |
     |      Ctrl-T     Terminate after current caller disconnects.        |
     |      Ctrl-X     Abort the caller.                                  |
     |      Ctrl-Z     Terminate chat mode.                               |
     |                                                                    |
     +--------------------------------------------------------------------+


     Command Line Usage
     ------------------
     When  you  start GT,  there are several command line switches that are 
     available to you: 


     name      You may indicate a script file to be executed upon  start-up 
               of GT.  

     /D        You may indicate whether or not you wish to have GT drop the 
               DTR signal to the modem when GT exits back to DOS.  


                                   - 28 -




     /C        You  may indicate whether you are connected via cable to the 
               host computer.  

     /K        You may initiate the capture mode from the very start of the 
               program.  

     /M        Suppress the "Check for personal mail?" function.

     /MN       This would allow the "Check for personal mail?" function to 
               continue, *but* would change the default prompt from [Y/n] 
               to [y/N].  

     /P        You may enable logging to the system printer.

     /S        This option will allow the Sysop Page to be heard during 
               quiet mode.  Normally, nothing would be heard during quiet 
               mode.  

     /Tn       This option will override the normal keyboard timeout value 
               of 10 minutes.  When this timeout occurs, GT will disconnect 
               the caller.  For example:

                   /T5     Lower the timeout to 5 minutes.
                   /T45    Raise the timeout to 45 minutes (my favorite).

     /1        You may configure the port addresses in use by  your  serial 
               port.  The  actual  port  number to be configured,  1-4,  is 
               placed  after  the  slash.  The  new  base  address  of  the 
               indicated  port  is  placed  after  the slash number with an 
               intervening blank.  The address must be given with a leading 
               $ sign and be in hex notation,  for example $3F1 would be  a 
               valid address.  Refer to your hardware documentation for the 
               correct  address  to use.  GT uses standard addresses if you 
               do not override with this option.  

     /Rn       This option applies to the GT host mode.  It  specifies  the 
               ring  number  upon which GT will answer incoming calls.  For 
               example /R3 would cause GT to answer on the 3rd ring.  NOTE: 
               that the host mode modem init string must  contain  S0=0  to 
               allow this to work properly.  

     /RBmm:nn  This  option applies to the GT host mode.  It specifies that 
               GT should answer the modem after a "ring  back".  To  enable 
               this to work properly,  the host mode modem init string must 
               contain S0=0.  Once installed properly this option makes the 
               GT host mode answer the phone on the 2nd or 3rd ring after a 
               gap of between 'mm' and 'nn' seconds.  If  the  gap  between 
               rings  is  less  than  'mm'  seconds  or  greater  than 'nn' 
               seconds,  GT will not answer the phone.  This allows the use 
               of  an  answering  machine  on  the  same  phone line as the 
               computer.  The answering machine  should  be  programmed  to 
               answer on a later ring, the 4th for example.  The 'mm:nn' is 
               optional, and will default to a 9 to 32 second gap.  


                                   - 29 -




     /V:s      This option will cause selected funstions to overlay GT when 
               they are executed.  The 's' parameter represents the list of 
               functions that are to be  overlaid.  For  example,  's'  may 
               contains  the following letters,  representing the functions 
               shown: 
                         E .... External protocols.
                         D .... Door batch files.
                         L .... Logon/Logoff batch files.

               If GT is overlaid  by  a  function,  then  when  the  caller 
               disconnects,  GT  will  exit  to DOS with an 'errorlevel' of 
               255.  So,  the HOST.BAT file must be built to trap  the  255 
               'errorlevel': 

                      HOST.BAT File
                      -------------
                         GT1500 /V:DL host.scr
                         IF errorlevel 255 HOST

                      HOST.SCR File
                      -------------
                         host
                           
     +------------------------------------------------------------------+
     |                                                                  |
     |   This listing of command line switches came from the main GT    |
     |   documentation file.  Please refer to that document for sample  |
     |   usage of these switches.                                       |
     |                                                                  |
     +------------------------------------------------------------------+


     Using a LAN with GT
     -------------------
     Running  a  multi-node  BBS  with  GT is easy.  GT will allow up to 10 
     nodes on a network to share common message bases and file  areas.  The 
     first thing you must do is decide on a structure for your network BBS.  
     One  of  the systems must be identified as the 'server' and it will be 
     referred to as "PID Zero" in the coming  document  (however,  you  can 
     easily  have multiple servers,  PID Zero is special).  PID Zero is the 
     central system on the  network,  where  all  the  caller  records  are 
     stored,  and  where  the  "PID_FILE.BBS" is maintained.  Once you have 
     decided on the structure of the network,  you must install GT on  each 
     node  ---  part  of  the  installation process for GT on a LAN node is 
     setting the  LAN  parameters  under  the  Alt-I  configuration.  Three 
     pieces of information must be provided for each node: 


         PID Number ... Must be a unique number between 0 and 9.

         PID Name ..... The name by which this node is known to the network 
                        software.  



                                   - 30 -



         LAN Path ..... This  must  be  the  home  directory  for GT on the 
                        network  server  (PID  Zero).  The  LAN  Path  will 
                        contain the USER.CTL, USER.IDX and PID_FILE.BBS (at 
                        the  least).  These  are created automatically.  It 
                        is assumed that these files will  be  shared  among 
                        the other systems on the LAN.  


     The  LAN  Path must be specified to get file and message sharing fully 
     enabled.  Without a LAN  Path,  GT  will  assume  that  a  non-sharing 
     environment is established (like a regular single node BBS).  

     File sharing is implemented using the record locking facilities of DOS 
     3.1+ SHARE.EXE.  It is recommended that you give this program adequate 
     facilities  to do its job.  This command line seems to work well,  but 
     more resources may need to be allocated on busy systems: 

                               SHARE /F:7168 /L:70

     It should also be  noted,  that  some  LANs  require  your  CONFIG.SYS 
     parameters  to  be changed.  For example FCBS may need to be specified 
     on LAN servers, for example: 
     
                                   FCBS=24,12

     And STACKS are very important under a LAN enviroment.  With DOS 3.2, I 
     would  recommend  switching  to  DOS  3.3.   With  DOS  3.3,  I  would 
     recommend: 

                                  STACKS=62,512

     DOS 3.2 has some bugs that do not make it a good choice for the DOS on 
     the  LAN  server.  It has also been observed that BUFFERS are critical 
     on a LAN.  Setting BUFFERS above 30 is a sure formula for a  crash.  I 
     recommend: 

                                   BUFFERS=25

     If this response of the server becomes to slow, due to the low setting 
     of BUFFERS,  rather than raising the BUFFERS, I would suggest that you 
     obtain a LAN compatible disk cache program.  Ask  your  LAN  maker  to 
     recommend one for you.  

     Finally,  resist the temptation to overload the directory indicated as 
     the  "LAN  Path".  For example,  do not have the workstations use that 
     directory for  the  log  files.  This  would  result  in  chaos.  Each 
     workstation must have its own GTPATH and LOG Path.  









                                   - 31 -



     Host Mode LOG
     -------------
     A  few sections above,  I suggested that logging be TRUE,  while GT is 
     running in Host Mode.  Here is why:  during Host Mode  operations,  GT 
     will log all of the calls received,  who called and the password used.  
     A record will also be kept of who tranfered each  file,  how  long  it 
     took  and the efficiency of the transfer.  I consider the gathering of 
     this information to be critical to the operation of a GT Host.  

     The Shell to DOS
     ----------------
     The DOS Shell allows remote callers to operate your computer remotely.  
     When the "Shell to DOS" option of the main menu is selected,  GT  will 
     shell  to  the  file GTDOOR.BAT.  This file will set up for the remote 
     shell by executing the proper CTTY command,  then execute a  secondary 
     DOS shell and let the user into the system.  He will have the console, 
     so  be  cautious!  The  caller  will be instructed to issue the "EXIT" 
     command to return to GT.  

     While the DOS Shell is active and the caller is out in the system,  GT 
     will  not  be  idle.  GT will act as a watchdog.  If the caller should 
     hang up while the DOS shell is active, GT will force the system to re-
     boot and will drop the DTR signal to the modem.  If commands to  start 
     GT  are  placed in the AUTOEXEC.BAT file and a script is used to start 
     Host Mode,  then GT will automatically recycle.  The script command to 
     start Host Mode is simply HOST.  

     NOTE:  For  this process to work correctly,  the COMMAND.COM file must 
            reside in a  directory  pointed  to  by  the  PATH  environment 
            variable.  In order for this to work on a normal drive C:  hard 
            disk, "C:\" should be added to the PATH variable.  For example: 

                      PATH=c:\dos;c:\lotus;c:\

            This will ensure that the COMMAND.COM file can be  located  for 
            execution by the GTDOOR.BAT runstream.  

            A  problem  with the DOS Shell has been reported when using DOS 
            2.xx.  This is caused by  the  fact  that  DOS  2.xx  does  not 
            support  full  pathnames  when  requesting  the  execution of a 
            program.  To work around this problem,  if you have  DOS  2.xx, 
            you  should  place  the GTDOOR.BAT file in some other directory 
            besides the GT home directory.  If GT finds GTDOOR.BAT  in  his 
            home  directory,  then GT will issue an EXEC function with full 
            pathname,  otherwise GT will not specify any pathname and  will 
            rely  on  the DOS PATH command.  The directory where GTDOOR.BAT 
            is stored must be pointed to by the DOS PATH  command  in  this 
            case.  








                                   - 32 -



     Using the Shell to DOS
     ----------------------
     What  can  one do,  once one is running DOS remote via a CTTY command?  
     Well,  one can't use any of the Fn keys or the other special  keys  on 
     the  IBM  key-board!  One  can't  run  any  program  that  does direct 
     hardware control of the screen or keyboard.  All screen  and  keyboard 
     input must be done through DOS.  Well,  then what can one do?  One can 
     run any  DOS  command;  for  example  COPY,  ERASE,  DIR  and  others, 
     including  EDLIN,  all work properly.  In fact,  any program that uses 
     the standard DOS handles for input and  output  to  the  console  will 
     work.  But  one  still  won't have F1 - F10 or the other special keys.  
     Well, that's not quite so...if the Host Mode computer is setup so that 
     the ANSI.SYS device driver is loaded via  the  CONFIG.SYS  file.  Just 
     put a line like this one into the CONFIG.SYS file: 

                               DEVICE=ANSI.SYS

     Naturally,  ANSI.SYS must be located in the root directory of the boot 
     disk.  After that has been done,  re-boot the computer.  ANSI.SYS will 
     then  be  loaded.  One can now re-map the keyboard so that the special 
     keys are mapped to Ctrl keys instead.  This will enable programs to be 
     run that use these keys; for example EDLIN uses the arrow keys as well 
     as several function keys.  

     How does one re-map keys with ANSI.SYS?  The following  sequence  must 
     be issued for each key that needs to be re-mapped: 

                            ESC [ ##;##;##;...p

     The  (...)  indicate that the sequence may be repeated as needed,  but 
     each sequence only re-maps one  key.  Once  a  file  containing  these 
     mapping  commands  has  been created,  they can be sent to ANSI.SYS by 
     TYPEing the file.  The "##" in the sequence above indicate  the  ASCII 
     codes  for  the  keys to be mapped.  For example,  let's map F3 to the 
     Ctrl-D key.  The ASCII codes for F3 are 0,61 and the  ASCII  code  for 
     Ctrl-D  is  4.  (Note:  the special keys have two codes - the first is 
     always 0.  These  codes  are  really  called  extended  ASCII  codes.) 
     Therefore,  the  proper  ANSI.SYS command to re-map F3 to Ctrl-D would 
     be: 

                            ESC [ 4;0;61p

     Note:  Blanks are included for  readability  only,  the  "p"  must  be 
            lowercase,  and the symbol ESC stands for the escape character, 
            CHR$(27).  











                                   - 33 -



     Generic Tool Interface
     ----------------------
     The GT Host Mode now supports a Generic Tool  Interface.  The  purpose 
     of  which  is  to  allow  utility writers to more intimately interface 
     their programs to GT.  In this process,  GT gives up all of its memory 
     to  the tool program,  thus allowing much greater access to memory for 
     the tool program.  The GTI will be based upon the DOS EXEC function as 
     implemented in the C library function "exec...".  This means  that  GT 
     will  be  completely overlaid by the tool program and to return to GT, 
     the tool program must invoke GT in the same  manner  it  was  invoked.  
     Here  is the complete interface description,  the nomenclature is that 
     of the C manual,  since this is expected to be of use to C programmers 
     only.  

          arg0 .... Name of child program (full pathname).
          arg1 .... "-exr", indicates remote operations.
                    "-exl", indicates local operations.
          arg2 .... Name  of  parent  program  (full  pathname,  needed for 
                    return).  
          arg3 .... COM port number.
          arg4 .... Baud rate.
          arg5 .... Parity.
          arg6 .... Databits.
          arg7 .... Stopbits.
          arg8 .... Flags (for use by GT only).
          arg9 .... Registration key ("-nokey" is unregistered).

     Much of this information is included simply to  restart  GT  once  the 
     tool  program  is  finished  with  its work.  When the tool program is 
     prepared to return to  GT,  it  should  swap  'arg0'  and  'arg2'  and 
     reinvoke GT via the "exec..." function.  

     If  you  write  a  program  that  uses this interface you will need to 
     inform your users that they can invoke the interface thru a macro key.  
     The {@/} is the macro command that invokes the GTI in GT.  The  actual 
     coding of the macro key would look like this: 

               {@/}c:\gt\gtexec.exe|

     Which would invoke a program called GTEXEC.EXE in the C:\GT directory.  
     Naturally,  this program had better be prepared for this invokation or 
     it will not return to GT when finished!  

     Remote Sysop Interface
     ----------------------
     This interface is totally user configurable.  At the main menu of  the 
     GT   Host   mode,   the   sysop   can   enter   one   of  the  numbers 
     1,2,3,4,5,6,7,8,9,0.  These numbers correspond to the macro keys  Alt-
     F1  through  Alt-F10.  For  example,  if the sysop enters a 1 then the 
     command in Alt-F1 is executed.  If he enters a 0 then the  command  in 
     Alt-F10  is  executed.  If  a  non-sysop  tries  to enter any of these 
     numbers the program will treat them as  invalid  input.  This  feature 
     could  have many uses,  but is intended primarily as a way to remotely 
     execute the GTI (described above).  


                                   - 34 -



     Usage of Color
     --------------
     The GT Host mode now includes color built-in to  the  various  prompts 
     and  menus.  These  colors  can be configured.  The colors used are of 
     two different sets.  The first set is composed of the colors  for  the 
     "Window foreground and background", and the "Phone directory high lite 
     foreground  and  background".  These  colors should be subdued,  since 
     they are used for normal informational type  displays.  For  important 
     command  line  and  menu  displays,  the  program  will use the colors 
     designated for "Option high lite" and "Option low lite".  

     The user  can  customize  the  sysop  prompt  with  these  colors,  by 
     including  the  color  codes  in the SYSOP.BBS file.  Here is the code 
     scheme: 

          %  ...... Used to kill the meaning of the next character.
          %% ...... Used to display the % character.
          $  ...... Shift   the   pallette  to  the  "Window  foreground  / 
                    background" set.  
          &  ...... Shift the pallette to the "Option  high/low  lite"  set 
                    (the default).  
          [] ...... High lites whatever is between the [ and ].
          ~  ...... Kills the color.  Goes back to standard B&W image.

     For example:

          $ [SYSOP] John~ here.

     This  would  shift pallette to the "Window foreground/background" set, 
     high lite the word "SYSOP" and kill the color after the name "John".  

     Actually,  this scheme was only intended to add color to the SYSOP.BBS 
     file  and  other  built-in  menus  and prompts,  but some have already 
     discovered that these colors  can  be  added  to  the  GTMDIR.BBS  and 
     GTDIR.BBS files, to add color and emphasis.  


     Logon DOOR
     ----------
     In the GT POWER home directory,  it is possible to create a DOOR file, 
     with a special name,  that will be executed whenever a user logs  onto 
     your system.  The file is named 'GTLOGON.BAT' and it is constructed in 
     the  same  manner  as  a  normal  DOOR  batch file (shown above).  For 
     example: 

             GTLOGON.BAT
             -----------
                 %1 com%2
                    .
                    .    { Logon door executes here }
                 %1 con

     The sequence of events goes like this after a user calls your system: 



                                   - 35 -



          1.  The GTWELCOM.BBS is displayed.
          2.  Then any BULLETx.BBS is displayed.
          3.  Then the GTBMENU.BBS is displayed.
          4.  Then the GTLOGON.BAT is executed, if available.

     It  is  possible  to have a special logon door for new callers.  It is 
     named 'GTNLOGON.BAT'.  It will execute just prior to the regular logon 
     door.  If you have logon/logoff doors overlaid,  then you  must  chain 
     from  the  new caller logon door to the regular logon door.  Remember, 
     this is only required if you use the command line  options  /V:L.  For 
     example: 

             GTNLOGON.BAT
             ------------
                 %1 com%2
                    .
                    .             { New user logon door executes here }
                    .
                 %1 con
                 GTLOGON          { Chain to regular logon, if overlaying }
     

     Logoff Batch File
     -----------------
     It is, also, possible to have a logoff batch file, 'GTLOGOFF.BAT',  in 
     the  GT  home directory.  This is not a DOOR,  but simply a batch file 
     that GT POWER will run,  if it  is  available,  whenever  a  user  has 
     disconnected  from your system.  It may contain any normal DOS command 
     or other processing as required, if enough memory is available.  

     GT  remains  in  memory while this batch file executes in a normal DOS 
     Shell.  It can be useful for sysops that want to backup their files if 
     they are using a RAM disk for things like the log file.  

     Please note, this is not a DOOR, that CTTY is not redirected, and that 
     the 'watchdog' is not enabled during the execution of this batch file.  

     In addition,  when you have a new caller to your system,  GT will run, 
     if  available,  a  batch  file  called  'GTNLOGOF.BAT'.  If  you  have 
     requested overlaid logon/logoff doors,  then you  must  chain  to  the 
     logoff door (if you have one).  Remember, this is only required if you 
     use the command line option /V:L.  For example:

             GTNLOGOF.BAT
             ------------
                    .            { No DOS redirection in logoff doors }
                    .
                    .            { New user logoff door executes here }
                    .
                 GTLOGOFF        { Chain to regular logoff, if overlaying }






                                   - 36 -



     APPENDIX
     --------
     Here is a handy list of extended ASCII codes:

               Key       Codes                 Key            Codes
               ---       -----                 ---            -----
               F1        0,59                  Right Arrow    0,77
               F2        0,60                  Left Arrow     0,75
               F3        0,61                  Up Arrow       0,72
               F4        0,62                  Down Arrow     0,80
               F5        0,63                  Home           0,71
               F6        0,64                  End            0,79
               F7        0,65                  PgUp           0,73
               F8        0,66                  PgDn           0,81
               F9        0,67                  Ins            0,82
               F10       0,68                  Del            0,83



     Here are some sample ANSI sequences!

                    Escape Codes         Meaning to ANSI.SYS
                    ------------         -------------------
                    ^[[4;0;61p           F3          -> Ctrl-D
                    ^[[5;0;62p           F4          -> Ctrl-E
                    ^[[19;0;77p          Right Arrow -> Ctrl-S
                    ^[[1;0;75p           Left Arrow  -> Ctrl-A

     With these kinds of mappings,  almost any program should  be  able  to 
     run,  if  it uses the DOS handles for standard input and output.  This 
     should make the "Shell to DOS" quite useful.  

























                                   - 37 -



     Setup for Power-Loss Protected Operation
     ----------------------------------------
     It is quite easy to prepare a set of files  that  will  allow  you  to 
     bring  GT  POWER  up  into  what  I  should  like to call a Power-Loss 
     Protected Host Mode of operation.  First, however, a few concepts: 

     Whenever power  is  first  applied  to  your  system,  (or  re-applied 
     following  a blackout),  the system will boot your DOS into memory and 
     that, in turn,  will look for two files;  CONFIG.SYS and AUTOEXEC.BAT.  
     Finding the CONFIG.SYS, the DOS will tailor your environment according 
     to  its  contents  (such  as setting a new maximum number of files and 
     file buffers).  Finding the AUTOEXEC.BAT file will cause the system to 
     immediately execute the set of DOS instructions found therein.  

     GT POWER may be caused to  run  in  an  unattended  Host  mode  either 
     through  GT commands entered at the keyboard (Alt-dash) or via script.  
     The GT command to do so in a GT script is simply: HOST.  

     The user should have a TSR called DOORMAN  loaded  if  the  'watchdog' 
     function  is  required  during  a remote shell to DOS or a remote door 
     activation.  DOORMAN will reboot the computer  in  the  event  that  a 
     caller drops carrier while is the shell or door.  

     Given  the  above,  to set up the system for Power-Loss_Protected Host 
     mode operation of GT POWER you must construct the following files: 

          Your normal AUTOEXEC.BAT
          A copy of the normal AUTOEXEC.BAT called AUTOEXEC.OLD
          A new file called AUTOEXEC.GT
          A new file called HOST.BAT
          A GT script file called HOST.SCR

     The first four of these files belong in your root directory while  the 
     script  file  should  be  placed  in  the  same  directory as GT POWER 
     resides.  When you want to enter the Power-Loss-Protected Host mode of 
     GT POWER you need only type the single word HOST from  any  directory.  
     The  result will be the invoking of the HOST.BAT file which,  in turn, 
     copies the AUTOEXEC.GT file on top of  your  normal  AUTOEXEC.BAT  (so 
     that if a re-boot occurs it will get control),  it then sets a default 
     directory so that your  private  directories  are  not  accessible  to 
     callers  into the system,  and then it invokes GT POWER specifying the 
     name and location of the HOST.SCR script file you  created.  Thus,  GT 
     will  be  given  control  and  placed  into  Host  mode.  Upon  normal 
     termination,  GT exits to DOS which returns to the unexecuted  portion 
     of  the HOST.BAT file and continues by doing a copy of AUTOEXEC.OLD (a 
     copy of your original AUTOEXEC.BAT) on top  of  the  current  one  and 
     ending.  

     In the event of a power failure while in Host mode, or loss of carrier 
     while  in  the DOS Shell,  the AUTOEXEC.BAT file that is in place will 
     reset to the default (safe) drive and reinvoke the  Host  mode  of  GT 
     POWER.  




                                   - 38 -



     Sample Files for Power-Loss Protected Operation
     -----------------------------------------------
     Original AUTOEXEC.OLD:

          PATH=C:\DOS;C:\;C:\GT
          set GTPATH=C:\GT

     AUTOEXEC.GT:

          PATH=C:\DOS;C:\;C:\GT
          set GTPATH=C:\GT
          host

     HOST.BAT:

          copy    autoexec.gt autoexec.bat
          cd      \bullet
          gt1500  host.scr
          if      errorlevel 255   host
          cd      \
          copy    autoexec.old autoexec.bat

     HOST.SCR:

          host































                                   - 39 -



     GT POWER under DESQview(tm)
     ---------------------------
     GT POWER runs quite well as  a  task  under  the  DESQview(tm)  multi-
     tasking  system.  There  are  a few things that should be kept in mind 
     when doing so, however.  

     For example,  in order to prevent any 'bleeding' of  your  GT  screens 
     into  another  task,  you  must  set the BIOS parameter of GT to TRUE.  
     Note that the effect of doing so totally eliminates any use of  direct 
     screen  writes  by GT and that it will substantially increase the time 
     it takes GT to 'open' a window.  It does not affect any other function 
     of GT nor does it affect any other aspect of GT performance.  
  
     Also, you will need to provide enough memory for GT to run while under 
     DESQview(tm).  If you do not have to consider KERMIT  or  ZMODEM  then 
     you  can  run  GT  in  a  partition  of  as  small  as  330K  of  RAM.  
     Experimentation has shown that in order  to  support  ZMODEM  and  the 
     other  protocols  mentioned  above  you will need to set the partition 
     size to 440K.  

     GT,  as it requires rapid access to the serial port you are using  for 
     communications must be the first task loaded in DESQview(tm).  And,  a 
     performance option of DESQview(tm) (set by invoking the SETUP program) 
     must be set showing the existence of High Speed Communications.  Other 
     options that need to be set include the fact that GT is NOT  SWAPPABLE 
     to  disk and time slices somewhere between 3 and 6 ticks in length per 
     partition.  
 
     (tm) DESQview is the trademark of QuarterDeck Office Systems.


                                   - THE END -
























                                   - 40 -