Tel Codes - A TTY/TDD history, courtesy Telecom Digest (13 March 1990)


From: CER2520@ritvax.bitnet (Curtis E. Reid)
Subject: Brief TDD History
Date: 15 Feb 90 00:25:00 GMT
Sender: news@accuvax.nwu.edu
Organization: TELECOM Digest
           Telephone Devices for Deaf Users: Milestones
 
Source: _1990 International Telephone Directory for TDD Users_ by
Telecommunications for the Deaf, Inc., 814 Thayer Avenue, Silver Spring, MD
20910, Copyright 1989.
 
1964:
 
An acoustic coupler modified for Baudot which permitted
teletypewriters to be connected to standard telephones, was invented
by Robert Weitbrecht, a deaf scientist.  Dr. James C. Marsters, a deaf
orthodontist, had sent Weitbrecht a Teletype Model 32ASR with a
request that a system be set up so that Marsters, in Pasadena,
California, could communicate with Weitbrecht in Redwood City.  Unlike
Weitbrecht, Marsters did not have a ham radio license, so they decided
to use the public phone system.
 
Weitbrecht's acoustic coupler was based on a half duplex operation in
which signals are transmitted one at a time.  Teletypewriters were
Baudot coded.  These machines were available because AT&T, Western
Union and other communications companies were in the process of
conversion to a new telegraphic code.
 
Weitbrecht's acoustic coupler was first publicly demonstrated at the
1964 biennial meeting of the Alexander Graham Bell Association for the
Deaf, Salt Lake City, Utah.
 
1968:
 
Approximately 25 teletypewriter stations were in operation for/by the deaf.
 
1969:
 
Tax-exempt status was granted to TDI [Telecommunications for the Deaf,
Inc.] by the U.S. Internal Revenue Service.
 
1971:
 
"Scanatype", a digital readout form of the TTY was introduced by ESSCO
Communications.
 
1979:
 
Telecommunication Device for the Deaf (TDD) was accepted as the
appellation for all TTY-like devices.
 
1985:
 
Krown Research introduced dual ASCII/Baudot modems to be used with
dumb terminals.  Audiobionics, Inc. introduced an enhanced version of
a synthesized voice "talking" portable TDD.  Ultratec, Inc. introduced
a low-cost basic TDD.  Other manufacturers discontinued production of
TDDs as competition for lower cost TDDs increased.  Nevada Association
for the Deaf hosted the Sixth TDI Convention.  Distribution of free
TDDs began in many more states such as Florida, Arizona, Nevada,
Wisconsin, Illinois and Massachusetts.
 
1987:
 
California opened first state-wide, 24 hour, 7 day a week relay
service operated by AT&T.
 
1988:
 
President Ronald Reagan signed the bill to expand federal
telecommunication services for speech and hearing-impaired people;
which was introduced by Representative Steve Gunderson (R-WI) and
Senator John McCain (R-AZ).
 
-=-=-=-=-=-=-=-=-=-=-=
From: CER2520@ritvax.bitnet (Curtis E. Reid)
Subject: Common TDD Terms
Date: 15 Feb 90 00:26:00 GMT
Sender: news@accuvax.nwu.edu
Organization: TELECOM Digest
                             Common TDD/TTY Terms
 
TTY  Teletypewriter
TDD  Telecommunication Device for the Deaf
GA   Go Ahead, your turn to type
SK   Stop Key, meaning end of conversation
CUZ  Because
HD   Hold, please
PLS  Please
OIC  Oh, I see
U    You
UR   Your
CD   Could
Q    Question mark (Also ?)
MTG  Meeting
R    Are
NBR  Number (Also NU or NO)
OPR  Operator
CUL  See you later
SHD  Should
WLD  Would
TMW  Tommorrow (Also TOM)
 
*  To be effective, punctuations are not used during TDD
   conversations.
*  Please identify yourself while answering TDD calls as it is
   rather difficult to recognize one's voice through printed
   letters.
*  Tap the space bar several times for numbers that use both TDD
   and Voice.
 
-=-=-=-=-=-=
From: CER2520@ritvax.bitnet (Curtis E. Reid)
Subject: TDD Specifications
Date: 15 Feb 90 00:25:00 GMT
Sender: news@accuvax.nwu.edu
Organization: TELECOM Digest
               Specifications For TDD Data Transmit/Receive
 
All TDD manufacturers follow these specs but no tolerance level is given:
 
1.  Acoustic coupling (standard G- and K- type handset)
 
    Input level: 65 dB SPL minimum / 110 db SPL maximum
                                   -4        2
                 (0 dB SPL = 2 x 10   dyne/cm )
 
    Output level: 95 dB SPL minimum / 100 dB SPL maximum
                  (acoustic pressure to produce a -9 dBm
                   signal at the telephone set line terminals
                   on an average loop)
 
2.  Direct modular connection
 
    Connector:  standard 6-position modular jack
 
    USOC No.:   RJ11C
 
    Input level: -50 dBm minimum / 0 dBm maximum
 
    Output level: -13 dBm minimum / -9 dBm maximum
 
3.  Modem
 
    Modulation method:  Frequency Shift Keying
 
    Mark frequency:  1400 Hz +-5 Hz
 
    Space frequency:  1800 Hz +-5 Hz
 
    Signal to noise ratio:  13 dB
 
    Carrier to data delay:  180 ms
 
    Carrier to hold time:  156 ms
 
4.  Protocol
 
    Code:  Baudot
 
    Mode:  Half duplex
 
    Transmissions:  Asynchronous
 
    Start bit:  1
 
    Stop bit:   1
 
    Data bits:  5
 
    Parity:  None
 
    Data rate:  45.5 baud (buffered)
 
Note: The above information is from Plantronics, Inc. (manufacturer of
the Vu-Phone) and is assumed to be consistent with other brands as the
Vu-Phone is compatible with all other TDDUs.