01
      A     -  Select Auto Log Feature.

           The  'A'  command selects the Auto Log  feature  which 
           provides  a  means  to make a hard copy  record  of  a 
           simulation run.   The 'AE' commands enables the  auto-
           log feature and allows selection of the destination of 
           the log output.  'S' selects the display screen on the 
           numeric display screen,  'D' selects a disk file named 
           'HISTORY.DAT',  and  'P' selects the printer connected 
           to  'LPT1:'.   Auto-Log reocrds every command  isssued 
           and any danger warnings issued by the  reactor.   This 
           feature  can  be  disabled by the 'AD'  option  or  by 
           pressing 'A' and 'Return'.
02
  B     -  Set Bias value.

           The  'B' command allows the setting of the bias  value 
           used  by the automatic control system to maintain  the 
           heat exchanger temperature near the set point tempera-
           ture.   This  value may range from 1 to 5.   1 is  the 
           most sensitive setting and should be used whenever the 
           reactor is operating close to its' limits.  This value 
           may only be changed when automatic control is on.  The 
           set  point  temperature is controlled by the 'C'  com-
           mand.
03
  C     -  Set Automatic Control Temperature.

           This command sets then heat exchanger temperature that 
           will  be  maintained by the automatic control  control 
           system {F5}.   The value can be set anywhere from 350F 
           to  505F.   The automatic control program will  adjust 
           rod height to maintain the heat exchanger  temperature 
           within  the  Bias setting of the control  temperature.  
           This  temperature  will be automatically  adjusted  to 
           meet power demand when Automatic Set-point {F6} is on.  
           This value can only be changed when automatic  control 
           is on.
04
  D     -  Make-up Feed Destination.

           This  key allows selection of the destination for  the 
           make-up feed flow.  'P' causes make-up feed to be sent 
           to the primary loop, 'S' causes feed to be sent to the 
           secondary  loop,  and 'N' causes feed to be  recircul-
           ated.   The  make-up feed pump should be operating for 
           flow  to go to the primary or  secondary  loops.   The 
           secondary  loop will drain if 'S' is selected and  the 
           make-up feed pump is off.
05
  E     -  Emergency Coolant Pump Speed.
 
           This command selects the emergency cooling pump speed.  
           The pump can either be off, speed 0, or on, speed 1 to 
           100%.   This  pump is used to provide rapid cooling to 
           the  reactor core.   The emergency cooling  supply  is 
           limited, but is adequate to lower the core temperature 
           to safe levels.
06
  F     -  Freeze and Save Simulation Run.

           This  command  stops the simulation run and saves  the 
           pertinent variables to a file named 'RXFRZ.DAT'.  When 
           the simulation is started at a later time,  the opera-
           tor  is asked whether the saved simulation  should  be 
           executed.   A 'Y'es answer will load the variables and 
           restart  the  simulation at the point it  was  frozen.  
           Only one simulation run can be frozen at any time.
07
  G     -  Current Production Graph

           This command graphs the electrical output against  the 
           demand.   The  graph  shows  the most recent  10  hour 
           period.
08

09
  M     -  Make-up Feed Pump Speed.

           This  command  selects the speed of the  make-up  feed 
           pump.  The pump can be off, speed 0, or on, speed 1 to 
           100%.  This pump is used to provide additional coolant 
           to the primary and secondary cooling systems.   As the 
           reactor  heats up,  primary coolant must be drained to 
           maintain  the primary volume within  limits.   As  the 
           reactor  cools down,  coolant must be added to make up 
           for the drained coolant.   The secondary system  loses 
           coolant through gland sealing steam and minor leakage.  
           This pump should be on at all times, running at 50% or 
           less.   In  this recirculation mode,  make-up feed  is 
           instantly available.
10
  P     -  Primary Coolant Pump Speed.

           This  command  selects the pump speed of  the  primary 
           coolant  pump.   This  pump circulates  high  pressure 
           water through the reactor core and transfers heat from 
           the reactor to the heat exchanger.  This pump normally 
           operates at 90% or above.  Both the primary and secon-
           dary coolant pumps must both be off to completely shut 
           down the reactor.
11
  Q     -  Alarm and Warning Test
                 
           This command tests the alarm and warning indicators on 
           the  console.   Pressing this key a second time resets 
           the  alarm and warning indications and shows only  the 
           active alarms.
12
  R     -  Rod Height.

           This  command  selects the control  rod  height.   The 
           control   rods   provide  direct  control   over   the 
           reactivity of the core, and thereby control the core's 
           temperature.   The  higher the rods,  then the core is 
           more reactive,  and more heat is produced.  The opera-
           ting  range of the rods is between 0,  on the  bottom, 
           and 100%,  completely withdrawn.   The two SCRAM  com-
           mands {ESC  and  F1} cause the rods  to  be  instantly 
           dropped to the bottom.
13
  S     -  Secondary Coolant Pump Speed.

           This  command selects the speed of the secondary cool-
           ant  pump.   This pump circulates the condensed  steam 
           from the cooling tower/condenser to the heat exchanger 
           where  it again produces steam.   This  pump  normally 
           operates  at  90% or above.   Both this pump  and  the 
           primary  coolant  pump must be off to completely  shut 
           the reactor down.
14
  T     -  Terminate Simulation

           This command terminates the simulation and  calculates 
           a  score based on the production rate,  damages incur-
           red,  and production deficit.   The score is  adjusted 
           for  the length of the simulation run.   A  cumulative 
           score   is  maintained  in  the  file  'RXSTATUS.DAT'.  
           Erasing this will clear the cumulative score.
15
  U     -  Disable Alarm

           This  command switched the audible alarm system on and 
           off.  
16
  V     -  Current Version

           This  command displays the current version  number  of 
           the  Reactor-100 main program.   Please refer to  this 
           number when reporting any problems with the program.
17
  Z     -  Change Timer Setting

           This command allows changes to the time interval  bet-
           ween  screen updates.   The allowable intervals are  0 
           (no  delay),  or 3 to 10 seconds.   The normal  update 
           interval is once every 2.5 seconds.
18
  'H'   -  Provides information.

           Help  is available by using the help key or using  the 
           lightpen.   The  help menu can be used by entering the 
           number next to the subject of interest.   The lightpen 
           can be used to select Help on any item of interest  by 
           pointing  the lightpen at the subject and pressing the 
           switch.   The  lightpen can also be used on  the  Help 
           menus.
19
  Tab   -  Bypass Sign-on Message

           This command can be used during the program sign-on to 
           bypass  the delay.   This will also bypass the initial 
           Help screen.
99