System:    Pressurizer

Operating Limits:    Level - 50% to 85%

Function:  Maintains  primary  loop  pressure by  creating  steam
           bubble.   Provides  reservoir  of primary  coolant  to
           handle sudden changes in temperature, thereby insuring
           that  the core remains covered.   Pressurizer  heaters
           must  be covered at all times {heaters  located  below
           45% level}.

Controls:  Pressurizer heaters operated by F7.  Pressurizer level
           controlled  by F2 {Primary Drain Valve} and 'D' {Make-
           up Feed Direction Control}.  Use F2 to drain, and 'DP'
           to fill pressurizer.  Note:  Make-up Feed Pump must be
           operating {'M' control}.


System:    Reactor Vessel

Operating Limits:    Temperature - 75 to 800F
                     Pressure - 0 to 3000 Psi.
                     Level - 100%
                     Rod Height - 0 to 100%

Function:  Provide  control,  structure,  and cooling for reactor
           core.   Designed  to maintain core completely  covered
           and  adequately cooled.   Core must not be above  212F
           without pressurization {See pressurizer}.   Rod height
           controls reactivity of core and heat produced.

Controls:  'ESC' command  initiates complete  shutdown  including
           starting  emergency pump and make-up  feed  pumps,  as
           well  as shutting pressurizer drain valve and dropping
           rods to bottom.   'F1' drops rods to bottom and  shuts
           pressurizer drain valve.  Both SCRAM commands turn off
           automatic  control system.   'R' command controls  rod
           height.   Pressurizer  level  maintains  pressure  and
           reactor  level.   'P'  command controls  coolant  flow
           through core.   'E' command controls emergency cooling
           flow to core.


System:    Primary Loop

Operating Limits:    Primary Flow - 0 to 100%

Function:  Primary  loop  provides recirculation  of  pressurized
           water  to remove heat from the reactor core.   Flow is
           maintained by the primary coolant pump.   The  primary
           loop  is  monitored  for any  leakage,  and  excessive
           radiation levels {indicating core damage or failure}.

Controls:  'P' command controls coolant flow rate.   See  reactor
           vessel,  emergency  cooling system and pressurizer for
           other controls.


System:    Emergency Cooling System

Operating Limits:    Level - 0 to 100%
                     Flow - 0 to 100%

Function:  Provides  rapid  cooling directly to reactor  core  in
           case of primary or secondary loop failure.   Emergency
           cooling  system  is  designed for one  time  operation
           only.   It must then be repaired during a normal main-
           tenance shutdown.

Controls:  'ESC' starts 100% flow to reactor.   'E' command  con-
           trols  emergency cooling pump flow.   Reactor must  be
           completely  shutdown  to  re-fill  emergency   cooling
           reservoir.


System:    Heat Exchanger

Operating Limits:    Temperature - 75 to 500F
                     Level - 65 to 100%

Function:  Provides   heat   transfer  from  primary  system   to
           secondary system.  Provides steam generation for oper
           ation of the turbo-generator system.  Isolates potent
           ially contaminated coolant from rest of system.   Pro
           vides  surge  volume  for changes  in  temperature  of
           secondary system.  Pressurizes secondary system.

Controls:  'DS' controls heat exchanger level.   If make-up  feed
           pump  is off and 'DS' is selected,  the heat exchanger
           will be drained.   Otherwise,  heat exchanger will  be
           filled.   'P'  controls heat flow into heat exchanger,
           and 'S' controls heat flow out of heat exchanger.


System:    Secondary Cooling System

Operating Limits:    Flow  - 0 to 100%
                     Temperature - 75 to 500F
                     Level  - 50 to 100%
                     Pressure - 0 to 1000 Psi
                     Condenser Inlet Temperature - 75 to 300F
                     Condenser Pressure - 14 to 0 Psi.
                     Condenser Outlet Temperature - 75 to 212F

Function:  Provides  recirculation of water to produce steam  for
           turbine.   System takes suction on condenser discharge
           and provides pressurized water to heat exchanger.

Controls:  'S'  controls coolant flow in secondary system.   'DS'
           directs make-up feed water to secondary system.   'F3'
           and 'F4' control turbo-generator.


System:    Turbo-Generator

Operating Limits:    Heat exchanger temperature - 212 to 500F
                     Turbine Speed  - 3,600 RPM

Function:  Produces  electricity  from  steam generated  in  heat
           exchanger.   Field control starts electricity  genera
           tion and controls turbine speed.

Controls:  'F3' trips turbine on and off line.   Turbine must not
           have  secondary coolant temperature below 212F.   'F4'
           trips  generator field on and off.   Field  should  be
           selected  at 3,250 RPM and will regulate speed.   'F8'
           controls lube oil pump.


System:    Lubricating Oil System

Operating Limits:    Lube Oil Level - 50 to 100%
                     Lube Oil Pressure - 80 to 90 Psi
                     Lube Oil temperature - 75 to 200F

Function:  Provides lubrication to the turbine and generator.

Controls:  'F8'  trips lube oil pump on and off.   Lube oil level
           can  only be increased during  maintenance  shutdowns.
           Auxiliary power 'F10' must be on for pump to operate.


System:    Make-up Feed System

Operating Limits:    Level  - 10 to 100%
                     Flow - 0 to 100%
                     Recirculation Flow - 0 to 50%

Function:  Provides  additional coolant to the primary and secon
           dary cooling systems to make-up for losses from  leak
           age or expansion.  Make-up feed pump should be left in
           recirculation  mode  when not in  use.   Make-up  feed
           reservoir is replenished continuously.

Controls:  'M'  controls  make-up feed flow  rate.   'D'  directs
           make-up  feed  to 'P' primary  system,  'S'  secondary
           system, 'N' recirculation.


System:    Auxiliary Power

Operating Limits:    None

Function:  Provides  electrical  power during start-up and  shut
           down, and whenever generator is not producing power.

Controls:  'F10' trips auxiliary power on and off.



System:    Alarm and Warning

Operating Limits:    None

Function:  Provides  warnings,  advisory  and  emergency  alarms.
           Yellow alarms are advisory or warning in  nature,  and
           red  alarms are emergency conditions.   Warning alarms
           provide  indication of a condition approaching  damage
           levels.  Other warning indications are provided by the
           symbols  of  pumps.   An '+' indicates  pump  off,  an
           'O'indicates  pump  running and an 'X' indicates  pump
           damaged.   Turbine speed is indicated by the vanes  in
           the turbine assembly.   When the vanes are horizontal,
           the turbine is stopped.   When the vanes are verticle,
           the  turbine is at normal operating speed.   The  same
           symbols apply to the generator.   Detailed information
           on  the  warning  and  alarm  system  is  availble  by
           lightpen on the alarm or through the Help key.

Controls:  'Up  Arrow' silences the audible alarm,  and resets it
           so that when a new warning occurs,  the alarm  sounds.
           'U'  disables the audible alarm,  until 'U' is pressed
           again.  'Q' tests all alarms by turning them all on.


System:    Automatic Rod Control System

Operating Limits:    Operating Range - 350 to 505F
                     Engagement Range - 500 to 750F

Function:  Controls  heat  exchanger temperature to within  limit
           set  by  Control Bias value,  1 to  5  degrees.   Heat
           exchanger  temperature may be set to the Control  set
           point or may be automatically  calculated.   Automatic
           Rod  control  system should be used whenever heat  ex
           changer temperature exceed 494F.

Controls:  'F5' selects automatic control system on or off.   'C'
           sets heat exchanger temperature to reference.  'B' set
           sensitivity range for control.   This range should  be
           set  to  1  for operation near  system  limits.   'F6'
           enables automatic temperature calculation depending on
           demand.  'ESC' and 'F1' turn off this system  whenever
           they are used.


                           SYSTEM ALARMS

01
               RX TEMP - High Reactor Temperature

      This alarm indicates high reactor core temperature.   Imme-
      diate action should be taken to reduce core temperature  by
      using Emergency SCRAM 'ESC', SCRAM 'F1', or Rod Height 'R0'.
      Also consider using Emergency Cooling 'E100'.

      Warning  (Yellow)  Point:   Reactor core temperature  above
      750F.

      Danger (Red) Point:  Reactor core temperature above 800F.

02
              RX PRESS - Low Reactor Pressurization

      This alarm indicates low reactor core pressurization, which
      could result in localized boiling and fuel element failure.
      Use Emergency SCRAM 'ESC'.

      Warning (Yellow) Point:  Reactor pressure below 2 X Reactor
      temperature.

      Danger (Red) Point:   Reactor pressure below 1.8 X  Reactor
      temperature.

03
                  RX Level - Low Reactor Level

      This  alarm  indicates a loss of reactor coolant such  that
      the reactor core is in danger of becoming  uncovered.   Use
      Emergency Cooling 'E100',  or Make-up Feed to Primary 'M100
      DP'.

      Warning (Yellow) Point:  None.

      Danger (Red) Point:  Reactor coolant level below 100%.

04
               Rod Bottom - Rod Bottom Indication

      This indication indicates when the control rods are comple-
      tely inserted.

      Warning (Yellow) Point:  Control Rods on bottom, completely
      inserted.

      Danger (Red) Point:  None

05
                 RAD HIGH - High Radiation Level

      This  alarm indicates above normal radiation levels in  the
      containment building.  This may be due to normal continuous
      high  power operation or to fuel element failure.   No  im-
      mediate action necessary.

      Warning  (Yellow) Point:   Radiation level above 200 Milli-
      rem/hour.

      Danger  (Red)  Point:   Radiation level  above  500  Milli-
      rem/hour.

06
                  Press Lvl - Pressurizer Level

      This  alarm indicates that the pressurizer level is out  of
      specification.   A  level  too high will result in a  pres-
      surizer failure and primary coolant  leakage.   Pressurizer
      level too low will result in pressurizer heater failure and
      loss of pressurization to the reactor.   Control level with
      Primary Drain Valve 'F2' and Make-up Feed 'DP'.

      Warning  (Yellow)  Point:   Pressurizer level above 85%  or
      below 50%.

      Danger (Red) Point:   Pressurizer level above 90% or  below
      45%.

07
              Pri Flow - Primary Coolant Flow Rate

      This  alarm indicates that the primary coolant flow rate is
      out  of range.   If the flow is too low,  the reactor  core
      receives inadequate cooling.  If too high, the primary pump
      is overstressed and may fail prematurely.

      Warning (Yellow) Point:   Primary flow above 90%,  or below
      .12 X Reactor temperature.

      Danger (Red) Point:  Primary flow 0.

08
             Emerg Low - Low Emergency Coolant Level

      This alarm indicates that the Emergency Coolant  reservoir
      is below safe operating levels.

      Warning (Yellow) Point:  Emergency Coolant below 25%.

      Danger (Red) Point:  Emergency Coolant level below 10%.

09
           Xchg Temp - High Heat Exchanger Temperature

      This alarm indicates that the Heat Exchanger temperature is
      exceeding design limits.   Action should be taken to reduce
      Primary  temperature and to increase Secondary Coolant Flow
      'S100'.

      Warning (Yellow) Point:   Heat Exchanger temperature  above
      495F.

      Danger (Red) Point:  Heat Exchanger temperature above 500F.

10
               Sec Level - Secondary Coolant Level

      This alarm indicates low Secondary Coolant level.   Make-up
      Feed 'DS' should be used to bring the level back to 100%.

      Warning (Yellow) Point:  Secondary Coolant level below 90%.

      Danger (Red) Point:  Secondary Coolant level below 50%

11
                Sec Flow - Secondary Coolant Flow

      This  alarm indicates that the Secondary Coolant flow  rate
      is out of range.  Low Secondary Coolant flow can cause Heat
      Exchanger  failure or Secondary Coolant pump damage.   High
      flow can result in overstressing the pump.

      Warning (Yellow) Point:   Secondary Coolant Flow rate above
      90%.

      Danger (Red) Point:  Secondary Coolant Flow rate 0.

12
         Cnd In Temp - High Condenser Inlet Temperature

      This  alarm  indicates high  condenser  inlet  temperature.
      This can result in damage to the turbine, Secondary Coolant
      pump and to the Condenser circulating pump.

      Warning (Yellow) Point:  Condenser inlet temperature  above
      275F.

      Danger  (Red)  Point:   Condenser inlet  temperature  above
      300F.

13
             Cnd Hi Press - High Condenser Pressure

      This  alarm  indicates high Condenser Pressure due to  high
      condensate temperature or low Secondary Coolant flow.  High
      Condensate  pressure  damages the Secondary  Coolant  pump.
      Increase Secondary Coolant Flow 'S100'.


      Warning (Yellow) Point:  Condenser Pressure above 4 Psi.

      Danger (Red) Point:  Condenser Pressure above 10 Psi.

14
         Cnd Out Tmp - High Condenser Outlet Temperature

      This  alarm  indicates high Condenser  outlet  temperature.
      High condensate temperature causes damage to the  Secondary
      Coolant pump.   Increase Secondary Coolant flow 'S100',  or
      decrease Heat Exchanger Temperature.

      Warning (Yellow) Point:  Condenser Outlet Temperature above
      195F.

      Danger  (Red)  Point:   Condenser Outlet Temperature  above
      212F.

15
               Turb Speed - Turbo-Generator Speed

      This alarm indicates that the Turbo-Generator system is not
      on  design speed of 3,600 RPM.   Turbo-Generator  overspeed
      damages  the turbine and generator.   Generator Trip  valve
      'F3'  and Generator Field control 'F4' effect Turbo-Genera-
      tor speed.

      Warning (Yellow) Point:   Turbo-Generator speed other  than
      3,600 RPM.

      Danger (Red) Point:  Turbo-Generator speed above 3,636 RPM.

16
          LOil Temp - High Lubricating Oil Temperature

      This  alarm  indicates High  Lubricating  Oil  temperature.
      This  can  damage the Lubricating Oil pump and  the  Turbo-
      Generator.

      Warning (Yellow) Point:   Lubricating Oil Temperature above
      200F.

      Danger  (Red)  Point:   Lubricating Oil  Temperature  above
      212F.

17
               LOil Level - Lubricating Oil Level

      This alarm indicates low Lubricating Oil level.   Low level
      can damage the Lubricating Oil Pump and Turbo-Generator.

      Warning (Yellow) Point:  Lube Oil Level below 35%.

      Danger (Red) Point:  Lube Oil Level below 15%.

18
              LOil Press - Lubricating Oil Pressure

      This alarm indicates unsafe Lubricating Oil Pressure.   Low
      Lube Oil pressure can damage the Turbo-Generator.  Lube Oil
      Pump control 'F8'.

      Warning  (Yellow)  Point:   Lube Oil pressure above 90  and
      below 79.

      Danger (Red) Point:   Lube Oil pressure above 95 and  below
      72.

19
              MkFeed Level - Low Make-up Feed Level

      This  alarm indicates when Make-up Feed level is below safe
      operating levels.   Make-up feed replenishment will  slowly
      take place during normal operations; system refilled during
      maintenance shutdowns.

      Warning (Yellow) Point:  Make-up Feed level below 40%.

      Danger (Red) Point:  Make-up Feed level below 5%.

20
                Pump Temp - High Pump Temperature

      This  alarm indicates that one or more of the six pumps  is
      overheating.   The  pumps  are Primary  Coolant,  Secondary
      Coolant,  Condenser Circulation,  Lube Oil, Emergency Cool-
      ing, and Make-up Feed.

      Warning (Yellow) Point:  Pump temperature above 175F.

      Danger (Red) Point:  Pump temperature above 212F.

21
          Cntrl Warn - Control/Auxiliary Power Warning

      This  alarm indicates loss of auxiliary power or  an  error
      detected  by  the automatic control system.   Loss of  aux-
      iliary  power results in failure of all pumps and  controls
      if the generator is not producing power.

      Warning (Yellow) Point:   Automatic Control off above  600F
      reactor temperature.

      Danger  (Red) Point:   Automatic Set-point off and  Control
      set point above 494F.  Loss of Auxiliary Power.

22
               Turb Trip - Turbo-Generator Tripped

      This alarm indicates that the Turbo-Generator trip valve is
      open,  and  that  the  secondary coolant  is  being  dumped
      directly into the condenser.

      Warning (Yellow) Point:  Turbo-Generator Trip valve open.

      Danger  (Red) Point:   Turbo-Generator not tripped and Heat
      exchanger temperature below 212F.

23
              Pri Drain - Primary Drain Valve Open

      This  alarm indicates that the Primary Drain Valve is  open
      and allowing Primary Coolant to drain from the pressurizer.

      Warning (Yellow) Point:  Primary Drain Valve open.

      Danger (Red) Point:  None.

24
              Pr Htr OFF - Pressurizer Heaters Off

      This alarm indicates that the Pressurizer Heaters are  off.
      The  Reactor  temperature should not exceed 212F  when  the
      Pressurizer Heaters are off.

      Warning (Yellow) Point:  None

      Danger (Red) Point:  Pressurizer Heaters Off
99


               FUNCTION KEY DEFINITIONS (file FUNKEY.DOC)
01
      ESC  -  Emergency Shutdown.

                This  function key causes the reactor to  execute
                an  Emergency  SCRAM.   The rods are sent to  the
                bottom,  and  the make-up feed pump speed is  in-
                creased  to  100% and the make-up  feed  flow  is
                directed to the primary loop.   The primary drain
                valve  is shut and the emergency cooling pump  is
                started.   This function key will safely shutdown
                the  reactor  and minimize damage to the  reactor
                core.  It should be used in any emergency.
02
      F1  -  SCRAM.

                This function key shuts down the reactor by send-
                ing  the rods to the bottom and by  shutting  the
                primary drain valve.  This function key should be
                used  while conducting a normal shut-down of  the
                reactor.  Care must be taken to prevent damage to
                the  reactor  core due to low  pressurizer  level
                when using this function key.
03
      F2  -  Primary Drain Valve.

                This  function  key  controls the  primary  drain
                valve which is used to maintain pressurizer level
                within the required range on 50-85%.   This  fun-
                ction  key alternately opens and shuts the  drain
                valve.

04
      F3  -  Turbine Trip Valve.

                This  function key controls the position  of  the
                turbine  trip  {bypass}  valve which is  used  to
                prevent  liquid water from entering the  turbine.
                This  valve  should be open  {Turb  Trip  warning
                (Yellow)  on} whenever heat exchanger temperature
                is  below  100C.   Care should be  taken  not  to
                exceed  the condenser pressure/temperature limits
                when operating this valve.
05
      F4  -  Generator Field Control.

                This  function key controls the  generator  field
                and  speed control system.   The generator  field
                must  be  on for production of power.   When  the
                generator field is on, the turbine speed is auto-
                matically regulated to 3,600 RPM to maintain  the
                electric  current frequency at 60 Hz.   This fun-
                ction  key  provides the only direct  control  of
                turbine speed.
06
      F5  -  Automatic Control.

                This  function  key controls  the  automatic  rod
                height  control system which is designed to main-
                tain  the  heat exchanger  temperature  near  the
                control set point temperature.   This system fun-
                ctions  only  above 500C reactor temperature  and
                will  maintain the temperature within  the  range
                specifed  by  the Bias setting below the  control
                set point temperature.
07
      F6  -  Automatic Set-point.

                This  function  key controls  the  automatic  set
                point   computer.    This  computer  adjusts  the
                control set point and primary and secondary cool-
                ant  pumps to maintain the production rate  above
                the demand.   This computer should generally only
                be used when the demand is above 1700 KW.
08
      F7  -  Pressurizer Heaters.

                This  function key controls the pressurizer  hea-
                ters which are used to maintain a steam bubble in
                the pressurizer.   The steam bubble creates pres-
                sure  on the primary loop which prevents  boiling
                in the reactor core,  which could cause fuel ele-
                ment failure or meltdown.    The pressurizer hea-
                ters  must be on any time the reactor temperature
                exceeds 100C.    Primary coolant pressure must be
                at  least 2X reactor core temperature to  prevent
                damage to the reactor core.

09
      F8  -  Lube Oil Pump.

                This  function key controls the operation the the
                turbine and generator lubricating oil circulation
                pump.   This  pump provides high pressure oil  to
                the bearings of the turbine and  generator.   The
                Lube  oil pump must be on whenever the turbine is
                operating.
10
      F9  -  Condenser Circulating Pump

                This   function   key  controls   the   condenser
                circulating  pump.   This pump  provides  coolant
                flow  for the condenser.   The exhaust steam from
                the  turbine  is condensed into  water,  and  the
                condensate  is pumped to the steam generator  for
                recycling.   This pump should be operating  when-
                ever the secondary temperature is above 212F.
11
      F10  -  Auxiliary Power.

                This  function key controls the  auxiliary  power
                source  which  is used to provide electricity  to
                the  reactor plant whenever the generator is  not
                functioning.   Auxiliary power is required during
                start up and shutdown of the reactor  plant,  and
                should be on at all times.
12
      Left Arrow  -  Plant Display.

           This  function  key swithes the  display  between  the
           graphic  and  numeric displays.   The numeric  display
           shows the current value of the specific system values.
           This display also shows the last 5 log entrys,  if the
           Autolog-Screen  function  is  selected.   The  graphic
           display  shows  a schematic of the plant and  a  chart
           displaying  the  last  30 minutes  of  the  four  most
           important indicators.   Pumps,  valves, and levels are
           indicated  on the schematic.   Pumps that are off  are
           indicated  by  an  '+',  pumps that  are  running  are
           indicated  by an 'O',  and pumps that have failed  are
           indicated  by an 'X'.   Shut valves are indicated by a
           solid  white circle.   Open valves are indicated by  a
           black stripe indicating the direction of flow  through
           the valve.  Fluid levels are indicated by white blocks
           in the various vessels and storage tanks.  Turbine and
           generator  speeds  are indicated by the angle  of  the
           throttle  vanes  in the symbols.   A  horizontal  vane
           indicates  speed  0,  and  a verticle  vane  indicates
           normal operating speed.

13
      Up Arrow  -  Alarm Silence.

           This  function key switches the audible alarm  on  and
           off.   The alarm sounds whenever there is a warning or
           danger indication on the alarm panel.


                      COMMAND KEYS (file COMKEY.DOC)

01
      A     -  Select Auto Log Feature.

           The  'A'  command selects the Auto Log  feature  which
           provides  a  means  to make a hard copy  record  of  a
           simulation run.   The 'AE' commands enables the  auto-
           log feature and allows selection of the destination of
           the log output.  'S' selects the display screen on the
           numeric display screen,  'D' selects a disk file named
           'HISTORY.DAT',  and  'P' selects the printer connected
           to  'LPT1:'.   Auto-Log reocrds every command  isssued
           and any danger warnings issued by the  reactor.   This
           feature  can  be  disabled by the 'AD'  option  or  by
           pressing 'A' and 'Return'.
02
  B     -  Set Bias value.

           The  'B' command allows the setting of the bias  value
           used  by the automatic control system to maintain  the
           heat exchanger temperature near the set point tempera-
           ture.   This  value may range from 1 to 5.   1 is  the
           most sensitive setting and should be used whenever the
           reactor is operating close to its' limits.  This value
           may only be changed when automatic control is on.  The
           set  point  temperature is controlled by the 'C'  com-
           mand.
03
  C     -  Set Automatic Control Temperature.

           This command sets then heat exchanger temperature that
           will  be  maintained by the automatic control  control
           system {F5}.   The value can be set anywhere from 350F
           to  505F.   The automatic control program will  adjust
           rod height to maintain the heat exchanger  temperature
           within  the  Bias setting of the control  temperature.
           This  temperature  will be automatically  adjusted  to
           meet power demand when Automatic Set-point {F6} is on.
           This value can only be changed when automatic  control
           is on.
04
  D     -  Make-up Feed Destination.

           This  key allows selection of the destination for  the
           make-up feed flow.  'P' causes make-up feed to be sent
           to the primary loop, 'S' causes feed to be sent to the
           secondary  loop,  and 'N' causes feed to be  recircul-
           ated.   The  make-up feed pump should be operating for
           flow  to go to the primary or  secondary  loops.   The
           secondary  loop will drain if 'S' is selected and  the
           make-up feed pump is off.
05
  E     -  Emergency Coolant Pump Speed.

           This command selects the emergency cooling pump speed.
           The pump can either be off, speed 0, or on, speed 1 to
           100%.   This  pump is used to provide rapid cooling to
           the  reactor core.   The emergency cooling  supply  is
           limited, but is adequate to lower the core temperature
           to safe levels.
06
  F     -  Freeze and Save Simulation Run.

           This  command  stops the simulation run and saves  the
           pertinent variables to a file named 'RXFRZ.DAT'.  When
           the simulation is started at a later time,  the opera-
           tor  is asked whether the saved simulation  should  be
           executed.   A 'Y'es answer will load the variables and
           restart  the  simulation at the point it  was  frozen.
           Only one simulation run can be frozen at any time.
07
  G     -  Current Production Graph

           This command graphs the electrical output against  the
           demand.   The  graph  shows  the most recent  10  hour
           period.
08

09
  M     -  Make-up Feed Pump Speed.

           This  command  selects the speed of the  make-up  feed
           pump.  The pump can be off, speed 0, or on, speed 1 to
           100%.  This pump is used to provide additional coolant
           to the primary and secondary cooling systems.   As the
           reactor  heats up,  primary coolant must be drained to
           maintain  the primary volume within  limits.   As  the
           reactor  cools down,  coolant must be added to make up
           for the drained coolant.   The secondary system  loses
           coolant through gland sealing steam and minor leakage.
           This pump should be on at all times, running at 50% or
           less.   In  this recirculation mode,  make-up feed  is
           instantly available.
10
  P     -  Primary Coolant Pump Speed.

           This  command  selects the pump speed of  the  primary
           coolant  pump.   This  pump circulates  high  pressure
           water through the reactor core and transfers heat from
           the reactor to the heat exchanger.  This pump normally
           operates at 90% or above.  Both the primary and secon-
           dary coolant pumps must both be off to completely shut
           down the reactor.
11
  Q     -  Alarm and Warning Test

           This command tests the alarm and warning indicators on
           the  console.   Pressing this key a second time resets
           the  alarm and warning indications and shows only  the
           active alarms.
12
  R     -  Rod Height.

           This  command  selects the control  rod  height.   The
           control   rods   provide  direct  control   over   the
           reactivity of the core, and thereby control the core's
           temperature.   The  higher the rods,  then the core is
           more reactive,  and more heat is produced.  The opera-
           ting  range of the rods is between 0,  on the  bottom,
           and 100%,  completely withdrawn.   The two SCRAM  com-
           mands {ESC  and  F1} cause the rods  to  be  instantly
           dropped to the bottom.
13
  S     -  Secondary Coolant Pump Speed.

           This  command selects the speed of the secondary cool-
           ant  pump.   This pump circulates the condensed  steam
           from the cooling tower/condenser to the heat exchanger
           where  it again produces steam.   This  pump  normally
           operates  at  90% or above.   Both this pump  and  the
           primary  coolant  pump must be off to completely  shut
           the reactor down.
14
  T     -  Terminate Simulation

           This command terminates the simulation and  calculates
           a  score based on the production rate,  damages incur-
           red,  and production deficit.   The score is  adjusted
           for  the length of the simulation run.   A  cumulative
           score   is  maintained  in  the  file  'RXSTATUS.DAT'.
           Erasing this will clear the cumulative score.
15
  U     -  Disable Alarm

           This  command switched the audible alarm system on and
           off.
16
  V     -  Current Version

           This  command displays the current version  number  of
           the  Reactor-100 main program.   Please refer to  this
           number when reporting any problems with the program.
17
  Z     -  Change Timer Setting

           This command allows changes to the time interval  bet-
           ween  screen updates.   The allowable intervals are  0
           (no  delay),  or 3 to 10 seconds.   The normal  update
           interval is once every 2.5 seconds.
18
  'H'   -  Provides information.

           Help  is available by using the help key or using  the
           lightpen.   The  help menu can be used by entering the
           number next to the subject of interest.   The lightpen
           can be used to select Help on any item of interest  by
           pointing  the lightpen at the subject and pressing the
           switch.   The  lightpen can also be used on  the  Help
           menus.
19
  Tab   -  Bypass Sign-on Message

           This command can be used during the program sign-on to
           bypass  the delay.   This will also bypass the initial
           Help screen.