Note to SIO2PC users:

KEYER.OBJ is a program for ham radio which took up about 2 years
of my programming time before I started SIO2PC. I'm throwing it in
just as a curiosity, to fill in disk space. If you have friends who
are ham operators, they may be interested in it. If not, you may
want to erase KEYER2.DOC (this file) and KEYER.DOC (short form of 
instructions for KEYER.OBJ) from the disk and KEYER.OBJ from the
ATARI.ATR disk image. If you want to play with it, plug a joystick
into stick #2, run KEYER.OBJ and send some Morse code.





                             Instructions: The WA5BDU Keyer
         
         
         OPTION: Enter command mode.
         SELECT: Keyboard to MEMO/TRANSMIT window toggle.
         
         
                                C O M M A N D S
         
         [OPTION] plus ...

         HS: Help Screen
         HP: Help text dump to printer
         SP: Speed
         RT: Ratio, doT
         RH: Ratio, dasH
         SW: Spacing, Word (in 1/2 dot length units)
         SC: Spacing, Char (in 1/2 dot length units)
         CS: Console Speaker toggle (400/800 only)
         VO: Video Off/On toggle
         KD: Key Down (tune)
         OA: On Air/Off Air toggle
         IK: Inverse Keying (Invert output logic)
         TO: Sidetone frequency
         OM: Open message (Create or Edit; ESC to exit)
         BE: Buffer Enable (Start/Stop sending)
         TAB key: Same as above
         BC: Buffer Clear (SHIFT-CLEAR is the same thing)
         MA: Thru MZ: Send message A-Z immediately.
         Inverse A-Z: Put message A-Z in buffer to send
         PL: Parameter Load (Set up keyer the way you like it)
         PS: Save current parameters to file
         NOTE: File AUTOPARA.KEY will auto-load
         TL: Textfile Load (Load message file)
         TS: Save messages to file
         NOTE: File AUTOTEXT.KEY will auto-load.

         Messages can call each other (embed inverse A-Z in message)

         A message can call itself.  Hit any key to stop the infinite
         loop.

         Commands may be embedded within messages, "*" signals start
         of command.
         
         
         INTERFACING: Stick 2: Pin 1: Output, Pin 2: Command button
         (optional), Pin 3: Dash paddle contact, Pin 4: Dot contact,
         Pin 8: Common
         
         
         Special codes from paddle: .-... (AS) enters COMMAND mode
         (same as OPTION), .----- (EOM) exits message edit mode (same
         as ESC key).
         
         
         WA5BDU, 300 S. VANCOUVER, RUSSELLVILLE, AR 72801