TRS-80 COLOUR COMPUTER 2 EMULATOR Ver. 1.40 (C) 1993,94 Jeff Vavasour
=====================================================================

(Internet e-mail to jeffv@physics.ubc.ca)

1. DESCRIPTION
--------------

This package is a complete* emulator designed to make your PC imitate a 
genuine CoCo 2 with 64K and four disk drives.  It has also been tested
successfully with the Dragon 32's 16K ROM, though you must use the Options
Menu (F6 in the emulator) to select the Dragon keyboard.

It requires EGA graphics and 256K RAM.  Also, a 286 with at least 16 MHz 
is recommended, though you'll need a faster processor to get operating 
speed that matches the real machine.  (A 33 MHz 486, on the other hand, 
is drastic overkill.  A slowdown option is provided for users fortunate 
enough to posess such a beast.)

Version 1.40 is the third release of this package, and includes many
enhancements and a few corrections.  The file NEWSTUFF.DOC summarises all
changes since version 1.30 for those who've seen the earlier releases.  Also,
MANY things in this COCO.DOC file have changed.  Please read it thoroughly.

This program is freeware, though copyright remains with the author.  You
are permitted to distribute the UNALTERED .ZIP package, as long as all  
programs listed in section 2 are included.  Also, this package may not be
sold or distributed commercially or for profit, though a reasonable media 
charge for distribution is acceptable.  

The .ZIP package contains the following 12 files:

- The emulator itself: 
        COCO.EXE
- Documentation:
        README - a brief overview
        COCO.DOC - this file
        NEWSTUFF.DOC - outlines upgrades since version 1.30
- CoCo disk programs:  
        DSKINI.EXE - formats CoCo disks on your PC.  Also can write the
                     emulator's "virtual disks" to a real CoCo disk.
        RETRIEVE.EXE - reads a CoCo disk and makes a "virtual disk" on your
                       hard drive.
        PORT.EXE - moves files between CoCo disks and your MS-DOS directory,
                   or between virtual disks and your MS-DOS directory.
- CoCo cassette programs:
        CASIN.EXE - a program to read CoCo cassettes on your PC through a
                    SoundBlaster or from a .WAV file sample.
        CASOUT.EXE - a program to make CoCo-compatible cassettes using a
                     SoundBlaster.
- Other programs:
        CAS2ROM.EXE - PC program to retrieve your CoCo's ROM by cassette.
        COCOUTIL.DSK - CoCo program to retrieve your CoCo's ROM by disk.
        VGACHECK.EXE - a program to test your VGA board for compatibility
                       with the shareware CoCo 3 emulator.

Please feel free to forward any comments to me at the email address above,
or the postal address given in the Section 8 below.  (Alternate email 
addresses are given there as well, but they should only be used if my 
primary email address fails.)


* Footnote: For those technically inclined, all features and hardware of the
  standard equipped CoCo have been reproduced with the exception of the
  cassette port and the 63.5us horizontal sync interrupt.  The standard 60Hz
  clock interrupt *is* reproduced.  The "bit-banger" serial output has also
  been rerouted to the PC's printer port, allowing for its use as a printer
  port.  The DSKINI command will also not work within the emulator, but all
  disks are automatically formatted when first used anyway.


2. GETTING STARTED
------------------

The only thing that you will need that is not provided with the emulator
is the ROM of a genuine CoCo.  Naturally, this could not be included here
for copyright reasons.  If you own a CoCo 1 or 2, however, this section
will describe how to copy it to your PC for use with the emulator.  

There are three methods to copy the ROM to your PC:
- by disk;  (You'll need a disk drive on your CoCo and a 5 1/4" drive on your
  PC.  Section 2.1 describes this method.)
- by cassette;  (You'll need a SoundBlaster on your PC.  See Section 2.2.)
- or, by serial port.  (You'll need to build a simple cable.  You'll also
  need a serial port in your PC.  See Section 2.3.)

CoCo 3 ROMs can also be used, but extra steps are required.  See Section 2.4
on using a CoCo 3 to obtain the ROMs.

As another alternative, users of Paul Burgin's Dragon emulator (found at the
SimTel mirrors in the directory "pub/msdos/emulator" as PCDGN101.ZIP) can
use the steps in Section 2.5 to convert that emulator's ROMs for use with
my program.


2.1 OBTAINING THE ROM VIA DISK
------------------------------

In MS-DOS, place a blank 5 1/4" disk in your drive and type:

DSKINI d: COCOUTIL

where "d:" identifies the drive containing the disk (e.g. "A:", "B:", etc.).  
Place this disk in drive 0 of your CoCo and type (on the CoCo):

RUN"GETROM"

Next, place the disk back into your PC and type:

RETRIEVE /R d: COCO.ROM

Again, "d:" identifies the drive containing the disk.  (Note that in both
cases, "A:" is the default if this parameter is omitted.)

You are now ready to run the emulator.  (See section 3.)

   
2.2 OBTAINING THE ROM VIA CASSETTE
----------------------------------

This will require the use of the CASIN.EXE program to read CoCo cassette
files via the SoundBlaster (see Section 5.3) or from a .WAV recording (Section
5.4).  On your CoCo, save the ROM to cassette using the CoCo command:

CSAVEM"COCO",&H8000,&HBFFF,0

Make a virtual cassette file of this on your PC by following the steps in 
Section 5.3 or 5.4.  Once the file has been completely read into your PC, 
type the command:

CAS2ROM filename[.CAS]

at the MS-DOS prompt, where "filename" is the name you gave to the virtual 
cassette containing the ROM.  This will create the COCO.ROM file used by the 
emulator.  The .CAS file can then be deleted.  You are now ready to run the 
emulator.  (See section 3.)


2.3 OBTAINING THE ROM VIA THE SERIAL PORT
-----------------------------------------

This method requires at least version 1.1 of the CoCo BASIC ROM, a PC with a
serial port, and the cable described in the Appendix.

Once the cable is built and tested, connect your PC and CoCo together and 
load your favourite terminal program on your PC, setting it to 2400 baud,
no parity, 1 stop bit, 8 bit word length.  Select the file capture option 
and record all data received to the file "COCO.ROM".  Then, run the 
following program on your CoCo:

10 POKE 150,18
20 PRINT#-2,CHR$(0);CHR$(128);
30 FOR X=&H8000 TO &HBFFF
40 PRINT#-2,CHR$(PEEK(X));
50 NEXT

Pay particular attention to the semicolons in this program.  Once the CoCo
is done and the "OK" prompt returns, close the captured file.  Check that
it should be 16386 bytes long in your MS-DOS directory.  You may now run
the emulator.  (See section 3.)

If the file is too long or too short, there may be a problem with your terminal 
program and you should try another.  (The file is being transmitted as a binary
file so no filters should be used in your terminal program.)


2.4 SPECIAL INSTRUCTIONS FOR USING THE COCO 3 ROMS
--------------------------------------------------

The CoCo 3 operates differently than the CoCo 1 and 2.  Before beginning
one of the methods in Sections 2.1 through 2.3, you must issue the CoCo
BASIC command:

POKE &HFFDE,0

Then, after you have completed all the steps for the method you choose, you
must enter the following commands at the MS-DOS prompt:

DEBUG COCO.ROM
A 40F4
DB 1,0,1,3,1,F,1,C,1,6,1,9,A0,27
{press ENTER an extra time here to get the "-" prompt back.}
W
Q

This will patch the ROM so it may be used with the CoCo 2 emulator.


2.5 USING PCDGN101.ZIP'S ROM FILES (DISKLESS SYSTEMS)
-----------------------------------------------------

Follow the instructions with Paul Burgin's emulator to generate the *.DGN
ROM file.  Then, type the following commands in MS-DOS:

DEBUG filename.DGN
M 110 L 4000 102
A 100
DW 8000
{press ENTER an extra time here to get the "-" prompt back.}
N COCO.ROM
W
Q

You have now generated the file "COCO.ROM" which COCO.EXE can use.


3. RUNNING THE EMULATOR
-----------------------

With COCO.ROM in the default directory, type "COCO" at the MS-DOS prompt and
press ENTER.  The emulator will start, with a title banner and list of 
function keys appearing.  Pressing any key will begin the operation of the
emulator.  This screen may be redisplayed at any time by pressing [F10].

To exit the emulator either press [F1] or [F6] followed by "Q" and then "Y" to
confirm.

The special function keys are summarised as follows:

[F1] Activates the 6809 debugger.  See Section 7 for details on its use.  If 
     you enter this option accidentally, press "C" to return to the emulator.
     Pressing "Q" will quit the emulator and return to MS-DOS.  You will be 
     prompted to enter "Y" to confirm if you attempt to quit.

[F2] The virtual disk menu.  If you obtained the ROM from a CoCo with Disk
     BASIC, this menu will allow you to specify what the emulator should use
     as drives 0, 1, 2, or 3.  See Section 4 for details on using CoCo disks
     with the emulator.

[F3] Snapshots.  The entire state of the emulator, such as a program or a 
     game-in-play may be saved to an MS-DOS file, to be retrieved later
     (even if you exit the emulator or turn off the computer between 
     sessions.)

     To save a snapshot, press "S" and then type in a name or select it from
     those already in the directory.  To load, press "L" and select a name
     as before.  ESC aborts this option.

     Snapshots may also be loaded when the emulator is first run at the 
     MS-DOS prompt by typing "COCO filename[.PAK]" where "filename" is the 
     name of the snapshot.

[F4] The virtual cassette menu.  Cassette commands such as CSAVE, CLOAD, etc.
     can be rerouted to your PC's hard drive using this menu.  More can be
     found on cassette features in Section 5.

[F5] This turns the sound option on or off.  Sound output can either be routed
     to a SoundBlaster or the PC's feeble internal speaker, whichever is 
     selected in the [F6] Options Menu below.

[F6] Options menu.  Pressing the right mouse button will also summon this menu.
     In the menu, pressing the letter associated with an option changes it.
     Also, the "+" and "-" keys speed up or slow down the emulator.  The "<"
     and ">" keys will adjust the SoundBlaster volume if it is selected.  The
     following options are available in this menu:

        [A] Select a keyboard layout.  This is the same as the [F7] key below,
            but includes additional modes for Dragon 32 compatibility.  See 
            the note at the end of this section for Dragon 32 users.
        
        [B] Select what to use as the "left joystick" for the emulator.  The
            options are "Game A", "Game B", "Mouse", or "None".  Game A/B
            refer to the PC's game port adapter (also found in SoundBlasters).
            Most PCs only have a single joystick, which is usually "Game A".
            Be sure to calibrate a joystick for use with the emulator if you
            select one here or in option C.  Do not select "Game A" or 
            "Game B" if there is no corresponding joystick, as the emulator 
            will be slowed by unsuccessful attempts to read the non-existent
            joystick.

        [C] Same thing for the CoCo's "right joystick".

        [D] Select sound source.  Your choices are "Internal" for the PC's
            internal speaker, "External" for the SoundBlaster, or "Off".

        [E] This determines the character set:  You can choose from the 
            factory-standard normal/inverse set, or an upper/lowercase set 
            which can sometimes be more pleasant to look at.
        
        [F] Select artifacting mode.  When "red" or "blue" is selected the
            hi-res screen will be blurred slightly, similar to when seen on a 
            normal TV set.  This was considered a "feature" in some games.
            If you don't want this, set this option to "off".

        [G] Select printer mode.  The CoCo's serial port output is rerouted to
            the PC's printer in the emulator.  There are three options here:
            "CR only" which prints the data unmodified, "CR/LF" which adds 
            linefeeds to the output as required by PC printers so all text
            does not appear on a single line, and "Disabled" which disables
            output to the printer.

        [H] Select clock frequency.  You can change the timer interrupt to
            be either 60Hz or 50Hz, conforming to either NTSC or PAL standards 
            respectively.

        [I] Select disk drive mode.  If your PC has a 1.2Mb drive, you can
            use it as either a 40- or 80-track CoCo disk drive.  The initial
            setting is 40-track as is standard on most CoCo's.  Use this
            unless you have a customised CoCo with 80-track disks that you
            wish to read.

     In addition, the Options Menu offers several other commands:

        [K] Debug.  Same as the [F1] key.

        [L] Virtual Disk Menu. Same as the [F2] key.

        [M] Snapshot/Program Pak Menu.  Same as the [F3] key.

        [N] Modify keyboard layout.  Same as the [F8] key.

        [O] Calibrate joystick.  You must do this before using a joystick
            with the emulator.  You will be prompted to move the joystick to
            the upper-left corner and press the button, then to move it to the
            lower-right and press the button again.  ESC aborts.  This command
            must be issued once for each joystick connected to your PC.

        [P] File import/export utility.  Same at the [F9] key.

        [Q] Quit.  Press "Y" to confirm, or "N" to cancel.

        [R] Restart.  This is the same as rerunning "COCO".  Press "Y" to
            confirm, or "N" to cancel.

        [S] Shell to DOS.  Calls the MS-DOS prompt.  Type "EXIT" to return to
            the emulator.

        [T] Virtual Tape Menu.  Same as the [F4] key.

[F7] This changes the keyboard layout.  You have a choice between the PC, 
     CoCo, or your own Custom layout.  In the CoCo layout, SHIFT-2 would be a 
     quote while in the PC layout, SHIFT-2 is an "@".  Other keys may not be 
     so obvious: ESC is the BREAK key, ALT is the CLEAR key, SCROLL LOCK is
     SHIFT-@.  The arrow keys on the keypad also work.

[F8] Modify the custom keyboard layout.  The emulator includes a Custom layout
     which you can modify with this option.  Select the PC key you wish to
     modify by using the arrow keys to scroll through the list, then press
     [F1] to modify its unSHIFTed definition or [F2] to modify its SHIFTed
     definition.  Pressing [F4] will erase the custom layout and copy one of 
     the two preset layouts ("PC" or "CoCo") over it.  The custom keyboard 
     layout is saved and is automatically reloaded next time your run the 
     emulator.  You must select the "Custom" layout with [F7] during normal
     emulator operation (or with the Option Menu's option A) in order for the 
     custom layout to take effect.
    
[F9] File import/export utility.  This runs the "PORT.EXE" program described
     in Section 4.3.

[F10] Print the help screen summarising these function key choices.

[CTRL-F10] Same as the CoCo's RESET button.


NOTE FOR DRAGON 32 USERS: (KEYBOARD SELECTION)

The keyboard layout is also selectable in the [F6] menu, though it has six 
options rather than three.  They are "PC", "CoCo", and "Custom" -- as 
described for the [F7] key -- and "DragonPC", "Dragon", or "DgnCustom" which 
are the analogous choices for the Dragon 32 keyboard mapping.  If you select
Dragon or DragonPC in this menu, the [F7] key will then toggle between these 
three settings, rather than "PC", "CoCo", and "Custom".

If you use the keyboard selection for one of the CoCo or Dragon, but the ROMs 
of the other, then the keys will not respond properly.  (For example, the "A" 
and "1" keys will be exchanged.)  This is corrected simply by pressing [F6] 
and using the keyboard layout option to select the correct keyboard. 


4. USING DISK FILES WITH THE EMULATOR
-------------------------------------

To use the emulator's CoCo disk functions, you will need to have copied the
Disk BASIC ROM to your PC.  This is done by using the method in Section 2.1.

It is also possible to "write protect" a drive containing a virtual disk by
pressing SHIFT and the drive number in the Virtual Disk Menu.  Write protected
drives are indicated by a block over the drive number.  This will have no
effect on physical disks, which must be write protected in the usual manner.


4.1 USING THE VIRTUAL DISK MENU
-------------------------------

CoCo disks can be used with the emulator using two methods:  Either by 
specifying a disk drive containing a CoCo disk in the [F2] menu, or by copying
the disk to a "virtual disk file" on your hard drive, and then telling the
emulator to find the files there.  

In either case, this is accomplished by first selecting the [F2] Virtual Disk
Menu.  Then, select the CoCo drive number 0, 1, 2, or 3 to assign.  At the
prompt, enter a drive designation such as "A:" or "B:" to use a physical
drive,* or enter a "virtual disk" file name.  (You can create new virtual
disks by typing a name of one not found in the directory on the right.  All
virtual disks are given the ".DSK" extension, and are automatically formatted
for use with the CoCo's Disk BASIC.)

You may then use the CoCo's LOAD, SAVE, OPEN, etc. commands on the selected
CoCo disk or virtual disk file.

*Note: If you are using Disk BASIC 2.0 or later, CoCo drives 0 and 1 will 
 access the first side of a physical disk, while drives 2 and 3 will access 
 the second side of a double-sided physical disk.  Virtual disks are always
 single sided.


4.2 MOVING DISK IMAGES BETWEEN REAL DISKS AND VIRTUAL DISK FILES
----------------------------------------------------------------

You may make virtual disk files from real CoCo disks (i.e. copy the entire
disk image to your hard drive) or vice versa using the RETRIEVE and DSKINI
commands respectively.

Any virtual disk file may be written to a 5 1/4" disk, readable by the
CoCo by entering:

DSKINI [/2] [/8] [d:] [diskname[.DSK]]

where "d:" is the destination drive and "diskname" is the source virtual disk
file.  At least one of these two parameters must be given.  (The default
drive for "d:" is A:.)  Paths may be included in the diskname parameter.
If "diskname" is omitted, a blank disk is formatted.  If the "/2" option
is specified, the second side of a double-sided disk will be used.  If the
"/8" option is specified AND YOU ARE USING A 1.2Mb DRIVE, the disk will be 
formatted for 80-track drives.

Disks may also be read back to virtual disk files using:

RETRIEVE [/2] [/4] [/8] [d:] diskname[.DSK]

The "/2" and "/8" options have the same meaning as for DSKINI.  The "/4"
tells RETRIEVE that the disk is a 40-track disk.  The default is 35 tracks.

Some CoCo disks may not be readible by the PC.  If you encounter sector
read errors using RETRIEVE, try the following transfer method:

1. Create a CoCo disk on your PC using DSKINI.EXE.

2. On your CoCo, use BACKUP or COPY to copy the files onto the disk you've
   just created in step 1.

3. Put the disk back in your PC and use RETRIEVE.EXE to make a virtual disk
   file from it.


4.3 MOVING COCO FILES TO AND FROM THE MS-DOS ENVIRONMENT
--------------------------------------------------------

The program PORT.EXE can move files between CoCo disks (Disk BASIC format only)
and the MS-DOS directory, or virtual disks and the MS-DOS directory.  At the 
MS-DOS prompt, it is entered simply by typing "PORT".  If you are using this 
program standalone (without the emulator) and wish to access 80-track CoCo 
disks, you must instead type "PORT /H".

The PORT program may also be run from within the emulator by pressing [F9]
or selecting option P in the Options Menu.

You may exit the PORT program any time by pressing ESC.  Upon entering the
PORT program, you must tell it where to find the CoCo disk you will be using.
Either give a physical drive designation (e.g. "A:" or "B:") or enter the
name of a virtual disk.  The directory for the selected CoCo disk and your
current MS-DOS directory will be shown.

The following options are now available:

[F1] To select a new CoCo disk or virtual disk.  You must also select this
     option if you change the disk in the selected physical drive.

[F2] To select the direction in which you wish to move files.  This will
     either be "MS-DOS to CoCo" or "CoCo to MS-DOS".

[F3] If you are using a real CoCo disk and it is double-sided, this will allow
     you to select which side you are using.

[F4] Change maximum allowable number of tracks on the disk.  The choices are
     either 35, 40, or 80.  (If a disk is formatted for less than this maximum
     the displayed "free space" may not change when a higher track count is
     selected.)

[F5] When moving ASCII files, this option will select whether or not the PORT
     program changes the end-of-line characters in text files to match the
     format used by the destination computer.  (i.e. whether to change CR/LFs
     to CRs or back)  This has no effect on binary files.

[F6] When moving ASCII files, this will either add a CTRL-Z to the end of file
     if moving to MS-DOS, or remove it if moving to the CoCo.  Again, this has
     no effect on binary files.

[F7] When moving files to the CoCo, this tells PORT what file type to assign
     to it in the directory.  The choices are "BASIC", "Data", "EXEC", or
     "Editor".

[F8] When moving files to the CoCo, this tells PORT whether or not the file
     is ASCII, so it can set the CoCo's directory entry appropriately.  The
     choices are "ASCII" or "Binary".

You may also enter the name of a file to move, or click it from the directory
listings with the mouse.  (If you use the mouse, the direction is automatically
selected so it is moved from whichever enivronment it is in -- MS-DOS or CoCo 
-- to the other one.)  The mouse may also be used to change any of the options
above by clicking on them.


5. USING COCO CASSETTES WITH THE EMULATOR
-----------------------------------------

Within the emulator, CLOAD, CSAVE and other cassette commands are rerouted
to disk files called "virtual cassette files".  If you have a SoundBlaster
you may then read or write real CoCo cassettes by using the external utilities 
CASIN.EXE and CASOUT.EXE provided with the emulator.

Section 5.1 explains how to use virtual cassettes with the emulator while
Section 5.2 explains how to transfer them to a CoCo via the SoundBlaster,
and Sections 5.3 and 5.4 explain how to transfer from the CoCo to the PC.


5.1 THE VIRTUAL CASSETTE MENU
-----------------------------

The Virtual Cassette Menu is summoned within the emulator by pressing [F4] or
choosing option T of the Options Menu.  In it, you have the following options, 
selected by pressing the appropriate key:

[N] Select the name of the virtual cassette file.  (All virtual cassettes end
    in the .CAS extension.)  You may choose a virtual cassette from the 
    directory listing, or create new one by typing a new name.

[M] Select read/write mode.  Pressing this key toggles between "RECORD" 
    (for CSAVE, CSAVEM, PRINT#, etc.) and "PLAYBACK" (for CLOAD, CLOADM,
    INPUT#, etc.)

[S] Rewinds the counter (shown in the upper-right corner of this menu) to the
    beginning of the file.

[R] Moves backwards through the virtual cassette file.  The counter will 
    decrease.

[F] Move forward, the counter will increase.

[E] Moves to the end of the virtual cassette file.

Note that the counter represents the position in the virtual cassette file
in bytes.  A virtual cassette file cannot exceed 64K.  Be sure that the 
virtual cassette menu is set correctly before entering a cassette command
at the emulated CoCo's "OK" prompt.


5.2 USING THE SOUNDBLASTER TO WRITE CASSETTES
---------------------------------------------

By connecting a cassette recorder to your SoundBlaster's output, you can
record CoCo files on cassette which may be loaded in a real CoCo using CLOAD,
CLOADM, etc.  Follow the instructions in your SoundBlaster manual on how to
properly connect a cassette recorder.

To output a cassette file via the SoundBlaster, do the following:

1. Press RECORD on your cassette recorder.

2. Use a command of the form: 

   CASOUT [/Vn] filename[.CAS] 
   
   at the MS-DOS prompt, where "filename" is the name of the virtual cassette
   created within the emulator.  The "/Vn" option sets the volume to "n" where
   n=7 is the loudest and n=0 is the quietest.  (It is usually sufficient to 
   use the default setting of /V7.  You may wish to listen to a CoCo cassette
   tape and compare the volume levels to get it right.)

As an alternative, it is also possible to connect the black plug of your
CoCo's cassette cable directly to the SoundBlaster SKPR OUT jack, if your
SoundBlaster is configured to use its internal amplifier.  (Again, see your
SoundBlaster's instructions for details.)  Step 1 would then be to issue a
CLOAD or CLOADM command on your CoCo as appropriate, followed by the same
step 2.


5.3 USING THE SOUNDBLASTER TO READ CASSETTES
--------------------------------------------

You can also load CoCo cassettes into your PC by connecting a cassette player
to your SoundBlaster.  See the SoundBlaster manual for details on how to 
properly connect a player.

To input a cassette via the SoundBlaster, follow these steps:

1. At the MS-DOS prompt, issue a command of the form `CASIN filename[.CAS]', 
   where "filename" is the name you wish to give the virtual cassette file 
   in your PC's directory.

2. Press PLAY (or release the PAUSE) on your cassette player.

CASIN will initially display "Matching phase...".  Once it has synchronised 
with the cassette input, "Ready..." will appear, and an asterisk will blink 
in the upper-right hand corner to indicate data is being recorded.  When the 
data stops for more than five seconds, CASIN will automatically end recording.
You can manually end recording by pressing ESC.

If you want to forgo using a cassette player as a go-between, connecting a 
CoCo directly to your PC for use with CASIN is a little trickier:  

1. On a CoCo 3, you should connect the SoundBlaster's LINE IN jack to the AUDIO
   OUT of the CoCo.  On a CoCo 1 or 2, you will have to route your channel 3/4
   TV output through a VCR or a TV with an AUDIO OUT jack, and then connect
   that AUDIO OUT to the SoundBlaster's LINE IN.  DO NOT CONNECT THE CASSETTE
   CABLE'S GREY PLUG TO YOUR SOUNDBLASTER.

2. Type `POKE &HFF23,&H3C' on the CoCo.

3. Next, issue the CASIN command on your PC to get it ready to receive data 
   (i.e. displaying the "Matching phase..." line).  

4. Finally, issue the CSAVE or CSAVEM command on your CoCo, as appropriate, to 
   send the file.


5.4 READING CASSETTES FROM A .WAV FILE RECORDING
------------------------------------------------

For users who have a soundcard which is not SoundBlaster-compatible, or who
are having trouble with the method in Section 5.3 above, you may instead take
a .WAV recording of the CoCo cassette and use CASIN to convert it into a 
virtual cassette file.

The .WAV recording must be an 11025Hz/mono/8-bit sample (which is the usual
default of the WREC program).  Follow the steps in Section 5.3 using WREC
instead of CASIN to record the CoCo cassette data, and then use the command:

CASIN /W filename[.CAS]

to convert the file.  "filename" is the name of the virtual cassette output
file.  You will be prompted for the name of the .WAV file when CASIN starts.

There is no analogous .CAS to .WAV conversion for CASOUT.


6. USING PROGRAM PAKS WITH THE EMULATOR
---------------------------------------

There are two ways to read a Program Pak on a CoCo while staying in BASIC.
Either you can cover up the pin on the cartridge that tells the CoCo to
auto-start it, or you can plug the cartridge in with the power on, after
starting the following program.

WARNING: THERE HAVE BEEN MANY HORROR STORIES OF AN IMPROPERLY INSERTED
         CARTRIDGE BLOWING THE UNPROTECTED CPU WHEN THE POWER IS ON.  If
         you elect to use the latter method, do so carefully and proceed
         at your own risk.

To transfer your Program Pak to a PC, you will need the same cable used for
the diskless ROM transfer.  Then, complete the following steps:

1. IF YOU ARE USING THE COVER-THE-PIN METHOD, take the cartridge you are
   going to use and pull the cover back to expose the pins.  Then, cover
   up the fourth pin position in on the left on the bottom (pin 8, the
   "CART" signal).  (IMPORTANT: Most cartridges have no contacts for the
   first three positions, so this may be the first plated-contact from the
   left.  In this case, you can usually see where the other three positions
   should be by the scratch marks from frequent use.)  If needed, you can
   also cover up the pin on the top side directly above this one, as well as
   the three pin positions to each of their lefts if necessary.  Be careful
   not to cover the fifth pins in as this will make the cartridge unreadable.

   Once this is done, insert the Pak into your CoCo with the power off, then
   turn on the computer.  If you are successful, the CoCo will power up into
   BASIC's "OK" prompt despite the cartridge being present.

2. Next, for both methods, type in the following program in your CoCo:

   10 POKE 65315,54
   20 INPUT"INSERT PAK AND PRESS [ENTER] TO SEND";X$
   30 POKE 150,18
   40 PRINT#-2,CHR$(0);CHR$(&H20);      'Length of Pak ROM in bytes (LSB/MSB)
   50 PRINT#-2,CHR$(0);CHR$(&HC0);      'Start address of Pak (LSB/MSB)
   60 FOR X=&HC000 TO &HDFFF            'Loop for each byte in Pak
   70 PRINT#-2,CHR$(PEEK(X));
   80 NEXT X

   Note: You may omit lines 10 and 20 if using the covering-the-pin method.

3. Connect your PC to the CoCo and prepare a terminal capture program on your
   PC as described in section 2.2.  (Use the extension ".PAK" for Program 
   Paks.)

4. Run the BASIC program on your CoCo.  If you are using the insert-with-
   power-on method, insert the cartridge when you are prompted to do so and
   then press ENTER.  This will begin transmission of the cartridge's data.

The resulting file on your PC should be 8196 bytes long.  

To run the Program Pak in the emulator, simply use the Snapshot Menu, or type
"COCO pak_name" at the MS-DOS prompt when running the emulator.  To return to 
BASIC, select "Restart" in the Options Menu.

It is also possible to save snapshots of what you are doing in a Program Pak 
(such as a game-in-progress), but when reloading, you must first reload the 
Program Pak's .PAK file before loading the snapshot's .PAK file.

For those who have copied their Program Paks to their PCs using some other
method, the general format of the file constructed by the above program is:

- 2 byte ROM length (LSB/MSB, usually 8192 decimal)
- 2 byte start address (LSB/MSB, usually C000H)
- ROM data (usually 8192 bytes)

Program Pak files created on earlier versions of the emulator are compatible
to this version.


7. THE DEBUGGER
---------------

The debugger halts the emulator, displaying the current state of all the
registers in the "6809" CPU, and also includes a 128-byte memory map and
a disassembly of current instructions.  In the lower-left corner, the first
few entries on the U and S stacks are shown.  Several commands are available
to you, as summarised in the box on the lower-right:  (These commands are
probably best understood through experimentation.  [ESC] will cancel any
option except [E]DIT, which is immediate.)

[B] Sets a BREAKPOINT address.  The emulator will resume normal execution
    until the breakpoint is hit, at which time the debugger reappears.  Only
    one breakpoint can be set at a time.  The breakpoint is cleared the next
    the the debugger or another menu is displayed.

[C] CONTINUE emulation.  The breakpoint is cleared and the program returns
    to normal emulation.

[D] Change the start address of DISASSEMBLY.  A register or hexidecimal
    address can be specified.  If a register is given, the start address of
    the disassembly will always follow whatever is in that register.  The
    default for this prompt is the next byte after the last instruction
    displayed on the current disassembly.

[E] EDIT memory.  Places a cursor on the memory map with which you can
    directly modify memory.  Arrows, PG UP and PG DN work.  ROM and memory-
    mapped device addresses behave as in the genuine machine.  ESC or ENTER
    when done.

[F] Change the 6809 FLAG registers.  Press the letter of the flag to toggle
    its true (1) or false (0) value.  ESC to abort, ENTER to keep changes
    and return to main debugger options.

[H] HEXIDECIMAL CALCULATOR.  Enter a hex number or register to start.  You
    then enter one of the following operations:

    [+], [-], [*], [/], [A]nd, [O]r, [X]or, [N]eg, [S]hift, [R]ot, [D]ecimal

    The first seven of these will prompt for a second number or register to
    operate with.  [N] will NEGate the current result.  [S] or [R] followed
    by the left or right arrows will shift or rotate the bit positions of
    the result as appropriate ([ESC] to return to calculator options).  [D]
    will display the decimal equivalent and/or allow you to enter a decimal
    value.  [ESC] will return to the main debugger options.

[M] Change the MEMORY DUMP start address.  Enter either a hex address or a
    register.  If a register is used, the start address of the memory dump
    will always follow that register's contents.

[Q] QUIT EMULATOR.  Exits back to MS-DOS.  You must confirm this choice with
    a "Y".  An other reply will return to the main debugger options.

[R] Change REGISTER contents.  Select a register using the arrow keys
    followed by [ENTER], or by pressing its letter.  Then type a new hex
    value for its contents, or the name of another register to copy that
    register's contents to the currently selected register.

[S] SINGLE STEP.  Execute one 6809 instruction and return to the debugger.

[V] VIEW VIDEO.  Display the current CoCo screen and wait for a key to be
    pressed.  Pressing any key will return you to the debugger's main
    options.

Register names are just there 6809 names, without brackets, except for the
D register.  D is entered as "A/B" to distinguish it from the hex numbers
000D, 000A, 000B, and 00AB.


8. COMMENTS AND HOW TO OBTAIN THE COCO 3 EMULATOR
-------------------------------------------------

In version 1.30 I mentioned the possibility of developing a CoCo 3 emulator
if there was sufficient interest.  The response was overwhelming, so many
months later, the first release of the CoCo 3 emulator is now available.

The design is largely based on this CoCo 2 emulator, though it supports 
virtually all CoCo 3 hardware features (including the 63.5us interrupt and
timer if you are operating a fast machine).  It has been tested with a 
variety of CoCo 3 programs including OS/9 Level II.  There are a couple of 
extra PC hardware requirements that you should be aware of however:

- A VGA board (EGA graphics are not sufficient).  This VGA board must pass
  all seven tests in the VGACHECK.EXE included here.

- At least 333K of free DOS low-memory.

- Without EMS memory, the emulator acts as a 128K CoCo 3.  To emulate a 
  CoCo 3 with 512K, you need 384K of free EMS memory, an additional 96K of 
  free low memory, and an EMS 4.0 driver (such as EMM386 in MS-DOS 5.0).

- An original CoCo 3 will be needed to copy additional ROM information to
  your PC.

To order the emulator, send the $25 shareware registration fee and a blank 
disk to the address below.  (If you have an Internet account, and the ability 
to receive uuencoded .ZIP files, you can elect to receive the emulator via 
email rather than on disk.)

PLEASE BE SURE TO RUN THE VGACHECK PROGRAM INCLUDED HERE BEFORE ORDERING.
The CoCo 3 emulator takes full advantage of the standard VGA and SVGA board
functions.  Rarely, some boards do not support all these special features.
(This applies to at least one laptop computer that I know of.)  VGACHECK
will determine whether your board supports all the features required.

Also, MAKE SURE THE COCO 2 EMULATOR'S "RETRIEVE" COMMAND WILL READ COCO 
DISKS ON YOUR PC.  I don't want anyone ordering the CoCo 3 emulator only to
be disappointed to find that their hardware does not support it.

Send registration, comments or questions to:

e-mail address: jeffv@physics.ubc.ca
postal address: Jeff Vavasour
                c/o Department of Physics
                6224 Agricultural Road
                University of British Columbia
                Vancouver, B.C.
                Canada  V6T 1Z1

Please note, I CANNOT PROVIDE ROM IMAGES OR THE SOURCE CODE.
                                                                             
If you are having trouble with the above email address, then try 
"jeffv@smaug.physics.mun.ca" or "jeffv@morgan.ucs.mun.ca".  For Internet
users, I also have an email discussion group for users of my emulators.  
Drop me a line if you want to be included.


Disclaimers:  Neither this software package nor its development is in any
way associated with the University of British Columbia.  It is merely the
most reliable address I currently have.  Also, I assume no responsibility
for any damage that may result.

Acknowledgements:  Thanks to Jim Veneskey and Lori Paniak for their helpful 
references in developing and debugging this package.


APPENDIX: THE SERIAL CABLE
--------------------------

For diskless users, you will need a cable to link the serial port of your
PC to the CoCo's built-in serial port.  There are two kinds of serial
connectors on most PCs - the 9-pin and the 25-pin versions.

To start you will need a connector to mate with your PC's serial port.  For
those not used to hardware, it's best to get the "crimping" version.  No
soldering is necessary.

You'll also need a male 4-pin DIN connector.  Though Radio Shack has 
discontinued this part, many other electronics stores may still stock them
stocks these parts.  Also some Radio Shacks may still have a dusty unit
or two in stock.

The cable itself is very simple.  The pin numbers on the 9-pin and 25-pin
PC serial connectors are actually visible on the connector itself, next to
each pin.  For the 4-pin DIN connector, I will use the convention of the
CoCo's technical reference manual.  Looking at the serial I/O port on the
back of the computer itself, the pins are numbered as shown:
     
     _____              
   /  |_|  \                    Pin names: 1 = CD
4 | o     o | 1                            2 = RS232 IN
  |         |                              3 = GND
3 |  o   o  | 2                            4 = RS232 OUT
   \ _____ /


Three wires must be connected in this cable, listed below.  (The names of
the pins are also given for the reference of those interested.)  Be sure
to select the column appropriate to your PC serial connector.

From CoCo       To PC's        To PC's
4-pin DIN       9-pin          25-pin 
=========       =======        =======
Pin 2 --------> Pin 4   - or - Pin 20
(RS232 IN)      (DTR*)         (DTR*)

Pin 3 --------> Pin 5   - or - Pin 7
(GND)           (GND)          (GND)

Pin 4 --------> Pin 2   - or - Pin 3
(RS232 OUT)     (RD)           (RD)

Once the cable is assembled, it may be tested by loading a terminal program
on your PC and selecting the appropriate COM: port with the settings:
2400 baud, 1 stop bit, 8 word length, no parity.  Next, power on your CoCo
and type the following:

POKE 150,18
PRINT#-2,"THIS IS A TEST"

If the cable is working properly you should see the message "THIS IS A TEST"
on your PC.  If no message appears on the PC, but the "OK" prompt returns 
on your CoCo, check the line connected to the CoCo's pin 4 (RS232 OUT).
(A ohmmeter or continuity checker would be useful for this.)  If the "OK"
prompt fails to return, check pin 2 (RS232 IN).  Also, it is a good idea
to check the GND line in both cases.