ÜÛÛÛÛÛÛÜ     ÜÛÛß ÜÛÛÛÛÛÛÜ
                            ÛÛÛ  ÛÛÛ   ÜÛÛß   ÛÛÛ  ÛÛÛ
                            ÛÛÛÜÜÜÜ  ÜÛÛß ÜÜÜ ßÛÛÜÜÛÛß
                             ßßßßÛÛÛ ÛÛÛÜÜÛÛÛ ÜÛÛßßÛÛÜ
                            ÛÛÛ  ÛÛÛ ßßßßßÛÛÛ ÛÛÛ  ÛÛÛ
                            ßÛÛÛÛÛÛß      ÛÛÛ ßÛÛÛÛÛÛß

           A Full Screen Simulator for 8048 Compatible Microprocessors

                                  William Luitje
                                 11 February 1995


       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Background ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        I  wrote this simulator as part of my work on a consulting job  a 
        few years ago.   There is still quite a lot of work one could  do 
        to improve it,  such as simulating the timer,  providing a way to 
        manually  change  RAM and ports,  simulating changes  in  inputs, 
        command files...  A LOT!  Still, I think it's useful, as is,  for 
        learning the 8048  instruction set and debugging small  programs.  
        I  hope  it's  useful  to you;  if you use it,   please  see  the 
        registration section at the end of this document (relax, no money 
        is involved). 

        With  the  work I mentioned above and some features  specifically 
        for  an educational environment,  this program would make a great 
        tool   for  teaching  microprocessor  programming.     Commercial 
        programs  like  this  cost from $200  to $300.    If  I  make  an 
        educational  version  of  S48,   I   envision  a  site  licensing 
        arrangement  which  would cost a very modest amount per  student.  
        If  you are an instructor or administrator and are interested  in 
        pursuing this, contact me at the address given at the end of this 
        document even if you use a different micro in your course. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Introduction ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        S48   simulates the instruction set and some of the hardware  for 
        the 8048,  8049,  8050, 8021, 8022  microprocessors originated by 
        Intel and now widely second-sourced.  The simulator handles these 
        hardware parameters: 

        * 4096 bytes of ROM
        * 128 bytes of internal RAM
        * 256 bytes of external RAM
        
        The  hardware  registers  and  flags  and  RAM  are  continuously 
        displayed  on  screen  and  are updated as  each  instruction  is 
        executed.  There is a disassembly window showing the instructions 
        as they are executed.   You can trace through instructions one at 
        a time or execute them continuously until a breakpoint is reached 
        or you stop the program manually. 
        
        The  hardware requirements to run S48  are quite simple;   you'll 
        need  a  PC with a CGA,  EGA,  or VGA compatible video card  (the 
        program does direct screen writes so you'll see snow using  CGA).  
        A  color  display is not strictly necessary,   but  is  certainly 
        helpful in reading the screen easily.  Obviously, the faster your 
        CPU,   the  faster the simulation will run.  A  4.77  MHz  PC  is 
        adequate for small programs.   The software requirements are even 
        simpler: you'll need some version of DOS, S48 and an 8048 program 
        to simulate.  
         
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Sample Program ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        I've included a very simple sample program for you to play  with, 
        called demo.bin.  demo.asm is the source file and implements a 16 
        bit  counter in software.   There is an interrupt service routine 
        which  captures  the low byte of that counter and  stores  it  in 
        consecutive  locations  in  external RAM when  the  interrupt  is 
        invoked.    It's short enough that I can reproduce  its  assembly 
        listing here: 

                                   .org   0
         0000 00                   nop    
         0001 04 06                jmp    start
         0003                      .org   3
         0003 00                   nop
         0004 04 14                jmp    intsvc
                          ;
         0006 27          start    clr    a
         0007 B8 18                mov    r0,#24
         0009 A0                   mov    @r0,a
         000A A8                   mov    r0,a
         000B A9                   mov    r1,a
         000C 05                   en     i
         000D 18          loop     inc    r0
         000E F8                   mov    a,r0
         000F 96 0D                jnz    loop
         0011 19                   inc    r1
         0012 04 0D                jmp    loop
                          ;
         0014 F8          intsvc   mov    a,r0
         0015 D5                   sel    rb1
         0016 90                   movx   @r0,a
         0017 18                   inc    r0
         0018 C5                   sel    rb0
         0019 93                   retr
         001A                      .end

        You'll also need an understanding of the 8048 instruction set and 
        architecture.  You won't find much help in this document. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Tutorial ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The 8048 program to be executed must be in binary form,  like you 
        would use to program an EPROM,  not in "hex" form.   To start the 
        simulation, just give the name of the binary file as an argument, 
        e.g: 

        s48 demo.bin 

        Take  a  minute to familiarize yourself with the  layout  of  the 
        screen: 

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³Cmd:                                                                        ³
 ³ 26 bytes read from demo.bin                                                ³
 ³ÚÄPC¿ ÚAÄ¿ÚPSWÂCYÂACÂF0ÂF1ÂRBÂSTK¿ÚTEÂTFÂIE¿                                ³
 ³À000Ù À  ÙÀÄ08ÁÄ ÁÄ ÁÄ0ÁÄ0ÁÄ0ÁÄÄ0ÙÀÄ0ÁÄ0ÁÄ0Ù                                ³
 ³ ÚMB¿ ÚBus¿ÚP1ÂP2ÂP3ÂP4ÂP5ÂP6ÂP7¿ ÚT0ÂT1ÂII¿                                ³
 ³ ÀÄ0Ù ÀÄ  ÙÀ  Á  Á  Á  Á  Á  Á  Ù ÀÄ ÁÄ ÁÄ Ù                                ³
 ³    ÉÍ00ÍÍ10ÍÍ20ÍÍ30ÍÍ40ÍÍ50ÍÍ60ÍÍ70ÍÍÍ»          ±000±00±±±±NOP±±±±±±±     ³
 ³ 00 º °°                               º 08        001 04 06 JMP  006       ³
 ³ 01 º °°                               º 09        003 00    NOP            ³
 ³ 02 º °°                               º 0A        004 04 14 JMP  014       ³
 ³ 03 º °°                               º 0B        006 27    CLR  A         ³
 ³ 04 º °°                               º 0C        007 B8 18 MOV  R0,#18    ³
 ³ 05 º °°                               º 0D        ÚÄÄÄÄBreakpointsÄÄÄÄ¿    ³
 ³ 06 º °°                               º 0E        À±±± ±±± ±±± ±±± ±±±Ù    ³
 ³ 07 º °°                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»    ³
 ³    ÌÍ00ÍÍ10ÍÍ20ÍÍ30ÍÍ40ÍÍ50ÍÍ60ÍÍ70ÍÍ80ÍÍ90ÍÍA0ÍÍB0ÍÍC0ÍÍD0ÍÍE0ÍÍF0ÍÍÍ¹    ³
 ³ 00 º                                                                  º  08³
 ³ 01 º                                                                  º  09³
 ³ 02 º                                                                  º  0A³
 ³ 03 º                                                                  º  0B³
 ³ 04 º                                                                  º  0C³
 ³ 05 º                                                                  º  0D³
 ³ 06 º                                                                  º  0E³
 ³ 07 º                                                                  º  0F³
 ³    ÈÍÍÍ0FÍÍ1FÍÍ2FÍÍ3FÍÍ4FÍÍ5FÍÍ6FÍÍ7FÍÍ8FÍÍ9FÍÍAFÍÍBFÍÍCFÍÍDFÍÍEFÍÍFFÍ¼    ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The  top  line is where you type your commands to the  simulator.  
        The  second  line is where any messages from S48  are  displayed.  
        The hardware registers and flags are displayed with a light  blue 
        background  at  the  top  left  of  the  screen.    There  is  an 
        instruction disassembly window at the top right with the  current 
        instruction (the one to be executed next) shown in reverse video.  
        Below   it   are  the  5  instructions  following   the   current 
        instruction.    Above  it will be displayed the 6  most  recently 
        executed instructions.  Below the disassembly window is where the 
        breakpoints are displayed. 
              
        The large L shaped box shows all of RAM.   The top part shows 128 
        bytes of internal RAM and the lower shows 256  bytes of  external 
        RAM.   There isn't enough room on the screen to have blank  space 
        between  the columns so they are distinguished by the  background 
        color.   The first column contains locations 00  through 07;  the 
        second holds 08 through 0F, and so on.  The light blue background 
        in internal RAM shows the active register bank. 

        When  the simulator is started the processor is in  reset.    The 
        values  of registers which are initialized by RESET,  e.g.    the 
        Program Counter,  are shown;  registers which are undefined after 
        RESET, such as the Accumulator and RAM are shown as blank. 

        Let's do some simulation.  Give a Trace command by pressing the t 
        key  and  return.   The NOP instruction has now moved  above  the 
        current  instruction  line,  the PC has changed to 001   and  the 
        current instruction is JMP 006.   Give another trace command  and 
        the  current  instruction  changes to CLR A.    Notice  that  the 
        instructions  after the current instruction have now  changed  to 
        reflect  the jump.   Their color has changed,  too,  to  make  it 
        easier to see that that has happened.  (This is especially useful 
        for following conditional jumps.)  Trace again and notice how the 
        Accumulator is initialized to zero. 
        
        Now  let's  watch the simulation run for a while.   Give  the  Go 
        command  by  pressing the g key and return.   As  the  simulation 
        runs,  notice how memory location 0 counts up quickly and  memory 
        location 1 counts slowly.  Press any key to stop the simulation. 

        To invoke the interrupt, press the i key and return.   Notice how 
        the  current instruction changes to the first instruction of  the 
        interrupt  service routine at location 003.   Trace  through  the 
        rest  of  the  interrupt  service  routine  and  notice  how  the 
        background  of the register banks changes as the active  register 
        bank is switched. 

        To  demonstrate setting a breakpoint,  type "b 11"   and  return.  
        This  will  set a breakpoint at the instruction which  increments 
        the high byte of the 16 bit counter. Now give a go command and in 
        a few seconds the simulation will stop at location 11.  To remove 
        the  breakpoint,   use the kill command with the address  of  the 
        breakpoint you want to remove.   In this case, "k 11"  and return 
        will do the trick. 

        To Quit the simulator, press q and return. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Command Summary ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        You've  seen all of the commands except for Reset and Port in the 
        tutorial;   here  we'll  summarize them and give  a  little  more 
        information about them.   Only the first letter of the command is 
        parsed  and  it can be either upper or lower case.   Some of  the 
        commands can take a numeric argument which is always expressed in 
        hexadecimal and need not be given. 

        g #   Go: Start simulating at address #.  Simulation stops when a 
              breakpoint  is reached or when a key is pressed.   If #  is 
              not given,  simulation starts at the location given by  the 
              Program Counter. 

        t #   Trace:  Trace  #  instructions.   If # is not  given,   one 
              instruction is traced. 

        b #   Breakpoint:  Set  a breakpoint at the given address.    The 
              command has no effect if a number is not given. 

        k #   Kill  breakpoint:   Remove  the  breakpoint  at  the  given 
              address.    The  command has no effect if a number  is  not 
              given or if there is no breakpoint at that address. 

        p # # Port value:  Set the port  specified by the first # to  the 
              value  specified by the second #.   Two parameters must  be 
              given. 

        r     Reset:  Simulate a  reset.   The Program Counter is set  to 
              zero and other registers are set as appropriate.  Registers 
              which are not affected by RESET are not changed. 

        i     Interrupt:  Simulate an interrupt.   The Program Counter is 
              set  to  the  location of the  interrupt  service  routine, 
              0003H, and further interrupts are disabled. 

        q     Quit:  Quit the simulation.  Come back again soon!

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Registration ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        While this software may be freely copied and used,  I  do request 
        that  you  register  it if you use it.   Just send  me  either  a 
        postcard   or   some  e-mail  telling  which  program   you   are 
        registering.   I'd prefer a local,  picture postcard;  after all, 
        whether  it's great or whether it's a pit,  the place  where  you 
        live is probably interesting in some way, right? 
          
        This  is only partially an ego massage for the author.   I  enjoy 
        writing  useful  utilities  and  have  several  other  pieces  of 
        freeware  out floating around the net.   I'd like feedback  about 
        which of them is worth expanding and supporting.  Postware really 
        works!    I  support the programs which are most used.   I'm  not 
        planning on adding features to this program, but I might if I get 
        enough postcards.  

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Conditions of Use ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The program has not been tested against a real live 8048  because 
        I  don't  have access to an 8048   hardware  development  system.  
        That's why I wrote this simulator in the first place!   The Intel 
        data  books  I used were ambiguous in places so  I  made  guesses 
        about  how  some of the subtler points of the  simulation  should 
        work.  (E.g.,  does INC set AC?  I  guessed not.)   There may  be 
        instances  where  I  guessed wrong.   Bug  reports  are  welcome, 
        especially  when  you  can provide documentation  about  how  the 
        simulation really should work. 

        So, keep in mind that this software is provided as is.  I make no 
        guarantees about it except that it will take up space on any disk 
        you place it on.  Further, any software you write with the aid of 
        this simulator is your responsibility.   Verify that it  operates 
        properly  with  actual  hardware before you use it  in  the  real 
        world. 

        William Luitje
        2677 Wayside Drive
        Ann Arbor, MI 48103
        USA

        Internet:  luitje@m-net.arbornet.org

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± History ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Version 1.0  1 Aug 94 
          Initial public release
        Version 1.1 11 Feb 95 
          Added command to set ports
          Added color change of prospective disasssembly window after 
          jump, branch or interrupt.