RATEHD.PRG & RATEHD.DOC
Copyright 1989-1991  ICD, Inc.
 
This document and the program RATEHD.PRG, may be distributed by 
any non-commercial means (may not be sold) as long as the they
are distributed together and no modifications are made.  
Language translations are allowed.

The copyright holder is:

     ICD, Inc.
     1220 Rock Street
     Rockford, IL  61101-1437

     Voice:  (815) 968-2228
     BBS:    (815) 968-2229
     FAX:    (815) 968-6888
     Orders: (800) 373-7700   NO TECH SUPPORT on this number!!!

RATEHD.PRG was written in Personal Pascal, a product of ICD, Inc.
-----------------------------------------------------------------

RATEHD was written to show performance characteristics of 
various hard disk drives.  It was developed at ICD to allow fair
comparison when evaluating hard disk drive mechanisms, embedded
SCSI drives and SCSI controllers when used on the Atari ST.  It
does not go through a hard disk handler (like ICDBOOT.SYS) so it
is not useful in rating the speed of different handlers.  
Generally, the ICD hard disk handler provides a significant 
speed improvement in actual use due to its caching.

We were a bit apprehensive about releasing this to the public 
because of our fears that people would not understand it and 
will use it for the wrong purpose.  It is intended as a
comparison test and should not be used to verify a drive or
controller against printed specifications.  Drive manufacturers
test their drives on specialized test equipment and not on an
Atari ST.  Data rates are also usually shown as a burst rate.  
What we are measuring is the sustained rate, which is closer to
the top end in real life usage.

Our final decision to release RATEHD was twofold:

1) There is too much misinformation out there when it comes to 
   computers and hard drives.  There needed to be a uniform
   benchmark test for the Atari ST.  Magazine reviews have
   typically mislead the public, not maliciously, but because of
   the reviewer's ignorance on the subject and lack of 
   scientific testing methods.  Now you have a benchmark; just
   don't abuse it.

2) When we finished the FA-ST Tape Backup, we realized that a 
   hard drive system would need a certain amount of finesse to
   keep up with the streaming tape.  If the tape had to keep
   backing up and waiting for the hard drive to catch up, the
   backup time would become laboriously long and almost not 
   usable.  A data rate of about 300 K/s (kilobytes per second)
   is required to keep the tape moving without any stopping and
   backing up.  As the data rate gets slower, the tape will begin
   to backup and restart several times per partition.  A data
   rate of less than 200 K/s would probably become unbearable at
   attempting a backup.

We have tested many drives and controllers at their optimum 
interleaves and found that Adaptec MFM controllers (including
Atari SH204, Megafile 20) run about 300 K/s if they are formatted
at 1:1 interleave.  Adaptec RLL controllers (including Atari
Megafile 30 and 60) run about 315 K/s at 2:1 interleave.  Omti
MFM controllers move along about 360 K/s using 1:1 with Omti RLL
at about 375 K/s at 1:1.  Embedded controller drives are usually
the speedsters with the Seagate ST138N and ST157N cruising at 550
K/s at 1:1.  The quickest we have measured was a Quantum LP105S
which flies at 1197 K/s which is probably fast enough to do real
time video.  It also had 21 ms average access time and had a 105
Megabyte formatted capacity.


THE PROBLEM WITH MOST TEST METHODS
----------------------------------

There are many variables in something as complex as a computer 
with a hard disk drive that can make testing a cumbersome task.  
The most obvious way to test hard drive speed is to copy files
from a hard drive to a RAMDISK and then back to a clean hard
drive while timing the process.  Although on the surface a test
like this appears sufficient, it cannot give an accurate picture
of what to expect in performance after using the drive for a
while.  Both hard drives would need to be freshly formatted (no
files yet) and with identical partition sizes.  If not freshly
formatted, the DOS fat table delays and fragmentation would enter
a significant amount of error into the rating equation.  Of
course the same DOS and same computer must also be used.

While this seems like a reasonable test method, it would only 
show the data rate (assuming both drives were formatted at their
optimal interleave).  Step rate in this type of test would not be
a measurable factor as it would later on when the files on the
drives become fragmented.  Fragmentation occurs as a hard drive
gets used and files are modified.  They increase in size and 
when rewritten to the drive, not all the file parts are in
consecutive sectors anymore, probably not even in the same area
of the disk.  The file eventually becomes a group of "fragments."
This is where the movement of the head from track to track (step
rate measured as average access time) really becomes an 
important speed factor.  It would not be an easy task to create 
two freshly formatted drives of different manufacture with
identical fragmentation on each drive.

Many of the magazine reviews we have seen give no indication of 
the test method.  It is almost as if the numbers were arrived at
by magic.  We now offer RATEHD as a solution to all magazine
reviewe