SUPERCHARGER NOTES

The ICD host adapter software fully supports the Supercharger PC
emulator.  You MUST determine the SCSI ID of your Supercharger.
They are shipped as ID 3.  After setting up your hard drive to
auto-boot with HDUTIL, go to the Config option of that program.
Near the bottom of the screen you will see a line that says 'Skip
SCSI ID's:'.  Normally only ID 6 is skipped; this is the ICD real
time clock.  You MUST also set the ID of your Supercharger here,
then save.  This means that all ICD programs will not do any SCSI
commands on this ID.  (This means that you need no longer hold
down the Supercharger's reset button when booting the computer 
with the Supercharger attached).

You must also disable write caching when running the 
Supercharger, otherwise you will never write to your hard disk.
This can be accomplished in several ways.  First, you can set up
your booter to disable write caching.  Second, you can
permanently enable write caching and turn it off temporarily with
the DESKTOP.ACC or with the CACHEOFF.PRG.  There is also a
CACHEON.PRG to turn the caching back on.  See below for a more
complete explanation.

If using COLDBOOT.PRG you must also configure it with 
CFGCBOOT.PRG to skip the Supercharger's ID.

Please note that the Supercharger is fully compatible with old
ICD Host Adapters.  It is NOT compatible with early release 
versions of the ICD AdSCSI ST and AdSCSI Plus ST host adapters.
In addition to the software you will need a hardware upgrade kit
which