SMARTDRIVE OVERHAUL
          
          SMARTDRIVE is a disk cache program that works with
          computers that have extended memory.  A disk cache uses
          a portion of memory to store information that DOS reads
          from disk.  DOS can read the information from the disk
          cache much faster than it can read information from a
          drive.  However, with DOS 6.0 Microsoft had their
          SMARTDRIVE program default to both read caching and write
          caching.  The problem with write caching is that if you
          turned your computer off immediately after quitting a
          program, you could potentially lose data.
          
          With DOS 6.2 SMARTDRIVE write caching is turned off by
          default.  If you upgrade to DOS 6.2 from 6.0 and you had
          SMARTDRIVE write cache your drives, then SMARTDRIVE
          leaves write caching turned on.
          
          You can force DOS immediately to write the cached data to
          the hard drive, by typing at the system prompt:
          
                              smartdrv /c <ENTER>
          
          With DOS 6.2 SMARTDRIVE automatically flushes a write
          cached disk before returning you to the system prompt. 
          
          This means it gets the data from memory and writes it to
          the hard drive before you are returned to the system
          prompt.  If you are using DOS at the command line, you
          should always exit your program and return to the DOS
          prompt before you turn your machine off.
          
          With DOS 6.2 Microsoft has added a new /X switch to turn
          off write caching for all drives. 
          
          For most people, the SMARTDRIVE line is in their
          AUTOEXE.BAT file which is a text file that resides on the
          root directory of the start-up disk.  See pages 205 - 208
          in LEARNING DOS FOR THE COMPLETE NOVICE, 2nd Edition for
          examples and exact instructions on how to use EDIT and
          modify your AUTEXEC.BAT file to selectively turn off
          write caching.  Those people with exotic ("bus-mastering"
          hard disk controllers) such as SCSI, or ESDI, may need to
          have SMARTDRIVE installed in the CONFIG.SYS file.  The
          CONFIG.SYS file also resides in the root directory of
          your start-up disk and can be viewed and modified with
          the DOS EDIT program.  See pages 209 through 211 in
          Learning DOS for the Complete Novice, 2nd Edition, for
          how to view and modify your CONFIG.SYS file. 
          
          With DOS 6.2, you could add the /X switch to turn off
          write caching like so:
          
          SMARTDRV /X
          
          You can selectively disable write caching by following
          the SMARTDRV command with the letters of your hard
          drives.  Suppose you had hard drives C, D, E, and you
          wanted to disable write caching on these drives.  Use the
          DOS EDIT program to change the SMARTDRV line in the
          AUTOEXEC.BAT file to read the following:
          
          SMARTDRV C D E 
          
          The above line tells DOS to allow read caching while
          disabling write caching for drives C, D, and E. 
          SmartDrive does not cache compressed drives (DoubleSpaced
          drives); however, for increased performance, you can
          cache the host drive.  If you are running DoubleSpace,
          you can get information on all your drives by typing:
          
                              dblspace /i <ENTER>
          
          If you are running DoubleSpace, the above command gives
          you information about all your drives.  It also tells you
          which drive is your host drive.  Suppose you have only
          one hard drive and are running DoubleSpace.  Suppose you
          typed the above command and found out that your
          DoubleSpace host drive is called H.  If that is the case,
          you can configure SMARTDRIVE to read cache, but not write
          cache the host drive by changing your SMARTDRIVE line in
          your AUTOEXEC.BAT file to read:
          
          SMARTDRV H  
          
          
          SmartDrive does not cache network drives, or RAM drives. 
          
          
          With DOS 6.2, SMARTDRIVE read caches CD-ROM drives.  This
          is a very nice feature because CD-ROM drives are often
          too slow.  Caching should help performance.
                    
          If you want to see which drives SMARTDRV is caching, at
          the system prompt type:
          
                              smartdrv <ENTER>
          
          
          TIP
          
          If after typing SMARTDRV <ENTER> you notice that your CD-
          ROM drive is not being cached, there may be a perfectly
          logical reason.  The line which loads the MSCDEX program
          needs to be loaded BEFORE the SMARTDRV line.   
          
          To see how to modify an AUTOEXEC.BAT or CONFIG.SYS file
          see LEARNING DOS FOR THE COMPLETE NOVICE, 2nd Edition. 
          For most people the line that loads the MSCDEX program
          (for the CD-ROM) and SMARTDRV will be in the AUTOEXEC.BAT
          file.  The AUTOEXEC.BAT file resides in the root
          directory of the start-up disk (usually drive C). 
          
          
          EXOTIC HARD DRIVES 
          
          If you are one of those people who have an exotic "bus
          mastering" hard drive controller, you may need to have
          SMARTDRIVE load in the CONFIG.SYS file.  For specific
          instructions on how to modify a CONFIG.SYS file look in
          Learning DOS for the Complete Novice, 2nd edition.  Try
          using the following line in the CONFIG.SYS file:
          
          DEVICE=C:\DOS\SMARTDRV.EXE /DOUBLE_BUFFER
          
          The above SMARTDRIVE command needs to come before the
          DEVICE command that loads EMM386.  Note that when in the
          CONFIG.SYS file, SMARTDRV.EXE is used.  Remember, before
          an AUTOEXEC.BAT or CONFIG.SYS start up file can take
          effect, you must reboot your machine.  After you reboot
          type:
                              smartdrv <ENTER>
          
          With the above DEVICE=C:\DOS\SMARTDRV.EXE /DOUBLE_BUFFER
          line in your CONFIG.SYS file the SMARTDRV <ENTER> command
          loads SMARTDRIVE into upper memory.  After you do that
          you can type the following:
          
                              smartdrv /s <ENTER>
          
          Here, the /S stands for Status.  A table appears on your
          screen that looks something like:
          
                       DISK CACHING STATUS
          
          drive    read cache    write cache    buffering
            A:        yes            no            no
            B:        yes            no            no
            C:        yes            yes           no   
            S:        yes            no            no
          
          Look in the buffering column.  If all the entries say
          "no" then your hard drive does not need this Double
          Buffering and you would be better off taking the
          SMARTDRIVE line out of your CONFIG.SYS file and just
          using a SMARTDRV line in your AUTOEXEC.BAT file.  This
          Double Buffering makes SMARTDRIVE operate slower.  So, if
          your hard drive can support SMARTDRV in the AUTOEXEC.BAT
          file, you are better off.
          
          If you want more information about the DOS 6.2 SMARTDRIVE
          program type:
          
                              help smartdrv <ENTER>
          
          Of course, you will have to be using DOS 6.2.  If you
          need any help on using the DOS HELP see pages 192 - 194
          in LEARNING DOS FOR THE COMPLETE NOVICE, 2nd Edition.
          
          
          TIP
          
          If you are using DOS at the command line, you should
          always exit your program and return to the DOS prompt
          before you turn your machine off.  Make sure the rest of
          the family knows this, too.