Textshot Version 3.1
          
                                      +++++++++
          
                                by McAdams Associates
          
          
          
          
          *****************************************************************
          
          
          
          
                                    **IMPORTANT**
          
           To register Textshot, see "Registering Textshot" on page 10 of 
                                    this manual.
          
          
          
          Contents                                   Page
          --------                                   ----
          
          Description................................ 2
          Hardware Requirements...................... 2
          Loading Textshot........................... 2
          Removing Textshot From Memory.............. 3
          Activating Textshot........................ 3
          Using Textshot............................. 4
          Saving a Screen............................ 6
          Image Editing.............................. 6
          A Word About Palettes...................... 7
          If There Are Problems...................... 7
          Tips For Getting a Good Picture............ 8
          Disclaimer & Agreement..................... 9
          Registering Textshot....................... 10
          Index...................................... 11
          
          
          
          
          
          
          
          
          
          
          
          
          
              (C)Copyright 1993 by T.C. McAdams.  All Rights Reserved.

          Textshot Description
          --------------------
          
          Textshot is a pop-up TSR (Terminate and Stay Resident) program 
          designed to be a text screen counterpart to ZSoft's FRIEZE(tm), 
          producing output files for use in word processors and desktop 
          publishing applications.  The user loads Textshot into memory, 
          presses the hot key from within a character-based application, 
          and a menu pops up permitting entry of a filespec and a choice of 
          various file options.  When the [ENTER] key is pressed, the 
          screen is restored and is saved to disk in the form of either a 
          16-color or monochrome (2-color) PC Paintbrush-format .PCX 
          graphics file.  This file can be loaded into any application that 
          accepts .PCX files or into ZSoft's PC Paintbrush(tm) itself, for 
          editing.  PC Paintbrush is not needed to use Textshot.  Textshot 
          also permits image "clipping" prior to writing an image to disk, 
          as well as the optional preservation of image settings between 
          pop-ups.  Textshot should work on any DOS computer running DOS 
          2.11 or above.
          
          Hardware Requirements
          ---------------------
          
          Textshot will work with any of the common PC video standards.  
          Specifically: MDA/Hercules, CGA, EGA and VGA.  Textshot is 
          intended to work only in text modes, not in graphics modes.
          
          Textshot will capture 80x25 screens (all standards), 80x43 
          screens (EGA and VGA) and 80x50 screens (VGA).  Screen formats of 
          other than 80 columns are not supported.
          
          Since Textshot relies on a computer's internal graphics fonts for 
          its output, the computer on which it's run must have, at minimum, 
          a complete CGA font set.  In instances where this is not the 
          case, a DOS utility called GRAFTABL must be run to supply the 
          "upper half" of the necessary font set.  EGA and VGA cards supply 
          their own complete font sets.
          
          
          Loading Textshot
          ----------------
          
          Textshot is loaded into memory by typing
          
                          TEXTSHOT [ENTER]
          
          at the DOS command line.  If you use an expanded memory manager, 
          Textshot will function happily in high memory, leaving your DOS 
          memory free for other things.  For example, if you use 
          Quarterdeck's QEMM, you can load Textshot into high memory by 
          typing 
          
                          LOADHI TEXTSHOT [ENTER]
          

          
          
                                          2

          When Textshot is loaded a message appears telling you so.  As 
          mentioned above, on some machines a full (256-character) ROM font 
          set may not be available; Textshot checks to see before loading.  
          If this is the case, you are told to run the DOS GRAFTABL utility 
          before proceeding.  Screen printing is disabled while Textshot is 
          resident.
          
          Removing Textshot From Memory
          -----------------------------
          
          To remove Textshot from memory simply type
          
               TEXTSHOT [ENTER]
          
          from the command line, just as if you were loading it.  Note: If 
          you loaded Textshot into high memory through a memory manager, 
          don't bother invoking the memory manager a second time to remove 
          Textshot.  Just type "TEXTSHOT [ENTER]".
          
          Textshot will tell you it's unloaded itself, else it will tell 
          you that it CAN'T unload itself.  There are many reasons why a 
          TSR could be unable to remove itself from memory, but most of 
          them come down to some other program, used after Textshot was 
          loaded, altering the computer's interrupt table.  In these cases, 
          the only way to unload Textshot is to reboot.   
          
          Activating Textshot
          -------------------
          
          Textshot's hot key is [PrScr] or, on some machines, 
          [SHIFT + PrScr], which means hold down the [SHIFT] key while 
          pressing [PrScr].  
          
          If the hot key is pressed while in a graphics mode, you'll hear 
          two beeps.  This is Textshot's way of telling you to stop doing 
          that.  You will also hear two beeps if your video adapter is in 
          other than an 80-column text mode.  In the special case of the 
          Hercules adapter, it doesn't seem to be possible to tell with 
          100% reliability when it is and isn't displaying graphics; 
          sometimes, if you press the hot key while Hercules graphics are 
          being displayed, instead of hearing beeps you'll see "splotches" 
          appear at the top of the screen.  This means that Textshot has 
          failed to accurately gauge modes and you'll see what ASCII 
          characters written to a graphics screen look like.  Solution: 
          press [ESC] to leave Textshot.  Your graphics screen will be 
          restored.
          
          Another potential problem lies with other programs that play with 
          a computer's interrupt table, particularly the keyboard 
          interrupts.  Textshot attempts to be good to your computer's 
          interrupt table, taking over and using no more of your computer's 
          resources than it absolutely has to; but it has to have access to 
          some things simply to function.  If Textshot refuses to pop up, 
          or if you have trouble typing inside Textshot, try changing the 
          loading order of any other TSR programs you might be using.  If 
          
          
                                          3

          you're not running any other TSRs simultaneously with Textshot 
          and it still refuses to function correctly, the problem probably 
          lies with the running application, and there may not be much to 
          be done about it.
          
          Using Textshot
          --------------
          
          After pressing the hot key in text mode, a menu will appear at 
          the top of your screen.  On the first line is a prompt saying 
          "Enter filespec:".  This is where you type a name for your screen 
          capture file.  Textshot's default pop-up mode is black-and-white. 
          Pressing [F6] (described a little later on) will switch you to 
          color output mode.
          
          On the second and third lines are what might be called "status 
          prompts", giving you your options: [ESC] and [F1] through [F6].  
          Here's what they do:
          
          [ESC]  Leaves the program, "pops it down".
          
          [F1]   Controls image inversion in monochrome mode.  Textshot 
                 pops up with this option set to "OFF".  The correct 
                 setting of this toggle (called a "toggle", because 
          when you press it, it goes to its opposite state; pressing once 
          produces "ON", pressing again produces "OFF", and so on) can only 
          be determined by examining the final printed output of whatever 
          document or file you've loaded your screen image into.  Some 
          applications will print a normally-output ("OFF" setting) screen 
          black-on-white while others will print it as white-on-black.  
          What you want your output to look like will determine the setting 
          of this switch.  Try it both ways.  Note that this option is 
          disabled ("NA", for "Not Applicable" is shown) when color output 
          is active.
          
          [F2]   The state of this toggle determines whether dot patterns 
                 are used in the file to simulate, to the degree it's 
                 possible, what the background colors of a screen look 
          like in monochrome mode.  6 of the 8 possible background colors 
          have their own pattern.  No patterns are necessary for white-on-
          black and black-on-white areas.  Whether or not it's worthwhile 
          to use color patterns will depend entirely on the nature of the 
          screen you're taking a picture of and what you want the final 
          output to look like.  Again, give both a try.  This option isn't 
          available (or necessary) in monochrome screen modes, and "NA", 
          for "Not Applicable", is shown in color output mode.
          
          [F3]   On MDA/CGA-equipped machines, pressing this key does 
                 nothing; CGA fonts are all there are.  On EGA/VGA-equipped 
                 machines, you can tell Textshot to use any font available 
          in your computer by pressing this toggle.  For an EGA, this means 
          CGA and EGA fonts.  For a VGA adapter, it means CGA, EGA and VGA 
          fonts.  Where you have a choice, each option represents 
          tradeoffs: EGA or VGA fonts will give a higher-resolution 
          picture, but at the cost of increased file size.  CGA fonts 
          
          
                                          4

          produce the smallest output files, but with the coarsest picture 
          resolution.  The resolution question must be decided by what 
          you're using the output files for, and what quality is necessary.  
          The file size issue might become important if you're loading 
          screen images into an application that already hogs most of 
          memory, when a change in font resolution could mean the 
          difference between using or not using a file.  Also be aware that 
          .PCX file editors that don't use scroll bars may be unable to 
          load higher-resolution Textshot files.
          
          Textshot pops up with the font switch set to the highest possible 
          resolution by default.  This can be changed by using the [F4] 
          key.
          
          [F4]   This key preserves Textshot's toggle settings, including 
                 the position of the clipping box (discussed next).  
                 Filespecs are not preserved.  The color mode (described 
          under [F6], below) is unaffected by this toggle.
          
          [F5]   Pressing this key enables you to tell Textshot which areas 
                 of your screen to save.  When pressed, it causes the menu 
                 to (temporarily) disappear and a white "clipping box" to 
          appear on your screen.  The first time this key is pressed, the 
          box will be as large as your screen; changing the box's shape 
          tells Textshot which part of the screen you want saved -- those 
          parts that are covered by the box.  The clipping box is 
          "inclusive", which is to say that whatever is covered by the 
          edges of the box will be included in what is saved.  This would 
          permit, for example, collapsing the clipping box down to the size 
          of a single character, if that's what you wanted, and saving that 
          single character to a file.
          
          The clipping box is controlled by pressing the arrow keys.  When 
          [F5] is pressed and the box first appears, the arrow keys control 
          the "upper left" sides of the box.  The top and left sides.  
          Pressing [ENTER] with the box still visible "flips" the arrow 
          keys, which then control the "lower right" sides of the box.  The 
          right and bottom sides.  Pressing [ENTER] again toggles sides yet 
          again, which can be repeated as many times as necessary.
          
          Pressing [SHIFT + ARROW] accelerates the clipping box's 
          movements, allowing you to "cover more territory" quickly.
          
          After setting the clipping box, pressing [ESC] makes the box 
          disappear and the menu reappear.  
          
          If you should want to quickly restore the clipping box to its 
          default (whole screen) size without having to use the arrow keys, 
          make sure the [F4] toggle is set to "OFF", pop down Textshot, by 
          pressing [ESC] from the menu, and then pop it up again by 
          pressing [PrScr].  The box dimensions will then be reset.
          
          Note: At least one older version of PC Paintbrush has 
          intermittent difficulties with less-than-full-screen (clipped) 

          
          
                                          5

          color Textshot files.  No other editor or viewer we've tried has 
          any trouble with these images.  
          
          [F6]   This toggle controls Textshot's color mode setting.  
                 Textshot's default pop-up mode is monochrome, displayed as 
                 "B/W".  Pressing [F6] changes this to "COLOR", and all 
          subsequent output will be in color.  Note that pressing the [F4] 
          toggle has no effect on the color setting, which will remain as 
          set until [F6] is pressed again.  
          
          Color output files are considerably larger than an equivalent 
          monochrome file, and so will take correspondingly longer to write 
          to disk.
          
          Saving A Screen
          ---------------
          
          Textshot doesn't care whether or not you use a .PCX file 
          extension in your filespec.  So if you want your files to be 
          "real" PC Paintbrush files, it will be necessary for you to give 
          them a .PCX or .PCC extension.
          
          Filespecs can be as long as the available screen space.  The 
          cursor will stop automatically when you've reached the limit.  
          
          After entering your filespec and selecting the desired options, 
          pressing [ENTER] causes Textshot to restore the screen and write 
          the file you've specified.  Since a high-resolution file might 
          take a little while to write, especially on slower machines, 
          Textshot will beep when it's finished writing to disk.  That will 
          mean your picture is complete.
          
          Textshot does not include the cursor in the pictures it makes.  
          If whatever you're using the picture for requires a text cursor, 
          one can be "faked in" by loading the file into PC Paintbrush (or 
          some another .PCX file editor) and drawing it.  Concerning which, 
          be sure to read the "Image Editing" section immediately 
          following.
          
          Image Editing
          -------------
          
          As with any other .PCX-format file, screen images produced by 
          Textshot can be loaded and edited inside a .PCX file editor.  
          Your editor may need to be reconfigured (PC Paintbrush through 
          PBSETUP) to match the color mode of the image.
          
          Depending on the "match" between Textshot's output and the 
          current default aspect ratio of the .PCX file editor you load it 
          into, some image distortion may be apparent.  If, for example, 
          you capture a VGA- or EGA-resolution screen image with Textshot, 
          in monochrome mode, and load it into a CGA-configured PC 
          Paintbrush, all the characters will seem elongated.  Don't worry.  
          These files can be edited easily enough inside PC Paintbrush.  
          When, however, the images are imported into an application they 
          
          
                                          6

          will automatically assume the aspect ratio (the ratio of height 
          to width) of the "frame" into which they're "poured".  A 
          computer's video screen has an aspect ratio of about 3:4.  If the 
          frame you pour the image into, inside your application, has this 
          same aspect ratio, the screen images will look natural.  If your 
          Textshot images are saved using the CGA font, the resulting 
          images would appear to have a "natural" aspect ratio inside PC 
          Paintbrush to begin with, when it is configured for CGA.
          
          It may also happen that a Textshot image might not completely 
          fill the screen of an editor.  A full 25-line VGA screen image, 
          for instance, will have a resolution of 640 x 400 pixels, less 
          than the standard VGA graphics screen resolution of 640 x 480 
          pixels.  What this means is that if, after editing such a file in 
          VGA screen mode, the file is saved back to disk, those blank 
          areas on the bottom -- and on the right as well, if editing on a 
          Hercules-configured screen -- will go with it.  This is something 
          to take into account.
          
          Every word processor or desktop publishing program we are 
          familiar with has no trouble importing PC Paintbrush images, 
          regardless of resolution or mode, and that includes Textshot 
          images; mode translation is always automatic.  Final judgements 
          regarding hardware and software compatibility, though, as with 
          any shareware product, must be yours.  Please make sure Textshot 
          works with everything you might need it to work with before 
          committing to it.
          
          A Word About Palettes
          ---------------------
          
          In color output mode, when running on CGA- and EGA-equipped 
          machines, Textshot uses the default color palette.  On VGA 
          machines, Textshot uses the active palette.
          
          In monochrome output mode, Textshot uses a generic, default CGA 
          palette for its output, which has the virtue of at least making 
          Textshot images visible in all screen modes.  The monochrome 
          palette has no effect that we've seen on how monochrome Textshot 
          images are handled in any word processor or desktop publishing 
          application.
          
          If There Are Problems
          ---------------------
          
          If Textshot has any trouble when writing the file, you'll hear 
          two beeps, a message window at the top of the screen will appear, 
          and whatever the problem might be is described.  You are then 
          asked to press any key, and the message window disappears.  Press 
          [PrScr] again to try the operation over.
          
          Make sure you've typed a correct pathname (a directory that 
          exists) and that the disk you're writing to has enough room for 
          the output file.  Textshot tells you specifically about most 
          common disk problems.  If you see the general message "Disk 
          
          
                                          7

          error", though, it's something sufficiently obscure that Textshot 
          (and probably you) can't do much about it.
          
          Finally, if there ever should be any difficulty in loading a 
          Textshot file into an application, you might try loading it first 
          into a .PCX file editor, saving it back to disk with the same 
          filename, and then trying again.
          
          Tips For Getting A Good Picture
          -------------------------------
          
          As mentioned previously, the first things to try when saving an 
          image is to use the toggle switches available when Textshot is 
          "popped up".  In monochrome mode, image inversion, the use of 
          color patterns and changing the image resolution should make it 
          possible to get an acceptable image under most circumstances.  
          But what do you do if none of these work?  This section has some 
          additional ideas.
          
          If your video adapter is able, try switching to a monochrome 
          display mode (VGA, MDA, or Hercules).  Most programs make their 
          screens differently, using ASCII characters and character 
          intensity only, when running in monochrome.
          
          In cases where the color patterns aren't what you want, but you 
          don't want to switch Textshot to color output, you can sometimes 
          solve the problem by changing the patterns used by changing the 
          top application's screen colors.  Since you are dealing with 
          Textshot's color patterns, remember that it doesn't matter what 
          the colors on the screen look like, whether they are pretty or 
          ugly; all that matters is that the color patterns turn out 
          acceptably.  If all else fails, try changing the application to 
          sheer black-on-white, or vice versa.
          
          If you need to put something into a captured image that wasn't in 
          the original, or take out something that doesn't belong, you must 
          resort to a .PCX file editor.  There, it will be possible to add 
          cursors and to capture small bits of an original file as .PCC 
          (cutout) files.
          
          














          
          
                                          8

          Disclaimer & Agreement
          ----------------------
          
          Users of Textshot must accept this disclaimer of warranty:
          
               "Textshot is supplied as is.  The author disclaims all 
               warranties, expressed or implied, including, without 
               limitation, the warranties of merchantability and of 
               fitness for any purpose.  The author assumes no 
               liability for damages, direct or consequential, which 
               may result from the use of Textshot."
               
          Textshot is a "shareware program" and is provided at no charge
          to the user for evaluation.  Feel free to share it with your
          friends, but please do not give it away altered or as part of
          another system.  The essence of "user-supported" software is to
          provide personal computer users with quality software without
          high prices, and yet to provide incentive for programmers to
          continue to develop new products.  If you find this program
          useful and find that you are using Textshot and continue to use
          Textshot after a reasonable trial period, you must make a 
          registration payment of $25 to McAdams Associates.  The $25 
          registration fee will license one copy for use on any one 
          computer at any one time.  You must treat this software just like 
          a book.  An example is that this software may be used by any
          number of people and may be freely moved from one computer
          location to another, so long as there is no possibility of it
          being used at one location while it's being used at another.
          Just as a book cannot be read by two different persons at the
          same time.
          
          Commercial users of Textshot must register and pay for their
          copies of Textshot within 30 days of first use or their license
          is withdrawn.  Site-License arrangements may be made by 
          contacting McAdams Associates.
          
          Anyone distributing Textshot for any kind of remuneration must
          first contact McAdams Associates at the address below for 
          authorization.  This authorization will be automatically granted 
          to distributors recognized by the ASP as adhering to its 
          guidelines for shareware distributors, and such distributors may 
          begin offering Textshot immediately (However McAdams Associates 
          must still be advised so that the distributor can be kept up-to-
          date with the latest version of Textshot.).
          
          You are encouraged to pass a copy of Textshot along to your
          friends for evaluation.  Please encourage them to register their
          copy if they find that they can use it.
          
          And since this is shareware and we are a member of the 
          Association of Shareware Professionals, please read the 
          following:
          
               "This program is produced by a member of the 
               Association of Shareware Professionals (ASP).  ASP 
          
          
                                          9

               wants to make sure that the shareware principle works 
               for you. If you are unable to resolve a shareware-
               related problem with an ASP member by contacting the 
               member directly, ASP may be able to help. The ASP 
               Ombudsman can help you resolve a dispute or problem 
               with an ASP member, but does not provide technical 
               support for members' products. Please write to the ASP 
               Ombudsman at 545 Grover Road, Muskegon, MI 49442
               or send a CompuServe message via CompuServe Mail to ASP 
               Ombudsman 70007,3536."
               
          Registering Textshot
          ---------------------
          
          Registering Textshot costs $25 and includes the latest version of 
          Textshot, a typeset manual, one year's free support by phone, 
          mail and CompuServe e-mail, free bug fixes, and TWO handy utility 
          programs: 1) SEARCH, a multitalented disk scanning file-finder 
          program, and 2) TO/RET, a "two-in-one" combo that work together, 
          enabling you to change to any disk/directory and return instantly 
          to your starting point.
          
          To register Textshot, simply print and fill out the file 
          REGISTER.DOC and send it, along with $25 (checks or M.O.s drawn a 
          U.S. banks only, please) to:
          
                                 McAdams Associates
                                  P.O. Box 835505 
                             Richardson, TX  75083-5505
          
                                 CIS PPN 70353,1644
          
          
          Textshot was created using QuickC and MASM, which are trademarks 
          of Microsoft Corporation.




















          
          
                                         10

          INDEX
          -----
          
          Activating Textshot, see [PrScr] key
          Beeps
               One (signifying completion), 6
               Two (disk error), 7
               Two (graphics mode error), 3
          Clipping (image), 2, 5
          Color mode, 6
               and [F4] key, 5
               and Image inversion, 4
               and Patterns, 4
          Color patterns, 4, 8
          Commercial distribution, 9
          Commercial use of Textshot, 9
          Disk errors, 7-8
          Editing Textshot images, 6-7
          [ESC] key,  4, 5
               and Hercules "splotches", 3
          [F1] function key, see Image inversion
          [F2] function key, see Color patterns
          [F3] function key, see Fonts
          [F4] function key, see Preserve settings
          [F5] function key, see Clipping
          [F6] function key, see Color mode
          File sizes, 6
          Fonts
               Aspect ratios of, 6-7
               [F3] toggle, 4-5
               File sizes using different, 4-5
               Hardware requirements, 2
          GRAFTABL DOS utility, 2, 3
          Graphics file format, 2
          Graphics modes, 2, 3
               Hercules (determining), 3
          Hot key, see [PrScr] key
          Image inversion, 4, 8
          Leaving Textshot, see [ESC] key
          Loading Textshot, 2-3
          Memory managers, 2, 3
          Palette
               Color, 7
               Monochrome, 7
          PCX file editors, 5, 6, 7, 8
          PCX file extension, 6
          PCX file format, 2, 6-7
          Preserve settings, 5
          [PrScr] hot key, 3
          Registering Textshot, 10
          Software compatibility, 3-4
          Support, 10
          Unloading Textshot, 3
          Video
               80-column modes supported, 2
          
          
                                         11

               Aspect ratio, 7
               Hercules & PC Paintbrush, 7
               Monochrome, 8
               VGA & PC Paintbrush, 7
               Standards (compatibility), 2


















































          
          
                                         12