AMIGA/FTERM
AMIGA/BBSTERM

    FTERM [-Nnet] [port#] [-c#] [-wcapturefile]

    FTERM opens a standard intuition window and connects to a CSH running on
    the remote UNIX machine.  If the remote machine is another Amiga, it
    connects to the terminal-window server (STERM).

    UNIX: The csh runs on a PTY and is NOT named, which means you don't show
    up in WHO or FINGER, and cannot TALK other people (nor can they talk you).
    To get a named shell, you must 'rlogin localhost'.  This adds another process
    to the character-loop.

    The default port# is 8195.	You can also specify another port # to
    connect to.

    The -N option specifies the network (default = 0).  This is the same
    network as was specified when you ran DNET (if was not specified, is 0)

    The -c# option (-c7 for example) sets the 'cooked' mode.  Bits are
    defined as follows:

		bit
		0   turn keyboard CR's into LFs when sent to remote
		1   Local Echo (half duplex)
		2   cause received LFs to generate a CR+LF (i.e. CSI20h)

    -wcapturefile   Specify name of capture file, else "ram:capture".

    Menus:  (partially implemented):  Capture -capture into ram:capture

				      Paste   -pastes from ram:paste

				      Flush   -get rid of buffered data
					       on remote end (that would
					       otherwise take a long time
					       to display)

    BBSTERM is simply FTERM renamed, and uses PORT_BBS (8200) instead of
    PORT_IALPHATERM (8195).

    RELEASE INFO:

    V1.10   DNET 1.10 release

	    -Implements auto window resize and auto-remote-resize
	    -Implements local echo (cooked mode) and buffering

	    Remote STERM implements equivalent options and now has the
	    same resize/echo/remote-resize capabilities as FTERM.

    V1.00   Initial Release