Thermal.doc

The    self   generated   heat    of 
transistors  used for small  signals 
such  as  low power  amplifiers  and 
oscillators  rarely  cause  problems 
due  to overheating but as  soon  as 
appreciable  power is involved  then 
all  sorts  of problems  may  arise. 
This  is very true of  power  supply 
units  that  may  need  to   provide 
output currents of several  amperes. 
To  avoid  destruction of  a  series 
pass transistor used in such a power 
unit  the  generated  heat  in   the 
transistor  must  be  dissipated  to 
prevent the transistor case and thus 
the   junction   rising  above   the 
manufacturers  maximum  rating.  For 
long  life it is desirable that  the 
transistor   'runs'   as   cool   as 
possible. 

The  programme will ask for  various 
parameters  to be entered  and  some 
of  these can be obtained  from  the 
transistor manufacturers data sheet. 
The  others  are determined  by  the 
characteristics of the power  supply 
circuit and components.  For example 
consider  a power unit  designed  to 
output  12 volts at  1  ampere.  The 
input   voltage  under   full   load 
conditions will need to be 12  volts 
plus the  volts  dropped  across the 
series pass transistor,  typically 2 
volts.  In  addition some  allowance 
must  be made for variations in  the 
mains  power  supply.  These  rarely 
exceed  5%.  Therefore the 12  volts 
must be increased by at least 5%  to 
12.6 volts. The final design voltage 
is  now 12.6 + 2 = 14.2  volts.  But 
this  assumes  that  the   rectifier 
filter  capacitor is  sufficient  to 
'hold  up'  the voltage  during  the 
trough  of  the  voltage  from   the 
rectifiers.   Again  the  rectifiers 
will  create a volts drop  of  about 
0.6  volts  each and  this  must  be 
allowed    for.     Under    typical 
conditions    the   rectified    and 
filtered  input to the  series  pass 
transistor, under full load, will be 
in the region of 15 volts at best.

As  an  example consider  a  popular 
transistor  type  2N3055 used  as  a 
series     pass     device.      The 
manufacturers absolute maximum  case 
temperature is 160 degrees  Celsius. 
At  that  temperature  there  is  no 
leeway  for temporary overloads  and 
it  is  preferable  that  a  maximum 
working  temperature of 100  degrees 
be used.

So  far things are straight  forward 
but now the tricky part is assessing 
the  specification of the heat  sink 
that  will be required to  dissipate 
the  transistor  heat  so  that  the 
maximum  temperature of 100  degrees 
is  not exceeded.  Fortunately  heat 
sink manufacturers normally  specify 
their heat sinks with a degrees  per 
watt figure. For example a heat sink 
specified  as 4 degrees C  per  watt 
means  that  it's  temperature  will 
rise  4  degrees above  ambient  for 
each watt dissipated:  e.g.  4 watts 
results  in  16 degrees  rise  above 
ambient.

If  the thermal contact between  the 
transistor and heat sink is  perfect 
then  the  transistor  will  operate 
near  the  same temperature  as  the 
heat  sink BUT this is an  imperfect 
world and some temperature  gradient 
will  exist between  the  transistor 
and heat sink. The magnitude of this 
gradient  is,  to  a  large  extent, 
under  your control.  The heat  sink 
surface   should  be  as   flat   as 
possible  and the transistor  should 
be  firmly  bolted to it  so  as  to 
provide the maximum surface  contact 
and lowest thermal  resistance.  The 
addition  of a  proprietory  thermal 
grease  between the mating  surfaces 
will make a substantial improvement. 
In  most  instances  the  electronic 
circuit  arrangement   neccessitates 
the  body  of the  transistor  being 
electrically insulated from the heat 
sink  and recourse must be  made  to 
fit a suitable insulator between the 
transistor and sink.  The choice  is 
limited  to  a  thin mica shim, hard 
anodised    aluminium (this being an
insulator  so long  as  the anodised
surface  is  not  damaged) and  heat 
conductive    plastic/fibre    glass 
compounds. Thermal grease must still
be   used   to maintain good thermal
contact. The Thermal.Prg  allows for
various transistor/heat sink types.

It is assumed that the heat sink  is 
mounted with it's fins vertical  and 
with free air circulation.

Example of programme use:-

Transistor:     2N3055
Case Size :     TO3 
Input Volts:     18
Output Volts:    12
Output Amps:      3
Case Temp:      100 degrees C
Sink Insulator: Mica with grease
Ambient Temp:   30 degrees C

Putting  the above  parameters  into 
the  programme will specify  a  heat 
sink  rated at 3.39 degrees  Celsius 
per watt.  Use the nearest  standard 
sink  available  that  has  a  lower 
figure eg 3 degrees per watt.

         - - - - - - - - -