MPC UPGRADE KIT'S 
                           MOST COMMONLY-ASKED
                          QUESTIONS AND ANSWERS

                             January 25, 1992

THE MEDIA VISION MULTIMEDIA PC UPGRADE KIT CONTAINS:
     Media Vision Pro AudioSpectrum Audio Adapter Board
     Internal SONY CDU-541 CD-ROM Drive (SCSI, 380ms, 150KB, 64K buffer)
          (one caddy, one terminator, one SONY manual)
     All necessary cables to connect the SONY drive to the PAS
          (one audio cable, one 50-pin flat ribbon SCSI cable)
     Multimedia Upgrade Kit Hardware Installation Disk v1.02 
          (MVSOUND.SYS, TSLCDR.SYS, MSCDEX) in both 3 1/2" and 5 1/4"
     Microsoft Windows 3.0 with Multimedia Extensions 1.0 on CD
     Compton's Multimedia Encyclopedia by Brittanica Software on CD
     Jones in the Fast Lane by Sierra On-Line on CD
     Introducing Windows with Multimedia v1.0 Manual (blue covers)
     Three Steps to a Multimedia PC Manual (blue covers)
     Installation Guide, Read Me First! (8-page pamphlet)

ABBREVIATIONS: 
     MPC            = Multimedia PC
     PAS            = Media Vision Pro AudioSpectrum
     TB             = Media Vision Thunder Board
     MWINDOWS       = Windows 3.00a with Multimedia Extensions v1.0
     CD-ROM Drive   = SONY CDU-541 SCSI CD-ROM Drive
     RMA            = Return Material Authorization number

Generic CONFIG.SYS:
     DEVICE = C:\MWINDOWS\HIMEM.SYS
     FILES = 30
     BUFFERS = 10
     LASTDRIVE = X       (Refer to Question 12 below)
     DEVICE = C:\DOS\SETVER.EXE    (Refer to Question 10 below)
     DEVICE = C:\PROAUDIO\TSLCDR.SYS /D:MVCD001 /R     
     DEVICE = C:\PROAUDIO\MVSOUND.SYS D:X Q:X V:X (Refer to Question 2
                                                  below)
     DEVICE = C:\MWINDOWS\SMARTDRV.SYS 2048 512

Generic AUTOEXEC.BAT:
     @ECHO OFF
     PATH = C:\;C:\DOS;C:\MWINDOWS;C:\PROAUDIO
     PROMPT $P$G
     C:\PROAUDIO\MSCDEX.EXE /D:MVCD001 /M:12 /L:X /V   
          (X is the drive letter assigned to the CD-ROM drive)

The current version for TSLCDR.SYS is v1.31e and for MSCDEX.EXE is v2.2. 
If you have an older version, please contact Media Vision Technical Support
for updated drivers.  When calling, please provide us with the version
number which you currently have.

SOUND TYPES:
     Digital Audio     = Recorded sounds, usually speech and sound effects. 
                         These sounds are played back by the Digital-To-
                         Analog Converter (DAC) on the PAS.  Called
                         "WaveAudio" and designated by the ".WAV" extension
                         in MWINDOWS.   
     Synthesized Audio = FM sounds, usually music but can also be used to
                         produce speech and sound effects.  These sounds
                         are played back by the FM Synthesizers on the PAS. 
                         Called "Sequencer" and designated by the ".MID"
                         extension in MWINDOWS.

     CD Audio          = Sounds produced by the CD-ROM drive which can be
                         heard when connecting the headphones directly to
                         the CD-ROM drive.  Also known as Red Book Audio.
     PC Speaker        = Crude music tones, speech and sound effects 
                         produced by the System Timer Chip on the
                         motherboard.  These sounds are played back by the
                         internal PC Speaker.

INTERNAL CD-ROM DRIVES SUPPORTED BY PAS:

Chinon              CDS-431.  Please contact Chinon at 310-533-0274 to get
                    the 40-pin to 50-pin converter.
Hitachi             CDR-3650
NEC                 CDR-80, CDR-82, CDR-83
Sony                CDU-541
Texel               DM-3020, DM-3021
Toshiba             XM-3201B

EXTERNAL CD-ROM DRIVES SUPPORTED BY PAS:

Apple               CD-SC (Sony CDU-8001)
CD Technologies     Porta-Drive
Chinon              CDX-431
Denon               DRD-253
Hitachi             CDR-1553S, CDR-1650, CDR-1750S
IBM                 3510
Laser Magnetics     CM212, CM214, CM231
NEC                 CDR-35, CDR-36, CDR-72, CDR-73, CDR-77
Panasonic           CR-501-S
Pioneer             DRM-600 6-disc changer
Sony                CDU-6211
Texel               DM-3010, DM-3120, DM-5020, DM-5021, DM-5120, DM-7120A,
                    DM-7120B
Toshiba             XM-3201A, XM-3301, XM-5100A

If your CD-ROM drive is not on this list, it will NOT work with the PAS. 
If it is on this list and you would like to use the Pro AudioSpectrum's
SCSI interface to control the CD-ROM drive, please contact Media Vision
Sales at 1-800-845-5870 to order an Internal SCSI Cable/Driver Kit for
$39.00 or an External SCSI Cable/Driver Kit for $79.00.
 
PRO AUDIOSPECTRUM USES THE FOLLOWING:

     DMA 1 at default.  Selectable between 1, 2 and 3.
     IRQ 7 at default.  Selectable between 3, 5, 6 and 7.
     And all of the following I/O port addresses which are fixed:

     Speaker             042h      Speaker Timer Count*
                         043h      Speaker Timer Control*
                         061h      Speaker Control*
     Joystick*           201h      Joystick Status
     FM Synthesizer      388h      Left FM Synthesizer Address
                         389h      Left FM Synthesizer Data
                         38Ah      Right FM Synthesizer Address
                         38Bh      Right FM Synthesizer Data
     Interrupt Ports     B89h      Interrupt Control
                         B8Ah      Audio Filter Control
                         B8Bh      Interrupt Control Register
     PCM Circuitry       F88h      PCM Data
                         F89h      Reserved
                         F8Ah      Cross Channel Control
                         1388h     Sample Rate Timer
                         1389h     Sample Buffer Count
                         138Ah     Local Speaker Timer Count
                         138Bh     Local Speaker Timer Control
     SCSI Interface      1F88-1F8B SCSI Register
                         3F88-3F8B SCSI Register
                         5F88-5F8B SCSI Data Register
*Located on PC system board

NOTE:
Windows 3.00a with Multimedia Extensions v1.0 is a Microsoft product which
is distributed by Media Vision.  Many problems and questions can be
answered by referring to your Windows 3.0 User's Guide.  For questions that
do not pertain to the Multimedia Extensions v1.0, please contact Microsoft
Product Support for Windows at (206) 637-7098 for assistance.  For
questions that pertain to the specific software applications that support
Windows 3.0 with Multimedia Extensions v1.0, please contact the software
manufacturers for assistance.

QUESTIONS & ANSWERS:

****************************PAS INSTALLATION******************************
1.   Q:   Do I have to change any switches or jumpers before I install the
          PAS?
     A:   The default settings will work in most computers.  Only try with
          different DMA and IRQ settings if you experience any problems. 
          Whenever changing the settings on the PAS, make sure you make the
          same changes in the MVSOUND.SYS statement, in CONFIG.SYS.

2.   Q:   What is the MVSOUND.SYS driver for?
     A:   You must have "DEVICE = C:\PROAUDIO\MVSOUND.SYS D:X Q:X V:X" in
          the CONFIG.SYS file.  The first two X's correspond to the DMA
          channel and IRQ settings.  The third X in "V:X" represents the
          initial volume level, a value between 0 and 40, where 40 is the
          maximum volume level.  This driver resets the mixers and the
          volume settings on the PAS.  Without this driver, none of your
          Adlib games will play sounds.

3.   Q:   I have tried with all settings and PASTEST.EXE still fails.
     A:   First, PASTEST.EXE may need to be run twice in a row.  Second,
          reduce the system to a generic CONFIG.SYS and AUTOEXEC.BAT to
          eliminate possible software conflicts.  Third, remove all
          unnecessary peripheral boards (scanner, tape controller, network
          cards, etc.) in the system to eliminate possible hardware
          conflicts.  Fourth, in most computers, it will accurately report
          if there are conflicts; however, in some 486/33 computers, it may
          not be accurate.  If you have already tried everything and
          PASTEST still fails, go on and install the CD-ROM drive and then
          MWINDOWS.

*****************************SCSI INTERFACE********************************
4.   Q:   Which CD-ROM drives can I use with the PAS?
     A:   See CD-ROM Drives Support List above.  The PAS has a SCSI
          interface which only allows it to control SCSI devices.  Please
          contact Media Vision Sales for the SCSI Cable/Driver Kit
          (Internal/External).  

5.   Q:   Do I have to use the PAS SCSI interface to control my CD-ROM
          drive which has its own controller?
     A:   If your CD-ROM drive is SCSI, you can use its own controller or
          the PAS SCSI interface.  

6.   Q:   Can I use the PAS to control other SCSI devices?
     A:   Yes.  Trantor Systems is currently selling SCSI drivers for the
          PAS for a variety of SCSI devices (hard disks, removable media,
          optical, etc.).  Please contact Trantor Systems for the PAS
          driver set at (510) 770-1400.  The price for the driver set is
          $59.00.
************************CD-ROM DRIVE INSTALLATION**************************
7.   Q:   I get the error "No SCSI host adapter found".
     A:   First, the SCSI CD-ROM driver is board dependent.  If you would
          like to use the PAS to control the CD-ROM drive, you need to use
          our TSLCDR.SYS driver; otherwise, if you would like to use
          another SCSI controller (such as Adaptec or Future Domain) to
          control the CD-ROM drive, you need to use its driver (contact the
          SCSI controller manufacturer for the driver).  Second, check the
          internal, flat ribbon SCSI cable to make sure it is properly
          connected to the PAS.  Third, make sure the red painted edge of
          the cable is closest to the 4-pin connector on the PAS at J6. 
          Fourth, make sure the terminator is connected securely to the
          back of the CD-ROM drive.  Try both with and without the
          terminator.  Fifth, reduce the system to a generic CONFIG.SYS and
          AUTOEXEC.BAT.  Sixth, reduce the computer's bus (I/O CLK) speed
          to 10MHz or less.  Seventh, if there is a co-resident Thunder
          Board, make sure Switch 4 (FM synthesizer switch) on the TB is
          set of OFF.

8.   Q:   I get the error "No devices respond on this SCSI host adapter".
     A:   First, check the internal, flat ribbon SCSI cable to make sure it
          is properly connected to the back of the CD-ROM drive.  Second,
          make sure the terminator is connected securely to the back of the
          CD-ROM drive.  Try both with and without the terminator.  Third,
          make sure you have inserted the computer's power plug into the
          CD-ROM drive connector and pushed it firmly into place.

9.   Q:   I get the error "Device driver not found: MVCD001.  No valid CD-
          ROM selected".
     A:   First, if you are using DR DOS 6.0, it is necessary to change the
          device name for both the TSLCDR.SYS and MSCDEX.EXE statements
          from "MVCD001" to "TSLCD".  Second, make sure that the device
          names in both of these statements match.

10.  Q:   MSCDEX.EXE issues the error "Incorrect DOS version".
     A:   If you are using MS DOS 5.0, MSCDEX.EXE v2.2 requires that
          CONFIG.SYS has the statement "DEVICE = C:\DOS\SETVER.EXE".  We
          will make an announcement in the BBS Newsletter when the new
          version of MSCDEX.EXE is available, which will not require
          SETVER.EXE when using MS DOS 5.0.

11.  Q:   I cannot use the CD-ROM drive.
     A:   First, make sure that you have connected the power supply's power
          cable to the CD-ROM drive.  Second, refer to all questions listed
          above.  Second, make sure the MSCDEX.EXE statement precedes any
          menu, DOS Shell, PCTOOLs, or any desktop manager statements in
          AUTOEXEC.BAT to ensure that the driver has been properly loaded.

12.  Q:   I get the error "Invalid drive specification" when I type the
          drive letter assigned to the CD-ROM drive.
     A:   First, make sure you have "LASTDRIVE = X" in the CONFIG.SYS,
          where X is the next logical drive letter after the letter
          assigned to the CD-ROM drive in the MSCDEX.EXE statement. 
          Second, make sure that the TSLCDR.SYS driver statement precedes
          any driver statement that creates a RAM drive such as
          RAMDRIVE.SYS.  Third, check if the TSLCDR.SYS and MSCDEX.EXE
          drivers have been loaded up properly.  If not, refer to the
          questions above.

13.  Q:   I get the error "CDR 101: Drive not ready".
     A:   First, check the internal, flat ribbon SCSI cable to make sure it
          is properly connected.  Second, make sure the terminator is
          connected securely to the back of the CD-ROM drive.  Try both
          with and without the terminator. 

14.  Q:   a.   I get the error "CDR 103: CD-ROM not High Sierra or ISO-9660
               format reading drive X.  Abort, Retry or Ignore?" 
          b.   My CD-ROM drive fails at random.
     A:   First, check if the LASTDRIVE statement and TSLCDR.SYS driver are
          loaded before a hard disk driver and/or a memory manager.  If so,
          load the hard disk driver and/or memory manager first.  Second,
          refer to the question above.

15.  Q:   a.   How do I connect the internal audio cable? 
          b.   I do not hear any CD-Audio at all.  
          c.   I only hear through one channel (speaker).
     A:   The audio connector on the back of the CD-ROM drive has been
          keyed to connect only one way.  Make sure it is properly
          connected.  One end of the cable plugs into the back of the CD-
          ROM drive and the other into the 5-pin connector on the PAS at
          J7.  

********************************MWINDOWS**********************************
16.  Q:   I have Windows 3.0 already installed.  Can I install MWINDOWS on
          top of my Windows 3.0?
     A:   We DO NOT recommend installing over Windows 3.0.  Either delete
          Windows 3.0 completely or install MWINDOWS into a new directory
          and call it \MWINDOWS.

17.  Q:   I have problems during MWINDOWS installation.
     A:   First, use generic CONFIG.SYS and AUTOEXEC.BAT.  Second, select
          the default VGA 640x480 16-color palletized driver.  After a
          successful installation, you can install the high-resolution
          driver for your graphics card. 

18.  Q:   While using DOS Shell, when I try to run MWINDOWS, I get an
          execution error and the computer locks up.
     A:   First, exit DOS shell before running MWINDOWS.  Second, make sure
          that MWINDOWS is in your path statement.  Third, you must have
          "SET TEMP = C:\MWINDOWS\TEMP" in AUTOEXEC.BAT and also a TEMP
          directory under MWINDOWS.

19.  Q:   MWINDOWS does not load with QEMM installed.  It loads fine after
          I removed QEMM.
     A:   First, make sure that you have QEMM 6.0 (or better).  Second, re-
          install QEMM 6.0 after you have successfully installed MWINDOWS.  
           
20.  Q:   The blue manual titled Introducing Windows with Multimedia, page
          3-5, states under the "Are There any Multimedia Samples?" that
          there are .MMM movie files located in the \MWINDOWS\MMDATA sub-
          directory and to use the Media Player to display the movie files. 
          However, I have not located any .MMM files.
     A:   The next version of the MWINDOWS CD-ROM disk will contain the
          movie player and .MMM movie files.  We will make an announcement
          in the BBS Newsletter when the next version of the MWINDOWS CD-
          ROM disk is available.

21.  Q:   I do not hear any digital audio and/or synthesized audio in
          MWINDOWS.
     A:   First, this may be caused by an IRQ or DMA conflict.  Try with
          different IRQs and DMAs.  IRQ 7 may conflict with LPT1.  DMA 2 is
          used by the floppy disk controller.  Second, make sure that the
          IRQ and DMA settings on the PAS board, in the MVSOUND.SYS
          statement, and in SYSTEM.INI (at end of file) all match up.

22.  Q:   I can hear sound inside of MWINDOWS but the computer locks up
          upon exiting.
     A:   We do not know what causes this problem. A few customers have
          been able to prevent the computer from locking up by going into
          the Sound section of the Control Panel to disable the sounds for
          SYSTEM_START and SYSTEM_EXIT.  This is done by assigning <None>
          to SYSTEM_START and SYSTEM_EXIT).

23.  Q:   I am having trouble using Sound Recorder.
     A:   First, Sound Recorder only allows 22Khz sampling rate, mono, and
          up to 1 minute of recording.  Second, you must go into ProMixer
          to enable recording from the input source (change "play" to
          "rec").  Third, we will make an announcement when a new version
          of Sound Recorder is available which will provide additional
          features.

24.  Q:   There is a lot of noise in the microphone recordings.
     A:   First, make sure that the microphone has 600-ohm impedance (or
          higher).  Second, mount the microphone on a stand instead of
          holding in your hand.  Third, use headphones instead of external
          speakers/amplifiers to eliminate the possibility of feedback
          which can cause distortion or noise.

*********************COMPTON'S MULTIMEDIA ENCYCLOPEDIA********************
25.  Q:   After running Compton's Multimedia Encyclopedia, I only hear
          sounds out of one channel (one speaker).
     A:   When Compton's plays digital audio (represented by .WAV file
          extension), it puts the CD-ROM drive into mono mode and also
          shuts down one channel.  You need to re-boot to reset the CD-ROM
          drive.  Please contact Brittanica Software at (415) 597-5555 to
          add your name to a waiting list for an update.

********************MPU-401 AND SOUND BLASTER EMULATION********************
26.  Q:   a.   Does the PAS support MPU-401?
          b.   Does the PAS support SB?
     A:   a.   No.  The MIDI Interface chip on the PAS is the Yamaha 3802
               MIDI controller and not the Roland MPU-401 MIDI Interface
               chip.  
          b.   No.  The method used on the PAS to record and play back is
               different on the existing SB card.  

     Note:     Media Vision has developed an emulation program which
               enables the PAS to emulate the MPU-401 in "DUMB mode" and
               the SB to work with most SB games.  Please note that this
               program requires a 386SX or better and will work in DOS and
               Windows 3.0.  This emulation program is called SB2MV.ZIP and
               is located in the ZIP files area of this BBS.

*********************************GAMES*************************************
27.  Q:   My PAS is set to DMA 3 and IRQ 5.  I hear music but I don't hear
          any sounds when running Sierra games that support the PAS.
     A:   The PAS driver in your Sierra games require that the PAS is set
          for DMA 1.  Some Sierra games also require IRQ 7.  Sierra is
          working on updating the PAS driver to allow DMA 1/2/3 and IRQ
          3/5/6/7 to be selected.  Please contact Sierra for the update.

28.  Q:   I have games/software that provide drivers for the SB and AdLib. 
          Which driver should I select?
     A:   The PAS is 100 percent AdLib compatible and will work with any
          package that provides driver for AdLib.  If the package does not
          support digital audio, then the AdLib driver or SB driver can be
          selected.  Otherwise, if the package does support digital audio
          with the SB driver, please refer to the "MPU-401 and Sound
          Blaster Emulation" section above. 

29.  Q:   Does the PAS make my game sound better than my AdLib board?
     A:   PAS.EXE is a utility that allows you to adjust the mixer, volume
          settings, bass, treble, loudness, enhanced stereo (will make a
          mono signal simulate stereo), and realsound (to improve PC
          speaker sounds).

30.  Q:   Sometimes when I play a game that supports AdLib, I only hear
          sound out of one speaker.
     A:   There are two ways to run PAS.EXE.  The first way is to run "PAS
          RESET" to reset the mixer.  The second way is "PAS *" to bring up
          the Mixer Control Panel on screen.  Press F1 to get help, then F4
          to reset the mixer.

31.  Q:   Until I run MWINDOWS, none of my games produce any sound.
     A:   You must have "DEVICE = C:\PROAUDIO\MVSOUND.SYS D:X Q:X V:X" in
          the CONFIG.SYS file.  Please refer to the "PAS Installation"
          section above.

32.  Q:   The joystick does not work at all or does not work properly when
          using the PAS's joystick port.
     A:   First, some computers have a built-in joystick port on the
          motherboard.  Other computers have a multi-I/O board that has a
          joystick port.  Make sure that only one joystick port is enabled
          and the other one is disabled.  Second, if the computer is too
          fast that may also cause a problem.  Reduce the computer's BUS
          (I/O CLK) speed and try again.  Refer to your computer user's
          guide for instructions on how to adjust the BUS (I/O CLK) speed. 
          Third, contact the game manufacturer to ask for a joystick driver
          that works on fast machines.

******************************MISCELLANEOUS*******************************
33.  Q:   Do you have a software development toolkit for the PAS?
     A:   Please contact Media Vision Sales at 1-800-845-5870 to order the
          Pro AudioSpectrum Developer's Toolkit for $79.95.  This toolkit
          contains a 3 1/2" disk which contains drivers, utilities, source
          codes for both DOS and MWINDOWS and a manual which contains a
          software reference and a hardware reference.

34.  Q:   Are there additional documentation and software available for the
          MPC upgrade kit?
     A:   You can order the Pro AudioSpectrum User's Guide and Software Kit
          from Media Vision Sales for $15.00.  The software in this kit is
          only for DOS and contains the following:
               Installation Software and Diagnostic
               AudioMate & Utilities
               SP Spectrum MIDI Sequencer
          If you have is kit and have questions/problems, please refer to
          the Pro AudioSpectrum's Most Commonly-Asked Questions and
          Answers.

Before returning a defective product for repair, please call to request an
RMA number first.  Please contact Media Vision Technical Support at 1-800-
638-2807 if you have any questions or would like an update to this list. 
Media Vision Sales can be reached at 1-800-845-5870.

mpcq&a.doc
-- 
Ken Germann              ZZZZ EEEE  OO   SSS    ZEOS International, Ltd.  
support@zeos.com   INET     Z E    O  O S       Technical Support Dept.
uunet!zeos!support UUCP    Z  EE   O  O  SS     530 5th Ave N.W.
800-228-5390      VOICE   Z   E    O  O    S    St. Paul, MN 55112
612-633-7337             ZZZZ EEEE  OO  SSS     FAX         612-633-4607