|~~\\\\\\\\\\\\\\\\\\\\\\\\
                       |___|//////////////////////
                       |      __  __ ___ _       |        
                       |      |  /\ /\  / |      |        
                       |      |_/__v__\/__|      |        
                       |                         |        
                       | MCI MIXER DOCUMENTATION |        
                       |                         |        
                       |_________________________|        
                       |                         |        
                       |  (c) 1991 Media Vision  |        
                       |         v.001a          |        
                       |_________________________|        





INTRODUCTION

For some time we have been promising (threatening?) the development
of an mixer driver for MCI.  Accompanying this document is the
initial release of mcimixer.drv, the first MCI mixer driver for the
MPC level 1 platform.  

With this MCI driver, you can begin adding mixer control
functionality to your applications without having to writing C code
that calls our MMMIXER.DLL.  

If you are a presentation designer using a tool that allows you to
send MCI strings, you now have new volume control commands at your
disposal.

We encourage you to begin using this new capability right away.  If
you have any feature requests or questions on how to use
mcimixer.drv, don't hesitate to call Media Vision's Ken Nicholson at
(415) 770-8600.

----------------------------------------------------------------------

DISTRIBUTION

Media Vision is offering the virtual mixer interface to MPC
developers license free in the hopes of a standard mixer interface
being developed.  We encourage developers to ship the following files
with their products license free:

	MCIMIXER.DRV
	MMMIXER.DLL
	MVMIXER.DRV

If you are shipping these files, please let us know.  We may wish to
assist you in promoting your product!


----------------------------------------------------------------------



INSTALLATION

The mcimixer.drv file should be in your \windows\system directory.

The driver entry in your system.ini file should be:

	mixer=mvmixer.drv

----------------------------------------------------------------------


STATUS

All of the commands have been through initial testing and appear to
be robust.  However, some permutations of command options may not
work properly.  If you have any such difficulties, please contract
Ken Nicholson at the above number or our Technical Support number.

We will be adding commands to the MCI layer in the near future.



----------------------------------------------------------------------



reset      <device>        

set        <device> <linetype> <linespec> <control> [channel] [to] <value>

get        <device> <linetype> <linespec> <control> [channel]

adjust     <device> <linetype> <linespec> <control> [channel] [to] <value>

connect    <device> <linetype> <linespec> [to] <linetype> <linespec>

disconnect <device> <linetype> <linespec> [from] <linetype> <linespec>

fade       <device> < [state <filename>] |
                      [<linetype> <linespec> <control> [channel]
                      [to] <value>]
                    > [delay] [duration]


                KEYWORD DESCRIPTIONS:
                =====================

the <device>  parameter must be either a valid mci device name or a 
              valid alias

the <linetype> parameter must be one of the following key words:

        LINE_IN
        LINE_OUT
        DEVICE_IN
        DEVICE_OUT

the <linespec> parameter is dependent upon the <linetype parameter>. 
               For "line_in" and "line_out", <linespec> must be a number
               between 1 and the number of lines (input or ouput) supported
               by the mixer.        

               For "device_in" and "device_out", <linespec> must be a one
               of the standard 3-letter names for device types:

               name:        Description:
               --------------------------------------------------                
               N/C        No Connection
               AAT        Analog Audio Tape
               AMP        Amplifier
               AUX        Auxillary
               CDA        Compact Disk Player
               DAT        Digital Audio Tape
               EQU        Equalizer
               LPA        Phonograph
               MIC        Microphone
               MIX        Mixer
               MUS        Musical Instrument
               RAD        Radio
               SPK        PC speaker
               TEL        Telephone
               TVA        Television Audio
               VTR        Video Tape Recorder
               VDP        Video Disc Player
               WAV        Digital Waveform Player
               UNK        Unknown Device Type

the <control> parameter is an optional parameter with the default
              being volume.  If used, this parameter must be one of
              the following key words:

        VOLUME          volume control 
        ALC             auto level control 
        BASS            Bass 
        MIDRANGE        Midrange
        TREBLE          Treble
        CROSSOVER       Stereo to left, right or exchange channels
        LOUDNESS        Bass boost for low volumes
        MUTE            disables audio, maintains current volume
        REVERB          reverb control
        STEREOENHANCE   increase stereo separation
        CUSTOM1                
        CUSTOM2
        CUSTOM3                        


the <channel> parameter is an optional parameter with the default
              being "BOTH".  If used, this parameter must be one of the
              following key words:

        LEFT
        RIGHT
        BOTH


the <value> parameter must be an integer between 0 and 100
            (inclusive).  This value represents the percentage
            of the maximum allowable value.          


the <delay> parameter must be a legal integer.  It represents the
            number of tenths of seconds that are to elapse before
            the specified fade operation is to begin.        


the <duration> parameter must be a legal integer.  It represents the
            time, in tenths of seconds, for the specified fade operation
            to occur.

the <filename> parameter must be a fully qualified pathname to a
            mixer state file (.MIX extension).  Promix.exe is used to 
            create these files.

!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@!@


The following are some sample MCI commands that can be used to 
control the mixer hardware.  The program MCITEST.EXE, which is 
included as a sample application with the Microsoft Multimedia
Development Kit (MDK), provides an easy way to try out some of
these commands.

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

You should precede each of the commands by the following line:
open mixer alias mix

When you are finished sending commands, send  this line:
close mix

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To reset the mixer to the startup settings as specified in WIN.INI:

        reset mix

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly change the volume of a specific mixer input line to 75%:

        set mix line_in 3 control volume to 75

which is the same as:
        set mix line_in 3 control volume 75
        set mix line_in 3 to 75
        set mix line_in 3 75

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly change the volume of a CD-ROM device on an unknown mixer input
line to 75%:

        set mix device_in CDA control volume to 75

which is the same as:
        set mix device_in CDA control volume 75
        set mix device_in CDA to 75
        set mix device_in CDA 75

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -


To find out the current volume of a CD-ROM device on an unknown mixer input
line to 75%:

        get mix device_in CDA control volume

which is the same as:
        set mix device_in CDA 
        set mix device_in CDA 75

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
To find out the current bass EQ setting of the AMPLIFIER output line:

        get mix device_out AMP control bass

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly reduce the setting of the AUX input volume to 10% less
than the current setting:

        adjust mix device_in AUX control volume -10


- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly connect both the microphone and the CD audio inputs to
the output which goes to the record circuitry:

        connect mix device_in MIC to device_out WAV
        connect mix device_in CDA to device_out WAV

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly disconnect the microphone input from the record circuitry:

        disconnect mix device_in MIC from device_out WAV


- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

To instantly change the state of the mixer to a state that was
previously saved to disk:

        fade mix state c:\windows\saved.mix

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
To gradually fade out the volume of the Adlib-compatible FM
synthesizer input over 30 seconds:

        fade mix device_in MUS to 0 duration 300


- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
To wait 10 seconds then gradually fade the master volume to 50% over
the course of 5 seconds:

        fade mix device_out AMP to 50 delay 100 duration 50

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

Note: It is not necessary to fade a volume gradualy over .1 seconds
      to avoid noise.  All mixer volume changes are implemented by 
      changing the volumes a step at a time to reach the desired
      setting.