WHATSUP.DOC
                           -----------

If you want to stay current with what's happening in the world of
multimedia, windows, and the CDPC, subscribe to CompuServe.  Once online
type GO MEDIAVISION.  This will take you to the Media Vision section of the
Multimedia Vendor forum.  Each day, Monday thru Friday, a Media Vision
representative will stop by to answer your questions.  We also hope to
establish a presence on Internet, BIX, America Online and Prodigy.  Look
for our representatives on those services.

Here is a description of some of the files on this disk:

MIX.EXE         This program allows you to modify those mixing controls
		that you'll want to change most often.
		Its main difference from promix is that it doesn't
		cover nearly as much screen area.
		This program can be added to your \windows directory.

PROMIX.EXE      ProMix can be launced from the WIN.INI 'load' line. 
		If you have Windows 3.1, use the Program Manager's
		File/Preferences menu item to select the open
		minimized option.
		This program can be added to your \windows directory.

		Here's a nifty feature:  When running Windows, you can
		use the CTRL-ALT-U, CTRL-ALT-D, and CTRL-ALT-M sequences
		to adjust the master volume.

		The system menu contains a new feature: a pair of
		DB meters.  The DB meters are active only during record
		and playback of waveform data.


MMMIXER.DLL     This DLL must be in your \WINDOWS\SYSTEM directory.
		MMMIXER.DLL is like MMSYSTEM.DLL in a couple of ways.
		First, it provides a driver-independent layer for all
		mixer API's.  Second, it loads any mixer device drivers
		in the system.

		If you build an application that makes use of our
		mixer API's, this DLL handles the call.  If there are
		no mixer device drivers in the system, the mixer
		API's will simply return an error.


MVMIXER.DRV     This file belongs in your \WINDOWS\SYSTEM directory.  
		This is Media Vision's Mixer driver for the CDPC
		In the [drivers] section of your system.ini file, 
                you must have the line:
		                mixer=mvmixer.drv


MCIMIXER.DRV    Put this file in your \WINDOWS\SYSTEM directory.
		This driver provides a set of extended MCI commands
		for accessing mixer capabiities.  

		Under the [mci] section of your system.ini file, you
		must have the line:
		    mixer=mcimixer.drv

		Developers may ship this driver, license free, with
		their products.

		See the MIXSPEC directory for detailed information on the
		Multimedia Mixer MCI command set (MCIMIXER.DOC).


MVPROAUD.DRV    This file belongs in your \WINDOWS\SYSTEM directory.
		This driver supports WAVE (digital sound) audio, MIDI I/O
		and auxillary volume control.

		In the [drivers] section of your system.ini file, you
		should have the following three entries:
		     wave=mvproaud.drv
		     midi=mvproaud.drv
		     aux=mvproaud.drv
		
		This driver keeps configuration information in your
		system.ini file under the header [mvproaud.drv]


VPASD.386       This file belongs in your \WINDOWS\SYSTEM directory.
		It provides extra buffer space needed to handle 
		16-bit digital audio.

		You must have the following line in system.ini's
		[386Enh] section:
		device=vpasd.386

		Also you must add the following line to system.ini's
		[mvproaud.drv] section:
 
		buffer=32


MCIMIXER.DOC    These two files describe Media Vision's proposed
MIXAPI.DOC      standard for software controlled mixer devices.  


_____________________________________________________________________



		SAMPLE SYSTEM.INI FILE DRIVERS SECTION

[drivers]
timer=timer.drv
Wave=mvproaud.drv
Wave1=tbwave.drv
MIDI=mvproaud.drv
MIDI1=opl3.drv
mixer=mvmixer.drv
Aux=mvproaud.drv

[mci]
CDAudio=mcicda.drv  **
WaveAudio=mciwave.drv 4
Sequencer=mciseq.drv
mixer=mcimixer.drv



			  Installation Notes
			  ------------------

If you have technical questions or feature requests regarding this
software, please contact Media Vision Technical Support:

       Tech Support Voice: (800) 638-2807 or (510) 770-9905
       Tech support's FAX: (510) 770-9592.  

We have increased the number of Tech Support lines from 6 to 15.


       BBS: (510) 770-0968   2400b  8n1 
       BBS: (510) 770-1661   2400b  8n1 
       BBS: (510) 770-0527   9600b  8n1 

We now have a total of four BBS lines at 2400 baud and four additional
lines at 9600 baud.  If one of the above numbers is busy, your call
will be "rolled-over" to one of the new lines.