(Comp.sys.handhelds) 
Item: 1771 by jn190068 at longs.LANCE.ColoState.EDU 
Author: [Jay Nestle] 
  Subj: Std Air Tables 
  Date: Tue Jan 22 1991 15:11  
 
        Following is the documentation file for my program 
that calculated temp, pressure, and density of air at  
altitudes from 0m to 105,000m.  Following this is a post of 
the downloadable source for the hp48. 
 
This program by:  Jay Nestle, January 1991  Colorado State University 
 
        This program uses several algorithms to calculate the temperature, 
pressure, and density of air at a certain altitude.  The algorithm was adapted 
from Introduction to flight, third edition.  The standard atmosphere calculated 
is a common one used throughout the aerospace industry.  The original model 
was the 1959 ARDC (the U.S. Air Force's previous Air Research and Development 
Command).  The algorithms are outlined in the above mentioned text on pages 74 
through page 77. 
 
        This should be useful to anyone who constantly uses tables to look up 
temp, pressure, and density from altitudes from 0m to 105000m.  The program is 
not copyrighted and can be freely distributed.  I hope someone can make use of 
it. 
 
        The custom menu is only an example of what someone might wish to use. 
Please feel free to use or not use this CST menu.  Without the CST just press 
run and the program will start, likewise with the CST.  Without the CST the 
program is less than 2K. 
 
        Units used:  SI system 
        ----------   --------- 
        Temp            K 
        Pressure        Pa 
        Density         kg/m^3 
        Height          m 
 
        Further modifications could be made to give English units fairly 
easy.  The program simply checks for what altitude is desired and then uses 
the correct algorithm for that altitude region, modifying the lapse rate, A 
and the various other starting point constants.