(Comp.sys.handhelds) 
Item: 904 by ard at siva.bristol.ac.uk 
Author: [Tony Duell] 
  Subj: HP48 digital logic simulator 
  Date: Mon Oct 15 1990 08:05  
 
Here's a digital circuit simulator for the HP48SX. It has 8 internal 
primatives: AND, OR, XOR, NOT, BUF (buffer), HI (node tied to logic 1), 
LO (node tied to logic 0) and CLK (clock generator of definable high and 
low times). It also supports nested macros defined from these elements. 
 
A circuit is entered as a list of lists. Each sublist defines one gate (or 
macro-circuit) in the design. The format of the sublist is as follows :  
{"NAME" I1 I2 I3..} 
Where NAME is either one of the primatives above or the variable name where the 
macro is stored entered as a string. I1 I2 etc are the names of the nodes in 
your circuit, and must be valid HP48 name objects (or in the case of "CLK", the 
first 2 arguments are integers). For example: 
{"AND" A1 A2 Both}  is the representation of the circuit : 
 
  A1----------!\ 
              ! )--------- Both 
  A2----------!/ 
 
  In the primatives, the inputs are always given first, and I suggest you do 
the same in macros (see below).  
 
2 - input gates 
--------------- 
There are 3 types of 2-input gate defined, AND, OR and XOR. The formats are 
 
 list format          equivalent expression (which you don't enter) 
{"AND" A1 A2 Q}       Q= A1 AND A2 
{"OR" A1 A2 Q}        Q= A1 OR A2 
{"XOR" A1 A2 Q}       Q= A1 XOR A2 
 
1 - input gates 
--------------- 
 
There are 2 types of 1-input gate, NOT and Buffer: 
 
 list format        equivalent expression 
{"NOT" A B}         B=NOT A 
{"BUF" A B}         B=A 
 
Tied nodes 
---------- 
A node can also be defined as permanently high or low :  
 
 list format    equivalent expression 
{"HI" A}        A=1 
{"LO" A}        A=0 
 
Clock Generators. 
The high and low times of the clock generator are defined in terms of 
time-steps which are defined as 1 horizontal pixel on the final timing diagram. 
Note that all gates have a propagation delay of one time-step. The format for 
defining a clock generator is : 
{"CLK" hi_time lo_time Output} 
Where hi_time and lo_time are real numbers giving the number of time-steps that 
the output will be high or low respectively and Output is the node name for the 
output. 
e.g. : 
{"CLK" 4 4 A} defines that node A will be low for 4 time-steps, high for 4 
time-steps, low for 4 time-steps etc. 
 
A circuit is defined by creating a list of these sub-lists e.g.: 
{{"CLK" 2 2 A} {"CLK" 4 4 B} {"AND" A B C}} 
 
The only commands you need to know to run the simulator are as follows: 
 
COMPILE 
------- 
Takes the variable name where a circuit is stored in top of stack, and sets up 
the internal variables to represent that circuit. Use this before attempting to 
simulate 
 
NODES 
----- 
Takes a list of nodes which are to appear in the final timing diagram in top of 
stack, and stores it in the internal variable OUT.L 
 
ALL 
--- 
sets up OUT.L to contain _ALL_ nodes in the circuit (including the internal 
ones in macros). Only useful for simple circuits. 
 
SIM 
--- 
Takes a length of simualtion in top of stack (a real number, max 100) and plots 
the timing diagram (in PICT) for the given circuit. After it has finished, 
press any key (except ATTN) to exit and restore the stack display  
 
Example :  
Given the circuit defined above in top of stack, store it in 'CSH' 
then execute the following 
'CSH' COMPILE            set up this circuit 
ALL                      we'll show all nodes 
100 SIM                  draw a timing diagram. 
 
 
MACROS 
------ 
A macro-circuit is a bit like a subroutine - it's a part of a circuit (e.g. a 
half-adder or a flip-flop) which is used several times. For an example, see the 
variable HADD in the directory which contains the macro that defines a half 
adder. 
Each macro definition has the form 
{{External list} {{GATE1}{GATE2}...}} 
where {{GATE1}{GATE2}...} is the circuit description of the macro as defined 
above, and {External list} is the list of external connections. 
e.g. the 2-input multiplexor (variable MUX) in the directory 
 
Circuit  
           !\ 
SEL --+----! >o------------!\ 
      !    !/              ! )--! 
      !             A------!/   ------\----\ 
      !                                )    )-------- Y 
      !             B------!\   ------/----/ 
      !                    ! )--! 
      !--------------------!/ 
 
 
Now, the external connections are SEL, A, B and Y 
 
           !\     NS 
SEL --+----! >o------------!\ 
      !    !/              ! )--! YA 
      !             A------!/   ------\----\ 
      !                                )    )-------- Y 
      !             B------!\   ------/----/ 
      !                    ! )--! YB 
      !--------------------!/ 
 
 
I've now labeled the internal nodes (NS, YA, YB) 
 
Thus, we get the definition: 
{{SEL A B Y}{{"NOT" SEL NS} {"AND" A NS YA} {"AND" B SEL YB} {"OR" YA YB Y}}} 
 
If this is stored in the variable MUX , the element 
{"MUX" X Y Z GO} will be valid, with the correspondence: 
X -> SEL 
Y -> A 
Z -> B 
GO -> Y 
 
circuits (and other macros) can be defined in terms of MUX. 
 
 
Example : the full adder 
------------------------ 
I have included a simple example to demonstrate the features of this logic 
simulator : the single-bit full adder. 
In the variable HADD is the macro for a half - adder, whereas in FADD, I have 
given the macro for a full-adder, defined in terms of FADD 
In the variable DEMO, I have defined a simple circuit with one full-adder, with 
its 3 input driven from clock-generators in the ratio 1:2:4. Here's how to run 
the demonstration: 
'DEMO' COMPILE      define the circuit 
{M N P S C} NODES   only display the inputs and outputs 
100 SIM             display the timing diagram (after it's finished, press any 
                    key to exit) 
 
 
I am quite willing to answer questions about how this program works, but as 
it's likely to be quite long, I'll only post it to the net if there is 
sufficient interest..... 
 
-Tony Duell 
ARD @ UK.AC.BRIS.PVA  (JANET) 
ARD @ SIVA.BRIS.AC.UK (BITNET) 
 
(This program and its documentation are public domain. They may be freely 
copied, used and published in user-group newsletters provided that my name 
remains attached to them. They may not be sold for profit)