This is the demo version of XCOGO. The only limitations of this 
	version is that point storage is restricted to points 1 thru 10. 
	 
	For a full working copy on an MS DOS 5 1\4" disk send $30.00 to: 
 
		Tom Falconer 
		4650 Blank Rd. 
		Sebastopol Ca. 95472  
 
                              	XCOGO 
 
	A coordinate geometry and surveying utility program for the HP 48SX. 
 
 
 
				by 
 
			Tom Falconer 
			4650 Blank Road 
			Sebastopol CA. 95472 
 
 
 
	(C) Copyright 1990,1991  Tom Falconer  All rights reserved 
 
 
 
 
	The author does not guarantee the program to be free from 
	defects	and may not be held responsible for loss caused by such. 
	Your use of this program constitutes your acceptance of these 
	terms. 
 
			CONVENTIONS USED IN THIS MANUAL 
	 
	Keys to be pressed are shown in square brackets. 
	The left shift key is shown as [<-]. 
	The right shift key is shown as [->]. 
	Menu keys are shown as |item|. 
 
			LOADING THE PROGRAM 
 
	1. Load the file "DEMOCOG1" into the home directory of the 48. 
	2. Press [VAR] to display the variable menu. 
	3. Select |DEMO| to switch to that subdirectory. 
	   The variable menu will now be displayed. 
	4. Select |GO| from the displayed menu. The 48 will shut its 
	   self off. 
	5. Turn the 48 on and press [VAR]. 
	6. Select |DEMO| from the menu. 
	7. Select |INIT| from the menu. The program will then initilize 
	   the variables and install the user key definitions. 
 
	The program is now ready to run. The main menu will be 
	displayed as follows: 
 
	|'FILE| |'PNTS| |'RSO | |'TRAV| | 'TO | | 'CO |  [NXT] 
	|'UTIL| |'TROT| |'GRDZ| | 'VC | | 'SS | |'CURV|  [NXT] 
	|'AREA| 
 
	Pressing [CST] from any point in the program will always bring 
	you back to the main menu. 
 
	(Note: You have to create a file before using any of the file 
	related functions.) 
 
			CONVENTIONS USED IN THIS PROGRAM 
 
	You will notice that certain menu items are preceded by a tick 
	(') mark. This indicates that another menu will be brought up 
	and no input is required. Menu items with no tick mark require a 
	value on the stack prior to selection. 
  
				POINT PROTECTION 
 
	If you try to create a new point with an existing point number 
	the 48 will beep and display this screen: 
 
		_________________________ 
		|Pt n used		| 
		|			| 
		|(Enter start number	| 
		|for unused search.)	| 
		|			| 
		|			| 
		_________________________ 
		|OK|NEW|NEXU|QUIT|	| 
 
	| OK |	Select this to hold the point number and overwrite 
		the old point. 
 
	|NEW |	Enter a new number. 
 
	|NEXU|	Enter number to start search from. The next unused 
	point will be displayed. Press | OK | to accept this number. 
 
	|QUIT|	Select this to abort the program. 
 
	 
				FILE UTILITIES 
	 
	The size and number of files are limited only by available memory. 
	File names MUST start with an alpha character. 
	Files contain point number, northing, easting, elevation, and 
	description. 
	When a file is created it will contain one point, point number 
	one with a northing and easting of 5000, an elevation of 100 
	and no description. The file will grow as points are added and 
	shrink if points are deleted. 
	The file format is comma delimited ASCII. PC files in this 
	format may be uploaded to the 48 and used directly. Conversely 
	48 files may be downloaded and used by a PC program that 
	accepts this format. 
	 
	From the main menu select |'FILE|. The current 
	file and the file utility menu will be displayed. 
 
		|'PICK|	This is used to select your working file. 
			The files will be listed as menu items. 
			Select a file and press [ENTER]. 
 
		|'DEL|	This is used to delete files. The files will 
			be listed as menu items. Select a file and press 
			[ENTER]. 
 
		|'NEW|	This is used to create new files. 				POINT UTILITIES 
	 
	There are no restrictions to the numbering of points. 
	In fact points may be given names. There is no limit to the 
	length of a point description. 
	 
	Select |'PNTS| from the main menu. The points menu 
	will be displayed. 
	 
	|'ENTE|	This is used to view, edit and enter point data. 
	 
	Enter menu: 
 
		| PT |	Enter a point number and press | PT |. If the 
			point exists its data will be displayed, if not 
			zeros will be displayed. 
 
		|NORT|	Enter northing with this key. 
 
		|EAST|	Enter easting with this key. 
 
		|ELEV|	Enter elevation with this key. 
 
		|DESC|	Enter point description with this key. 
			Descriptions should be enclosed in double quotes. 
 
		|'STOR| Use this key to store new or updated point 
			data. The next consecutive point will now be 
			displayed. 
			Enter new data or press [CST] to return to  
			the main menu. 
 
	| DEL |	Enter a point number to be deleted and press | DEL|. 
 
	|UNUS|	To find the next unused point number, enter a number 
		to start the search from and press |UNUS|. This can 
		be a slow process in a large file so try to pick a 
		close starting number. 
 				RADIAL STAKEOUT 
	 
	From the main menu press |'RSO|. This will bring up the setup 
	menu. The occupied point number, backsight point number, backsight  
	bearing, distance to backsight, elevation of occupied point, 
	plus to instrument, and instrument elevation will be displayed. 
	 
	Setup menu: 
 
		|'OK|	Select this when the setup data is correct. 
 
		|OC BS| Enter occupied point [SPC] backsight point. 
 
		|PLUS|	Enter plus to instrument. (Note: The HI is 
			stored in the variable 'HI' if you need to use it.) 
 
	Stakeout display: At the top of the display will be directions 
		for your rodman to the next point. That is, a bearing and 
		distance from the last point you set to the current 
		point. Also displayed are the point number, angle right  
		from the backsight and stakeout distance. 
	 
	Stakeout menu: 
 
		| PT |	Enter the point to be staked. 
 
		|DIST|	Enter the distance measured to a trial point. 
			The distance in (towards the instrument) 
			or out (away from the instrument) will be displayed. 
 
		|D ZA|	Enter distance [SPACE] zenith angle. The level 
			distance will be returned to the stack and the 
			vertical difference will be stored for use in the 
			|CUT| program. 
 
		|'CUT|	After setting the point press |'CUT| to bring 
			up the CUT/FILL menu. 
	 
		|'TO|	This will take you to the directly to the 
			TANGENT OFFSET program bypassing the setup menu. 
			This is useful if you are calculating or changing 
			the offset points as you are staking them. 
 
		|'CO|	Same as above for CURVE OFFSET program. 
 
	CUT/FILL menu. 
	 
		|'STOR|	This option will store the point elevation and the 
			cut or fill information. Note that this overwrites 
			the existing elevation and point description. You 
			are then returned to the staking menu. 
	 
		|VD|	Enter the vertical difference. 
 
		|ROD|	Enter the rod. 
 
		|GRAD|	The grade displayed will be the stored elevation of 
			the point you are staking. Change if needed. 
 
		|EXIT|	This option will return you to the staking menu 
			without saving the elevation and cut. 				TRAVERSE 
	 
	From the main menu press |'TRAV|. This brings up the traverse 
	setup screen. This displays the occupied point, the backsight 
	point, the next traverse point number, the backsight bearing, 
	distance to the backsight, occupied point elevation, plus to 
	the instrument and instrument elevation. 
		 
	Setup menu: 
		 
		|OK|	When the displayed information is correct press this 
			key to proceed to the next menu. 
		 
		|OC BS| Enter occupied point [SPC] backsight point. 
 
		|NX P|	Enter point to traverse to. 
 
		|PLUS|	Enter plus to instrument. If you are not carrying 
			elevations PLUS should be 0.00. The HI is stored 
			in the variable 'HI' if you need to access it. 
 
	Traverse menu: 
			 
		|'SIDE| Press this key to make a sideshot. 
 
		|'TRAV|	Press this key to traverse. 
 
	Distance Menu: 
			 
		|OK|	With distance to be traversed on the stack 
			press this key. The angle menu will then be 
			displayed. 
 
		|LAST|	Pressing this key will return the last 
			distance traversed to the stack. 
 
		|PINV|	This option will return the distance between 
			two points. Enter point [SPACE] point and 
			press |PINV|. 
 
		|'B-D|	Select this option to preform a bearing 
			distance intersection. Follow the prompts. 
				 
	(Note: All intersection problems assume the occupied and backsight 
	points form the base of the triangle to be solved.) 
 
		|'B-B|	Select this option to preform a bearing 
			bearing intersection. Follow the prompts. 
 
		|D ZA|	Enter distance [SPACE] zenith angle and press 
			|D ZA|.	The level distance will be returned to 
			the stack and the vertical difference will be 
			stored for use if you are carrying elevations. 
 
	[NXT]	|QUIT|	Use this key to abort the traverse. 
 	Rod VD menu:	(This only comes up if you entered a PLUS.) The last 
			used vertical difference and rod will be displayed 
			as default values. If you used |D-ZA| in the 
			distance menu the resultant vertical difference 
			will be displayed. 
 
		| OK |	Select this to accept the displayed values. 
 
		| VD |	Enter vertical difference. 
 
		|ROD |	Enter a new rod. 
 
		|QUIT|	Select this key to abort. 
 
	Angle menu: 
 
		| NE |	Enter northeast bearing or azimuth. 
 
		| SE |	Enter southeast bearing. 
 
		| SW |	Enter southwest bearing. 
 
		| NW |	Enter northwest bearing. 
 
		| RT |	Enter angle right or negative angle for angle left. 
 
		|DEFL|	Enter deflection right or negative angle for 
			deflection left. 
 
	[NXT]	| OK |	Use decimal azimuth value on stack. 
 
		|PINV|	Enter two point numbers and press this key to 
			return the azimuth between them. Press | OK |. 
 
		|LAST|	Press this key to return the last azimuth 
			traversed. Press | OK |. 
 
		|D-D |	To do a distance distance intersection enter 
			the second distance and press this key. You will 
			then be asked if the point is left or right of 
			the backsight as you look at it from the occupied 
			point. 
 
		|QUIT|	Press this key to abort. 
 
	Description menu: 
 
		| OK |	Enter a description in double quotes and press 
			this key. 
 
		|LAST|	Select this to use the last description. 
 
		|NONE|	Select this for no description. 
 
		|QUIT|	Select this to abort. 
  
				TANGENT OFFSET 
 
	This program will create points along a center line by station 
	and offset. 
	Start the program by pressing |'TO| from the main menu. 
 
	Setup menu: 
 
		| OK |	Select this when all the displayed data is correct. 
 
		|CL UP|	Enter a centerline point and a centerline point 
			upstation of the first point. The bearing and 
			distance between these points is displayed. 
 
		|CLSTA|	Enter the station of the first centerline point. 
 
		|SLOPE|	The program will calculate the slope between the two 
			given centerline points using their stored elevations. 
			You may override this by entering a new slope. 
 
		|+\-TC|	Enter the difference between centerline and top of 
			curb grade. The program will apply this factor to 
			the grade it calculates for the offset points 
			generated. 
 
	Generate points menu: 
 
		|STA |	Enter a station. 
 
		| OS |	Enter an offset distance.(Negative if left.) 
 
		|GRD |	The program calculates and displays a grade for the 
			given station. You may override this by entering a  
			new grade. 
 
		| PT |	Enter a point number. 
 
		|DESC|	Enter a point description. 
 
		|STOR|	Select this when the displayed data is correct to  
			generate and store the point. 
 
	[NXT]	|P->SO|	Entering a point number will return the station 
			and offset of that point. 
 
		|ANG |	Suppose your line staking a property line, from 
			a traverse point. Your at point 3, backsighting 
			point 4 and have defined this setup in the radial 
			stakeout program. The property line is from 1 to 
			2 and you have defined this setup in the tangent 
			offset program. Turn an angle that intersects the 
			property line where you want to set a line point 
			and enter the angle. The program will return the 
			station intersected at that angle. You may then 
			store the point and go to the radial program. 
 
		|RSO |	This will take you to the radial stakeout program 
			without going through the setup routine. Useful 
			in the last example or if your calculating offsets 
			as you stake them. 
 				CURVE OFFSET 
 
	This is the same as the tangent offset program except 
	that you enter a point an the centerline, the radius point 
	and if the curve is left or right. 
	Start the program by pressing |'CO| from the main menu. 
 
				UTILITIES 
 
	This menu has a few basic functions that are not readily available 
	on the 48. From the main menu press [NXT] |'UTIL|. 
 
		|->DEG|	Converts degrees, minutes and seconds to decimal. 
 
		|->DMS|	Displays decimal angles in degrees, minutes and 
			seconds. The decimal angle on the stack is not 
			changed. 
 
		|R->P|	Converts northing value in level 2 and easting 
			value in level 1 to polar value with the distance 
			in level 2 and decimal angle in level 1. 
 
		|P->R|	Converts distance in level 2 and decimal angle 
			in level 1 to northing in level 2 and easting 
			in level 1. 
 
		|D->R|	Converts degrees to radians. 
 
		|R->D|	Converts radians to degrees. 
 
	[NXT]	|SAS|	Solves side angle side triangle. Distance 1 in 
			level 3, DMS angle in level 2 and distance 2 in 
			level 1 returns distance 3 to level 1. 
 
		|PINV|	Inverses from point in level 2 to point in level 
			1. The bearing and distance will be displayed. 
			The azimuth will be in level 1 and the distance 
			in level 2. 
 				TRANSLATE AND ROTATE 
 
	Translates, rotates and scales blocks of points. From the main 
	menu press [NXT] |'TROT|. 
 
	Set up menu: 
 
		| OK |	Press this when all the information is entered 
			correctly. 
 
		|ANG|	Enter angle of rotation from old coordinate 
			system to new system. Enter in DMS. Negative for  
			angle left. 
 
		|OLD|	Enter old pivot point. 
 
		|NEW|	Enter new pivot point. 
 
		|SCALE|	Enter scale factor. 
 
	Results menu: 
 
		| OK |	Press this to start program when data is 
			entered	correctly. 
 
		|FROM|	Enter first point of block to move. 
 
		| TO |	Enter last point of block to move. 
 
		|START|	Enter starting point number for moved block of 
			points. You can enter the "FROM" point number 
			if you want to hold the point numbers. 
 
 
				GRADES 
 
	Calculates the elevation of a given station or the station for 
	a given elevation along a straight grade line. In the setup 
	screen you may either enter two stations and their elevations, 
	in which case the resultant slope is calculated and displayed, 
	or you may enter the first station and elevation and the slope. 
	Run the program from the main menu by pressing [NXT] |'GRDZ|. 
 
	Setup menu: 
 
		| OK |	Select this when the data is entered correctly. 
 
		|STA1|	Enter first station. 
 
		|ELEV|	Enter elevation of first station. 
 
		|STA2|	Enter a station that is upstation of the first 
			station. 
 
		|ELEV|	Enter elevation of the second station. 
 
		|SLOPE|	Enter the grade rate. (i.e. A 5% grade should be 
			entered as .05.) 
 
	Results menu: 
 
		|ST->E|	Calculates the elevation for a given station. 
 
		|EL->S|	Calculates the station for a given elevation. 
 				VERTICAL CURVE 
 
	Start program from the main menu by pressing [NXT] |'VC|. 
 
 
	Setup menu: 
 
		| OK |	Select this when the data is entered correctly. 
 
		|BVC|	Enter beginning station of vertical curve. 
 
		|ELEV|	Enter elevation of beginning station. 
 
		|LENG|	Enter length of vertical curve. 
 
		| G1 |	Enter incoming grade rate. 
 
		| G2 |	Enter outgoing grade rate. 
 
	Results menu: 
 
		|STA?|	Calculates the elevation of a given station. 
 				SLOPE STAKING 
	Definitions: 
 
		Hinge Point: The top of fill or the toe of cut of the 
		slope being caught. 
 
		Work Point: A point on the station being staked that is a 
		known distance from centerline. This is generally the scaled 
		catch point. 
 
	Field procedure: 
 
		1. Set the work point. 
		2. Start SS program and enter setup data. 
		3. Shoot the work point and enter VD and ROD in staking menu. 
		4. The program will display the distance, in or out from the 
		   work point that the slope would catch at that elevation. 
		   Tell the rodman the appropriate distance to move and take 
		   another shot. Repeat this until the displayed distance 
		   is the same as the distance on the ground. Press OK. 
		5. Set and shoot the RP point. 
		6. Enter VD and ROD in the RP menu. 
 
	Setup menu: 
 
		| OK |	Select this when all the data is entered correctly. 
 
		| HI |	Enter the instrument elevation. (The radial stakeout 
			HI is given as the default value.) 
 
		| H2W|	Enter the distance from the hinge point to the  
			work point. 
 
		|SLOPE|	Enter the slope. (i.e. For a 3:1 slope enter 3, 
			for a 1 1/2:1 slope enter 1.5, etc.) 
 
		|GRD|	Enter the grade of the hinge point. 
 
	Staking menu: 
 
		| OK |	Select this when the slope is caught to bring up 
			the RP menu. 
 
		| VD |	EDM: Shoot the trial point and enter the vertical 
			difference. 
			LEVEL: Enter 0. 
 
		|ROD|	EDM: Enter the rod. 
			LEVEL: Enter the rod reading on the trial point. 
 
		|SETUP|	Selecting this returns you to the setup menu. 
 
	Staking screen: The VD, ROD and resultant elevation are displayed. 
			Next the slope stake data, generated for that 
			elevation, is displayed. Next a distance "IN" 
			(towards centerline), or "OUT" (away from centerline) 
			is displayed. 
			 
	RP menu: 
 
		| OK |	Returns you to the staking menu. 
 
		| VD |	EDM: Shoot the RP and enter the vertical 
			difference. 
			LEVEL: Enter 0. 
 
		|ROD|	EDM: Enter the rod. 
			LEVEL: Enter the rod reading on the trial point. 
 
		|SETUP|	Selecting this returns you to the setup menu. 
 				CURVE SOLUTIONS 
 
	Given the radius or delta and one other element, solves for the 
	unknown curve elements. 
	From the main menu press [NXT] |'CURV|. 
 
	First menu:	Enter either radius and or delta. Entering both 
			automatically solves. 
 
		| OK |	Select this when the data is entered correctly. 
 
		| R |	Enter radius. 
 
		| D |	Enter delta. 
 
	Second menu:	Entering any one element solves for the rest. 
 
		| T |	Enter tangent length. 
 
		| L |	Enter length of curve. 
 
		| C |	Enter chord. 
 
		| E |	Enter external distance. 
 
		| M |	Enter middle ordinate. 
 
 
				AREA 
 
	Calculates area from stored points. From the main menu press 
	[NXT] [NXT] |'AREA|. 
 
		|FROM|	Enter starting point. 
 
		| TO |	Enter next point. 
 
		|RADPT|	Enter radius point. 
 
		| EC |	Enter EC point (negative if curve is to the left). 
			If the radii are not equal within a tolerance 
			of .01' an error will occur and the program will 
			halt. 
 
	When the starting point is returned to, either as a "TO" point 
	or as an "EC" point, The area and perimeter will be displayed. 				USER KEY ASSIGNMENTS 
 
	These user keys allow you to start programs directly without 
	going through the menus. 
 
	[->] [R]	Starts the radial stakeout program. 
 
	[->] [T]	Starts the traverse program. 
 
	[<-] [O]	Starts the tangent offset program. 
 
	[->] [O]	Starts the curve offset program. 
 
	[->] [G]	Starts the grades program. 
 
	[->] [V]	Starts the vertical curve program. 
 
	[->] [S]	Starts the slope stake program. 
 
	These user keys give you access to the functions in the utility 
	menu. 
 
	[<-] [H]	Converts DMS to DEG. 
 
	[->] [H]	Displays DEG as DMS. 
 
	[->] [P]	Rectangular to polar. 
 
	[<-] [P]	Polar to rectangular. 
 
	[->] [Z]	Side, angle, side solution. 
 
	[->] [I]	Point inverse. 
 
	These key assignments allow you to store and recall data in 
	registers 1 through 9. 
 
	[STO]		Stores value in level two, into register number 
			(1-9) in level one. 
 
	[->] [RCL]	Recalls value of register number in level one. 
 
	(Tecnical note: The data is stored in a list named 'STOPAR'. 
	You may increase the number of storage registers by increasing 
	the size of the list.)