(Comp.sys.handhelds) 
Item: 3834 by catto at author.ecn.purdue.edu 
Author: [Erin S Catto] 
  Subj: Fuzz & ML Blurbs 
  Date: Tue Aug 13 1991 
 
Well I promised myself that I would pass on what I've learned once I figured 
out what's going on with this machine language business.  Sorry, it's not a 
game.  Anyway, here's a small program which simply draws random dots on the 
stack display and exits when you press the drop key. 
 
I thank Jan Brittenson for the STAR assembler (excellent) and the MLDL (way 
excellent). 
 
This program covers most of the key hardware questions a freshie might have. 
 
+  Drawing on the stack display at a coordinate (0-127,0-63) 
+  Data storage acquisition so that data tables are temporary 
+  Turning off keyboard interupts (go ahead, press ON-A-F, nothing happens) 
+  Machine code keyboard scanning 
+  How to get random numbers you can't depend on 
 
 
I'll briefly cover a few topics: 
 
 
Preserving the RPL Operating System 
=================================== 
 
The HP48 has an operating system just like any other computer.  It was written 
in System RPL and machine code.  The HP48 OS uses the registers d0, d1, b, and 
d to take care of business, such as memory management and RPL command pointing. 
Thus you must save these important register and restore them at the termination 
of your machine code program.  You must also set the OS back on track.  Here's 
how it's done: 
 
save_regs = #0679B      ;ml routines to handle these tasks 
rest_regs = #067D2 
 
begin 
                  call.a     save_regs      ;save registers 
                           . 
                           . 
                           . 
                  call.a     rest_regs      ;restore registers 
                  move.a     @d0, a         ;a = next RPL instruction 
                  add.a      5, d0          ;point d0 to following instruction 
                  jump       @a             ;jump to instruction in a 
                                            ;address of object prolog? 
end 
 
Here's how I believe the last three instructions work: 
 
                                  d0 
                                   | 
                                   v 
RPL instruction stream:  ... 11EC7|65547|EF9D7|83188|... 
 
      move.a    @d0, a       ;a gets 74556 
      add.a     5, d0        ;does the following 
 
                                        d0 
                                         | 
                                         v 
RPL instruction stream:  ... 11EC7|65547|EF9D7|83188|... 
 
Lets say at the address 74556 there is the RPL program prolog 02D9D then 
 
       jump     @a 
 
will jump to the address 02D9D, a chain of pointers. 
 
Now the operating system is back on track, refreshing the screen, handling the 
keyboard, etc.  Evidence of this is seen when you exit the attached program, 
the RPL OS automatically returns the screen to its normal state. 
 
 
Drawing on the Stack Display 
============================ 
The stack display contains two grobs: the stack-message grob and the menu grob. 
 
Statistics: 
 
+ Screen Grob:   location of grob contained at #7055B 
                 size = 56 rows high by 136 bits wide (34 nibbles) 
 
+ Menu Grob:     location of grob contained at #70551 
                 size = 8 rows high by 136 bits wide 
 
Once you get to the grob in memory you must skip the 20 nibble prolog to get to 
the pixel data.  The pixel data begins at the upper left corner of the display 
and goes left to right, wrapping to the next row after 34 nibbles.  While the 
nibbles go left to right as the address increases the bits in each nibble are 
in right to left order. 
 
Example:         On Screen:          0101 
                 In memory:          1010 = #A 
 
It is useful to have a data table which contains the address of the start of 
each row of pixels.  This way you can take an arbitrary y coordinate and 
transform it into an index to the data simply by multiplying y by 5.  Lets 
look at this: 
 
Say y = 4, then  5 * y = 20, now the data table looks like this: 
 
start y=0   y=1   y=2   y=3   y=4 
       |     |     |     |     | 
       v     v     v     v     v 
       04347|26347|48347|6A347|8C347.....  (stream of row addresses) 
 
So you use start+20 to get the row address.  Below I talk about building a 
data 
string. 
 
Here's my plug for using the stack display instead of PICT. 
 
1)  Let PICT be the user's territory. 
2)  PICT sits and takes up 1098 bytes, unless you PURGE it. 
3)  The stack display is always the same size (131x64) 
 
 
Making Data Space 
================= 
 
Quite often data tables are used in mcode programs.  If the data is going to be 
generated by the program then it becomes a waste of space to attach non- 
executing data to your program.  A routine at #05B7D will make a string object 
whose data length (not including the header) is specified by the contents of 
the c reqister.  The address is returned in the address register d0. 
 
              d0 
               v 
   C2A20|04000|123DF8734872394729834...   ...2312| 
   <- header->|<--- length = c -----...   ...--->| 
 
All you need to do is: 
 
         move.p5  c, length      ;you specify length 
         call     make_str       ;make_str = #05B7D 
         swap.a   a, d0          ;d0 = string data area address 
         move.w   a, r0          ;store the address somewhere for reference 
 
 
Turning Off Interupts 
===================== 
 
Turning off interupts means turning off the keyboard, in a manner of speaking. 
It means your program will only be interupted when you want input.  It is  
simple to turn the interupts off, but you must be sure to turn them back on. 
 
Interupts Off:          clrb      15, st       ;clear bit 15 of status 
register 
                        intoff 
 
Interupts On:           inton 
                        setb      15, st       ;set bit 15 of status register 
 
It would be nice if someone in-the-know would explain the flags the ST register 
contains. 
 
 
Keyboard input, the ML way 
=========================== 
 
The instructions which must be used to grab key presses are OUT and IN. 
Sounds simple enough, sure if you know how to do it.  Here's how it's done 
 
1)  load register c with the row of keys you want to check (see table below) 
2)  perform  OUT.X  C to tell your HP to check that row 
3)  call IN_C = #01160, this address only contains:    IN.4   C  
                                                       RET 
    It seems that IN.4   C must be called, I think it messes with the  
    return stack. 
4)  move the adress field of register c somewhere safe, say register a 
5)  clear register c 
6)  perform OUT.X  C to tell your HP to stop checking 
7)  now if you stored register c in register a in step (4) then the low 
    nibbles of reg. a will contain bits set corresponding to the keys pressed 
    in the row of interest. 
 
The Keyboard Map:  (from an article by Jan Brittenson) 
 
 
             (IN) #20 #10 #08 #04 #02 #01 
              --------------------------- 
 
        (OUT) |    6   5   4   3   2   1 
 
        #100  |        B   C   D   E   F 
 
        #080  |       PRG CST VAR  ^  NXT 
 
        #040  |       STO EVL  <   v   > 
 
        #020  |       COS TAN sqt pwr inv 
 
        #010  |   ON* ENT +/- EEX DEL <== 
 
        #008  |   alp SIN  7   8   9   / 
 
        #004  |   yel MTH  4   5   6   x 
 
        #002  |   blu  A   1   2   3   - 
 
        #001  |        '   0   .  SPC  + 
 
 
   (*) The ON key is actually in a column of its own. 
   #xxx refers to the keyboard scan bits. The column 
   scan bit for the ON key is #8000. 
 
The numbers in the leftmost column are use to specify the row in the OUT  
command and the numbers in the topmost row correspond to a positive result 
from the IN command.  Note that these numbers have a binary representation  
which has only one bit set.  So multiple bits set by the IN command mean  
multiple key presses. 
 
 
The Random Thing 
================ 
 
Your HP48sx maintains a hardware checksum at #00104 which is constantly 
changing in a seemingly unpredictable manner.  You can get four random 
nibbles at a time from the above address which may be masked down to the 
range of numbers you are interested in. 
 
The program below takes two random numbers from the hardware crc, one 
for the x coordinate and one for the y coordinate.  Two dummy instructions 
were planted inbetween the two readings.  It turns out that without these 
two dummy instructions, the static on the screen reduces to two predictable 
lines. 
 
 
Notice 
====== 
 
I claim no proficiency at ML programming, but maybe this info will help others 
get started.  I did not hack out much of this.  Most of it came from studying 
the source code for SCHIP v1.0 by Erik Bryntse.  For those not familiar with 
this type of programming I suggest you actually run the program below and 
recognize that only one pixel is being draw at a time...it's FAST!!!  By the 
way, press the drop key to EXIT. 
 
 
                                  The ML Freshie, 
 
                                  Zoom 
                                  catto@ecn.purdue.edu 
 
 
P.S.  Has anyone finished Ant?  You must see the final round, it's a hoot. 
      The rolling (:() is actually quite easy, once you know how to get 
      by it.  There's a lot more game after that. 
 
--------------------------begin STAR source------------------------------------ 
;FUZZ: makes random static on screen, drop key exits 
 
;r0 = data string pointer 
;r1 = x coordinate in pixels 
;r2 = key data storage 
 
make_str        =       #05B7D 
save_regs       =       #0679B 
rest_regs       =       #067D2 
crc_val         =       #00104 
screen_ptr      =       #7055B 
menu_ptr        =       #70551 
in_c            =       #01160 
 
header 
code 
                call            save_regs       ;save d0, d1, b, d 
                clr.w           c               ;c = 0 
                move.w          c, r2           ;initialize key storage 
                clr.w           a               ;a = 0 
                move.p3         #140, c         ;c = data string size (64*5+4) 
                call            make_str        ;make a data string 
                swap.a          a, d0           ;a = string address 
                move.w          a, r0           ;save string address in r0 
                move.a          a, d0           ;point to string 
                move.5          screen_ptr, d1  ;d1 = address of screen grob 
                move.p2         56, a           ;a = # rows in screen grob 
                call            fill_table      ;make data table 
                move.5          menu_ptr, d1    ;d1 = address of menu grob 
                move.p2         8, a            ;a = # rows in menu grob 
                call            fill_table      ;complete data table 
                clrb            15, st          ;interupt flag off 
                intoff                          ;turn off interupts 
 
main:           move.5          crc_val, d0     ;d0 = address of hardware crc 
                move.a          @d0, c          ;c = pseudo random # 
                clr.a           a               ;a = 0 
                move.p2         #7F, a          ;a = mask for screen width 
                and.a           a, c            ;c = random and x mask 
                move.w          c, r1           ;save x coordinate 
 
                move.5          in_c, d0        ;these two lines do nothing 
                move.a          @d0, c          ;except make the crc random 
                                                ;it's a numbers game 
 
                move.5          crc_val, d0     ;point to crc again 
                move.a          @d0, c          ;c = pseudo random # 
                move.p2         #3F, a          ;a = mask for screen height 
                and.a           a, c            ;c = random and y mask 
                move.a          c, a            ;a = c = y coordinate 
                add.a           c, c            ;c = 2*c 
                add.a           c, c            ;c = 4*c 
                add.a           a, c            ;c = 5*c 
                move.w          r0, a           ;get data string address 
                add.a           a, c            ;add offset for y coordinate 
                move.a          c, d0           ;point to row address 
                move.a          @d0, c          ;get row address 
                move.w          r1, a           ;get x coordinate in pixels 
                srb.w           a               ;a = x/2 (shift right bit) 
                srb.w           a               ;a = x/4 = x coordinate in nibs 
                add.a           c, a            ;a = row start + (x offset) 
                move.a          a, d0           ;d0 points to nib of interest 
                move.w          r1, c           ;c = x coordinate in pixels 
                clr.a           a               ;a = 0 
                move.p1         3, a            ;a = 3 (#11b) 
                and.a           c, a            ;get pixel position in nib 
                clr.a           c               ;c = 0 
                move.p1         1, c            ;set up c 
 
;mirror_nib routine makes a nibble containing one bit set a x coordinate. 
;While grob nibbles are in order from left to right (up in memory), 
;the bits within the nibble are in reverse order.  So this routine 
;puts the nibble through a u-turn. 
 
mirror_nib:     dec.a           a               ;a = a - 1 
                                                ;if a(old) = 0 then sets carry 
                brcs            ready           ;jump if carry is set 
                add.a           c, c            ;c = 2*c = shift left bit c 
                jump            mirror_nib      ;loop 
 
;Now the old nibble of the lcd grob is xor-ed with the new nibble 
;BTW a nibble is just a four bit chunk, a hex digit (ex. #1111b = #Fh = #15d) 
 
ready:          clr.a           a               ;xor old and new nibble 
                move.1          @d0, a          ;a = old nibble (OLD) 
                clr.w           d 
                move.a          c, d            ;d = new nibble (NEW) 
                move.a          a, c            ;a = c = OLD 
                and.a           d, c            ;c = OLD and NEW 
                swap.a          c, d            ;d = OLD and NEW 
                or.a            a, c            ;c = OLD or NEW 
                not.a           d               ;d = not(OLD and NEW) 
                and.a           d, c            ;c = OLD xor NEW 
                move.1          c, @d0          ;place xor nibble  
 
                move.p3         #010, c         ;#010 specifies the row of 
                out.x           c               ;the drop key, the out.x 
                                                ;instruction scans a row 
 
                call            in_c            ;in_c returns the results 
                                                ;you have to call this command 
                                                ;something to do with return 
                                                ;stack 
 
                move.a          c, a            ;a = results 
                clr.a           c               ;c = 0 
                out.x           c               ;stop scanning 
 
;the following checks if the drop was pressed AND released for program exit 
;that way your not pushing the drop key when program exits 
 
                move.w          r2, c           ;get old key status 
                move.w          a, r2           ;put new key status 
                not.a           a               ;a = keys not pressed 
                and.a           c, a            ;and keys that were pressed 
                brbs            0, a, exit      ;bit 0 of contains flag 
                jump            main            ;for drop key column 
 
;fill_table:  make a data table containing addresses of lcd rows 
;IN:    d1 points to grob data 
;       d0 points to data string 
;       a = # rows to set up 
;AFFECTS:       a, c, d0 
 
fill_table:     move.a          @d1, c          ;c = grob adress 
                add.a           16, c           ;add 20 to skip grob header 
                add.a           4, c 
 
ftlp:           move.a          c, @d0          ;put row address into table 
                add.a           16, c           ;add 34 to skip to next row 
                add.a           16, c           ;lcd grob width = 34 * 4 = 136 
                add.a           2, c 
                add.a           5, d0           ;skip to next address space 
                dec.b           a               ;decrement row counter 
                brnz.b          a, ftlp         ;continue if counter <> 0 
                ret 
 
exit:           inton                           ;interupts on (keyboard) 
                setb            15, st          ;flag interupts on 
                call            rest_regs       ;recall d, b, d1, d0 
                move.a          @d0, a          ;return to RPL operating system 
                add.a           5, d0 
                jump            @a 
 
endcode 
-------------------------------end STAR source---------------------------------