HACK, 6 interesting (and dangerous) system-level routines by various authors. 
        Documentation by Joe Horn. 
 
        Uses Rick Grevelle's HACKIT library. 
 
        Some of these programs can easily cause a Memory Clear if not used 
        carefully.  Follow these instructions closely, and be sure to backup 
        your memory before experimenting with these tools. 
 
£ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ¨ 
 
STRIP: Strips the << and >> off the program in level 1. 
        By Conrad Winchester. 
           Argument: Program object with << and >> delimiters. 
           Caution: STRIP does not check, it just runs, removing the second 
        five and second-to-last five nibs of the object in level 1.  If you 
        give it something other than a program, you may get a Memory Clear. 
 
PACK: Packs a program's SYSEVALs into "External" form. 
        By Joe Horn. 
           Changes all << #nnnnn SYSEVAL >> pairs in a program into the single 
        2.5-byte System RPL object equivalent to that SYSEVAL.  Also works on 
        lists.  See PACK.DOC on EduCALC Goodies Disk #2 for details. 
 
FNXT: Find Next.  Searches ROM/RAM for any hex digits. 
           Input: #search, #start, any. 
           Level 1 is DROPped and SYSRCLed when search terminates, which allows 
        repeated pressing of FNXT.  Notice that the argument on level 3 is the 
        binary number to look for, immediately followed by the number of digits 
        to look for (minus 1!), which allows you to look for leading zeros. 
        (#1237 looks for the 8 digits 00000123.) 
           Example: Code objects begin with #02DCCh.  That's 5 hex digits, so 
        add the digit "4" (one less than 5) to it: #02DCC4h.  (Leading zeros do 
        not need to be typed, of course).  To look for all the Code objects in 
        the operating system (starting at address #0h), type: #2DCC4h #0h #0h 
        FNXT.  Pressing FNXT again finds the next one, etc. 
           Note: If you want speed and have a PC handy, don't use FNXT; use the 
        SEARCH command in Derek Nickel's Voyager program. 
 
PRCL: Recalls contents of an entire port to the stack. 
          Argument: Port number (real) 0, 1 or 2. 
          Example: 1 PRCL yields the contents of port 1 on the stack. 
          Note: The "objects" on the stack are only poiners, not yet NEWOB'd, 
        so you can recall the "contents" of a very large card into a very 
        little amount of MEM.  However, most operations on these will perform a 
        NEWOB (if there is sufficient MEM), such as STO.  You can find the 
        address of port objects, however, by using ADDR after PRCL. 
 
->RPN: Convert algebraic object into equivalent RPN object (list). 
        By Joe Horn. 
           Example: '1+2*3+4' ->RPN  -->  { 1 2 3 * + 4 + }.  (Try EVAL). 
 
RPN->: Convert RPN object (list) into equivalent algebraic object. 
        By Joe Horn. 
           Example: { 1 2 3 * + 4 + } RPN->  -->  '1+2*3+4'.  (Try EVAL). 
           Caution: Converting non-well-formed "RPN objects" into algebraics 
        will either result in an 'Invalid Expression' or 'UNKNOWN' on the 
        stack, which will evaluate the same as the list before conversion; or 
        in Memory Clear (in extreme cases).  For safety's sake, only use lists 
        containing ->RPN outputs, or similar.  Things like { << 5 >> } are not 
        meaningful and tempt Murphy's Law. 
 
…ŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽ—