(Comp.sys.handhelds) 
Item: 3767 by ftg0673 at tamsun.TAMU.EDU 
Author: [Rick Grevelle] 
  Subj: HP48 Conference Preview 
  Date: Thu Jul 25 1991 
 
This is one of the topics I plan to discuss in detail at the up and coming 
Handhelds Conference in Corvallis.  Since there are those who will not wish 
to wait until then to take advantage of this material, it is appropriately 
complete to now provide a sneak preview.  However the finer details will be 
reserved for the conference itself.  
 
 
Rick Grevelle 
ftg0673@tamsun.tamu.edu 
(409) 774-1169 
 
 
=========================================================================== 
 
 
                   HP48 Hard Key Assignment Interrupts 
         
  Normally each time one of the HP48's forty nine keys is pressed two system 
binaries are pushed to the stack by the underlying operating system.  These 
are never seen by the user who is probably unaware that his or her calculator 
is using the very same stack for the SYSTEM RPL as is used by the USER RPL.  
Once a key is pressed and the two system binaries are pushed to the stack, it 
is then up to the SYSTEM RPL to make a decision base on the value of these 
results as to what to do next (i.e. change menus, execute functions, initiate 
the command line, etc.). 
 
  Interrupting the SYSTEM RPL responsible for interpreting and executing the 
actual key stroke is easily done.  It is then possible to substitute a user 
scheme to effectively handle the task of key press management, but this is no 
small job, and the process can become quite lengthy.  All details regarding 
the interrupt mechanism and the SYSTEM RPL management of key presses will not 
be addresses here as I'm saving it for the August conference.  What will be 
covered here is involved enough for now, and should be more than adequate for 
the majority of users.  In other words, I'm providing all the support tools 
necessary for interrupting the 48's hard key assignments.  Keeping it in mind 
that this has nothing to do with the user key assignments as I have gone to 
great lengths to maintain the integrity of this feature that actually coexists 
with the regular key assignments. 
 
  The two directories at the end of this article are suitable for converting 
to library format.  The first will be primarily of interest to those concerned 
with hard addressing key assignments in software intended for ROM cards, and 
the second for those who wish to perform interrupts from RAM.  Although I have 
tried to stick to entry points supported by Hewlett-Packard, it wasn't always 
possible to do so. I apologize for this, especially to those who haven't spent 
the majority of their spare time for the past two years peeking at the hex in  
the HP28/48.  So with all that said, let's get started.  
 
 
 
        o  Hard key assignments in the 48 are found in the hidden ROM 
           and packaged in an Array of System Binary data object that 
           contains forty nine System Binary elements.  Each of these 
           elements is in fact the address of another Array of System 
           Binary within the hidden ROM containing six elements which 
           are the addresses of the various key configurations that a 
           particular key is assigned.  Each element corresponds to a 
           specific key-shift pattern as follows: 
 
 
                        1st element:    unshifted 
                        2nd element:    left-shifted 
                        3rd element:    right-shifted 
                        4th element:    alpha-shifted 
                        5th element:    alpha-left-shifted 
                        6th element:    alpha-right-shifted 
 
 
 
        o  The key assignment array in an HP48 version E is located at 
           # 7B4E4h in the covered ROM.  While it is not necessary for 
           this to be done, the Array of System Binary can be recalled 
           by using \<< #3FB1Fh SYSEVAL #C612h SYSEVAL \>>.  Implement 
           OUT\-> to decompose the array into its individual elements. 
           The first element in this array of forty nine elements is a 
           System Binary that is the address of an array of six System 
           Binaries that are the addresses of each of the six specific 
           key-shift patterns for the upper most left-hand key.  So to 
           continue associating each of the forty nine elements with a 
           particular key, simply move from left to right, assigning a 
           new element for each one of the 48's keys.  This means that 
           the upper most right-hand key is the sixth element, and the 
           lower most right-hand is the forty ninth array element.   
 
 
                         
                     CORRESPONDING KEYBOARD ARRAY ELEMENTS 
 
 
               [ A ]    [ B ]    [ C ]    [ D ]    [ E ]    [ F ] 
             <7AA5Dh> <7AA94h> <7AACBh> <7AB02h> <7AB39h> <7AB70h> 
 
               [MTH]    [PRG]    [CST]    [VAR]    [ ^ ]    [NXT] 
             <7ABA7h> <7ABDEh> <7AC15h> <7AC4Ch> <7AC83h> <7ACBAh> 
 
               [ ' ]    [STO]   [EVAL]    [ < ]    [ v ]    [ > ] 
             <7ACF1h> <7AD28h> <7AD5Fh> <7AD96h> <7ADCDh> <7AE04h> 
 
               [SIN]    [COS]    [TAN]    [SQx]    [pwr]    [1/x] 
             <7AE3Bh> <7AE72h> <7AEA9h> <7AEE0h> <7AF17h> <7AF4Eh> 
         
              [ENTER]      [+/-]      [EEX]      [DEL]      [<==] 
             <7AF85h>    <7AFBCh>   <7AFF3h>   <7B02Ah>   <7B061h>  
         
              [alpha]      [ 7 ]      [ 8 ]      [ 9 ]      [ / ] 
             <7B098h>    <7B0CFh>   <7B106h>   <7B13Dh>   <7B174h> 
 
              [left]       [ 4 ]      [ 5 ]      [ 6 ]      [ * ] 
             <7B1ABh>    <7B1E2h>   <7B219h>   <7B250h>   <7B287h>  
 
              [right]      [ 1 ]      [ 2 ]      [ 3 ]      [ - ] 
             <7B2BEh>    <7B2F5h>   <7B32Ch>   <7B363h>   <7B39Ah> 
 
              [ ON ]       [ 0 ]      [ . ]      [SPC]      [ + ] 
             <7B3D1h>    <7B408h>   <7B43Fh>   <7B476h>   <7B4ADh> 
 
 
 
        o  Key reassignments are made by replacing array elements that 
           correspond to the appropriate keys.  Utilizing the provided 
           shareware, this is accomplished through the modification of 
           the Array of System Binary stored in the KEYS variable from 
           directory number one, or the Array of Global Name stored in 
           the KEYS variable, but in directory number two instead.  In 
           addition directory two contains forty nine Global variables 
           sequentially named beginning with K.1 through K.49.  Stored 
           in each of these is an Array of System Binary corresponding 
           to the key number from which individual variable names were 
           derived.  Therefore, the Global name K.1 contains the Array 
           of System Binary recovered from the hidden ROM at # 7AA5Dh. 
 
 
 
        o  The Array of System Binary stored in the KEYS variable from 
           directory one is the cache for the default key assignments. 
           This is because it's easiest to begin customizing hard keys 
           by altering the default assignments rather than building an 
           array from scratch.  The scheme used by the first directory 
           to override the default key assignments is quite similar to 
           that of the one found in the 48.  An Array of System Binary 
           is the only type of array that is allowed, and each element 
           must be an address in memory where a second Array of System 
           Binary is located whose elements are the addresses of entry 
           points for the various key configurations associated with a 
           specific key.  This requires knowing the location in memory 
           where the arrays are stored and that once these assignments  
           are made they cannot be moved.  Clearly this application is 
           better suited for software that is hard addressed.  However 
           there are applications for RAM oriented software exploiting 
           this scheme.  For example it might be desirable to reassign 
           the hard keys differently from the factory's.  For instance 
           it would be more convenient for the top row of menu keys to 
           be closer to the numerical keys for someone who was working 
           with hexadecimal integers.  A third directory included here 
           is identical to the first but with one exception; the Array 
           of System Binary has had its elements rearranged so the top 
           row of keys has been exchanged with forth row.  This brings 
           the alpha keys A through F closer to the numerical keys for 
           quicker access.  Implementing CUSTOM swaps row one and four 
           and DEFAULT restores them to their factory assignments. 
 
 
 
        o  The second directory provides the flexibility necessary for 
           software intended to be used in RAM.  Mainly this is due to 
           an embellished CUSTOM function which permits two additional  
           types of arrays to be used.  These additional types include 
           the previously mention Array of Global Name, as well as its 
           library counterpart Array of XLIB Name.  Where the Array of 
           Global Name stored in the KEYS variable contains all of the 
           forty nine sequentially named Global variables.  This means 
           that the routine can now find arrays stored in Global Names 
           or XLIBs as well as by their memory locations.  Furthermore 
           the secondary arrays that house the individual key patterns 
           may also be composed of either Global Names or XLIBs.  This 
           allows user defined functions to be assigned to keys either 
           by their Global Names or XLIBs. 
 
 
 
        o  Reassign a key to functions stored in Global Names or XLIBs 
           by constructing an array of Global Names or XLIBs using the 
           ->ARR command from HACKIT and then storing it in any one or 
           more of the forty nine sequentially named global variables. 
           Once this is done implement the CUSTOM function in order to 
           interrupt the default key assignments.  Restore the default 
           key assignments using the DEFAULT function. 
 
 
 
             Example:  Assign the first menu page of the HACKIT 
                       library to a single key of your choice. 
 
        _________________________               _________________________ 
        |{HOME}                 |               |{HOME}                 | 
        |-----------------------|               |-----------------------| 
        |3:                     |               |4:                     | 
        |2:                     |               |3:                     | 
        |1: { ->ASCI ASCI-> SCRC|               |2:                     | 
        |   SEEK PEEK POKE   }  |               |1:   Array of XLIB Name| 
        |### ### ### ### ### ###|               |### ### ### ### ### ###| 
        -------------------------               ------------------------- 
     1) Place the six commands from          2) Implement OUT-> to explode 
        the first page of HACKIT in             the list and then ->ARR to 
        a list then enter it on the             obtain the array.  Storing 
        on the stack in level one.              it in any K.n assigns that 
       (Display model is not exact.)            key the six library XLIBs. 
 
 
 
        o  These directories effectively permit user defined functions 
           to be assigned to keys without utilization of the USER MODE 
           which is still available for regular use.  Essentially this 
           routine doubles the amount of possible user key assignments 
           previously available.  Extensive measures were taken not to 
           restrict user applications, meaning the scheme has not been 
           one hundred percent idiot-proofed.  Two specific areas that 
           could be potentially dangerous are as follows: 
 
                +  Do not store any objects other than arrays 
                   in the sequentially named Global variables 
                   because a decision was made to eval rather 
                   than rcl the elements from the KEYS array. 
 
                +  Avoid using subdirectories for this scheme 
                   because moving up to a parent directory or 
                   the HOME directory without first restoring 
                   control to the default could perhaps cause 
                   a memory loss. 
 
          One final note; if either of these two directories are to be 
          converted to libraries it would be advisable to place all of 
          variables other than CUSTOM and DEFAULT in a list in $HIDDEN 
          in order to hide them in the library.  This is because these 
          two variables are the only ones necessary for the control of 
          the scheme once the key assignments have actually been made. 
          Note that STDKEYS is an RPL subroutine called by CUSTOM.  Do 
          not implement it for any reason.  Both uuencode and ASC have 
          been provided.