Author: [Rick Grevelle] 
  Subj: CMACF Fix 
  Date: Wed Sep 12 1990 07:57  
 
Thanks to J"urgen Koslowski for pointing out an error in the create MACF 
routine.  However, the fix offered isn't quite right.  The one below is. 
 
CMACF [4152] 
 
%%HP: T(3)A(D)F(.);  
\<< 
       # 3174197160731741h 
       # 181314E331741607h 
       # 4173170EC6A830F8h 
       # C808461241731705h 
                   ^^^          digits transposed, ought to read 731! 
   1  3  START 
          # 5193h   SYSEVAL 
         NEXT  #2DCCh 
          # 5A03h   SYSEVAL 
          # 5ACCh   SYSEVAL 
\>> 
  
 
In regards to your question concerning the instruction DA; it is a MOVE, 
register to register, and is explained in the Processor Notes as follows: 
  
------------------------------------------------------------------------- 
 
MOVE Register to Register 
 
               ppz      MOVE.f s,d 
 
                                           pp | f     z | s d 
                                          --------   --------- 
                                           A8 | P     4 | B A 
                                           A9 | WP    5 | C B 
                                           AA | XS    6 | A C 
                                           AB | X     7 | C D 
                                           AC | S     8 | A B 
                                           AD | M     9 | B C 
                                           AE | B     A | C A 
                                           AF | W     B | D C 
                                           D  | A      
 
Examples: 
 
D9     MOVE.A  B,C       ; C gets B   (20 bits) 
AE4    MOVE.B  B,A       ; A gets B    (8 bits) 
AFB    MOVE.W  D,C       ; C gets D   (64 bits) 
DA     MOVE.A  C,A       ; A gets C   (20 bits) 
 
 
>Another suggestion concerning this program: It seems to me that the 
>new HP48 instruction NEWOB can be used to replace "" +, saving 2.5 bytes. 
 
In an effort to keep routines such as these short, it becomes necessary to 
use a bit of trickery.  STRING->CODE uses a combination of two tricks; one  
used by Alonzo in his PEEK scheme, and another one that I discovered.  The 
point here is that NEWOB will indeed work and save 2.5 bytes in doing so. 
 
However, neither of the two are particularly efficient.  They are merely a 
convenient manner in which to compensate for the forementioned lazy trickery. 
 
It should be mentioned that HP does not use trickery of this sorts.  Thanks 
to a variable length PEEK routine written for the 28, I was able to isolate  
and disassemble the routines responsible for updating low RAM when new objects 
are created.   
 
A more recent example of how this is done in the 48 can be found in the ->ASC  
and ASC-> routines recently posted by Dr. Wickes.  The details involved here 
are numerous, and time required to understand them would be great.  Now that 
school is back in full swing, I have no such luxury! 
 
Rick Grevelle