(Comp.sys.handhelds) 
Item: 3947 by _sun1 at hpcvbbs.cv.hp.com 
Author: Scott Ferry  (415) 845-1088 
  Subj: USA GROB (huge) w/ latitude/longitude output 
  Date: Sat Sep 07 1991 
(Donated to Goodies Disk Project at the Corvallis Conference 8/4/91) 
 
[Note: MAPD is over 14K long.  See MAPD2.DOC for a way to to run MAPD 
 in only 5K.  -jkh-] 
 
MAPD is a directory containing: 
 
     MAP 
     USGROB 
     MAPX 
     FIX2 
 
     The program `MAP' runs the whole thing.  When you run it, it 
calls up USGROB, a huge (424x262) GROB of the 48 contiguous United 
States.  Scroll around (using the arrow keys and blue shift) 
until you get the part of the country you're interested in, then 
press [left-shift] GRAPH.  The cross-cursor appears.  Now move that 
around until you get it directly over the place you're interested in 
and press [ENTER] followed by [ATTN].  The longitude and latitude 
will appear on the stack, tagged.  (Accuracy about 1/2 degrees). 
 
`MAP' is written in system RPL and mainly puts the GROB into 
PICT, etc.,  sets up the PPAR, and then lastly calls `MAPX'.  This 
routine is a small part of a 51K library I wrote that does a lot 
of stuff and is intended for a 128K ROM card.  Since there will be 
plenty of space on the card I didn't use PGROB and UPGROB [by Erik 
Bryntse; see PGROB.DOC on this disk.  -jkh-] in the interest of time 
and safety.  But it is certainly amenable to these programs (it 
cuts the size in half). 
 
     `MAPX' does the conversion from user coordinates to latitude 
and longitude, and is written in user RPL, this being plenty fast 
enough.  I basically figured it out by some math and a lot of 
trial and error, so it will, perhaps obviously, not work with 
any other map. 
 
     `MAPX' calls `FIX2', a system RPL program to properly round 
an HMS format number to 2 decimal places.  E.g.: 
 
     15 35' 34.2" => 15.35342 -> 15.36 
     15 35' 30"   => 15.353   -> 15.35 
     15 35' 29.9" => 15.35299 -> 15.35 
     15 59' 30"   => 15.593   -> 16 
 
and similarly for negative values. 
 
     Make sure you have a real number on the stack if you call 
the program alone. 
 
These programs are copyrighted, but may be used in any non-commercial, 
non-astronomy related program without further permission needed. 
 
They were written and tested on a Version E machine. 
 
               Good Luck, Scott