Saturn Instruction Set				Derek S. Nickel 
	================================================================ 
 
	0...	* misc operations (RTNs, modes, stack, status, P, logic) 
 
	1...	* data movement/loading (D0,D1,R0-R4) 
 
	2n	P=     n 
 
	3xn..n	LC(m)  n..n	(x = m - 1) 
	3mc..c	LCASC  \A..A\	(m = 2*characters - 1) 
	3nh..h	LCHEX  h..h	(n = digits - 1) 
 
	400	RTNC 
	4aa	GOC    label 
	420	NOP3 
 
	500	RTNNC 
	5aa	GONC   label 
 
	6aaa	GOTO   label 
	6300	NOP4 
	64000	NOP5 
 
	7aaa	GOSUB  label 
 
	8...	* misc, tests and branching 
 
	9...	* tests w/fs 
 
	Aax	* math and assignment w/fs 
	Abx	* math and assignment w/fs 
	Bax	* math and assignment w/fs 
	Bbx	* math and assignment w/fs 
 
	Cx	* math and assignment w/A 
	Dx	* math and assignment w/A 
	Ex	* math and assignment w/A 
	Fx	* math and assignment w/A  
 
	0 
	================================================================ 
 
	00	RTNSXM 
	01	RTN 
	02	RTNSC 
	03	RTNCC 
	04	SETHEX 
	05	SETDEC 
	06	RSTK=C 
	07	C=RSTK 
	08	CLRST 
	09	C=ST 
	0A	ST=C 
	0B	CSTEX 
	0C	P=P+1 
	0D	P=P-1 
	0Exx	* logic operations	 
	0F	RTI 
 
	-- field --- 
	 fs	 A 
	------------ 
	0Ea0	0EF0	A=A&B  field 
	0Ea1	0EF1	B=B&C  field 
	0Ea2	0EF2	C=C&A  field 
	0Ea3	0EF3	D=D&C  field 
	0Ea4	0EF4	B=B&A  field 
	0Ea5	0EF5	C=C&B  field 
	0Ea6	0EF6	A=A&C  field 
	0Ea7	0EF7	C=C&D  field 
 
	0Ea8	0EF8	A=A!B  field 
	0Ea9	0EF9	B=B!C  field 
	0EaA	0EFA	C=C!A  field 
	0EaB	0EFB	D=D!C  field 
	0EaC	0EFC	B=B!A  field 
	0EaD	0EFD	C=C!B  field 
	0EaE	0EFE	A=A!C  field 
	0EaF	0EFF	C=C!D  field 
 
	fs: P  WP XS X  S  M  B  W 
	a:  0  1  2  3  4  5  6  7  
 
	10, 11, 12 
	================================================================ 
 
	100	R0=A 
	101	R1=A 
	102	R2=A 
	103	R3=A 
	104	R4=A 
	105	 
	106	 
	107	 
	108	R0=C 
	109	R1=C 
	10A	R2=C 
	10B	R3=C 
	10C	R4=C 
	10D	 
	10E	 
	10F	 
 
	110	A=R0 
	111	A=R1 
	112	A=R2 
	113	A=R3 
	114	A=R4 
	115	 
	116	 
	117	 
	118	C=R0 
	119	C=R1 
	11A	C=R2 
	11B	C=R3 
	11C	C=R4 
	11D	 
	11E	 
	11F	 
 
	120	AR0EX 
	121	AR1EX 
	122	AR2EX 
	123	AR3EX 
	124	AR4EX 
	125	 
	126	 
	127	 
	128	CR0EX 
	129	CR1EX 
	12A	CR2EX 
	12B	CR3EX 
	12C	CR4EX 
	12D	 
	12E	 
	12F	  
 
	13 through 1F 
	================================================================ 
 
	130	D0=A 
	131	D1=A 
	132	AD0EX 
	133	AD1EX 
 
	134	D0=C 
	135	D1=C 
	136	CD0EX 
	137	CD1EX 
 
	138	D0=AS 
	139	D1=AS 
	13A	AD0XS 
	13B	AD1XS 
 
	13C	D0=CS 
	13D	D1=CS 
	13E	CD0XS 
	13F	CD1XS 
 
	---------- field ----------- 
	 A	 B	 fs	 d 
	----------------------------	 
	140	148	150a	158x	DAT0=A field 
	141	149	151a	159x	DAT1=A field 
	142	14A	152a	15Ax	A=DAT0 field 
	143	14B	153a	15Bx	A=DAT1 field 
	144	14C	154a	15Cx	DAT0=C field 
	145	14D	155a	15Dx	DAT1=C field 
	146	14E	156a	15Ex	C=DAT0 field 
	147	14F	157a	15Fx	C=DAT1 field 
 
	16x	D0=D0+ n 
	17x	D1=D1+ n 
	18x	D0=D0- n 
	19nn	D0=(2) nn 
	19hh	D0=HEX hh 
	1Annnn	D0=(4) nnnn 
	1Ahhhh	D0=HEX hhhh 
	1Bnnnnn	D0=(5) nnnnn 
	1Bhhhhh	D0=HEX hhhhh 
	1Cx	D1=D1- n 
	1Dnn	D1=(2) nn 
	1Dhh	D1=HEX hh 
	1Ennnn	D1=(4) nnnn 
	1Ehhhh	D1=HEX hhhh 
	1Fnnnnn	D1=(5) nnnnn 
	1Fhhhhh	D1=HEX hhhhh 
 
	fs: P  WP XS X  S  M  B  W 
	a:  0  1  2  3  4  5  6  7 
 
	x = d - 1		x = n - 1 
	d = x + 1		n = x + 1  
 
	80, 81 
	================================================================ 
 
	800	OUT=CS 
	801	OUT=C 
	802	A=IN 
	803	C=IN 
	804	UNCNFG 
	805	CONFIG 
	806	C=ID 
	807	SHUTDN 
	8080	INTON 
	808C	PC=(A) 
	808F	INTOFF	 
	809	C+P+1 
	80A	RESET 
	80B	BUSCC 
	80Cn	C=P    n 
	80Dn	P=C    n 
	80E	SREQ? 
	80Fn	CPEX   n 
 
	810	ASLC 
	811	BSLC 
	812	CSLC 
	813	DSLC 
	814	ASRC 
	815	BSRC 
	816	CSRC 
	817	DSRC 
	818	 
	819	 
	81A	 
	81B	 
	81C	ASRB 
	81D	BSRB 
	81E	CSRB 
	81F	DSRB  
 
	82 through 8F, 9 
	================================================================ 
 
	82n	no opcode, clear hardware status w/n as bit mask 
	821	XM=0 
	822	SB=0 
	824	SR=0 
	828	MP=0 
	82F	CLRHST 
 
	831yy	?XM=0 
	832yy	?SB=0 
	834yy	?SR=0 
	838yy	?MP=0 
 
	84n	ST=0   n 
	85n	ST=1   n 
	86nyy	?ST=0  n	?ST#1  n 
	87nyy	?ST=1  n	?ST#0  n 
	88nyy	?P#    n 
	89nyy	?P=    n 
	8Axyy	* tests w/A (equal and not equal) 
	8Bxyy	* tests w/A (inequality) 
	8Caaaa	GOLONG label 
	8Daaaaa	GOVLNG label 
	8Eaaaa	GOSUBL label 
	8Faaaaa	GOSBVL label 
	9zxyy	* tests w/fs 
 
	TEST00	RTNYES 
	TESTyy	GOYES  label  
 
	8A, 8B, 9 
	================================================================ 
 
	--- field ---- 
	  A      fs 
	-------------- 
	8A0yy	9a0yy	?A=B   field		?B=A   field 
	8A1yy	9a1yy	?B=C   field		?C=B   field 
	8A2yy	9a2yy	?A=C   field		?C=A   field 
	8A3yy	9a3yy	?C=D   field		?D=C   field 
	8A4yy	9a4yy	?A#B   field		?B#A   field 
	8A5yy	9a5yy	?B#C   field		?C#B   field 
	8A6yy	9a6yy	?A#C   field		?C#A   field 
	8A7yy	9a7yy	?C#D   field		?D#C   field 
	8A8yy	9a8yy	?A=0   field 
	8A9yy	9a9yy	?B=0   field 
	8AAyy	9aAyy	?C=0   field 
	8AByy	9aByy	?D=0   field 
	8ACyy	9aCyy	?A#0   field 
	8ADyy	9aDyy	?B#0   field 
	8AEyy	9aEyy	?C#0   field 
	8AFyy	9aFyy	?D#0   field 
 
	8B0yy	9b0yy	?A>B   field 
	8B1yy	9b1yy	?B>C   field 
	8B2yy	9b2yy	?C>A   field 
	8B3yy	9b3yy	?D>C   field 
	8B4yy	9b4yy	?A<B   field 
	8B5yy	9b5yy	?B<C   field 
	8B6yy	9b6yy	?C<A   field 
	8B7yy	9b7yy	?D<C   field 
	8B8yy	9b8yy	?A>=B  field 
	8B9yy	9b9yy	?B>=C  field 
	8BAyy	9bAyy	?C>=A  field 
	8BByy	9bByy	?D>=C  field 
	8BCyy	9bCyy	?A<=B  field 
	8BDyy	9bDyy	?B<=C  field 
	8BEyy	9bEyy	?C<=A  field 
	8BFyy	9bFyy	?D<=C  field 
 
	fs: P  WP XS X  S  M  B  W 
	a:  0  1  2  3  4  5  6  7 
	b:  8  9  A  B  C  D  E  F  
 
	A, C, D 
	================================================================ 
 
	-- field -- 
	A	fs 
	----------- 
	C0	Aa0	A=A+B  field 
	C1	Aa1	B=B+C  field 
	C2	Aa2	C=C+A  field 
	C3	Aa3	D=D+C  field 
	C4	Aa4	A=A+A  field 
	C5	Aa5	B=B+B  field 
	C6	Aa6	C=C+C  field 
	C7	Aa7	D=D+D  field 
	C8	Aa8	B=B+A  field 
	C9	Aa9	C=C+B  field 
	CA	AaA	A=A+C  field 
	CB	AaB	C=C+D  field 
	CC	AaC	A=A-1  field 
	CD	AaD	B=B-1  field 
	CE	AaE	C=C-1  field 
	CF	AaF	D=D-1  field 
 
	D0	Ab0	A=0    field 
	D1	Ab1	B=0    field 
	D2	Ab2	C=0    field 
	D3	Ab3	D=0    field 
	D4	Ab4	A=B    field 
	D5	Ab5	B=C    field 
	D6	Ab6	C=A    field 
	D7	Ab7	D=C    field 
	D8	Ab8	B=A    field 
	D9	Ab9	C=B    field 
	DA	AbA	A=C    field 
	DB	AbB	C=D    field 
	DC	AbC	ABEX   field 
	DD	AbD	BCEX   field 
	DE	AbE	ACEX   field 
	DF	AbF	CDEX   field 
 
	fs: P  WP XS X  S  M  B  W 
	a:  0  1  2  3  4  5  6  7 
	b:  8  9  A  B  C  D  E  F  
 
	B, E, F 
	================================================================ 
 
	-- field --- 
	A	fs 
	------------ 
	E0	Ba0	A=A+B  field 
	E1	Ba1	B=B+C  field 
	E2	Ba2	C=C+A  field 
	E3	Ba3	D=D+C  field 
	E4	Ba4	A=A+1  field 
	E5	Ba5	B=B+1  field 
	E6	Ba6	C=C+1  field 
	E7	Ba7	D=D+1  field 
	E8	Ba8	B=B-A  field 
	E9	Ba9	C=C-B  field 
	EA	BaA	A=A-C  field 
	EB	BaB	C=C-D  field 
	EC	BaC	A=B-A  field 
	ED	BaD	B=C-B  field 
	EE	BaE	C=A-C  field 
	EF	BaF	D=C-D  field 
	 
	F0	Bb0	ASL    field 
	F1	Bb1	BSL    field 
	F2	Bb2	CSL    field 
	F3	Bb3	DSL    field 
	F4	Bb4	ASR    field 
	F5	Bb5	BSR    field 
	F6	Bb6	CSR    field 
	F7	Bb7	DSR    field 
	F8	Bb8	A=-A   field 
	F9	Bb9	B=-B   field 
	FA	BbA	C=-C   field 
	FB	BbB	D=-D   field 
	FC	BbC	A=-A-1 field 
	FD	BbD	B=-B-1 field 
	FE	BbE	C=-C-1 field 
	FF	BbF	D=-D-1 field 
 
	fs: P  WP XS X  S  M  B  W 
	a:  0  1  2  3  4  5  6  7 
	b:  8  9  A  B  C  D  E  F  
 
	Data Storage Allocation 
	================================================================ 
 
	00..0	BSS    expr 
	nn..n	CON(m) expr 
	nn..n	REL(m) expr 
	zy..a	NIBASC 'chars' 
	zy..a	NIBASC \chars\ 
	hh..h	NIBHEX h..hh  
 
	Saturn Registers 
	================================================================ 
 
	+--------------------------------+ 
	|                                |  A 
	+--------------------------------+ 
	|                                |  B 
	+--------------------------------+ 
	|                                |  C 
	+--------------------------------+ 
	|                                |  D 
	+--------------------------------+ 
 
			      +----------+ 
			      |          |  D0 
			      +----------+ 
			      |          |  D1 
			      +----------+ 
 
				      +--+ 
				      |  |  P 
				      +--+ 
 
			      +----------+ 
			      |          |  PC 
			      +----------+ 
 
	+--------------------------------+ 
	|                                |  R0 
	+--------------------------------+ 
	|                                |  R1 
	+--------------------------------+ 
	|                                |  R2 
	+--------------------------------+ 
	|                                |  R3 
	+--------------------------------+ 
	|                                |  R4 
	+--------------------------------+ 
 
				+--------+ 
				|        |  IN (16 bits) 
				+--------+ 
				  |      |  OUT (12 bits) 
				  +------+ 
 
				       +-+ 
				       | |  Carry (1 bit) 
				       +-+ 
 
				+--------+ 
				| F .. 0 |  ST (16 bits) 
				+--------+ 
 
			   +-------------+ 
			   | MP SB SR XM |  HST (4 bits) 
			   +-------------+