(Comp.sys.handhelds) Option:  
Item: 3447 
Subj: Symbolic Matrix Utilities 
---------- 
  Resp: 1 of 1 by blair at en.ecn.purdue.edu 
Author: [Marc E Blair] 
  Date: Thu Jun 13 1991 12:14  
 
This is a newer version which allows symbolics in solving simeq and also 
simplifies answers further than the old program. 
 
->Q   This program toggles fraction mode (a little block appears to indicate 
      fraction mode) otherwise straight decimals will be used. Fractions can 
      eat up memory on lengthy calculations. 
 
det   returns a determinant of a matrix. It behaves much like the routine   
      Eliel Louzouen wrote a while back, although I wrote this with speed 
      as first priority. The approach I used resulted in a twelvefold  
      increase in speed with numeric evaluation and a threefold increase in 
      symbolic evaluation than the original routines. 
 
simeq solves a system of equations in matrix format... i.e. 4x+5y=9 and 
      3x+2y=10 would be entered { { 4 5 9 } { 3 2 10 } } and evaluated 
      returning { '32/7' '-(13/7)' } meaning x=32/7 and y=-13/7. 
      The program uses matrices to solve if there are less than five 
      variables, >5 results in row reduction. (this way a ten variable 
      equation takes 5 minutes, matrix methods would take 25 days) 
 
rr    row reduction program to reduce matrices into row-echelon form. 
      symbolic row reduction is supported. 
 
inv   invert a matrix using row reduction techniques 
 
mec   expand and collect and evaluate all items in a matrix to their most 
      simple form 
-----  All other variables are subprograms. 
 
I am not repsonsible for memory loss, hardware trouble, loss of math abilities, 
sudden shifts in the space-time continuum, or other problems which might occur 
due to the use of this program but in all likelihood will never happen. 
 
enjoy! 
 
[Note: See also SYMBMAT on Goodies Disk #1 for another approach.  -jkh-]