(Q_and_a) 
Item: 102 by akcs.getz@hpcvbbs.cv.hp.com 
Author: [Robin Getz] 
  Subj: fix for smith corona ram cards? 
  Date: Fri Jan 10 1992 
 
Hello Hp. 
 
I was wondering if you could tell me if, or how this could damage my 48. 
 
I realize there are some voltage regulation problems with non-HP ram 
cards (low voltage shutdown threshold).  [Note: For details about this 
problem, see MEMCARDS.DOC on Goodies Disk #3.  -jkh-]  I think I have 
found a way to bypass this problem. 
 
There is a control line going to the I/O chip from the voltage 
regulator. This line is Vcc until Vcc is lower than 4.1V (on the card 
I ripped apart) then it slams to zero, just as you said it would in 
all the other documentation you have previous posted on this subject. 
What I have done is disconnect this line from the voltage regulator 
and reconnect it to Vcc.  Now the card will not shut off until Vcc 
reachs card battery voltage (about 3.0 V).  Is not this what we want? 
 
I have this card in my calculator (rip up my warranty card please) and 
it works fine.  I have put nearly dead batteries in my calculator to 
simulate low voltage conditions and it works just fine. 
 
Before I run around and start telling everyone which connections to 
change I thought I would give you the first kick at the cat (per say). 
 
Robin Getz 
Electrical Engineer 
University of Saskactchewan 
873398@bell.usask.ca 
 
If you would like I can send you the changes I have made in order for you 
to test in your labs. 
 
[Note: This interesting posting brought a few responses from others, 
and no objections from HP....  -jkh-]