CLK.DOC File 
                                      
                  (c) Hewlett-Packard Company, 1992. 
 
 
Overview 
-------- 
 
The CLK application keeps the system clock as accurate as possible by 
synchronizing the clock with a time standard, and using the accumulated 
adjustments with the elapsed time to compute the necessary correction 
amount/rate.  It is especially useful for applications like navigation that 
require extremely accurate times. 
 
Adjustments are made relative to the nearest number of 1/2 hour time-zone 
changes. All changes that are multiples of 1/2 hour are assumed time-zone 
changes (and ignored in error correction computation); other changes are 
assumed error corrections.  For example, a change of +1:35 is assumed to be 
+1:30 time-zone change (ignored) and +:05 error correction (the clock is 5 
minutes slow).  A change of +1:25 is assumed to be +1:30 time-zone and -:05 
error (the clock is 5 minutes fast). 
 
 
Installation 
------------ 
 
Transfer CLK into your HP 48 HOME directory.  (Don't use the HP 48 built-in 
TIME SET/ADJST operations while this application is active.) 
 
 
Operation 
--------- 
 
1.  Press [VAR]|CLK| to access the application. 
 
2.  Enter a list containing the minimum interrupt rate and the maximum 
    clock deviation allowed, press |C.RST|.  (This initializes the 
    application.) 
 
3.  If necessary, enter a list containing the current time and date, press 
    |C.SET|. 
 
4.  Enter the desired adjustment, press |C.ADJ|. 
 
5.  Repeat steps 4 and 5 as needed. 
 
6.  Press |C.XCT| when the clock is synchronized. 
 
7.  Wait a few weeks and then repeat steps 4, 5, 6, and 7. 
 
8.  Press |C.STS| to review the status information. 
 
9.  Press |C.SSP| to suspend the correction alarm cycle temporarily; press 
    |C.CNT| to continue the suspended correction alarm. 
 
10. Repeat step 3 to cancel the correction alarm and reinitialize all CLK 
    variables. 
 
--------------------------------------------------------------------------- 
 Note:  If you abort the program, flags that were changed by the program 
        will remain changed. 
--------------------------------------------------------------------------- 
 
 
User Menu Keys 
-------------- 
 
The following five programs make up the user interface to this package. 
Each will give an error message if the expected input is not found. The 
error message attempts to indicate the form of the input expected. Time 
input should be in the form HH.MMSSs, and date input should be MM.DDYYYY. 
 
|C.SET|   Takes a level-1 list containing the current time and date.  The 
          clock is set to this time/date. 
 
|C.ADJ|   Takes from level 1 the amount of adjustment to be applied to the 
          current time.  A positive amount increases the time and a 
          negative amount decreases it. 
 
|C.XCT|   Takes nothing from the stack; tells the correction package that 
          the clock is now exactly synchronized with the time standard.  If 
          this is the first time it has been invoked, then a time base is 
          activated and all error corrections from this point on will be 
          accumulated.  If this is the second or subsequent invocation, 
          then the time base is extended to this point and the necessary 
          calculations are done to set up the clock correction package.  An 
          alarm is scheduled and the correction package will make the 
          needed clock corrections from now on.  Subsequent invocations 
          will refine the accuracy of the corrections. 
 
|C.RST|   Takes a level-1 list containing the minimum interrupt rate and 
          the maximum clock deviation allowed (both in "time" format).  The 
          correction package is reset to a virgin state--the time base is 
          deactivated, the alarm is removed, and further error corrections 
          will not be accumulated (the accumulators are cleared).  All 
          variables are reinitialized and the directory is reordered. 
 
          Maximum clock deviation specifies the maximum acceptable error 
          for the clock. If the absolute value of the given maximum 
          deviation is less than .01 second, then it is set to 1 second. 
 
          Minimum interrupt rate specifies the minimum amount of time 
          required between clock adjustments.  If the absolute value of the 
          given minimum interrupt rate is less than 1 second, then it is 
          set to 1 minute.  If the clock cannot be adjusted to accurate 
          time with the given maximum deviation without using alarms at a 
          more frequent rate than allowed by the minimum interrupt rate, 
          the correction amount will be increased as needed to ensure that 
          alarms do not occur more often.  Consequently, the clock may not 
          be as accurate as specified by the maximum deviation.  This 
          ensures that alarms are not occurring so often that the HP 48 has 
          no time to do anything else (see the "Note" at the end of the 
          documentation). 
 
|C.STS|   Takes no input from level 1; provides 3 pages of status 
          information about the correction package. 
 
          All pages have this header: 
 
              Correction status     -N-    (Where N = 1, 2, or 3) 
 
          All pages have this foot: 
 
              prev:{up-arrow}  exit:{down arrow}  next:{right arrow} 
 
          The first page of status information looks like this: 
 
             Exact initiated(*): 
             9.1455  10.301989 
             Deviation:   0.000025 
             Min rate:    1.0000 
 
          The first two lines show the time and date of the first exact 
          synchronization.  If the display shows "none," an exact has never 
          been done.  If there is an (*), then 2 or more exacts have been 
          done and the package is fully activated.  If there is no (*), 
          only one exact has been done (errors are being accumulated but no 
          corrections are being done yet).  The third line shows user 
          specified maximum clock deviation (1/4 second in example).  The 
          fourth line shows the user specified minimum interrupt rate (1 
          hour in example). 
 
          The second page contains adjustment data: 
 
             Timezones:    0.0000 
             Errors:       0.001890 
             Timebase:  1718.3909 
 
          The first line shows the total accumulated time-zone changes. 
          The second line shows the total accumulated error corrections 
          (18.9 seconds in example).  The third line shows the total time 
          included in the time base (1718 hours, 39 minutes, and 9 seconds 
          in example). 
 
          The third page contains correction data: 
 
             Next correction: 
             11.1644  1.101990 
             Repeat:     22.4520 
             Adjust:      0.000025 
 
          The first line may be either "Next correction:" (the next 
          correction time is displayed) or "Adjust suspended:" (the time 
          that the corrections were suspended is displayed).  The third 
          line shows the repeat interval of the alarm (22 hours, 45 
          minutes, and 20 seconds in example).  The fourth line shows the 
          correction adjustment amount (+1/4 second in example). 
 
          If a status is displayed for 1 minute with no keys pressed, it 
          times out and exits. 
 
|C.SSP|   Suspends the correction alarm (if corrections are active). The 
          status report will indicate the time of the suspension. If the 
          |C.SET|, |C.ADJ|, or |C.XCT| keys are used while the correction 
          alarm is suspended, the results may not be correct. (|C.SSP| is 
          found on page 2 of the menu.) 
 
|C.CNT|   Resumes (continues) the correction alarm cycle if corrections are 
          active. Any missed corrections will be made and the next 
          correction alarm will be set up. (|C.CNT| is found on page 2 of 
          the menu.) 
 
 
Application Menu Keys 
--------------------- 
 
The |C.TLS| menu key contains subroutines and variables used internally by 
the application. You do not need to use them to run the application. 
 
--------------------------------------------------------------------------- 
 Note:  The alarm should work regardless of the directory path when the 
        alarm occurs, and it should leave things as they were when it 
        happened.  However, if the HP 48 is off when the alarm occurs, it 
        will be turned on and left on until the HP 48 times out. If alarms 
        occur at a rate less than the time-out period, the HP 48 will 
        always be on. If anything is being done when the alarm occurs, the 
        alarm will either not process immediately (when a program is 
        running, the alarm doesn't process until the program terminates), 
        or it will abort what is happening (edits will be terminated as if 
        the [ATTN] key had been pressed). 
--------------------------------------------------------------------------- 
 
V. 1.0 04/26/92 04:09 PM