INPRT.DOC File 
 
                  (c)  Hewlett-Packard Company, 1990 
 
 
OVERVIEW 
-------- 
 
The INPRT application reads infrared (IR) printer output from different 
Hewlett-Packard calculators into the HP 48 stack.  INPRT assumes that the 
incoming bytes would print with the Roman 8 character set on an HP 82240 
printer, and it remaps these bytes to the HP 48 character set (ISO 8859 
Latin 1). 
 
 
PROCEDURE 
--------- 
 
These are the steps for transferring IR printer output to the HP 48: 
 
 1.  Transfer the INPRT file from your computer to the HP 48. (Use binary if 
     you're transferring INPRT from the HP 48.) The {INPRT} menu label will 
     show up in your HP 48 VAR menu. (If your calculator has a double- 
     spaced print mode, set it to single-spaced print.) 
 
 2.  Line up the calculators.  (See "Alignment Instructions" below.) 
     [Note: Do not remove the HP 48SX's port cover; I/R transfer actually 
     works better with the port cover in place.  -jkh-] 
 
 3.  Press {INPRT} on the HP 48.  (INPRT terminates in 10 seconds if no IR 
     output is received.) 
 
 4.  Execute the print command on the other calculator. 
 
 5.  Repeat steps 2 through 4 as needed to transfer additional output. 
 
RESULTS 
------- 
 
When the transfer is complete, the HP 48 returns the received data to the 
stack in the form of a string to level 2 and a flag to level 1.  If the flag 
is 0, uncorrectable transfer errors were detected; if the flag is 1, there 
still may be missing bytes. The 1 means that each byte that was detected was 
received correctly.  You should still check the received data since there 
may be a linefeed in strings, names, expressions, etc. more than 24 
characters long. If the flag is 0, each byte that was not correctable is a 
gray blot (character number 127) in the level 2 string. 
 
 
ALIGNMENT INSTRUCTIONS 
---------------------- 
 
The calculators should be no more than 0.5 inches (1.3 cm) apart for the 
transmission.  Also, other alignment issues apply to several calculators: 
 
  o  For the HP 41:  The IR printer module should be in one of the top 
     ports, and the shiny "IR cone" in the center of the module should be 
     aligned between the E and T of HEWLETT on the HP 48's Hewlett-Packard 
     logo. 
 
  o  For the HP 27S, HP 17B, and HP 42S:  The calculator must be raised 0.3 
     inches (0.75 cm). The center of the LED (which is located at the top 
     end of the calculator in line between the E and W of HEWLETT) should be 
     aligned between the E and T of HEWLETT on the HP 48's Hewlett-Packard 
     logo. 
 
  o  For the HP 28, HP 18C, and HP 19B:  Just line up the calculator's LED 
     between the E and T of HEWLETT on the HP 48's Hewlett-Packard logo.