(Files.hp48) 
Item: 106 by akcs.softcalc@hpcvbbs.cv.hp.com [brian maguire] 
Subj: UITL.LIB - user interface toolkit 
Date: 17 Dec 1992 
 
Here's a user interface toolkit that I wrote close to 2 years  
ago.  This library deals heavily with the user interface,  
which is comprised of the display, keyboard, and beeper.  It  
was written before HP released their development tools, when I  
was still learning the internals of the 48, so some of the  
commands may not be up to par.  Still, most of the commands  
perform powerful functions that are missing from the 48's  
built-in command set. 
  
I originally planned on releasing this library as part of a  
commercial software package containing various toolkits, but  
decided not to because of the poor market for toolkit  
libraries.  Instead, I'm releasing this library in the public  
domain.  It may be used and copied freely as long as it is  
NOT used commercially or as part of a third party software  
package without prior written permission by the author.  Nor  
may the user be charge for this library beyond the cost of  
reproduction. 
  
Remember, this is still my code, and I retain all rights to  
it.  If you would like to use portions of this library for any  
application that is sold commercially or posted to the public  
you MUST get my permission.  I'm a pretty easy going guy and I  
do n't mind other people using my code, but I would like to  
know when portions of it get used, so please send me e-mail to  
the fact (this is not an option!). 
  
This software is presented as is, without warrantee of any  
kind.  The user bears all risk.  To the best of my knowledge,  
this code will work correctly on ROM versions A-J.  Because  
this code was written before HP release their development  
tools, it m ay contain unfrozen entry points that may or may  
not cause the 48 to crash on future ROM versions. 
  
If you have questions about ROM version compatibility or you  
have problems/questions about any of the included commands,  
feel free to contact me. 
  
 
UITL : User interface tool library 
 
Copyright 1991 Brian J. Maguire 
All Rights Reserved 
 
 
The UITL library and this manual are presented as is, without 
warrantee, express or implied.  Neither the software nor manual 
may be copied, stored in a retrieval device, or used commercially 
without written permission of the author.  The user is granted 
limited use of this software for evaluation purposes only. 
Second parties may not have access to this software package.  The 
author retains the right to revoke the software package at any 
time unless otherwise stated.  Acceptance of this package 
constitutes agreement of these terms. 
A basic understanding of the 48 is expected by the user. 
 
Please forward comments or questions to... 
 
Brian Maguire 
139 Kingsbury 
Dearborn, MI 48128 
(313) 274-0428 
 
 
 
1.  PIXEL LOCATIONS 
 
Currently, the 48 uses two different graphic pointer.  A complex 
number specifies a pixel location as defined by PPAR while a list 
of two binary integers specifies a horizontal and vertical 
distance from the top corner. 
 
A new type of pixel location pointer is used in this library.  A 
single binary integer is used to specify both the horizontal and 
vertical distance from the top left corner.  The right most five 
nibbles specifies the vertical distance from the left side while 
next five nibbles defines the distance from the top.  For 
example, the list { #12345h #67890h } and the single binary 
integer #1234567890h define the same pixel.  As another example, 
the diagram shown below shows a 15 * 3 grob.  The pixel list 
representing the marked pixel is { # 9h, # 2h }.  The same pixel 
is also represented by single binary integer # 900002h. 
 
 
       ********************************************** 
       *  *  *  *  *  *  *  *  *  *  *  *  *  *  *  * 
       *  *  *  *  *  *  *  *  *  *  *  *  *  *  *  * 
       ********************************************** 
       *  *  *  *  *  *  *  *  *XX*  *  *  *  *  *  * 
       *  *  *  *  *  *  *  *  *XX*  *  *  *  *  *  * 
       ********************************************** 
       *  *  *  *  *  *  *  *  *  *  *  *  *  *  *  * 
       *  *  *  *  *  *  *  *  *  *  *  *  *  *  *  * 
       ********************************************** 
 
 
NOTE: In order to read a binary integer used in graphic 
operations your 48 should be set to HEX mode.  Likewise, your 
wordsize should be set to at least 40 bits to avoid loosing data. 
 
 
 
2.  BANG OPERATIONS 
This library contains commands that perform "bang" operations on 
graphics.  Unlike most 48 commands, which return a new object, a 
bang type operation directly alters an object in memory. 
Therefore, an bang operation cannot be undone with the UNDO or 
LAST operations.  Likewise, all pointers that referenced the 
original objects will point to the altered object.  All library 
commands that perform bang operations end with the "" character. 
If this character does not appear in the font used by you 
computer it is an upside-down "!".  This character can be typed 
into the 48 by pressing [Right-Shift] [DEL] while the alpha shift 
is on. 
 
As an example of a bang type operation, if a grob is stored in 
'G1', recalled to the stack, and used as a target grob by a bang 
type command, the grob in 'G1' is directly altered.  As another 
example, the program << LCDGROB { #5h #5h } { #20h #20h } GNEG 
>> recalls the LCD graphic object and negates a square section. 
 
Because they do not create a new copy of a target object, bang 
operations can save considerable time.  They also conserve memory 
since only one copy of the target object needs to exist in 
memory.  In addition, they allow direct manipulation of the LCD, 
PICT, and MENU grobs (see the library commands LCDGROB, PICTGROB 
and MNUGROB). 
 
 
 
3.  DISPLAY GROBS 
 
The 48 uses three GROBs to store display information.  The first 
grob is used to display the stack and status area.  It is 
normally 131 * 56 pixel, but can be resized to any dimensions. 
The library command LCDGROB returns the actual LCD grob (not a 
copy). 
 
The second grob contains the menu information and is normally 
displayed on the bottom 8 pixels of the display screen.  The menu 
grob is normally 131 * 8 pixel, but can be resized to any 
dimension.  The library command MNUGROB returns the actual menu 
grob. The built-in command LCD-> returns a copy of both the 
status/stack and menu GROBs overlaid on a 131 * 64 grob. 
 
The final display grob is PICT.  It is used for graphing and can 
be dimensioned to any size.  The library command PICTGROB returns 
the actual PICT grob. 
 
When any on the three display GROBs are recalled to the stack 
using the appropriate library command and used as a target grob 
by a bang command the display grob is directly altered. 
 
When using the LCD grob and a target for a bang type graphic 
command only the top 56 pixel can be manipulated.  If you want to 
display graphic information on the lower 8 pixels without 
altering the menu grob you can resize the LCD grob using the 
library command LDIM64 and turn the menu display off using the 
command MOFF. 
 
 
 
4.  LIBRARY COMMANDS 
 
 
 
ABOUTUI 
Info screen 
 
 
ALMCAT 
Programmable alarm catalog 
 
 
 
ALRT? 
Returns alert message (low battery, etc.) and 1 or 0 
 
 
     -> String 1 
     -> 0 
 
 
 
BDKYBP 
If the beeper is turned on BDKYBP will beep.  Otherwise, the 
display flashes. 
 
Flag -56 set     ->   Screen flashes 
Flag -56 clear   ->   Bad key Beep 
 
 
 
BORDR 
If the input object is a grob, BORDR draws a box around the 
graphic by expanding it by one pixel on the top, bottom, left, 
and right and drawing a box.  If the real number (n) is on level 
one, the object on level two is converted to a grob using the 
font size(n) and centered in a box. 
 
Graphic   ->   Graphic 
Any, Real(n)   ->   Graphic 
 
 
 
BZYTGL 
If 0 is on level one the busy annunciator is turned off.  Any 
other real number will turn the annunciator on. 
 
Real(0 or not 0)  ->  Busy annunciator is turned on or off 
 
 
 
B->PX 
Converts binary pixel location into a pixel list. 
 
Binary   ->   List 
 
 
 
„CAT 
Programmable STAT catalog. 
 
 
 
CMD? 
Returns 1 if last command is on, otherwise 0 is returned. 
 
Last command flag   ->  Real(1 or 0) 
 
 
 
CMDSET 
If 0 is on level one, last command is turned on.  Any other real 
number turns last command off. 
 
Real(0 or not 0)   ->   Last command flag changed 
 
 
 
CMLBL 
Converts the object on level one into a circular menu label grob. 
This is a new style menu label.  See SMENU. 
 
Any   ->   Graphic 
 
 
 
CTRGROB 
If two reals are on levels one and two, the object on level three 
is converted into a grob and centered.  The real on level two is 
used as the font size while the real on level one specifys the 
grob's width. 
 
If a grob is on levels three and one, and a pixel location is on 
level two, the grob from level one is centered on the grob from 
level three using the location from level two as the center 
position. 
 
Any, Real(font), Real(width)   ->   Graphic 
Graphic, point, Graphic   ->   Graphic 
 
 
 
DEFKEYS 
Redefines the keyboard.  The new keyboard definition continues 
until [ON] is pressed or flag 9 is set.  Upon exiting the 
redefine keyboard the exit key and menu row are returned to 
levels two and one respectively.  The DEFKEYS parameters are as 
follows. 
 
 
5: Menu list 
4: Keyboard definition list 
3: Valid key object 
2: Invalid key object 
1: { Menu key toggle flag, Special menu flag } 
 
 
  A) Menu list 
 
The menu list is any standard menu key list or a special menu key 
list (see SMENU).  If it is a special menu list then the menu 
flag in the list on level one must be 1.  Shifted key definitions 
are not acceptable in the DEFKEYS menu list.  If you want to 
assign a shifted menu key you must do so in the keyboard 
definition list. 
 
  B) Keyboard definition list 
 
This list must contain (key assignment, keycode) pairs.  A key 
assignment can be any object, but should be a program or global 
name.  A keycode is the standard HP keycode where a key is 
represented by its row, column, and shift plane.  Alpha shifted 
keys cannot be defined.  If the list is empty only the default 
keys are defined.  They are [RIGHT SHIFT], [LEFT SHIFT], [NXT], 
[ON], and the menu keys. 
 
  C) Valid key object 
 
An object, such as a program or global name, can be defined as a 
valid key object.  This object will be executed only after a 
valid key is pressed.  Any object other than a program, global 
name, or local name will be ignored. 
 
  D) Invalid key object 
 
An object, such as a program or global name, can be defined as an 
invalid key object.  This object will be executed only after an 
invalid key is pressed.  If the object is not a program, global 
name, or local name, it will be ignored and the 48 will beep when 
an invalid key is pressed. 
 
  E) Key toggle flag 
 
If the key toggle flag is a nonzero number, a menu label will 
flash when its associated key is pressed. 
 
Special menu flag 
 
If the special menu flag is a nonzero real number, the menu list 
on level five is used to create a special menu using the SMENU 
library command.  Otherwise, the menu list is used to create a 
standard custom menu. 
 
list, list, obj, obj, list  ->  real, real 
 
 
DISP1 
Displays the object on level two using the small font size.  The 
real number from level one specifies the row number(1-9). 
 
Any, Real   ->   Object from level two is displayed 
 
 
 
DISP3 
Displays the object from level two on the stack display using the 
large font size.  The real number from level one specifies the 
stack level the object is displayed on. 
 
Any, Real   ->   Object from level two is displayed 
 
 
 
DMLBL 
Converts the object on level one into a directory stype menu 
label grob(normal menu label with bar on top). 
 
Any   ->   Graphic 
 
 
 
EQCAT 
Programmable equation catalog command 
 
 
 
EQWRTR 
Programmable command that edits an algebraic using the equation 
writer application.  If [ON] is used to exit the application, the 
original expression is returned on level two and 0 is returned to 
level one.  If [ENTER] is used to exit, the edited expression is 
returned to level two an 1 is returned to level one. 
Algebraic   ->   Algebraic' 1 
Algebraic   ->   Algebraic  0 
 
 
 
ERRMSSG 
Returns the error message string for the error number input on 
level one. 
 
Binary   ->   String 
Real   ->   String 
 
 
 
FLIP 
The grob on level one is rotated 180 degrees 
 
Graphic   ->   Graphic 
 
 
 
FREEZE? 
Returns real number 0 through 7 specifying the FREEZE display 
status.  See FREEZE in the owner's manual. 
 
Freeze display status   ->   Real(0-7) 
 
 
 
FTGL 
Toggles flag state 
 
Real(flag)  ->  Flag state is toggled 
 
 
 
GAND 
Graphic AND operator.  The grob from level one is ANDed with the 
grob from level three starting at the position on level two. 
Operates similar to the built-in command GOR. 
 
Graphic, List, Graphic  ->  Graphic 
Graphic, Complex, Graphic  ->  Graphic 
Graphic, Binary, Graphic  ->  Graphic 
 
 
 
GDEL 
Deletes section of grob.  The pixel locations on levels two and 
one specify the area to delete. 
 
NOTE: This is a bang operation. 
 
Graphic, List, List  ->  Graphic 
Graphic, Complex, Complex  ->  Graphic 
Graphic, Binary, Binary  ->  Graphic 
 
 
 
 
GETKEY 
Waits for key stroke and returns the key number and shift number. 
Keys are consecutively numbered from 1 to 49, starting with the 
top left corner and advancing from left to right, top to bottom. 
 
          ******************************* 
          *  1 *  2 *  3 *  4 *  5 *  6 * 
          ******************************* 
          *  7 *  8 *  9 * 10 * 11 * 12 * 
          ******************************* 
          * 13 * 14 * 15 * 16 * 17 * 18 * 
          ******************************* 
          * 19 * 20 * 21 * 22 * 23 * 24 * 
          ******************************* 
          *   25    * 26 * 27 * 28 * 29 * 
          ******************************* 
          *  30 *  31 *  32 *  33 *  34 * 
          ******************************* 
          *  35 *  36 *  37 *  38 *  39 * 
          ******************************* 
          *  40 *  41 *  42 *  43 *  44 * 
          ******************************* 
          *  45 *  46 *  47 *  48 *  49 * 
          ******************************* 
             Sequential key numbers 
 
 
Keyboard  ->  Real(key, 1-49), Real(shift, 0-6) 
 
 
 
GKEEP 
Clears all pixels in a grob except those bounded by the 
rectangular region defined by the pixel locations input on levels 
one and two.  This is not a bang operation. 
 
Graphic, point, point  ->  Graphic 
 
 
 
GNEG 
Inverts all pixel in the rectangular region defined by the pixel 
locations input on levels one and two. 
 
NOTE: This is a bang operation 
 
Graphic, point, point  ->  Graphic 
 
 
 
GOR 
Performs OR operation exactly like the built-in command GOR 
except GOR is a bang operation. 
 
Graphic(target), point, Graphic  ->  Graphic 
 
 
 
->GRB 
The object on level two is converted into a grob.  The real 
number on level one(1-3) defines the font size.  This command is 
similar to the built-in command ->GROB with one exceptions. 
Unlike ->GROB, ->GRB recognizes carriage returns. 
 
Any, Real(1-3)  ->  Graphic 
 
 
 
GREPL 
Replaces a rectangular section in a grob exactly like the built- 
in command REPL except REPL is a bang operation. 
Graphic(target), point, Graphic  ->  Graphic 
 
 
 
GRID 
Draws a grid on LCD. The pixel location input on level three 
defines the top left corner.  The list or binary on level two 
defines the pixel distance between horizontal and vertical grid 
lines respectively.  Finally, the list or binary on level one 
defines the number of horizontal and vertical boxes contained in 
the grid. 
 
NOTE: An error will result if the bottom right corner of the grid 
is off the screen. 
 
List, List, List  ->  Draws grid on LCD 
Binary, Binary, Binary  ->  Draws grid on LCD 
 
 
 
GXOR 
Performs XOR operation exactly like the built-in command GXOR 
except GXOR is a bang operation. 
 
Graphic(target), point, Graphic  ->  Graphic 
 
 
 
HMRR 
This command creates a horizontal mirror image of the grob on 
level one. 
 
Graphic  ->  Graphic 
 
 
 
HOLD 
Similar to the built-in command FREEZE, HOLD holds, or maintains, 
the current display.  Unlike FREEZE, which updates the screen 
when any key is pressed, the display is not updated until an 
object is executed or the [ON] key is pressed.  The display is 
maintained similar to the message screens in the TIME, STAT, and 
PLOT menus.  The area to be held is defined by a real number 
between 0 and 7 (see FREEZE in owner's manual). 
 
Real(0-7)  ->  Sets hold status 
 
 
 
HOLD? 
Returns a real number(0-7) specifying the HOLD display status. 
See HOLD. 
 
Hold display status  ->  Real(0-7) 
 
 
 
IMLBL 
Converts any object into an inverse menu label grob (labels used 
in solver menu). 
 
Any  ->  Graphic 
 
 
 
IORCL 
Recalls IOPAR.  If IOPAR does not exist, it is created in the 
home directory. 
 
-> List 
 
 
 
IRPT 
IRPT is a must for programs that have a long run time.  It allows 
you to interrupt a program, perform other calculations, and then 
restore the original program environment. 
 
If the key buffer is empty no action occurs.  If however, a key 
has been pressed, the program is interrupted by saving and 
clearing the stack, saving the display, and halting the program. 
You can inspect the state of the stack before the program was 
halted with the library command IRPTSTK.  Entering KILL will 
abort the program while entering CONT will restore the stack and 
display, and continue the program.  When CONT is entered the 
display will jump slightly.  This is completely normal. 
 
Keyboard  ->  Enters the Interrupt environment if a key is 
pressed 
 
 
 
IRPTSTK 
Returns the stack before a program was interrupted with the 
library command IRPT.  The error message "Invalid Environment" is 
displayed if IRPT is not active. 
 
NOTE: IRPTSTK does not clear the current stack.  It adds the 
contents of the stack before an interrupt to the current stack. 
If you want the current stack replaced with the interrupt stack 
use the sequence CLEAR IRPTSTK. 
 
-> Stack before interrupt 
 
 
 
KEYRPT 
As long as the key number input on level one remains pressed 
KEYRPT repeatedly evaluates the object on level two.  Regardless 
of whether the key number from level one is pressed, the object 
on level two is evaluated at least once.  The key number must be 
in the standard HP key format(rowcol,shift). 
 
Global, Real  -> 
Local, Real  -> 
Program, Real  -> 
 
 
 
KEY-> 
Converts 48 key number (rowcol.shift) into consecutive key number 
and shift number.  See GETKEY for explanation on consecutive key 
numbers. 
 
Real  ->  Real, Real 
 
 
 
…KEY 
Returns the alpha string assigned to the HP key 
number(rowcol.shift) on level one.  The strings returned for 
shift numbers .1 through .3 are the same as those returned for .4 
through .6. 
 
Real  ->  String 
 
 
 
->KEY 
Converts a consecutive key number and shift number into a 
standard HP key code.  See GETKEY for an explanation on 
consecutive key numbers. 
 
Real, Real  ->  Real 
 
 
 
LBOX 
Draws a box on LCD.  The pixel locations input on levels one and 
two define opposite corners. 
 
point, point  -> 
 
 
 
LCDGROB 
Returns the actual grob(not a copy) defining the LCD(stack) 
display.  Its value continually changes every time the stack 
display changes.  To see how this works, key in LCDGROB DUP and 
enter the graphic environment ([orange shift] [left arrow]).  Now 
place the grob from level one on PICT ([blue shift] [up arrow] 
[blue shift] [left arrow] NXT NXT REPL ).  The last stack display 
is placed on the screen.  Now exit the graphic environment (ON) 
so the stack display can be updated.  Finally enter the graphic 
environment again and place the grob from level one on PICT as 
before.  This time a different value is placed on the screen. 
When used as a target grob by a bang command, the LCD grob is 
directly altered. 
 
-> Graphic 
 
 
 
->LCDR 
Replaced the LCD(stack) display with the graphic input on level 
one like the built-in command ->LCD except for several 
differences.  ->LCDR does not clear the display first, and grobs 
smaller than 131 pixel wide and 56 pixels tall are placed on top 
of the existing display. 
 
Graphic  -> 
 
 
 
LCMD 
Returns the last command line as a string.  If last command is 
turned off an empty string is returned. 
 
-> String 
 
 
 
LDIM56 
Redimensions the LCD(stack) grob to 56 pixel in height.  This is 
its default size. 
 
LDIM64 
Redimensions the LCD(stack) grob to 64 pixel in height.  This 
allows you to display graphics in the menu area(the menu display 
must be turned off using the library command MOFF). 
 
NOTE: You should reset the display with LDIM56 when exiting a 
program. 
 
 
 
LELINE 
The line connecting the two pixel locations input on levels one 
and two are erased on the LCD(stack) grob. 
 
point, point  -> 
 
 
 
LINEQ 
Returns the equation of the line passing through the two points 
defined by the complex numbers (pixel locations) input on levels 
one and two. 
 
Complex, Complex  ->  Algebraic 
 
 
 
LLINE 
Draws a line on the LCD(stack) grob connecting the pixel 
locations input on levels one and two.  The pixel locations 
cannot be outside the LCD grob. 
 
point, point  -> 
 
 
 
LSTKEY 
Returns the standard HP key number of the last key pressed in the 
DEFKEYS environment and the last menu row (see DEFKEYS).  The 
error "Invalid Environment" will occur if the DEFKEYS environment 
is not active. 
 
-> Real, Real 
 
 
 
LSTSTK 
Restores last stack as if [orange shift] [2] had been pressed. 
 
 
 
LSTSTK? 
Returns 1 if last stack is active, otherwise returns 0. 
 
Last stack flag  ->  Real(1 or 0) 
 
 
 
LTLINE 
Toggles the pixels on the LCD(stack) grob that lie on the line 
connecting the pixel locations input on levels one and two.  The 
pixel locations cannot be outside the LCD grob. 
 
point, point -> 
 
MDISP 
Displays the object from level one on the menu grob using the 
small font size. 
 
Any  ->  Object displayed in menu area 
 
 
 
MKY¤ 
Toggles a menu label from white on black to black on white and 
back to white on black.  The real number 1 though 6 defines the 
menu label to be toggled.  Any number less than 1 will toggle the 
first menu label.  Likewise, any number greater than 6 will 
toggle the last label. 
 
Real(1-6)  ->  Menu label is toggled 
 
 
 
MLBL 
Converts the object on level one into a normal menu label grob. 
 
Any  ->  Graphic 
 
 
 
MNUGROB 
Returns the actual grob(not a copy) defining the menu display. 
Its value continually changes every time the menu display 
changes.  To see how this works, key in MNUGROB DUP and enter the 
graphic environment ([orange shift] [left arrow]).  Now place the 
grob from level one on PICT ([blue shift] [up arrow] [blue shift] 
[left arrow] NXT NXT REPL ).  The last menu display is placed on 
the screen.  Now exit the graphic environment (ON) and copy the 
current menu display to temporary memory (NEWOB).  Finally, enter 
the graphic environment again and place the grob from level one 
on PICT as before.  This time a different value is placed on the 
screen.  When used as a target grob by a bang command, the menu 
grob is directly altered. 
 
-> Graphic 
 
 
 
MNUROW 
Sets menu row.  The real number on level one specifies the new 
row.  1 sets the next row, 2 sets the previous row, and 3 sets 
the first row. 
 
 
REAL(-1,0 or 1)  ->  Changes current menu row. 
 
 
 
MOFF 
Removes the menu display from the screen and redimensions LCD to 
131 by 64.  See the section titled DISPLAY GROBS 
 
 
 
MON 
Displays the menu grob on the lower 8 pixels of the screen. 
MON? 
Returns 0 if the menu display is off.  Otherwise, 1 is returned 
 
Menu display(off or on)  ->  Real(0 or 1) 
 
 
 
MTWRTR 
Edits a matrix using the matrix writer application.  If [ON] is 
used to exit the application the original matrix is returned 
along with the real number 0.  If [ENTER] is used to exit, the 
edited matrix is returned with the real number 1. 
 
Array(1)  ->  Array(1), 0 
Array(1)  ->  Array(2), 1 
 
 
 
MUPDT 
Updates the menu display. 
 
 
 
NEWEQ 
Programmable NEW command from SOLVE menu. 
 
 
 
NEW„ 
Programmable NEW command from STAT menu. 
 
 
 
OMLBL 
Converts object on level one into an oval menu label grob.  This 
is a new style menu label (see SMENU). 
 
Any  ->  Graphic 
 
 
 
PELINE 
The line connecting the two pixel locations input on levels one 
and two are erased on PICT. 
 
point, point  -> 
 
 
 
PICT? 
Returns 1 is PICT is currently being displayed.  Otherwise, LCD 
is displyed and 0 is returned.  PICT displayed when a graph is 
drawn or the built-in command PVIEW is entered.  LCD is the 
default display.  It can be displayed within a program using the 
built-in command TEXT. 
 
    ->  Real 
 
 
 
PICTGROB 
Returns the actual grob(not a copy) defining PICT, the graphic 
display.  Its value continually changes every time the stack 
display changes.  To see how this works, purge PICT and recall it 
to the stack by entering PICT PURGE PICTGROB.  Graphic 0 x 0 
should be displayed in level one.  Next redimension PICT by 
entering #131d #64d PDIM.  Graphic 132 x 64 should be displayed 
on level one now. 
 
When used as a target grob by a bang command, PICT is directly 
altered. 
 
-> Graphic 
 
 
 
PPARCL 
Recalls PPAR.  If it does not exist it is created in the current 
directory. 
 
-> List 
 
 
 
„PRCL 
Returns the STAT parameter list.  If „PAR does not exist in the 
current directory, it is created. 
 
-> List 
 
 
 
PRESET 
Resets PICT and PPAR to their default values. 
 
 
 
PRTRCL 
Returns the Print parameter list.  If PRTPAR does not exist in 
the home directory it is created. 
 
PX* 
If two pixel lists are on levels one and two, their corresponding 
components are multiplied.  If levels one and two contain a pixel 
list and a real or binary number, each component of the pixel 
list is multiplied by the number. 
 
List, Real  ->  List 
List, Binary  ->  List 
List, List  ->  List 
Real, List  ->  List 
Binary, List  ->  List 
 
 
 
PX+ 
Adds corresponding components of two pixel lists. 
 
List, List  ->  List 
 
 
 
PX- 
Subtracts corresponding components of two pixel lists. 
 
List, List  ->  List 
 
 
 
PX/ 
If two pixel lists are on levels one and two, each component on 
level two is divided by the corresponding component on level one. 
If level two contains a pixel list and level one contains a real 
or binary number, each component of from level two is divided by 
the number on level one.  Likewise, if a real or binary number is 
on level two and a pixel list is on level one, a new pixel list 
whose components are calculated by dividing the number from level 
two by the corresponding components on level one is returned. 
 
List, Real  ->  List 
List, Binary  ->  List 
List, List  ->  List 
Real, List  ->  List 
Binary, List  ->  List 
 
 
 
PX? 
Return 1 if the pixel location input on level one on.  Otherwise. 
0 is returned. 
 
Graphic, point  ->  Real(1 or 0) 
 
 
 
PXOFF 
Turns off one pixel in the grob from level two using the pixel 
location input on level one. NOTE: This is a bang operation 
 
Graphic, point  ->  Graphic 
 
 
 
PXON 
Turns on one pixel in the grob from level two using the pixel 
location input on level one.  NOTE: This is a bang operation 
 
Graphic, point  ->  Graphic 
 
 
 
PX->B 
Converts a pixel location from a list type to a binary integer 
type. 
 
List  ->  Binary 
 
 
 
PX->R 
Converts a pixel list into two real numbers. 
 
List  ->  Real, Real 
 
 
 
R->PX 
Converts two real numbers into a pixel list. 
 
Real, Real  ->  List 
 
 
 
SMENU 
Creates a custom menu from a list much like the built-in command 
MENU with the following exceptions. 
If the object used to create a menu label is a global name, a 
standard label is created.  All other objects are converted to a 
string.  Next, the first character is striped and, if it matches 
one of the control characters listed below, a special menu label 
is created.  Otherwise, a standard label is used. 
 
"D" - Directory Label 
White letters on a black box with a bar on top. 
 
"I" - Inverse Label 
Black letters on a white background, inside a box.  The same 
label that are used in the solver menu. 
 
"O" - Oval Label 
White letters on a black oval. 
 
"C" - Circular Label 
Black letters on a white background, inside a rounded cornered 
box. 
 
"F" - Flag Indicator Label 
An integer between -64 and 64, excluding 0, must follow the 
character "F".  This integer specifies a flag.  The remaining 
portion of the string is used as the name for the label.  If the 
specified flag is set, a small white box will appear on the right 
side of the label.  As an example, "F-20PRG" will create a 
standard label with the name PRG.  If flag -20 is set, a box will 
appear after the name. 
 
Three predefined menu labels can be displayed by using special 
strings. 
 
"BLANK" - No menu box 
 
"BOX"   - White label in black box 
 
"GREY"  - Grey pattern box 
 
As an example of how SMENU works, try creating the following 
menu. 
 
{ "BOX" "GREY" "BLANK" "DDIR" "OCRV" "ISOLV" { "F-56BPOFF" << -56 
FTGL >> } "CSEE" "ASTD" PRG1 } 
 
 
List  ->  Creates custom menu 
 
 
 
 STK 
Programmable interactive stack command. 
 
 
 
STKUPDT 
Updates the stack display. 
 
 
 
STSUPDT 
Updates the status display. 
 
 
 
UNHOLD 
Removes the HOLD and FREEZE display flags specified by the real 
number on level one.  See FREEZE in the owners manual and HOLD in 
this manual. 
 
Real  ->  Clears HOLD and FREEZE display status. 
 
 
YES? 
Create a custom menu with "YES" on the left and "NO" on the 
right.  Pressing "YES", "NO" or [ON] exits the routine.  If "YES" 
is pressed the real number 1 is returned to level one.  Likewise, 
pressing "NO" or [ON] returns 0 or -1 respectively. 
 
Menu prompt  -> Real(-1, 0 or 1)