F83 TUTOR
                               by
                           BILL KIBLER
                         (c) 1986, 1987



INTRODUCTION

F83  TUTOR  is a self paced tutorial for the public domain  Forth 
program F83. F83 is a Forth based operating system and programing 
language.  This  version contains the standard word set Forth-83 
making  the program structure different from previous  standards. 
Major  changes between F83 and older versions of Forth  (FIG  AND 
79) make it necessary for all users,  both users new to Forth and 
FIG or Forth-79 users, to study and understand these differences. 
This program,  TUTOR,  will help new users of F83 learn to use it 
more efficiently and faster. 

The  "CHAPTERS" are organized with the understanding that a  user 
will have a copy of "STARTING FORTH" by Leo Brodie.  Each chapter 
consists of a GLOSSARY,  LIST OF TERMS, and TEXT ( in that order) 
based on the books organization.  Enough text is provided to  get 
an understanding of the topic and the book should not be required 
by  experienced Forth programmers.  Experienced programmers  will 
find the GLOSSARY section to be the most important aspect of this 
program.  The  program is based on the F83 word set and not those 
of FIG or Forth-79.

TUTOR is very easy to use and can be modified to add more  infor
mation  or scanning functions.  Experienced Forth programmers can 
use this program by entering the following:
          A>F83
          OPEN TUTOR.BLK  
          1 LOAD
Use the space bar to scan through the screens of information, and 
then  choose  a chapter to start your review.  For novice or  new 
users  of Forth a more detailed introduction follows in the  next 
section.

GETTING STARTED

Forth  is  both a programming language and  a  operating  system. 
TUTOR  is a simple F83 tutorial consisting of "WORDS" that handle 
the  information and tutorial screens based on the book  "STARING 
FORTH".  All  new or novice users should use this book,  as  they 
will find the tutor text information to be too brief for  develo
ping  a good understanding of Forth.  The screens of  information 
will help you understand Forth and will help point out the diffe
rence  between  F83  and the FIRST EDITION of the  book.  As  you 
follow  through  the screens you will notice that  some  glossary 
words will be different from those in the book,  these  represent 
the  new  word set as specified in the Forth-83  standard.  Those 
readers  using the SECOND EDITION of "STARTING FORTH"  will  find 
tutor to be an on disk review of the book.

To  better  understand this program an introduction to Forth  and 
its  structure  is needed.  Forth is a stack  oriented  language. 
Values  are  placed on the stack and then WORDS  are  entered  to 
perform actions on these values. The most simple use would be the 
addition  of  two numbers.  To add the numbers 4 and 7 you  would 
enter 4 7 + . and Forth would return 11 ok. Considerable problems 
occur  for new Forth users over the use of text type  symbols  to 
represent  words or commands.  The sample used a .  to denote the 
command  to  print  the top item of the stack  on  the  computers 
screen.  In displaying information about Forth it is very hard in 
a document to prevent confusion between Forth WORDS and the  text 
used  to display them.  Until you can know which words are  Forth 
WORDS  and  which are text words,  reference to the text book  is 
needed.  The book puts a block around each word when described in 
the text, an option not available on all computer systems.

This problem of variations in computer  systems and languages has 
been handled by the FORTH INTEREST GROUP in respect to Forth. The 
term  FIG  Forth refers to an early set of Forth WORDS  that  the 
interest  group  established as the first standard Forth  system. 
The  next  standards  meeting  in  1979  made  some  changes  and 
established a new Forth standard called Forth-79.  The latest and 
one that this tutorial is intended to help is the 1983  standards 
meeting version,  this word  set is called Forth-83.  The program 
this  tutorial is for is F83 which is a public domain version  of 
Forth containing the Forth-83 word set.

Although  a  few  words  have been changed  between  standards  a 
considerable  amount of similarity exists between the  standards. 
F83  is very popular because of its cost and  utilities contained 
within  the  program.  F83  contains not only the  normal  screen 
editor and assembler, but also debugger, disassembler, and multi-
tasker  utilities.  There are many commercial and  public  domain 
versions of Forth,  in fact there is a version of Forth available 
for  almost  all  the  operating systems  and  computer  hardware 
systems currently being produced.  Forth is a  small,  fast,  and 
extensible  operating environment.   It has been used in numerous 
special  applications,  such as space vehicles,  where speed  and 
reliability are major concerns. The extensible nature of Forth is 
its most important aspect.

LOADING TUTOR AND EXTENSIONS

The  Forth  system can be stand-alone or work within an  existing 
operating system.  All Forths store information in SCREENS  which 
are  1K in size ( 1024 bytes).  When a screen is displayed it can 
consist of 60 characters across and 16 lines down ( one character 
is  equal to one byte of information).  The F83 operating  system 
stores  the  screens  on disk as BLOCKS of data (1  screen  is  1 
block).  Typically the file name will have an extension of BLK to 
indicate  Forth  information.  The  TUTOR program  is  stored  as 
"TUTOR.BLK" on most systems. Starting F83 would be done by typing 
F83 at the system prompt and using "RETURN"  on most MSDOS or CPM 
systems. 

To load the TUTOR program after starting F83, the file must first 
be OPENED,  you do this by typing "OPEN TUTOR.BLK" and a  return. 
Next  it is necessary to LOAD the Forth extensions which are used 
by  the TUTOR program.  You type  "1 LOAD" and return, this  will 
start the TUTOR program and give you more information about  F83. 
Should your system be different or you are new to computers,  you 
may  need to review and use programs supplied by the system manu
facturer until you understand and feel comfortable with your  new 
computer.  Some  versions of F83 use different words to open  and 
load files (due to operating system designs), check with your own 
documentation on specific instructions.

The   "1 LOAD" command loads screen 1 into memory and then starts 
compiling the new word definitions contained in it.  These  words 
are extensions to the orginal F83 word set.  After being compiled 
they  are part of the Forth DICTIONARY and can be used as if they 
were part of the original program. This ability to add words  and 
EXTEND  the dictionary is the source of the term "extensibility". 
Programs  are  created  by  extending  the  dictionary  with  new 
functions  and routines. The TUTORS new words are contained in  4 
of the first 10 screens and can be changed should you desire some 
special way of handling the tutor screens.

TUTOR WORDS

The new words are:

HELP      Loads the information about the tutor program and 
          general F83 words. The last screen lists words used by           
          tutor and relating to "STARTING FORTH".

START-TUTOR   Will start displaying the introduction to tutorial 
              information.

REPT      This command will display screens from the beginning 
          of the most recent chapter or group of screens. If CHP1 
          had been entered and you exited the listings to try a 
          F83 operation REPT will restarted at the first screen 
          of CHP1.

GET       GET will start displaying screens at the next one in 
          sequence. Using REPTs sample, if you had typed GET 
          instead of REPT you would get displayed the next screen           
          of information in CHP1.

21 TUTOR  Typing this will start displaying tutor screens 
          starting with screen 21 and continuing till the screen 
          contains $$. When you type CHP1 this word loads the 
          number of the first screen of chapter 1  on the stack 
          and then goes to TUTOR.

PRTSCR    This word will display the current GET and REPT 
          pointers.

LIST      Forths normal internal word for displaying screens of 
          information. Use this word whenever you want to view a 
          single screen. TUTOR uses a modified version of LIST 
          for displaying multiple screens.

10 90 INDEX    Use this input command line to get a list oF 
               "INDEX" lines (line 0 and NOT printed by tutor) of 
               screens 10 through 90 (the text screens). Line 0 
               is generally used as a descriptive line of what 
               the screen contains.

ESC       Using the ESCAPE key will end the display of 
          information, so that you can then tryout some of what 
          you just learned in the text.


ADVANCED INFORMATION

TUTOR uses most of the normal F83 words to perform its functions. 
A  major advantage of the tutor program is to retain easy  access 
to  the  normal F83 functions.  The tutor program will display  a 
series of screens starting with glossary information. Experienced 
programmers will find this part most helpful in learning the  new 
F83 words.  When finished displaying text screens, the F83 prompt 
"ok" will indicate completion of the lesson.  At this point  any 
F83  commands can be used.  Individual screens can be repeated by 
using the list function.

A  number  of blank screens have been provided at the end of  the 
program  for use during the learning sessions.  As new words  are 
created  in the lesson,  they can be saved in these screens  and 
auto loaded by adding "nn LOAD" to screen 5 (nn being first  used 
screen).  To  tie screens together use --> and F83 will  continue 
loading the next screen.

For  educators  and programmers,  they will find TUTOR to  be  an 
excellent  example of how to create a tutorial program in  Forth. 
It  is very hard to create a tutorial program in which  the  user 
has  enough control over the training structure that it can  meet 
their  needs adequately.  Most users of tutorials get  frustrated 
when  they can not exit or reenter the program at  will.  Usually 
lacking in tutorials is the ability to add sorting of information 
or  the creation of summary details.  Forth appears to handle all 
these  problems easily. Once the user understands Forths  use  of 
words it is possible to customize the tutorial for their personal 
needs.  An example of this would be the creation of a new word to 
keep  track of exiting and saving the screens pointers  to  disk. 
When  returning,  the user would type RESTART and the disk stored 
pointers would be restored,  and the next screen would be  loaded 
for viewing.

Although  not  shown  here,  interactive  uses  of  training  are 
possible. Forth has numerous words to allow for trapping of input 
data  and evaluating this information for correct  response.  The 
use of screens provides a simple way of grouping information such 
that  a  student who misses a concept (as found through  testing, 
see  screen  39)  could  be directed  back  to  that  information 
automatically. A new feature in F83 is the use of SHADOW screens. 
These  screens are from the original file UTILITY.BLK of F83  and 
contain  the  authors  comments on words in the  source  screens. 
Words  are  available  to toggle between these  screens  and  the 
source  screens.  Use of this feature may be helpful in  tutorial 
programs,  where  background or detailed discussions outside  the 
normal flow of instruction is needed.

CONCLUSION

The  creation  of  this  program was two  fold;  to  show  Forths 
abilities  in  creating  tutorials,   and  to  provide  on   disk 
information about F83. This project was part of a masters program 
in Computers and Education.  This is by no means a complete study 
of  using Forth for tutorials, of F83, or Forth.  I have released 
this version of TUTOR.BLK into public domain solely to help those 
who have had problems getting to understand the new words of F83. 
One  reason I feel that Forth has had problems being accepted  is 
the  lack  of tutorials accompanying new releases.  When I  first 
tried  F83,  I found the on disk documentation to be  inadequate. 
Although the use of shadow screens is an improvement, they do not 
equal the benefits of a good tutorial or disk based glossary. 

I am interested in your comments concerning this program and  any 
information  that  could make it better.  My  time  currently  is 
limited  and thus I can only take written queries.  I retain  all 
commercial rights to the screens 1 through 10,  as they represent 
the  idea  behind the tutorial,  as well as the information  con
tained  within  the  text  screens  not  directly  attributed  to 
"STARTING  FORTH" by Leo Brodie.  I am available  for  commercial 
activities  and would be willing to assist in developing  commer
cial tutorials.

          Bill Kibler
          Kibler Electronics
          PO BOX 487
          Cedarville, CA 96104

I  do  use  the  Sacramento Micro Users Group RBBS  and  can  get 
messages there: 300/1200 24 hrs (916)722-9337