NAME
	laplace - solve Laplace's equation

SYNOPSIS
	laplace  data  [ options ]

DESCRIPTION
	LAPLACE solves Laplace's equation in two dimensions, with Dirichlet
	boundary conditions on arbitrary boundaries.  In other words, it
	solves the partial differential equation
                                                    
                    2     2                         
                   d     d                  
                  --- + ---  V(x,y) = 0                  
                    2     2                          
                  dx    dy                            
                                                       
	where V(x,y) has specified constant values along each of one or
	more fixed curves.  In electrical terms, it will calculate the
	potential at various points on a cross section of a
	transmission line where the voltages and shapes of the
	perfectly conducting electrodes may be specified.

	LAPLACE calculates the potentials on a rectangular equally
	spaced grid of W * H points ranging from XMIN to XMAX and from
	YMIN to YMAX.  The user may use switch options to initialize
	these six parameters.  By default, W=H=32 and the grid spacing
	is large enough to just include the input file points.  LAPLACE
	will enlarge W or H, and then adjust XMIN, XMAX, YMIN, and/or
	YMAX to ensure that the grid spacing E is the same in both
	directions.

	After the problem is set up, only integer arithmetic is used. 

	Accuracy of the calculated potentials is to within a few
	percent for a set of boundaries within one grid spacing of the
	specified boundaries.

	LAPLACE calculates the potentials by means of relaxation 
	using the formula

		V(x,y) = ( V(x+e,y) + V(x-e,y) + V(x,y+e) + V(x,y-e) )/4

	with suitable adjustments on the edge of the grid to avoid 
	referencing nonexistent grid points.  This will always
	converge.  However, if the corners of the grid are not part of
	a specified boundary the convergence will be slow.  If one
	boundary encloses the others (a closed transmission line) the
	region outside that boundary is at a uniform potential and the
	convergence can be improved by adding to that outer boundary. 
	In other words, convergence will be slower with

	                  00       than with     0000000000000000
	                 0  0                    0     0  0     0
	                0    0                   0    0    0    0
	               0      0                  0   0      0   0
	              0   00   0                 0  0   00   0  0
	             0   0000   0                0 0   0000   0 0
	            0            0               00            00
	           0000000000000000              0000000000000000

	However, the convergence at the interesting points (between the 
	two boundaries) is not affected.  Adding an explicit rectangular boundary will also slow 
	the calculation.  The best solution is to set the outer boundary 
	at potential zero and use the -g switch (below).

INPUT DATA
	The data file is an ASCII list of X,Y pairs specifying the shape 
	of the boundaries.  The given points are assumed to be connected 
	by straight line segments.  The last point along each segment of the 
	boundary is followed by the potential along that segment, which may
	be in quotes.  For example, the data file:

			3  5
			7  5  "3"
			4  2
			6  2  "6"

	specifies this configuration:
	                                                              
	             |<----------  4  ----------->|                   
	 3 volts ->  ******************************   ---          
	                                               ^              
	                                               |              
	                                               |              
	                                               3              
	                                               |              
	                                               |              
	                                               V              
	        6 volts ->  ***************           ---           
	                    |<---  2  --->|                           
	                                                              
	                                                              
	...two parallel plates, of widths 4 units and 2 units, separated by
	3 units, one at 3 V and the other at 6 V.  (Note that the
	potentials, charge densities, and other calculated values are
	unchanged if the entire structure is enlarged by some factor.)
	Blank input lines are ignored.  Input lines beginning with a
	semicolon are echoed to the display but otherwise ignored.

	The input data file format is the same as for GRAPH, which can
	be used to display the file for debugging.

OUTPUT DATA
	The calculated potentials are written to a file with the same
	name as the data file, but the extension ".POT".  The first two
	lines specify the grid, and the remaining lines give the
	potentials at the grid points.  It has the following format:

		2g10.4i5
		2g10.4i5
		8g10.4
		8g10.4
		...
		8g10.4

	For example,

         0         1    8    minimum and maximum x values, width
         0         1    8    minimum and maximum y values, height
         0 2.1999E-1 3.5502E-1 4.5513E-1 5.4547E-1 6.4558E-1 7.8036E-1         1
 2.1999E-1 3.0496E-1 3.8981E-1 4.6490E-1 5.3583E-1 6.1079E-1 6.9551E-1 7.8024E-1
 3.5502E-1 3.8981E-1 4.3425E-1 4.7857E-1 5.2203E-1 5.6635E-1 6.1067E-1 6.4534E-1
 4.5513E-1 4.6490E-1 4.7857E-1 4.9310E-1 5.0750E-1 5.2191E-1 5.3558E-1 5.4523E-1
 5.4547E-1 5.3583E-1 5.2203E-1 5.0750E-1 4.9298E-1 4.7833E-1 4.6453E-1 4.5476E-1
 6.4558E-1 6.1079E-1 5.6635E-1 5.2191E-1 4.7833E-1 4.3389E-1 3.8933E-1 3.5453E-1
 7.8036E-1 6.9551E-1 6.1067E-1 5.3558E-1 4.6453E-1 3.8933E-1 3.0448E-1 2.1963E-1
         1 7.8024E-1 6.4534E-1 5.4523E-1 4.5476E-1 3.5453E-1 2.1963E-1         0

	The points are written in the following order:

		for (y=YMIN; y<=YMAX; y=y+EDGE)
			for (x=XMIN; x<=XMAX; x=x+EDGE)
				printf("%g10.4 ",V(x,y));

	...with newlines as needed to limit the output to 8 points per
	line.  The output file format is appropriate for CONTOUR, which can
	be used to calculate equipotentials.

OPTIONS
	-b	Displays a printer plot with zeros along the specified boundaries.

	-g	The edge of the grid is grounded (potential is 0).

	-m num	Extend the grid by the specified amount beyond the given 
		boundaries on all sides.  For open boundaries (for
		example, an isolated cylinder) it is more convenient to
		use the -g and -m switches than generating a box of the
		required size explicitly.  The resulting model will
		also be faster (because the boundary doesn't fall
		between grid points) and is easier to adjust.

	-p	Displays a matrix of the calculated potentials, with 
		XMIN,YMIN at the top left corner.

	-r	Periodically calculates and displays the number of times 
		each grid point has been updated and the root mean
		square value of the quantity

		   V(x) - (V(x+e,y) + V(x-e,y) + V(x,y+e) + V(x,y-e))/4

		which indicates the error remaining.

	-n <num>
		Sets the number of relaxation cycles N (default 64). 
		It should be approximately twice the larger of W and H.

	-w <num>
	-h <num>
		Set the number of grid points in the x and y direction
		(default 32).  Convergence is improved if W and H both
		have several factors of 2, allowing LAPLACE to
		initialize by recursively calculating on a coarser
		grid.  Calculation time is approximately proportional
		to W*H*N.  Internal table space limits the grid size to
		approximately W*H <= 10000.

	-x min [max]
	-y min [max]
		Specify the data range covered by the grid.  These are
		necessary, for example, for an open transmission line.

	-xs	The boundary conditions are symmetric across the line 
		x=xmin, which means the gradient has no x-component.

	-ys	Similarly for the line y=ymin.

	-?	Print a help message, such as the following:

		laplace   version 0.2
		usage: laplace [file][options]
		options are:
		  -b               display boundaries
		  -g               edge of grid is grounded (potential 0)
		  -p               display calculated potentials
		  -r               calculate and display residuals
		  -m  margin       amount to expand grid beyond given boundaries (default 0) 
		  -n  num          number of relaxation cycles (default 64) 
		  -h  num          height of grid in cells (default 32)
		  -w  num          width of grid in cells (default 32)
		  -x  [min [max]]  specify x range 
		  -y  [min [max]]  specify y range 
		  -xs              symmetric across the line x=xmin 
		  -ys              symmetric across the line y=ymin 

BUGS
	Subject to descretization errors.
	Should handle cylindrically symmetric 3D problems.

AUTHOR
	James R. Van Zandt <jrv@mitre-bedford>.
	Resale forbidden, distribution encouraged, comments welcome.