QED

This version of Quick Editor was derived from Nigel Gilbert's QED 4.6b.
It is a stripped down, quick, WordStar-like editor. It is essentially a
non-document insert mode editor without formatting commands. It does
extend on WordStar in a few areas however:

	1) -Jn command line option (or ^J editing option) will jump to
	   line "n"
	2) ^QKS switch controls auto-strip of trailing whitespace
	3) ^QKA switch controls auto-indent for block structured code
	4) ^QKT variable allows specifying TAB size
	5) ^QKL switch can shut off cursor line/column number display
	6) ^QKB switch can shut off backup file generation
	7) ^_ key will undo deletions so long as you don't leave the line
	7) -E command line option allows extended chars in text
	8) -R command line option for reverse video instead of bright

The following bugs have been fixed:

	1) TAB characters are portrayed correctly
	2) Screen is redisplayed on exit from ^QK (context) functions
	3) Help screen doesn't scroll off
	4) Recall buffer fixed (but still needs more work)
	5) Block menu hangup cured
	5) Block menu hangup cured

In addition, I've taken the liberty of making the following changes out
of personal taste:

	1) The verbosity of the ^K exit sequences have been reduced and
	   reorganized to more closely mirror those of WordStar
	2) ^KD (save & edit another file) and ^KS (save & resume) added
	3) Display attributes inverted to display text in low intensity
	4) Normal attribute altered to suit CGA

Use CTL(^) to enable or disable the help display.

If you have a RAM drive on M: and a Hercules monocrome card, the following
in a BAT file will use M: for the paging file (-dM option), use reverse
video (-r) instead of bright, and enable the help screen (-v) by default:

		QED %1 -r -dM -v

						Howard Vigorita
						NYACC, 2/87


                        DOCUMENTATION FOR QE AND QED
                       (J. W. Haefner - 7 August 1985)

This is documentation for the programs QE and QED:  two modifications of 
'e' version 4.6b.  QE is the modification for BDS-C and QED is the 
modification for DeSmet-C (hence the "D") under MSDOS version 2.x.  Since 
the basic structure of these modifications is still that of e, that 
documentation is relevant and I indicate here only the differences.

     'e' is a fine program, carefully written with good logical structure; 
however, editors are a personal matter and many features that I thought 
desirable were either missing, or awkwardly implemented.  Consequently, QE 
and QED is the result of an attempt to incorporate different and additional 
functions.  Most of these derive from WordStar, my favorite word 
processor.  Since the modifications are basically superficial and (at one 
level) "cosmetic", I have retained all references to Nigel Gilbert as the 
author and copyright holder.  Each file indicates that it is a modification 
of the original e (ver. 4.6).  On the other hand, my modifications conflict 
to some degree with the philosophy detailed in the documentation to the 
original 'e'.  Therefore, as indication of this possible conflict, I have 
given new names to these modifications.  The "Q" was originally to mean 
"quick", as my initial goal was to produce a smaller, faster version of 'e', 
as I thought it terribly long and slow.  I did not achieve this goal and 
instead came away with the perception that virtural memory editors must be 
this large and slow.  Mr. Gilbert has done an admirable job.

     The documentation is in two parts.  Part 1 describes the features 
common to both QE and QED.  Part two describes the features unique to QED.

I.   QE and QED
     A.   WordStar functions
     1.   SCROLLING:  ^W scrolls the screen down (i.e. UP through the text) 
and leaves the cursor on the line and column prior to scroll.  ^Z scrolls 
the screen up in the same manner.
     2.   Delete to End of Line: ^QY deletes all text from the cursor to the 
end of the line.
     3.   Delete Line: ^\ now deletes the current line (this makes it 
difficult to err, identical to my version of WordStar).  In 'e' v 4.6 and QE 
and QED lines deleted can be recovered if the cursor has not left its 
vertical sceen postion by typing ^N^_ (i.e. insert new empty line (^N), and 
recover (^_)).  A more elaborate UNDO function is implemented in 'e' ver 
4.8, but I don't feel a need for it.
     4.   Block manipulation: all of these are done through ^K as in 
WordStar.  These functions are: quit (Q, as in 'e'), save and exit (X, as in 
WordStar), file read (R), repeat a jump to the last jump line (J), and the 
block moves of 'e' (B).
     5.   Exit with Save: ^KX saves the file being edited and exits directly 
to the operating system.
     6.   BACKSPACE == LEFTKEY in all applications except find/replace 
editing.
     7.   QUICK functions;  analogous to WordStar, ^Q switches to other 
functions (i.e. environment (K), delete to end of line (Y), find (F), alter 
(A).
     8.   Top and Bottom o Screen:  ^Y moves cursor to top of screen, ^V
moves to bottom of screen.
     9.   KEYS:  wherever possible, I have used WordStar mnemonics for
control characters.  This is almost exact for the left hand; the right hand 
uses my own choices (e.g. move to left end of line = ^O, to right end of 
line = ^P, etc.   These are documented with a revised HELP display obtained 
via ^^ (difficult to type but the interface is so obvious that I rarely, if 
ever,  use HELP).  Below I give a map of the keys used in QE and QED.
     10.  READ ALL ON INITIAL LOAD:  As a matter of preference, the initial 
reading of a file from disk reads the entire file or as much as possible to 
fill memory before displaying the first page.  Alteration of this feature 
currently requires re-compilation, but it could easily be implemented as a 
command line option. 

     B.   Fixes to "bugs"
     1.   DIRECTORY:  'e' ver. 4.6 incorrectly calculated file sizes for my 
extended density 8" drives.  QE and QED fix this.  Moreover, I have added a 
directory masking option that permits the use of normal CP/M ambiguous file 
characters (*,?) to list a subset fo a directory.  In addition, 'e' did not 
print a complete directory if longer than one screenful.   I have modified 
the listing to pause after each page of files.
     2.   JUMP:  Use of "-Jn" on the command line where n is an integer 
causes the initial program load to jump to line number n, or the bottom of 
the file if n is greater than the number of lines in the file.  This is 
similar to 'e' ver 4.8. I have further modified the jump command to permit 
relative (+/-) jumps of any length (unlike page up or down; alas, not as 
useful as I had hoped).  Moreover, use of "^J,<CR>" or "^J,ESC" sets the 
"jumpto" variable to the current line.  Use of ^KJ repeats the last jump.  
Thus, a very simple "jump marker" is implemented as the following example 
illustrates:

               ^J,<CR> (mark this line),
               ...some editing...,
               ^U (top of file),
               ... more editing,
               ^KJ (back to line number marked earlier).

I find this feature very useful.  If editing following jump line marking 
adds or deletes lines, then ^KJ will not return to the identical text 
orginally marked (since that text now has a different line number).  This 
could be fixed in later versions.  More than one "jump marker" would be 
desirable.
     3.   REPEAT PAGING: In repeated use of page up or page down, 'e' ver 
4.6 causes all pages to be completely rewritten.  To speed up movement 
through a file, I allow the rewriting of a page to be interrupted if the 
next comand in the buffer is either "pageup" or "pagedown".  On the files 
QE2A and QE3A for terminals such as ADDS Viewpoint that do not have line 
insert functions, scrolling down (^W) requires re-writing the entire page, 
this is also enhanced by looking at the type-ahead buffer to interupt page 
re-writing if the next character is also for "scroll down".
     4.   CONTROL CHARACTERS:  Use of the sequence "ESC,char" to embed control 
characters into the text did not work properly on my 'e' ver. 4.6.  This has 
been fixed.
     5.   PRINTING CONTROL CHARACTERS:  'e' transmits only a few (none?) 
control characters to the printer.  QE and QED send most control characters 
so that dot matrix printers can be manipulated within the editor (e.g. set 
margins, condensed print, etc).
     6.   FAST DISPLAY 1:   QE and QED use the very nice algorithm in 'e' ver. 
4.8 to speed up console display using terminal cursor movement.
     7.   FAST DISPLAY 2:  I allow characters to be inserted into the type-
ahead buffer only after a line has been written except when inserting text.  
'e'  ver 4.6 checks for more input to buffer after every character is 
written.  This slows down the display.  Checking at the end of each line 
seems to cause no problems.  Moreover, 'e' ver 4.6 does not check for type-
ahead buffer overflow; this is a problem on fast terminals with repeat keys. 
Text insertion is checked after each character inserted so that fast typists 
do not lose characters.
     8.   HIGH-LIGHT CURRENT LINE:  The use of all text displayed in normal 
attributes or dimmed with current line normal as in verson 4.6 is controlled 
by a conditional compile statement.  'e' ver 4.8 uses an internal global 
variable permitting switching within sessions.  Since I never want that 
feature and since the fewer "if-checks" the better, I opted for the re-
compilation solution.
     9.   FIND/ALTER STRINGS:  'e' ver 4.6 allowed most control characters 
to be embedded in the string to find or alter, but escape (0x1b) was used to 
terminate the string and thus could not be searched for.  I implemented a 
kludge to work around this.  ^] is translated to 0x1b and embedded in the 
string.  A reminder of this is presented when the find/alter function is 
selected.  Also several other control characters can now be embedded that 
could not have been in 'e'.  Other changes to this function allow the 
"retrieve" function to replay the last previous string to find and alter
from the current positon of the cursor in the string to the end.  Thus, if 
the previous search string is non-empty, then the retrieve function prints 
the previous string from the current position to the end.  If the previous 
search string is empty or the cursor is at the end of the non-empty previous 
search string, then use of the retrieve function will embed the key code for 
the retrieve function into the search string.  For the file of terminal 
characteristics currently used, this is ^L, which is also form feed.  The 
current implementation allows primitive editing of the search string without 
re-typing the entire line.  Assume the previous search string is non-empty; 
the retrieve function (^L) will display to end; backspace and replace 
character to be edited; ^L will re-display the remainder of the string.  To 
re-initialize a search string to be empty, simply backspace to the 
beginnning and hit ESC or <cr>.

     C.   Miscellaneous
     1.   Files named QEAxx are altered QExx files that have special 
routines to speed up an ADDS Viewpoint 3A+ on a slow (4MHz) computer.  Mr. 
Gilbert warns in the original documentation that terminals without hardwired 
"deleteline" functions are not worth installing on 'e'.  He is just about 
right, these files help a bit.  
     2.   HINTS TO FUTURE MODIFICATIONS:  For others that wish to modify 
the program for their own purposes, I have these observations.  (1)  The 
files "QEFUNCS.DOC" and "QEDFUNCS.DOC" with this submission lists the 
functions in each file used in QE and QED respectively.  QEFUNCS.DOC is 
relevant to 'e' ver 4.6 also.  (2)  Debugging messages can be  displayed 
within the editor by using the statements:

               gotoxy(55,0);       /* go to the right end of the status line*/
               puts(yourmsg);      /* yourmsg is a char pointer */

Messages written in this location will not usually be overwritten
immediately.  If numeric output is required, the function "uspr" in QE7 can
be used.


II.  QED SPECIFIC MODIFICATIONS

     QE has been tranlated to DeSmet-C under MSDOS 2.x  and called QED.  
Because of difference in the compiler and the operating system, several 
additional changes have been made.
 
     1.   MSDOS Ver 2.0:   QED requires generic MSDOS version 2.0 or higher 
and checks with a BDOS call that the system uses this version.  No IBM-PC etc 
specific BIOS calls are used.  I.e. no software interrupts below 20 hex are 
used, nor are any port or memory specific references made.
     2.   DIRECTORY:     A paging, maskable MSDOS directory can be listed, 
as in QE.  Path names and sub-directories are supported.
     3.   NO BDOS ERROR RECOVERY:  I don't know how to trap BDOS errors in 
MSDOS, therefore Mr. Gilbert's elegant CP/M BDOS traps have been eliminated.  
I would, of course, be interested in knowing how to do this.
     4.   PATHS:    Specification of paths is supported for files.  A 
function to display and alter the path is implemented (via the file context 
function:  ^QKF).  Since full path names can be almost arbitrarily long, the 
status line displays only the file name.
     5.   MODIFICATION CHECK: If the user attempts to discard a modified 
file without saving it, a query is presented to ensure this was intentional.
     6.   DEFAULT EXTENSION:  The extension of the file called on the 
command line is saved in a default file extension string.  Future file 
requests (performed within a given QED session) do not require a file 
extension to be given.  If no extension is given, the directory is first 
searched for a file as typed.  If this fails, the default extension is 
appended to the input file name and the search repeated.  The default 
extension is overridden by using an explicit extension.  The desirable 
modification of not having to give the file extenson on the command line is 
not necessary in MSDOS by using batch files to invoke QED.  For example, if 
a series of editing sessions is to be undertaken using assembly language 
programming, then the following .BAT file is useful:

               QED %1.ASM -T8 -J%2

If this batch file is called, say, "e" then the command line "e myprog 150" 
will invoke QED to load MYPROG.ASM, set the tabs to 8 spaces, and jump to 
line 150.  This could also be done with CP/M, but SUBMIT is slower than 
typing in the entire command line.
     7.   DeSmet SPECIFIC MODIFICATONS:  The DeSmet compiler is adequate and 
a good buy.  Several changes were made from QE (using BDS-C) to accomodate 
the different compiler and operating system.  (a)  The function "uspr" was 
altered to take 2 arguments to print either a short or long integer.  Long 
integers are necessary to display disk space on my 8" disks.  (b) The 
following functions were renamed to avoid collision with functions loaded by 
the DeSmet BINDer: "putc" to "eputc", "getc" to "egetc", "puts" to "eputs".  
This renaming might not be necessary, but the manual suggests it is.  (c) 
the use of "sint" to "char" macro in 'e' was changed to "sint" is "int".  
Several variables and intermediate values went negative under MSDOS, causing 
problems.  So at the expense of data storage, I implemented the easiest 
solution I knew.

IV.  MAP OF KEYS AS DEFINED IN QETERM, QEADDS, AND QEDTV925

     ^A        WORD LEFT
     ^B        BOTTOM OF FILE
     ^C        DOWN PAGE
     ^D        CHARACTER LEFT
     ^E        UP 1 LINE
     ^F        WORD RIGHT
     ^G        DELETE CHARACTER UNDER CURSOR
     ^H        NON-DESTRUCTIVE BACKSPACE
     ^I        TAB RIGHT
     ^J        JUMP TO LINE n or increment of +/- n
     ^K        BLOCK MANIPULATIONS
               B   BLOCK MOVES (AS IN 'e')
               Q   QUIT
                     W=WRITE FILE
                     A=ABANDON EDITED FILE
               X   WRITE FILE AND EXIT TO SYSTEM
               J   REPEAT JUMP TO LAST MARKED LINE NUMBER
               R   READ FILE
     ^L        REPEAT LAST FIND/ALTER
     ^M        CARRIAGE RETURN
     ^N        NEW LINE
     ^O        MOVE TO LEFTMOST CHARACTER ON LINE
     ^P        MOVE TO RIGHTMOST CHARACTER ON LINE
     ^Q        'QUICK' OPTIONS
               A    FIND AND REPLACE
               F    FIND
               K    EDITING CONTEXT (TABS, FILES, ETC.)
               Y    DELETE TO END OF LINE
     ^R        UP 1 SCREEN
     ^S        CHARACTER LEFT
     ^T        MOVE TO TOP OF SCREEN
     ^U        MOVE TO TOP OF FILE
     ^V        MOVE TO BOTTOM OF SCREEN
     ^W        SCROLL UP THROUGH TEXT (CURSOR POSITION CONSTANT)
     ^X        LINE DOWN
     ^Y        MOVE TO TOP OF SCREEN
     ^Z        SCROLL DOWN THROUGH TEXT (CURSOR POSITION CONSTANT)
     ^[        ESCAPE
     ^\        DELETE LINE
     ^]        NO FUNCTION
     ^^        HELP
     ^_        RESTORE EDITED/DELETED LINE
     DEL       DELETE CHARACTER TO LEFT OF CURSOR

V.  FUTURE MODIFICATIONS

     My future projects with QED are the following.  In further violation 
of Nigel Gilbert's philosopy, I will create another editor based on QED that 
has wordwrap, variable right margins and simple reformatting capabilites so 
that QED plus a runoff program (NRO, ROFF, etc) will look more like a word 
processor.  Second, I would like to add to this latter editor outline 
processing capabilities along the lines of "Thinktank".  Third, I want to
add regular expression capabilities to the find/alter function of QED so as 
to implement a better version of the UNIX editor "vi."  This should not 
be terribly difficult with the appropriate subroutines used from a public 
domain "grep" or from the vanNuys Toolkit (e.g. "sub").  Finally, (and 
actually more immediately) I am porting QED to the VAX 780.  It will be 
disappointing at 1200 baud, but better than the line editor currently 
available.