ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-1      

                       CHAPTER 2  GETTING STARTED 
 
2.0  PRELIMINARY DISCUSSION 
 
This chapter covers the procedures for setting up Enable Reader. 
You should do this before actually running the Enable Reader  
program, which will be detailed in the next chapter.   
 
The first topic is a description of the different versions of  
the Enable Reader Professional Speech System .  Then the contents
of the Enable Reader  package is described, detailing the
Operations Manual and the Enable Reader Disks, and how they are
meant to be used for learning Enable Reader.   
 
Then there is an explanation of how to connect your speech  
synthesizer to the computer, followed by the procedure to create 
work disks from the disks that came with the Enable Reader  
package.  The last section discusses how auto execution works,  
and how you can change it for your own purposes.  Once you have  
completed the above sections, you are ready to actually run the  
Enable Reader program.   
 
You will just read or listen to the first part of this chapter.  
When you reach  SECTION 2.4  ATTACHING THE VOICE SYNTHESIZER,  
you will actually follow the instructions given from then on.   
 
 
2.1  VERSIONS OF ENABLE READER PROFESSIONAL 
 
The Enable Reader program currently supports seven speech  
synthesizers:  
  *ARTIC BOARD          (ARTIC TECHNOLOGY)
   CALLTEXT 5050        (SPEECH PLUS)
   DECTALK DT C01       (DIGITAL EQUIPMENT)
   ECHO GP              (STREET ELECTRONICS)
  *VOTALKER IB BOARD    (VOTRAX, INC.)        
   VOTRAX PSS           (VOTRAX, INC.)
   VOTRAX PSS/B         (VOTRAX, INC.)
  
 *NOTE: BOTH THE ARTIC AND VOTALKER BOARDS REQUIRE THE PORTTTALK  
        PROGRAM FOR OPERATION. THE ENABLE READER PROGRAM USES A 
        SPECIAL HARDWARE INTERRUPT AS ONE METHOD OF ENTERING THE
        SCREEN REVIEW MODE - CONTROL SHIFT.  THIS OPTION IS NOT   
        AVAILABLE WHEN RUNNING THE ABOVE BOARDS DUE TO CONFLICTS
        IN THE BOARDS MEMORY RESIDENT SOFTWARE AND PORTTALK.      
        THIS MEANS THAT PROGRAMS SUCH AS SUPERKEY MUST USE THE
        SOFTWARE INTERRUPT - CONTROL RIGHT BRACKET - AND WILL NOT 
        ALLOW SCREEN REVIEW ON MANY PROGRAMS THAT WRITE THEIR
        KEYBOARD HANDLING ROUTINES SUCH AS SIDEKICK AND SUPERKEY.
        
        WE STRONGLY RECCOMMEND THE PURCAHSE OF A SYNTHESIZER      
        ACCESSED THROUGH A SERIAL PORT. NOT ONLY ARE THEY PORTABLE 
        FROM MACHINE TO MACHINE, BUT ARE MORE COMPATIBLE WITH 
        IBM PC SOFTWARE.










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-2      


There is a different version of the Enable Reader program for  
each synthesizer. Each version starts up and has default controls
for that synthesizer.  Any version of the program can run with any
synthesizer by just loading in the correct table. This can be done
even when the program was started up with another synthesizer.
 
You can identify which version of Enable Reader you are running  
by listening to the Startup Message that is spoken when you  
first execute Enable Reader.  Thus you can check whether the  
version of the program matches your synthesizer.  The Startup  
Message and the name of the Enable Reader program for each of  
the synthesizers is given here:  

 
SYNTHESIZER:      ARTIC BOARD

PROGRAM NAME:     ARTIC.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE ARTIC SPEECH SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.

SYNTHESIZER:      CALLTEXT 5050

PROGRAM NAME:     ENABLE_C.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE CALLTEXT 5050 SPEECH        
                  SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.
 
SYNTHESIZER:      DECTALK DT C01 

PROGRAM NAME:     ENABLE_D.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE DECTALK SPEECH SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.
 
SYNTHESIZER:      ECHO GP 

PROGRAM NAME:     ENABLE_E.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE ECHO GP SPEECH SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.









ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-3      


SYNTHESIZER:      VOTALKER

PROGRAM NAME:     VOTALKER.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE VOTALKER SPEECH SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.

SYNTHESIZER:      VOTRAX PSS

PROGRAM NAME:     ENABLE_V.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE VOTRAX PSS SPEECH           
                  SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.

SYNTHESIZER:      VOTRAX PSS/B

PROGRAM NAME:     ENABLE_B.EXE 
 
STARTUP MESSAGE:  THE ENABLE READER PROFESSIONAL SPEECH SYSTEM .
                  VERSION 4.0 FOR THE VOTRAX PSS/B SPEECH         
                  SYNTHESIZER.
                  COPYRIGHTED 1987 BY ENABLE TALKING SOFTWARE.    
                  ALL RIGHTS RESERVED.
                  THIS IS A USER SUPPORTED PROGRAM.
 

2.2  THE OPERATIONS MANUAL 
 
The Enable Reader 4.0 Professional Speech Systems Operations
Manual is provided  on three different media:  
 
1.  PRINTED on 8-1/2 x 11 paper.   
 
2.  RECORDED on SIX 90 minute audio cassette tapes. 
      (AVAILABLE SOON)   
 
3.  RECORDED ON A FLOPPY DISKETTE.  The disk is called the MANUAL 
    Disk, and the Manual is broken up into eleven text files on  
    the disk.  There is also a file named  README.DOC  which  
    contains updates to the Manual.   
 
      README.DOC       Getting Started; Updates to Manual. 
      INTRO.DOC        Acknowledgements
                       Introduction, 
                       Table of Contents
                       Chapter 1. 
      STARTUP.DOC      Chapter 2. 
      USING.DOC        Chapter 3. 








ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-4      


      HELPKEYS.DOC     Chapter 4
      CURSKEYS.DOC     Chapter 4  
      READKEYS.DOC     Chapter 4  
      SYSTKEYS.DOC     Chapter 4  
      AIDKEYS.DOC      Chapter 5. 
      INTKEYS.DOC      Chapter 6. 
      WORDSTAR.DOC     Chapter 7. 
	 WORDPERF.DOC     Chapter 8.  
	 SUPERKEY.DOC     Chapter 9. 
      APPENDIX.DOC     Appendix Tables, Trademarks. 
 
Thus the Operations Manual can be read from the printed  
material, or listened to by playing the cassettes in a tape  
recorder.  Once you are familiar with Enable Reader, you can use 
it to listen to the Manual.  You can use the DOS  TYPE  command  
to display the files on the screen and speak them.  Or, if you  
have a word processor that will handle standard Ascii text  
files, you can just load the MANUAL Disk files into your word  
processing program on your computer, and listen to them through  
your speech synthesizer.   
 
When written text is spoken through a speech synthesizer, it  
will not always sound exactly as the text implies.  For  
instance, punctuation marks are used to denote pauses, end of  
sentences, et cetera, but a voice synthesizer will actually  
speak some of the punctuation marks.  Sections of the Manual on  
the disk may be deliberately oriented towards listening through  
a synthesizer.  Therefore, a lot of the punctuation (mostly  
commas) may have been taken out of some of the text files.  This 
makes the files a little harder to read, but a lot easier to  
listen to.  

The printed Manual is the same text as the files on the MANUAL
Disk, so it too may be missing a lot of punctuation in some
sections.  If you listen to the text files and there are too many
commas spoken, you can use the  M  PUNCTUATION FILTER command, or
the  N  PUNCTUATION LEVEL command to screen out the commas.  (You
will learn about these punctuation commands later.)  
 
The recorded tapes of the Manual match the printed manual.  (In  
fact, the recordings were made by reading the manual out loud.)  
Thus when learning to use Enable Reader, a blind person can  
listen to the tapes, and a sighted person can follow along with  
the printed Manual.   
 
 
2.3  CONTENTS OF ENABLE READER DISKS 
 
There are FOUR floppy disks in the Enable Reader package.  The
names of these disks, are 1) PROGRAM, 2) MANUAL, 3) VOTRAX
WORDPROCESSING, and 4) DECTALK WORDPROCESSING.  A description of
their contents, follows:  
 
 









ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-5      


PROGRAM Disk -
 
The program diskette is divided into seven sections called sub
directories.  The main directory is called the root directory and
looks as follows when DIR <ENTER> is typed.

Volume in drive A is 1 PROGRAM
Directory of A:/

README                   xxxxx  12-22-86    1:00p
ARTIC          <DIR>            12-22-86    1:00p
CALLTEXT       <DIR>            12-22-86    1:00p
DECTALK        <DIR>            12-22-86    1:00p
ECHO           <DIR>            12-22-86    1:00p
VOTALKER       <DIR>            12-22-86    1:00p
VOTRAX         <DIR>            12-22-86    1:00p
VOTRAX_B       <DIR>            12-22-86    1:00p
          8 File(s)           xxxxx bytes free

The seven sub-directories contain the following synthesizer
programs and tables:

SUB-DIRECTORY:      SYNTHESIZER:
ARTIC               ARTIC BOARD
CALLTEXT            CALLTEXT 5050
DECTALK             DECTALK DTC01
ECHO                ECHO GP
VOTALKER            VOTALKER IB
VOTRAX              VOTRAX PSS
VOTRAX_B            VOTRAX PSS/B
 
The SEVEN sub-directories and their contents are accessed by
changing directories with the Change Directory Command.  For 
example, to access the contents of the sub-directories type at the
DOS command prompt   cd/   and then the name of the subdirectory
desired followed by a carriage return.  TO ACCESS THE VOTRAX PSS
PROGRAM AND THE TABLES FOR GENERAL OPERATION TYPE:

A>cd/votrax  <ENTER>

THIS IS READ  "C D BACKSLASH VOTRAX ENTER" 

Once the command is typed the sub-directory is available for
reading with the DIR command.  This will allow you to look at the
contents in the directory of the diskette.  Later in this chapter
you will be instructed on how to create your own diskettes. 

Below are the contents of each sub-directory:

1.  One of the files is the Enable Reader Professional Speech     
    program for your particular speech synthesizer.  This program 
    is generic, in the sense that it can run with any supported   
    synthesizer by just loading in the correct table for that     
    synthesizer.   

    







ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-6      


    In chapter 4 you will be taught how to load    
    and save tables.  We send a ready to run program as a         
    convenience so you can get up and running without having to   
    know how the Enable Reader program. This program is ONE of       

    the following files, depending on which sub-directory you have
    entered:
 
        ARTIC.EXE        - ARTIC speech synthesizer.
        ENABLE_C.EXE     - CALLTEXT 5050 speech synthesizer.
        ENABLE_D.EXE     - DECTALK DT C 0 1 speech synthesizer.
        ENABLE_E.EXE     - ECHO GP speech synthesizer.
        VOTALKER.EXE     - VOTALKER IB speech synthesizer.
        ENABLE_V.EXE     - VOTRAX PSS speech synthesizer.   
        ENABLE_B.EXE     - Votrax PSS/B speech synthesizer.   
 
2.  Another file is the Enable Default Table for Enable Reader,   
    called   ENABLE.TBL . This file is automatically read by the  
    Enable Reader program when Enable Reader is first executed.   
    It contains the command settings and parameters used by       
    Enable Reader.  While you are using Enable Reader, you can    
    change settings in it and then save the changes.   If the     
    changes are saved as the ENABLE.TBL file,  the next time the  
    program is run it will start up with the new changes as       
    default settings.  

    
3.  There are TABLES for the Enable Reader Professional Speech
    System for different PORTS at different SPEEDS.  Any of these
    tables can be renamed to ENABLE.TBL in order to have the 
    Enable Reader Professional Speech System start for any
    supported speech synthesizer or they can be loaded directly
    while Enable Reader is running in order to change the 
    Port/Setup parameters of a new synthesizer on the fly.  Many
    times the system you need to connect to (ie. a mini or
    mainframe computer or an IBM LAN ) is preset to a certain 
    configuration.  The following tables can allow the Enable 
    Reader Program to be set at different speeds and for different
    communications ports:   
 

          	   1200 BAUD/ COMMUNICATION PORT 1   
 
        1200COM1.CTX     - CALLTEXT 5050 speech synthesizer
	      
        1200COM1.DEC     - DECtalk DT C 0 1 speech synthesizer.   

        1200COM1.ECO     - Echo GP speech synthesizer.   

        1200COM1.VTX     - Votrax PSS speech synthesizer.   

        1200COM1.VXB     - Votrax PSS/B speech synthesizer.   

 









ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-7      


                  1200 BAUD/ COMMUNICATION PORT 2   
 
        1200COM2.CTX     - CALLTEXT 5050 speech synthesizer
	      
        1200COM2.DEC     - DECtalk DT C 0 1 speech synthesizer.   

        1200COM2.ECO     - Echo GP speech synthesizer.   

        1200COM2.VXT     - Votrax PSS speech synthesizer.   

        1200COM2.VXB     - Votrax PSS/B speech synthesizer.   


          	   9600 BAUD/ COMMUNICATION PORT 1   
 
        9600COM1.CTX     - CALLTEXT 5050 speech synthesizer
	      
        9600COM1.DEC     - DECtalk DT C 0 1 speech synthesizer.   

        9600COM1.ECO     - Echo GP speech synthesizer.   

        9600COM1.VTX     - Votrax PSS speech synthesizer.   

        9600COM1.VXB     - Votrax PSS/B speech synthesizer.   


          	   9600 BAUD/ COMMUNICATION PORT 2   
 
        9600COM2.CTX     - CALLTEXT 5050 speech synthesizer
	      
        9600COM2.DEC     - DECtalk DT C 0 1 speech synthesizer.   

        9600COM2.ECO     - Echo GP speech synthesizer.   

        9600COM2.VTX     - Votrax PSS speech synthesizer.   

        9600COM2.VXB     - Votrax PSS/B speech synthesizer.   


           ARTIC AND VOTALKER/ COMMUNICATIONS PORT 1 AND 2

        ENABLE.TBL       - COM PORT 1 
        PORT2.TBL        - COM PORT 2 


MANUAL DISK - 
 
The contents of the Enable Reader MANUAL Disk are as follows:  
 
1.  An Update File for the Operations Manual, called   
    README.DOC.  This file contains changes and updates to the  
    Operations Manual.   
 










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-8      



2.  The Enable Reader Professional Speech Systems Operations      
    Manual.  The manual is divided into fourteen files, whose     
    names all end with ".DOC" .  The order of the filenames in    
    the directory of the MANUAL Disk is the same order in which   
    the text occurs in the Manual.   
 
3.  A sample Ascii file called  EXAMPLE .  You can display it on  
    the screen, and try out the Enable Reader screen review  
    commands on it.   


VOTRAX AND DECTALK DISKS:

The VOTRAX and DECTALK disks have two sections.  The root
directory and the sub-directory called WORDSTAR. Both disks
contain the same structure.  They have programs, tables, and macro
files for SUPERKEY for the respective synthesiser the disk is
named for. The ROOT directory contains the AUTOMATION PACKAGE FOR
WORDPERFECT.  The WORDSTAR sub-directory contains the AUTOMATION
PACKAGE FOR WORDSTAR.

THE WORDSTAR SUB-DIRECTORY CONTAINS THE FOLLOWING:

1.  Integration Tables for Wordstar.  We have included these  
    18 tables as a convenience for those of you who will  
    be using Wordstar.  Thus you do not have to create your own  
    tables to use with the Integration feature of the Enable  
    Reader program.  These tables are all of the files whose  
    names end with ".TBL" , except ENABLE.TBL .  Each of these  
    tables is to be used with a different Wordstar screen  
    display.  Chapter 7 in the Manual contains a list of these  
    Tables and where each Table is used. They will be             
    automatically loaded for you.
 
2.  Superkey macro files for Wordstar.  There are 9 corresponding
    and macro files for the major screens in Wordstar.            
    The Superkey macro files are automatically loaded when they   
    are needed.  A more detailed discussiion can be found in      
    Chapters 7, 8, and 9 on their contents, how they are created, 
    and how they run.  

3.  A sample Wordstar text file called  TESTFILE .  You can use  
    this file with Wordstar to try out the "Matchup" command of  
    the Integration feature.  The file itself contains the  
    instructions for doing so.   
 
4.  The Startup File, called  RUN.BAT .  It tells the computer  
    to load and activate Superkey, the Enable Reader program, then
    prompts you whether to enter the date and time or run         
    Wordstar. 
 
5.  Another file named  INIT.BAT configures the Superkey Program  
    before running the Automation Package.  It only needs to be   
    run once when Superkey is first copied into the Word          
    Proccessing sub-directory on your machine.  







ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-9      


THE ROOT DIRECTORY CONTAINS:

1.  Integration Tables for WORD PERFECT.  There are 5 
    tables created as a convenience for those of you who will  
    be using Word Perfect.  Thus you do not have to create your   
    own tables to use with the Integration feature of the Enable  
    Reader program.  These tables are all of the files whose  
    names end with ".TBL" , except ENABLE.TBL .  Each of these  
    tables is to be used with different Word Perfect screen  
    displays.  Chapter 8 in the Manual contains a list of these  
    Tables and where each Table is used.   

2.  Superkey macro files for Word Perfect.  There are 43
    corresponding tables and macro files for the major screens in 
    Wordstar. The Superkey macro files are automatically loaded   
    when they  are needed.  A more detailed discussiion can be    
    found in Chapters 7, 8, and 9 on their contents, how they are 
    created, and how they run.

3.  A sample Word Perfect text file called  TESTFILE .  You can   
    use this file with Word Perfect to try out the "Matchup"      
    command of the Integration feature.  The file itself contains 
    the instructions for doing so.   

4.  The Startup File, called  RUN.BAT .  It tells the computer  
    to load and activate Superkey, the Enable Reader program, then
    prompts you whether to enter the date and time or run         
    Word Perfect. 
 
5.  Another file named  INIT.BAT configures the Superkey Program  
    before running the Automation Package.  It only needs to be   
    run once when Superkey is first copied into the Word          
    Proccessing sub-directory on your machine.  
 
 
2.4  ATTACHING THE VOICE SYNTHESIZER 
 
Up to this point, you have been just reading or listening to the 
Manual.  This rest of this chapter describes the setup  
procedures that you need to do before running Enable Reader.   
You should actually follow the instructions given.   
 
 
All seven versions of Enable Reader are pre-set to use Serial Port
One, and handshake using the XON/XOFF protocol.  The CALLTEXT,
ECHO GP, VOTRAX PSS, and the VOTRAX PSS/B versions run at 9600
Baud; the DECtalk Version runs at 1200  Baud.   
 
Your particular speech synthesizer is to be connected directly  
to your computer with a cable, and no special interfaces are  
required.  The cable is connected between Serial Port One on the 
computer, and the Serial port on the synthesizer.  A cable can  
be provided for your synthesizer if you do not have one.   










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-10     



WARNING - You can NOT use just any cable that happens to fit  
into the serial port connectors on your computer and your  
synthesizer.  The cable has to be made specifically for  
connecting your particular computer and synthesizer together.   
Otherwise you may damage your synthesizer.  Also be sure to plug 
the correct end of the cable into each device -- the two ends of 
the cable might not be wired identically.   
 
The CALLTEXT and ECHO GP has only one port, and it is serial. 
However, the Votrax and DECtalk each have two ports on the back. 
The serial port on the Votrax is the left side port as you face
the synthesizer from the front, and it is labeled  SERIAL PORT . 
It is located in the middle of the machine.  The DECtalk has two  
Serial ports, but you want to use the one labeled  HOST PORT ,  
which is the right side port as you face the synthesizer from  
the front.   
 
The Votrax synthesizer also has some DIP switches that need to  
be set.  Refer to the Votrax Operator's Manual for the settings. 
You should set the switches for:  9600 baud; XON/XOFF protocol;  
7 bit word length; power-up message ON; SERIAL port; RUN mode.   
 
 
2.5  SETTING UP YOUR DISKS 
 
NOTE - WE STRONGLY RECOMMEND THAT THE FOLLOWING STEPS BE DONE IN  
       THE PRESENCE OF A SIGHTED PERSON.  UNTIL YOU ARE USING  
       ENABLE READER, YOU WILL NEED SOMEONE TO TELL YOU WHAT THE  
       COMPUTER PRINTING TO THE SCREEN.   
 
The Enable Reader package comes with FOUR disks:  a PROGRAM  
Disk, a MANUAL Disk, and two AUTOMATION PACKAGE DISKS for the
VOTRAX PSS and the Dectalk speech synthesizer. 

The first thing to do before using Enable Reader is to protect
yourself in case you  accidentally damage your only copies of the
software.  You need  to make copies of each of the disks in the
Enable Reader  package.  Then you can use the copies, and store
the originals in a safe place.  Next you need to put the Enable
Reader program  on a System Disk.  The following will guide you
through the steps for accomplishing these tasks.   

WE DO NOT RECCOMEND RUNNING THE AUTOMATION PACKAGES WITHOUT A HARD
DISK.  THE TABLES AND MACROS MUST BE AVAILABLE AT ALL TIMES. THIS
REQUIRES THE STORAGE CAPACITY OF A HARD DISK.



If you have a computer with two floppy disk drives, proceed with 
the next section entitled "For Computers With Two Floppy Disk  
Drives".  If you are using a Hard Disk, skip ahead to the  
section "For Computers With A Hard Disk".   










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-11     


 
FOR COMPUTERS WITH TWO FLOPPY DISK DRIVES: 
 
1.   Turn on your computer and boot it with an MSDOS or PCDOS  
     System Disk in Drive A .  The DOS has to be Version 2.00 or  
     higher.  When the boot process is finished, there will be  
     an  A>  showing on the screen signifying that the default  
     drive is Drive A .   
 
2.   If you want to listen to the computer's responses during  
     the following operations, you can use Enable Reader to do  
     so.  If your synthesizer is not yet hooked up to your  
     computer, or you otherwise do not wish to run Enable Reader  
     during these operations, then skip this step and proceed  
     with  Step 3  to make copies of the Enable Reader Disks.   
 
     To run Enable Reader:  
 
     A)  First turn on your synthesizer.   
 
     B)  Put the Enable Reader PROGRAM Disk into Drive A .   
         CHANGE SUB-DIRECTORIES TO YOUR SYNTHESIZER TYPE. 
         Next, type in the name of your version of the Enable     
         Reader program, and then hit the  ENTER  key.  (To find  
         which name to type in, refer back to  SECTION 2.1        
         VERSIONS OF ENABLE READER  PROFESSIONAL, or  SECTION 2.3 
         CONTENTS OF ENABLE READER DISKS, in this manual.)  For   
         example, if your synthesizer is the Votrax PSS, you will 
         type:

               A>ENABLE_V.EXE   <ENTER>   
 
     C)  You should hear the Enable Reader Startup Message.       
         Enable Reader is now running.  It is set to speak any  
         characters that are sent to the screen to be displayed.  

 
3.   Make copies of the Enable Reader Disks.  To do this:  
 
     1)  Put a DOS System Disk (with FORMAT.COM and  
         DISKCOPY.COM on it) into Drive A .   
 
     2)  Type:

                A>DISKCOPY A: B:   <ENTER>   
 
     3)  When the computer says to put disks into the  
         drives, put the Enable Reader PROGRAM Disk into Drive A  
         and put a blank disk into Drive B .  Then hit any key to 
         begin duplicating the Enable Reader Disk.   
 












ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-12     


     4)  When the copying is done, the computer will ask you      
         if you wish to copy another disk.  Take the disks out of 
         the drives.  The disk from Drive B is your copy of the  
         Enable Reader PROGRAM Disk.  Put a label and a write- 
         protect tab on it.  Type    Y    for yes to tell the  
         computer that you want to copy another disk.   
 
     5)  Now repeat the copy procedure THREE more times,  
         following the computer's instructions.  Copy the Enable  
         Reader MANUAL , and the TWO AUTOMATION DISKS.   
 
After the last copy, type    N    for NO to tell the computer that 
you do not want to make any more copies.   
 
You should put the original Enable Reader Disks in a safe place, 
and use the copies from now on.  Next, you will put the Enable  
Reader program on a System Disk.   
 
4.   Format a blank disk, putting the Operating System on it in  
     the process.  To do this:  
 
     1)  Put the DOS Disk back in Drive A and type:
      
                 A>FORMAT B:/S   <ENTER>   
 
     2)  When the computer tells you, put a blank disk into  
         Drive B and hit any key to go ahead with the formatting. 
 
     3)  When the formatting is done, the computer will ask  
         you if you wish to format any more disks.  Just hit the  
         letter N key to tell it NO .  The  A>  prompt will       
         return.  You now have a formatted disk with the          
         Operating System on it.   
 
5.   We will now copy the Enable Reader Program, and the
     ENABLE .TBL default file. for the synthesizer you wish to    
     work with. To do this:  
 
     1)  Put the PROGRAM Disk into Drive A , and the disk  
         you just formatted into Drive B .   
 
     2)  Change to the Synthesizer Sub-directory using the Change 
         Directory Command  CD\ .  Then type:
                 
                 A>COPY *.* B:/V   <ENTER>

         The PROGRAM, TABLES INCLUDING THE DEFAULT TABLE, AND     
         AUTOMATIC STARTUP FILES on the PROGRAM Disk will now be  
         copied onto your formatted disk. 

         THIS DISK IS NOW AN ENABLE READER SYSTEM DISK AND        
         CAN BE USED WITH THOUSANDS OF IBM PC PROGRAMS. 
 










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-13     


When you use this Enable Reader System Disk to boot your  
computer, Enable Reader will automatically start up for you.   
 
Now that your disks are set up, you are ready to use Enable  
Reader.  Chapter 3 gives a general summary of how to work with  
the Enable Reader features.  Chapters 4 and 6 give detailed  
descriptions of each of the commands.  Chapters 7, 8, and 9 give
detailed instructions on how to run the Automation Package with
Enable Reader.  
 
The next section is for setting up Enable Reader with a hard  
disk.  If you have a computer with two floppy disk drives, and  
if you have already set up your disks by following the  
instructions in the previous section, then skip ahead to   
SECTION 2.6  AUTO EXECUTION  in this manual.  If you have a  
computer with a hard disk, proceed with the next section  
entitled "For Computers With A Hard Disk".   
 
 
FOR COMPUTERS WITH A HARD DISK: 

 
1.   Turn on your computer and go through the boot process.  The  
     DOS has to be Version 2.00 or higher.   
 
2.   If you want to listen to the computer's responses during  
     the following operations, you can use Enable Reader to do  
     so.  If your synthesizer is not yet hooked up to your  
     computer, or you otherwise do not wish to run Enable Reader  
     during these operations, then skip this step and proceed  
     with  Step 3  to make copies of the Enable Reader Disks.   
 
     To run Enable Reader: 
 
         A)  First turn on your synthesizer.   
 
         B)  Type:
                     A:    <ENTER>
             
             This will set the default drive to Drive A .   
 
         C)  Put the Enable Reader PROGRAM Disk into Drive A .   
             CHANGE DIRECTORIES TO YOUR SYNTHESIZER TYPE.
             Next, type in the name of your version of the        
             Enable Reader program, and then hit the  ENTER  key.
             (To find out which name to type in, refer back to    
             SECTION 2.1  VERSIONS OF ENABLE READER, or  SECTION  
             2.3 CONTENTS OF ENABLE READER   DISKS, in this       
             manual.)
              













ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-14     


             For example, if your synthesizer is the Votrax PSS,  
             you will type:

                     ENABLE_V.EXE   <ENTER>   
 
         4)  You should hear the Enable Reader Startup Message.   
             Enable Reader is now running.  It is set to speak    
             any characters that are sent to the screen to be     
             displayed.   
 
3.   Make copies of the Enable Reader Disks.  To do this:  
 
         1)  If the file  DISKCOPY.COM  is on your Hard Disk,  
             type:

                      C:     <ENTER>

             This will set the default drive to Drive C  .   
 
         2)  If the file  DISKCOPY.COM  is NOT on your Hard  
             Disk, put a DOS System Disk (with  DISKCOPY.COM  on  
             it) into Drive A , and type:

                      A:     <ENTER>   
 
         3)  Type:

                      DISKCOPY A: B:   <ENTER>            

         4)  When the computer says to put disks into the  
             drives, put the Enable Reader PROGRAM Disk into      
             Drive A and put a blank disk into Drive B .  If you  
             have just one floppy drive, then just put the Enable 
             Reader PROGRAM Disk  into Drive A ; the computer     
             will prompt you to switch disks.  Then hit any key   
             to begin duplicating the Enable Reader Disk.   
 
         5)  When the copying is done, the computer will ask you  
             if you wish to copy another disk.  Take the disks    
             out of the drives.  The disk from Drive B is your    
             copy of the Enable Reader PROGRAM Disk.  Put a label 
             and a write protect tab on it.  Type    Y    for yes 
             to tell the computer that you want to copy another   
             disk.   
 
         6)  Now repeat the copy procedure THREE more times,  
             following the computer's instructions.  Copy the     
             Enable Reader MANUAL, and two AUTOMATION DISKS.
   
After the last copy, type    N    to tell the computer that      
you do not want to make any more copies.   
 
You should put the original Enable Reader Disks in a safe place, 
and use the copies from now on.  Next you will put the Enable  
Reader program on your Hard Disk.   
 







ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-15     


4.   Copy the necessary files from the Enable Reader PROGRAM  
     Disk onto your Hard Disk.  To do this:  
 
         1)  Put the PROGRAM Disk into Drive A .   
 
         2)  Change from C: to A: and change direcrtories to the  
             synthesizer you are working with. then change back   
             to C:  For example, after the C> prompt type:
 		
             a:             <ENTER>

             CD\VOTRAX      <ENTER>

             C:             <ENTER>

             
         3)  From the C: prompt type:

                 COPY A:*.EXE C:/V   <ENTER>

                 COPY A:ENABLE.TBL C:/V  <ENTER>
 
                 COPY A:AUTOEXEC.BAT C:/V <ENTER>

         The PROGRAM, DEFAULT, AND AUTOMATIC STARTUP FILES on     
         the PROGRAM Disk will now be copied onto your hard disk. 
 
         THE HARD DISK IS NOW SET UP TO AUTOMATICALLY RUN THE     
         ENABLE READER PROGRAM AND CAN BE USED WITH THOUSANDS OF  
         IBM PC PROGRAMS. 

         IF YOU WOULD LIKE TO CREATE AN AUTOMATION SUB-DIRECTORY 
         FOR THE WORDSTAR OR WORD PERFECT PROGRAM PROCEED WITH STEPS 
         3 THROUGH 6  BELOW.  IF YOU ARE NOT GOING TO MAKE AN 
         AUTOMATION SUB-DIRECTORY THEN SKIP AHEAD TO SECTION 2.6 AUTO
         EXECTION FILES.  

     3)  It is reccomended that a special sub-directory is        
         created to run the Wordstar and Word Perfect automation  
         packages.  Below is an example of how to create and copy 
         files into a sub-directory.  First, we create a sub-     
         directory with the MAKE DIRECTORY command.  To create a  
         sub-directory for the Word Perfect Automation Package    
         you would type from the C> prompt:

			       mkdir \wordperf <ENTER>

         Or for the Wordstar Automation Package type:

                      mkdir \wordstar <ENTER>                     

     4)  Now we need to change SUB-DIRECTORIES on BOTH Drive A:   
         and drive C:.  Then we will copy the Automation Package  
         over.









ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-16     


         From the C> prompt, change to the Sub-directory you      
         created by typing: 
           
                     cd\wordperf  <ENTER>

         or for the Wordstar sub-directory type:

                     cd\wordstar  <ENTER>

         The sub-directory for Wordstar on the Automation Disk    
         in drive A: is accessed by  changing directories with    
         the CD/ or Change Directory command. For example, to     
         access the contents of the sub-directory type at the DOS 
         command  prompt: 

                      a:          <ENTER>

         This will change to the Floppy diskette as the default   
         drive.  then type:

                      cd\WORDSTAR  <ENTER>


         Once the command is typed the sub-directory is available 
         for use.  Next we will copy all the files in this 
         sub-directory by typing:

                      copy a:*.* c:/v  <ENTER>


         This will transfer all the files needed to run the       
         Enable Reader program and Superkey with the Wordstar     
         or Word Perfect program.  
 
     4)  The final copy of files is to copy the Superkey Program  
         and the word processing program onto the newly created   
         system disk.  First, place the Superkey disk into
         drive A:  and type:

                    A>copy a:key.exe c:/v <ENTER>

         Then type:

                    A>copy a:key.hlp c:/v <ENTER>
   
         FOR WORDSTAR
     
         Next, place the Wordstar Master diskette into Drive A:   
         and type:

                    A>copy a:ws.com c:/v  <ENTER>

         Then type:
           
                    A>copy a:*.ovl c:/v   <ENTER>
        







ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-17     


         FOR WORD PERFECT

         You must copy all disks onto the hard disk in the same   
         sub-directory.  This is done by placing each disk in turn 
         into Drive A: and typing:

                     A>copy *.* c:/v      <ENTER>

     5)  When the  A>  prompt returns, the copying is done.   
         The sub-directory in Drive C: is your Enable Reader      
         Automation System .
   
     6)  Take the disk out of Drive A:   
 
When you want to run the Auotmation Package, change to this
sub-directory that contains the Enable Reader automation package
and type:

                   RUN    <ENTER KEY> 

The Enable Reader automation package will automatically start up
for you.   
 
Now that your disks are set up, you are ready to use Enable  
Reader.  Chapter 3 gives a general summary of how to work with  
the Enable Reader features.  Chapters 4 and 6 give detailed  
descriptions of each of the commands.  Chapters 7, 8, and 9 give
detailed instructions on how to run the Automation Package with
Enable Reader.  
 
If you would like to have the Enable Reader program  
automatically start up for you whenever you boot your  
computer, you will have to add a command for the name of  
the Enable Reader program to your  AUTOEXEC.BAT  file.   
(See SECTION 2.6  AUTOEXECUTION.)  This is not necessary at      
this time, so if you are not sure how to do this, you can  
skip it for now.   
 
Now that your Hard Disk is set up, you are ready to use Enable  
Reader.  Chapter 3 gives a general summary of how to work with  
the Enable Reader features.  Chapters 4 and 6 give detailed  
descriptions of each of the commands.   
 
 
2.6  AUTO EXECUTION 
 
The MSDOS Operating System looks for a specific Startup File  
called  AUTOEXEC.BAT  when it first starts up.  If this file  
exists on the disk, then the computer executes the instructions  
in the file before turning control of the computer over to you.   
The following discussion is only a short example of how to write 
a simple startup file.  For a more complete explanation, refer  
to the MSDOS manual for the sections on COPY and on BATCH FILES.  










ENABLE READER 4.0         OPERATIONS  MANUAL        CHAPTER 2-18     



The Enable Reader PROGRAM Disk contains an  AUTOEXEC.BAT  file.   
This startup file contains only three instructions.  These  
instructions will load and run the Enable Reader program, ask  
you to enter the date, and then ask you to enter the time.   
These instructions are the same as could be typed in from the  
keyboard when running the Operating System.  Using an  
AUTOEXEC.BAT  file means you do not have to type the name of the  
Enable Reader program every time you startup the machine.  The   
AUTOEXEC.BAT  file can be created from the Operating System  
without having to use a word processor.  

The following procedure was used to create the file we supplied you. 
  
1.   Type     COPY CON: AUTOEXEC.BAT           <ENTER>

2.   Type     program name  (eg. ENABLE_V.EXE) <ENTER>

3.   Type     DATE                             <ENTER>

4.   Type     TIME                             <ENTER>
 
5.   Hit the  F6  key, then hit the  ENTER  key.  (NOTE:  The F6  
     key enters a  CONTROL Z  , so if you want, you can hold  
     down the  CONTROL  key, tap the  Z  key, release the  
     CONTROL key, and tap the  ENTER  key for this step.)  
 
The computer then creates the  AUTOEXEC.BAT  file and saves it  
on the disk.  From now on, every time you start or reboot the  
computer with this disk, the instructions in this file are  
executed first.   
 
If you have followed the instructions for creating an Enable  
Reader System Disk on a floppy disk, then the  AUTOEXEC.BAT   
file on that disk will automatically start Enable Reader  
whenever you boot your computer with that disk.   
 
If you are booting from a hard disk, chances are that there  
already is an  AUTOEXEC.BAT  file on the hard disk.  If you want  
Enable Reader to start automatically when you boot the hard  
disk, you need to add the name of your Enable Reader program to  
the existing  AUTOEXEC.BAT  file.  You can do this by looking at 
the current contents of  AUTOEXEC.BAT , and retyping all the  
instructions with the name of the Enable program inserted.  Or  
you can use a word processing program to add the Enable program  
to  AUTOEXEC.BAT .  The Enable program gets inserted into the  
list of commands AFTER any hard disk initialization commands,  
and BEFORE any other commands.  If your hard disk does not  
already have an  AUTOEXEC.BAT  file on it, you can just copy the 
AUTOEXEC.BAT  file from the Enable Reader PROGRAM Disk onto your 
hard disk.  Putting the name of your Enable Reader program into  
the  AUTOEXEC.BAT  file on your hard disk is not really  
necessary at this time, so if you are not sure how to do it, you 
can skip it for now.   
 
 
END OF   CHAPTER 2  GETTING STARTED