CHAPTER 6    THE 86 INSTRUCTION SET                       6-1

Effective Addresses

Most memory data accessing in the 86 family is accomplished via 
the mechanism of the effective address.  Wherever an effective 
address specifier "eb", "ew" or "ed" appears in the list of 8086 
instructions, you may use a wide variety of actual operands in 
that instruction.  These include general registers, memory 
variables, and a variety of indexed memory quantities.  

GENERAL REGISTERS: Wherever an "ew" appears, you can use any of 
   the 16-bit registers AX,BX,CX,DX,SI,DI,SP, or BP.  Wherever an 
   "eb" appears, you can use any of the 8-bit registers 
   AL,BL,CL,DL,AH,BH,CH, or DH.  For example, the "ADD ew,rw" 
   form subsumes the 16-bit register-to-register adds; for 
   example, ADD AX,BX; ADD SI,BP; ADD SP,AX.  

MEMORY VARIABLES: Wherever an "ew" appears, you can use a word-
   memory-variable.  Wherever an "eb" appears, you can use a 
   byte-memory-variable.  Variables are typically declared in the 
   DATA segment, using a DW declaration for a word-variable, or a 
   DB declaration for a byte-variable.  For example, you can 
   declare variables: 

     DATA_PTR  DW ?
     ESC_CHAR  DB ?

   Later, you can load or store these variables:

     MOV SI,DATA_PTR    ; load DATA_PTR into SI for use
     LODSW              ; fetch the word pointed to by DATA_PTR
     MOV DATA_PTR,SI    ; store the value incremented by the LODSW
     MOV BL,ESC_CHAR    ; load the byte-variable ESC_CHAR

   Alternatively, you can address specific unnamed memory 
   locations by enclosing the location value in square brackets; 
   for example, 

     MOV AL,[02000]     ; load contents of location 02000 into AL

   Note that A86 discerned from context (loading into AL) that a 
   BYTE at 02000 was intended.  Sometimes this is impossible, and 
   you must specify byte or word: 

     INC B[02000]       ; increment the byte at location 02000
     MOV W[02000],0     ; set the WORD at location 02000 to zero

                                                          6-2
INDEXED MEMORY: The 86 supports the use of certain registers as 
   base pointers and index registers into memory.  BX and BP are 
   the base registers; SI and DI are the index registers.  You 
   may combine at most one base register, at most one index 
   register, and a constant number into a run-time pointer that 
   determines the location of the effective address memory to be 
   used in the instruction.  These can be given explicitly, by 
   enclosing the index registers in brackets: 

        MOV AX,[BX]
        MOV CX,W[SI+17]
        MOV AX,[BX+BP+5]
        MOV AX,[BX][BP]5 ; another way to write the same instr.

   Or, indexing can be accomplished by declaring variables in a 
   based structure: 

        STRUC [BP]         ; NOTE based structures are unique to A86!
          BP_SAVE   DW ?
          RET_ADDR  DW ?
          PARM1     DW ?
          PARM2     DW ?
        ENDS
        INC PARM1         ; equivalent to INC W[BP+4]

    Finally, indexing can be done by mixing explicit components 
    with declared ones: 

        TABLE    DB  4,2,1,3,5
        MOV AL,TABLE[BX]


Segmentation and Effective Addresses

The 86 family has four segment registers, CS, DS, ES, and SS, 
used to address memory.  Each segment register points to 64K 
bytes of memory within the 1-megabyte memory space of the 86.  
(The start of the 64K is calculated by multiplying the segment 
register value by 16; i.e., by shifting the value left by one hex 
digit.)  If your program's code, data and stack areas can all fit 
in the same 64K bytes, you can leave all the segment registers 
set to the same value.  In that case, you won't have to think 
about segment registers--no matter which one is used to address 
memory, you'll still get the same 64K.  If your program needs 
more than 64K, you must point one or more segment registers to 
other parts of the memory space.  In this case, you must take 
care that your memory references use the segment registers you 
intended.  

Each effective address memory access has a default segment 
register, to be used if you do not explicitly specify which 
segment register you wish.  For most effective addresses, the 
default segment register is DS.  The exceptions are those 
effective addresses that use the BP register for indexing.  All 
BP-indexed memory references have a default of SS.  (This is 
because BP is intended to be used for addressing local variables, 
stored on the stack.) 

                                                          6-3
If you wish your memory access to use a different segment 
register, you provide a segment-override byte before the 
instruction containing the effective address operand.  In the A86 
language, you code the override by giving the name of the segment 
register you wish before the instruction mnemonic.  For example, 
suppose you want to load the AL register with the memory byte 
pointed to by BX.  If you code MOV AL,[BX], the DS register will 
be used to determine which 64K segment BX is pointing to.  If you 
want the byte to come from the CS-segment instead, you code CS 
MOV AL,[BX].  Be aware that the segment-override byte has effect 
only upon the single instruction that follows it.  If you have a 
sequence of instructions requiring overrides, you must give an 
override byte before every instruction in the sequence.  (In that 
case, you may wish to consider changing the value of the default 
segment register for the duration of the sequence.) 

NOTE: This method for providing segment-overrides is unique to 
the A86 assembler!  The assemblers provided by Intel and IBM (MS-
DOS) attempt to figure out segment allocation for you, and plug 
in segment-override bytes "behind your back".  In order to do 
this, those assemblers require you to inform them which variables 
and structures are pointed to by which segment registers.  That 
is what the ASSUME directive in those assemblers is all about.  I 
wrote Intel's first 86 assembler, ASM86, so I have been watching 
the situation since day one.  Over the years, I have concluded 
that the ASSUME-mechanism creates far, far more confusion that it 
solves.  So I scrapped it; and the result is an assembler with 
far less red tape.  But if your program needs more than 64K, you 
do have to manage those segment registers yourself; so take care!  


Effective Use of Effective Addresses

Remember that all of the common instructions of the 86 family 
allow effective addresses as operands.  (The only major functions 
that don't are the AL/AX specific ones: multiply, divide, and 
input/output).  This means that you don't have to funnel many 
through AL or AX just to do something with them.  You can perform 
all the common arithmetic, PUSH/POP, and MOVes from any general 
register to any general register; from any memory location 
(indexed if you like) to any register; and (this is most often 
overlooked) from any register TO memory.  The only thing you 
can't do in general is memory-to-memory.  Among the more common 
operations that inexperienced 86 programmers overlook are: 

   * setting memory variables to immediate values
   * testing memory variables, and comparing them to constants
   * preserving memory variables by PUSHing and POPping them
   * incrementing and decrementing memory variables
   * adding into memory variables

                                                          6-4
Encoding of Effective Addresses

Unless you are concerned with the nitty-gritty details of 86 
instruction encoding, you don't need to read this section.  

Every instruction with an effective address has an encoded byte, 
known as the effective address byte, following the 1-byte opcode 
for the instruction. (For obscure reasons, Intel calls this byte 
the ModRM byte.)  If the effective address is a memory variable, 
or an indexed memory location with a non-zero constant offset, 
then the effective address byte will be immediately followed by 
the offset amount.  Amounts in the range -128 to +127 are given 
by a single signed byte, denoted by "d8" in the table below.  
Amounts requiring a 2-byte representation are denoted by "d16" in 
the table below.  As with all 16-bit memory quantities in the 86 
family, the word is stored with the least significant byte FIRST.  

The following table of effective address byte values is organized 
into 32 rows and 8 columns.  The 32 rows give the possible values 
for the effective address operand: 8 registers and 24 memory 
indexing modes.  A 25th indexing mode, [BP] with zero 
displacement, has been pre-empted by the simple-memory-variable 
case.  If you code [BP] with no displacement, you will get 
[BP]+d8, with a d8-value of zero.  

The 8 columns of the table reflect further information given by 
the effective address byte.  Usually, this is the identity of the 
other (always a register) operand of a 2-operand instruction.  
Those instructions are identified by a "/r" following the opcode 
byte in the instruction list.  Sometimes, the information given 
supplements the opcode byte in identifying the instruction 
itself.  Those instructions are identified by a "/" followed by a 
digit from 0 through 7.  The digit tells which of the 8 columns 
you should use to find the effective address byte.  

For example, suppose you have a perverse wish to know the precise 
bytes encoded by the instruction SUB B[BX+17],100.  This 
instruction subtracts an immediate quantity, 100, from an 
effective address quantity, B[BX+17].  By consulting the 
instruction list, you find the general form SUB eb,ib.  The 
opcode bytes given there are 80 /5 ib.  The "/5" denotes an 
effective-address byte, whose value will be taken from column 5 
of the table below.  The offset 17 decimal, which is 11 hex, will 
fit in a single "d8" byte, so we take our value from the "[BX] + 
d8" row.  The table tells us that the effective address byte is 
6F.  Immediately following the 6F is the offset, 11 hex.  
Following that is the ib-value of 100 decimal, which is 64 hex.  
So the bytes generated by SUB B[BX+17],100 are 80 6F 11 64.  

                                                          6-5

Table of Effective Address byte values

s  =    ES   CS   SS   DS
rb =    AL   CL   DL   BL   AH   CH   DH   BH
rw =    AX   CX   DX   BX   SP   BP   SI   DI
digit=   0    1    2    3    4    5    6    7
                                               Effective
EA byte                                         address:
values: 00   08   10   18   20   28   30   38    [BX + SI]
        01   09   11   19   21   29   31   39    [BX + DI]
        02   0A   12   1A   22   2A   32   3A    [BP + SI]
        03   0B   13   1B   23   2B   33   3B    [BP + DI]
        04   0C   14   1C   24   2C   34   3C    [SI]
        05   0D   15   1D   25   2D   35   3D    [DI]
        06   0E   16   1E   26   2E   36   3E    d16 (simple var)
        07   0F   17   1F   27   2F   37   3F    [BX]
        40   48   50   58   60   68   70   78    [BX + SI] + d8
        41   49   51   59   61   69   71   79    [BX + DI] + d8
        42   4A   52   5A   62   6A   72   7A    [BP + SI] + d8
        43   4B   53   5B   63   6B   73   7B    [BP + DI] + d8
        44   4C   54   5C   64   6C   74   7C    [SI] + d8
        45   4D   55   5D   65   6D   75   7D    [DI] + d8
        46   4E   56   5E   66   6E   76   7E    [BP] + d8
        47   4F   57   5F   67   6F   77   7F    [BX] + d8
        80   88   90   98   A0   A8   B0   B8    [BX + SI] + d16
        81   89   91   99   A1   A9   B1   B9    [BX + DI] + d16
        82   8A   92   9A   A2   AA   B2   BA    [BP + SI] + d16
        83   8B   93   9B   A3   AB   B3   BB    [BP + DI] + d16
        84   8C   94   9C   A4   AC   B4   BC    [SI] + d16
        85   8D   95   9D   A5   AD   B5   BD    [DI] + d16
        86   8E   96   9E   A6   AE   B6   BE    [BP] + d16
        87   8F   97   9F   A7   AF   B7   BF    [BX] + d16
        C0   C8   D0   D8   E0   E8   F0   F8    ew=AX   eb=AL
        C1   C9   D1   D9   E1   E9   F1   F9    ew=CX   eb=CL
        C2   CA   D2   DA   E2   EA   F2   FA    ew=DX   eb=DL
        C3   CB   D3   DB   E3   EB   F3   FB    ew=BX   eb=BL
        C4   CC   D4   DC   E4   EC   F4   FC    ew=SP   eb=AH
        C5   CD   D5   DD   E5   ED   F5   FD    ew=BP   eb=CH
        C6   CE   D6   DE   E6   EE   F6   FE    ew=SI   eb=DH
        C7   CF   D7   DF   E7   EF   F7   FF    ew=DI   eb=BH

d8 denotes an 8-bit displacement following the EA byte,
to be sign-extended and added to the index.

d16 denotes a 16-bit displacement following the EA byte,
to be added to the index.

Default segment register is SS for effective addresses containing
a BP index; DS for other memory effective addresses.

                                                          6-6
How to Read the Instruction Set Chart

The chart below summarizes the machine instructions you can 
program with A86.  In order to use the chart, you need to learn 
the meanings of the specifiers (each given by 2 lower-case 
letters), that follow most of the instruction mnemonics.  Each 
specifier indicates the type of operand (register byte, immediate 
word, etc.) that follows the mnemonic to produce the given 
opcodes.  

"c" means the operand is a code label, pointing to a part of the 
    program to be jumped to or called.  A86 will also accept a 
    constant offset in this place (or a constant segment-offset 
    pair in the case of "cd").  "cb" is a label within about 128 
    bytes (in either direction) of the current location.  "cw" is 
    a label within the same code segment as this program; "cd" is 
    a pair of constants separated by a colon-- the segment value 
    to the left of the colon, and the offset to the right.  Note 
    that in both the cb and cw cases, the object code generated 
    is the offset from the location following the current 
    instruction, not the absolute location of the label operand.  
    In some assemblers (most notably for the Z-80 processor) you 
    have to code this offset explicitly by putting "$-" before 
    every relative jump operand in your source code.  You do NOT 
    need to, and should not do so with A86.  

"e" means the operand is an Effective Address.  The concept of an 
    Effective Address is central to the 86 machine architecture, 
    and thus to 86 assembly language programming.  It is 
    described in detail at the start of Chapter 8.  We summarize 
    here by saying that an Effective Address is either a general-
    purpose register, a memory variable, or an indexed memory 
    quantity.  For example, the instruction "ADD rb,eb" includes 
    the instructions: ADD AL,BL, or ADD CH,BYTEVAR, or ADD 
    DL,B[BX+17].  

"i" means the operand is an immediate constant, provided as part 
    of the instruction itself.  "ib" is a byte-sized constant; 
    "iw" is a constant occupying a full 16-bit word.  The operand 
    can also be a label, defined with a colon.  In that case, the 
    immediate constant which is the location of the label is 
    used.  Examples:  "MOV rw,iw" includes the instructions: MOV 
    AX,17, or MOV SI,VAR_ARRAY, where "VAR_ARRAY:" appears 
    somewhere in the program, defined with a colon.  NOTE that if 
    VAR_ARRAY were defined without a colon, e.g., "VAR_ARRAY DW 
    1,2,3", then "MOV SI,VAR_ARRAY" would be a "MOV rw,ew" NOT a 
    "MOV rw,iw".  The MOV would move the contents of memory at 
    VAR_ARRAY (in this case 1) into SI, instead of the location 
    of the memory. To load the location, you can code "MOV 
    SI,OFFSET VAR_ARRAY".  

"m" means a memory variable or an indexed memory quantity; i.e., 
    any Effective Address EXCEPT a register.  

"r" means the operand is a general-purpose register.  The 8 "rb" 
    registers are AL,BL,CL,DL,AH,BH,CH,DH; the 8 "rw" registers 
    are AX,BX,CX,DX,SI, DI,BP,SP.