02200000000801
1
2
9[...............................................................]0
�ASSEMBLY LANGUAGE COURSE PART VI €by Mark van den Boer

‰Shift and Rotate Operations€

Instruction:   ASL
Syntax:        ASL #,Dn (the immediate operand always modulo 8)
               ASL Dn,Dn (the first operand always modulo 8)
               ASL <ea>
Data sizes:    byte,  word,  long  except for ASL <ea> which  only
               allows word and long as data sizes.
Condition codes affected:
               X    set to the last bit shifted out
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    set  if  the most significant bit  is  changed
                    during the operation
               C    see the X-bit





Addressing modes allowed with the ASL <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform  a shift left of the destination  operand.  This
          instruction can be used as a fast form of multiplying an
          operand  with a power of two.  On a processor  like  the
          6502  this  instruction  is the only way  to  perform  a
          multiply operation.  The lower bit of the destination is
          always set to zero.
Examples:
Instruction              Before         After
ASL.L d0,d1              d0=33333333    d0=33333333
                         d1=00000005    d1=00000028
ASL.W $4ee               $4ee=0009      $4ee=0012


Instruction:   ASR
Syntax:        ASR #,Dn (the immediate operand always modulo 8)
               ASR Dn,Dn (the first operand always modulo 8)
               ASR <ea>
Data sizes:    byte,  word,  long  except for ASR <ea> which  only
               allows word and long as data sizes.
Condition codes affected:
               X    set to the last bit shifted out
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    set  if  the most significant bit  is  changed
                    during the operation
               C    see the X-bit
Addressing modes allowed with the ASR <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform a shift right of the destination  operand.  This
          instruction  can be used as a fast form of  dividing  an
          operand  with a power of two.  On a processor  like  the
          6502  this  instruction  is the only way  to  perform  a
          divide  operation.  The upper bit (sign bit)  is  always
          repeated.
Examples:
Instruction              Before         After
ASR.L d0,d1              d0=33333333    d0=33333333
                         d1=00000005    d1=00000002
ASR.W $4ee               $4ee=8009      $4ee=c004


Instruction:   LSL
See the ASL instruction.  The LSL instruction is exactly the same.
At the moment I haven't got the machine codes for the ASL and LSL
operations  but I think that even the machine codes are the  same.
E.g.  on the 6809 both ASL and LSL exist but translate to the same
machine code.



Instruction:   LSR
Syntax:        LSR #,Dn (the immediate operand always modulo 8)
               LSR Dn,Dn (the first operand always modulo 8)
               LSR <ea>
Data sizes:    byte,  word,  long  except for LSR <ea> which  only
               allows word and long as data sizes.
Condition codes affected:
               X    set to the last bit shifted out
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    set  if  the most significant bit  is  changed
                    during the operation
               C    see the X-bit
Addressing modes allowed with the LSR <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform a shift right of the destination  operand.  This
          instruction differs from ASR in that the high order  bit
          is always cleared.
Examples:
Instruction              Before         After
LSR.L d0,d1              d0=33333333    d0=33333333
                         d1=00000005    d1=00000002
LSR.W $4ee               $4ee=0009      $4ee=0004


Instruction:   ROL
Syntax:        ROL #,Dn (the immediate operand always modulo 8)
               ROL Dn,Dn (the first operand always modulo 8)
               ROL <ea>
Data sizes:    byte, word, long
Condition codes affected:
               X    not affected
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    always cleared
               C    set to the last bit shifted out the operand

Addressing modes allowed with the ROL <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform  a  bitwise  rotate  left  of  the   destination
          operand.
Examples:
Instruction              Before         After
ROL.L d0,d1              d0=00000001    d0=00000001
                         d1=88000001    d1=10000002  (C bit set)
ROL.W $4ee               $4ee=8009      $4ee=0012






Instruction:   ROR
Syntax:        ROR #,Dn (the immediate operand always modulo 8)
               ROR Dn,Dn (the first operand always modulo 8)
               ROR <ea>
Data sizes:    byte, word, long
Condition codes affected:
               X    not affected
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    always cleared
               C    set to the last bit shifted out the operand
Addressing modes allowed with the ROR <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform  a  bitwise  rotate  right  of  the  destination
          operand.
Examples:
Instruction              Before         After
ROR.L d0,d1              d0=00000001    d0=00000001
                         d1=88000001    d1=c4000000  (C bit set)
ROR.W $4ee               $4ee=8009      $4ee=c004


Instruction:   ROXL
Syntax:        ROXL #,Dn (the immediate operand always modulo 8)
               ROXL Dn,Dn (the first operand always modulo 8)
               ROXL <ea>
Data sizes:    byte, word, long
Condition codes affected:
               X    set to the last bit shifted out the operand
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    always cleared
               C    set to the last bit shifted out the operand




Addressing modes allowed with the ROXL <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l
Function: Perform  a  bitwise  rotate  left  of  the   destination
          operand.  There  is very little difference with the  ROL
          instruction.  By  the way,  it is very handy to  have  a
          wordprocessor    with   cut/paste    and    find/replace
          facilities.  All  I  did was cut out  the  complete  ROL
          instruction and replaced all ROL's by ROXL's.
Examples:
Instruction              Before         After
ROXL.L d0,d1             d0=00000001    d0=00000001
                         d1=88000001    d1=10000002
ROXL.W $4ee              $4ee=8009      $4ee=0012


Instruction:   ROXR
Syntax:        ROXR #,Dn (the immediate operand always modulo 8)
               ROXR Dn,Dn (the first operand always modulo 8)
               ROXR <ea>
Data sizes:    byte, word, long
Condition codes affected:
               X    set to the last bit shifted out the operand
               N    set to the most significant bit of the result
               Z    set if the result is zero, cleared otherwise
               V    always cleared
               C    set to the last bit shifted out the operand
Addressing modes allowed with the ROXR <ea> instruction:
Destination:
          (An)
          (An)+
          -(An)
          w(An)
          b(An,Rn)
          w
          l


Function: Perform  a  bitwise  rotate  right  of  the  destination
          operand.  There  is very little difference with the  ROR
          instruction.  By  the way,  it is very handy to  have  a
          wordprocessor    with   cut/paste    and    find/replace
          facilities.  All  I  did was cut out the  complete  ROXL
          instruction and replaced all ROXL's by ROXR's.
Examples:
Instruction              Before         After
ROXR.L d0,d1             d0=00000001    d0=00000001
                         d1=88000001    d1=10000002
ROXR.W $4ee              $4ee=8009      $4ee=0012

Originally published in �ST NEWS€ Volume 2 Issue 5.