02200000000801
1
2
9[...............................................................]0
�MC 68000 ASSEMBLY LANGUAGE COURSE PART VIII €by Mark van den Boer

‰Program Control Instructions€

This  class of instructions enables a programmer to create  loops 
and  IF-THEN-ELSE  like  decisions.  That's  why  it's  �the€  most 
important group of instructions and every programmer should  have 
a  thorough knowledge of this group.  This class of  instructions 
are specifically meant to affect the program counter.

Instructions:  Bcc  (cc stands for Condition Code)
Syntax:        Bcc  <address>
Data sizes:    Byte  or word.  This implicates that  the  branch-
               instructions  can branch in an area of  32K.  When 
               using a branch with a byte offset you can put a .S 
               suffix behind the instruction e.g.  BEQ.S  .  When 
               using a branch with a word offset you can put a .W 
               suffix behind the instruction e.g.  BEQ.W  .  Most 
               assemblers  will  determine if the short  or  word 
               form is needed. Also most assemblers will optimize 
               word-branches to byte-branches whenever possible.

Condition codes affected:
               None
Function: Test  a  combination of the NZVC-flags in  the  status-
          register and conditionally perform a branch to  another 
          address. If the testing of the condition codes is true, 
          then  the  branch  will be  taken,  in  the  other  the 
          instruction  immediately following the Bcc  instruction 
          will  be executed. A total of 15 possible variations of 
          this instruction are listed below.
          BCC: where  CC stands for Carry Clear.  The  branch  is 
               taken if the C-bit is 0. This instruction is often 
               used   in  combination  with  shift   and   rotate 
               instructions.
          BCS: where CS stands for Carry Set. The branch is taken 
               if  the  C-bit  is  1.  This  instruction  is  the 
               counterpart of the BCC-instruction.
          BEQ: where EQ stand for EQual.  The branch is taken  if 
               the  Z-bit is 1.  This instruction is  often  used 
               after a TST-instruction or CMP-instruction.
          BNE: where NE stands for Not Equal. The branch is taken 
               if  the  Z-bit  is  0.  This  instruction  is  the 
               counterpart of the BNE-instruction.
          BPL: where PL stands for PLus.  The branch is taken  if 
               the  N-bit is 0.  This instruction is  often  used 
               after a TST-instruction or CMP-instruction.
          BMI: where MI stands for MInus.  The branch is taken if 
               the   N-bit  is  1.   This  instruction   is   the 
               counterpart of the BPL-instruction.
          BVC: where VC stands for oVerflow Clear.  The branch is 
               taken if the V-bit is 0. This instruction is often 
               used after an Integer Arithmetic instruction  like 
               ADD, SUB, MUL etc.
          BVS: where  VS stands for oVerflow Set.  The branch  is 
               taken if the V-bit is 1.  This instruction is  the 
               counterpart of the BVC-instruction.
          BRA: where   RA   stands  for   bRanch   Always.   This 
               instruction is often used at the end of a loop  to 
               go back to the beginning of the loop.
         Branches often used after an arithmetic operation on
         two's complement numbers.
          BGE: where GE stands for Greater or Equal.  This branch 
               is  taken  if the N and V-bits  contain  the  same 
               value.

          BGT: where GT stands for Greater Than.  This branch  is 
               taken in the following cases:
               - N is 1, V is 1, Z is 0
               - N is V is Z is 0
          BLE: where LE stands for Lower or Equal. This branch is 
               taken in the following cases:
               - Z is 1
               - N and V-bits contain different values
          BLT: where  LT  stands for Less Than.  This  branch  is 
               taken  if  the  N  and  V-bits  contain  different 
               values.
         Brances often used after an arithmetic operation on
         unsigned numbers.
          BHI: where HI stands for HIgher.  This branch is  taken 
               if the N and V-bits contain the same value.
          BLS: where LS stands for Lower or Same.  This branch is 
               taken  if  the  C  and  Z-bits  contain  different 
               values.
Example:
          This  shows  a piece of a C-program and  an  equivalent 
          piece  of  a PASCAL-program which are  translated  into 
          assembler. (variabele is signed)
          C:
               if (variable == 1 || variable > 4) variable = 5;
               else var *= 3;
          PASCAL:
               if (variable == 1) or (variable > 4)
               then variable := 5
               else variable := variable * 3

          * Most assemblers will optimize the branch-instructions
          * to the short forms
                 CMP.W   #1,variable
                 BEQ     L10000
                 CMP.W   #4,variable
                 BLE     L2
          L10000:
                 MOVE.W  #5,variable
                 BRA     L3
          L2:
                 MOVE.W  variable,R0
                 MULS    #3,R0
                 MOVE.W  R0,variable
          L3:
Instructions:  DBcc  (cc stands for Condition Code)
Syntax:        DBcc  Dn,<address>
Data sizes:    byte  or word.  This implicates that  the  branch-
               instructions can branch in an area of 32K.  Dn  is 
               considered to contain a word.
Condition codes affected:
               None
Function:
          The  group of Decrement and Branch (DBcc)  instructions 
          provide  an efficient way of creating loops.  They  are 
          nearly  always placed at the end of a loop.  First  the 
          condition   is  tested,   then  the   dataregister   is 
          decremented.  The  branch  is taken  in  the  following 
          cases:
          - Dn is -1;
          - The condition cc in DBcc is satisfied.
          There  are 16 possible variations of this  instruction. 
          They  all are nearly the same as the  Bcc-instructions, 
          with two exceptions. These are:
          DBF or DBRA:
               This  loop can only be terminated by  count  since 
               the other condition can never be satisfied.
          DBT: Only performs a decrement on the dataregister  and 
               never branches.  To me this seems a pretty useless 
               instruction,  which is only there to make the DBcc 
               series logically complete.
Example:
          This  piece of code is an efficient  implementation  of 
          the strcpy-function of the C-language.  A0 contains the 
          address  of  the  source string  and  A1  contains  the 
          address  of the destination string.  In C the end of  a 
          string is marked by a byte containing 0.
                 MOVE.W  #$ffff,D0
          LOOP:  MOVE.B  (A0)+,(A1)+
                 DBEQ    D0,LOOP
          This  piece of code can easily be transformed into  the 
          strncpy-function  by  loading D0 with  the  appropriate 
          value.


Instructions:  Scc  (cc stands for Condition Code)
Syntax:        Scc  <address>
Data sizes:    byte.

Condition codes affected:
               None
Function: Sets a byte to $ff if the condition codes satisfie.  If 
          the  condition is not satisfied the byte is set  to  0. 
          This  group of 16 instructions is rarely  used.  Nearly 
          all forms are the same as the DBcc group except for the 
          following two instructions:
          SF:  the same as a CLR.B instruction
          ST:  the same as a MOVE.B #$ff, <address>
Example:
          Be inventive, invent one yourself!


Instruction:   BSR, JSR
Syntax:        BSR  <address>
               JSR  <address>
Data sizes:    none
Condition codes affected:
               none



Addressing modes allowed (only for JSR):
Destination:
          (An)
          w(An)
          b(An,Rn)
          w
          l
          w(PC)
          b(PC,Rn)
Function: The  BSR  (Branch  to  SubRoutine)  and  JSR  (Jump  to 
          SubRoutine)   instructions   are   used   for   calling 
          subroutines.  BSR  can branch in a range  of  32K.  JSR 
          should  be  used when a jump out of the  32K  range  is 
          needed.   Some   assemblers  optimize  JSR   into   BSR 
          instructions  whenever  possible,  since  BSR  is  more 
          efficient   than   JSR.   When  executing   a   BSR/JSR 
          instruction,  the  68000 first pushes the PC  (program-
          counter) on the stack and then load the PC with the new 
          address. See below for the RTS (ReTurn from Subroutine) 
          instruction.


Instruction:   RTS
Syntax:        RTS
Data sizes:    none
Condition codes affected:
               none
Function: Counterpart  of BSR/JSR instructions.  Reloads  the  PC 
          with  the value on top of the stack.  This  value  will 
          nearly  always have been put on top of the stack  by  a 
          BSR/JSR instruction.
Example:  * the strcpy function discussed before
          STRCPY:
                 MOVE.W  #$FFFF,D0
          LOOP:  MOVE.W  (A0)+,(A1)+
                 DBEQ    D0, LOOP
                 RTS
          * some other code
          BEGIN:
                 MOVE.L  #SOURCE,A0
                 MOVE.L  #DEST,A1
                 JSR     STRCPY
                 RTS

          * the strings are put in a data area
          .DATA
          * 80 bytes for every string
          SOURCE .DS.B   80
          DEST   .DS.B   80
          * .DS.B means Define Storage Byte
          * so 80 bytes are define as storage for each string


Instruction:   JMP
Syntax:        JMP  <ea>
Data sizes:    none
Condition codes affected:
               none








Addressing modes allowed:
Destination:
          (An)
          w(An)
          b(An,Rn)
          w
          l
          w(PC)
          b(PC,Rn)
Function: Transfer program control to another address.  The PC is 
          loaded  with the specified address.  In fact this is  a 
          variant  of  the MOVE instruction.  In  this  case  the 
          destination register is inherently defined,  namely the 
          PC-register.  Therefore we could translate JMP <ea>  to 
          MOVE.L <ea>,PC .

Instruction:   RTR
Syntax:        RTR
Data sizes:    none
Condition codes affected:
               none

Function: ReTurn    and   Restore.    Counterpart   of    BSR/JSR 
          instructions.  Reloads the PC with the value on top  of 
          the stack.  This value will nearly always have been put 
          on top of the stack by a BSR/JSR instruction.  The only 
          difference  with the RTS is that with this  instruction 
          also  the CCR is reloaded.  This instruction is  rarely 
          used  but  comes  in  handy when  one  doesn't  want  a 
          subroutine to influence the condition codes. Before the 
          JSR instruction you should use the instruction:
          MOVE.B CCR,-(A7)
          which pushes the CCR on the stack

Next time:  The last part of the instruction set.  These are  the 
instructions  which can only be executed when supervisor-mode  is 
active.

Originally published in �ST NEWS€ Volume 2 Issue 8.