.HM A 1 1 1 1 1 1
.H 1 "Appendix for as2650 Frankenstein Assembler"
.H 2 "Pseudo Operations"
.H 3 "Standard Pseudo Operation Mnemonics"
.VL 40 5 1
.LI "End"
END
.LI "File Inclusion"
INCL
INCLUDE
.LI "If"
IF
.LI "Else"
ELSE
.LI "End If"
ENDI
.LI "Equate"
EQU
.LI "Set"
SET
.LI "Org"
ORG
.LI "Reserve Memory"
RES
RESERVE
RMB
.LI "Define Byte Data"
BYTE
DATA
DB
FCB
.LI "Define Word Data"
DW
FDB
WORD
.LI "Define String Data"
FCC
STRING
.LI "Define Character Set Translation"
CHARSET
.LI "Define Character Value"
CHARDEF
CHD
.LI "Use Character Translation"
CHARUSE
.LE
.H 3 "Machine Dependent Pseudo Operations"
.H 4 "Define Address Constant"
.DS I N
[Label] ACON expression [, expression] ...
.DE
The acon statement generates a two byte integer for each expression in the
expression list.
Each expression is limited in value from 0 to 32767, values outside this 
range will result in an "expression exceeds available field width" error.
There can be up to 128 expressions on the line, within the line length limit.
The optional label is set to the address of the first expression.
.H 2 "Instructions"
.H 3 "Instruction List"
.TS H
;
l l l.
Opcode	Syntax	Selection Criteria
.sp
.TH
.sp
ADDA	 ',' REG  expr
ADDA	 ',' REG '*' expr ',' REG ',' '+' 
ADDA	 ',' REG '*' expr ',' REG ',' '-' 
ADDA	 ',' REG '*' expr ',' REG
ADDA	 ',' REG '*' expr 
ADDA	 ',' REG expr ',' REG ',' '+'
ADDA	 ',' REG expr ',' REG ',' '-' 
ADDA	 ',' REG expr ',' REG
.sp
ADDI	 ',' REG expr
.sp
ADDR	 ',' REG '*' expr 
ADDR	 ',' REG expr
.sp
ADDZ	 REG
.sp
ANDA	 ',' REG  expr
ANDA	 ',' REG '*' expr ',' REG ',' '+' 
ANDA	 ',' REG '*' expr ',' REG ',' '-' 
ANDA	 ',' REG '*' expr ',' REG
ANDA	 ',' REG '*' expr 
ANDA	 ',' REG expr ',' REG ',' '+'
ANDA	 ',' REG expr ',' REG ',' '-' 
ANDA	 ',' REG expr ',' REG
.sp
ANDI	 ',' REG expr
.sp
ANDR	 ',' REG '*' expr 
ANDR	 ',' REG expr
.sp
ANDZ	 REG	REG1
ANDZ	 REG	REG2
ANDZ	 REG	REG3
.sp
BCFA	 ',' CONDITION '*' expr 	COND0
BCFA	 ',' CONDITION '*' expr 	COND1
BCFA	 ',' CONDITION '*' expr 	COND2
BCFA	 ',' CONDITION expr	COND0
BCFA	 ',' CONDITION expr	COND1
BCFA	 ',' CONDITION expr	COND2
.sp
BCFR	 ',' CONDITION '*' expr 	COND0
BCFR	 ',' CONDITION '*' expr 	COND1
BCFR	 ',' CONDITION '*' expr 	COND2
BCFR	 ',' CONDITION expr	COND0
BCFR	 ',' CONDITION expr	COND1
BCFR	 ',' CONDITION expr	COND2
.sp
BCTA	 ',' CONDITION '*' expr 
BCTA	 ',' CONDITION expr
.sp
BCTR	 ',' CONDITION '*' expr 
BCTR	 ',' CONDITION expr
.sp
BDRA	 ',' REG '*' expr 
BDRA	 ',' REG expr
.sp
BDRR	 ',' REG '*' expr 
BDRR	 ',' REG expr
.sp
BIRA	 ',' REG '*' expr 
BIRA	 ',' REG expr
.sp
BIRR	 ',' REG '*' expr 
BIRR	 ',' REG expr
.sp
BRNA	 ',' REG '*' expr 
BRNA	 ',' REG expr
.sp
BRNR	 ',' REG '*' expr 
BRNR	 ',' REG expr
.sp
BSFA	 ',' CONDITION '*' expr 	COND0
BSFA	 ',' CONDITION '*' expr 	COND1
BSFA	 ',' CONDITION '*' expr 	COND2
BSFA	 ',' CONDITION expr	COND0
BSFA	 ',' CONDITION expr	COND1
BSFA	 ',' CONDITION expr	COND2
.sp
BSFR	 ',' CONDITION '*' expr 	COND0
BSFR	 ',' CONDITION '*' expr 	COND1
BSFR	 ',' CONDITION '*' expr 	COND2
BSFR	 ',' CONDITION expr	COND0
BSFR	 ',' CONDITION expr	COND1
BSFR	 ',' CONDITION expr	COND2
.sp
BSNA	 ',' REG '*' expr 
BSNA	 ',' REG expr
.sp
BSNR	 ',' REG '*' expr 
BSNR	 ',' REG expr
.sp
BSTA	 ',' CONDITION '*' expr 
BSTA	 ',' CONDITION expr
.sp
BSTR	 ',' CONDITION '*' expr 
BSTR	 ',' CONDITION expr
.sp
BSXA	 '*' expr ',' REG	REG3
BSXA	 expr ',' REG	REG3
.sp
BXA	 '*' expr ',' REG	REG3
BXA	 expr ',' REG	REG3
.sp
COMA	 ',' REG  expr
COMA	 ',' REG '*' expr ',' REG ',' '+' 
COMA	 ',' REG '*' expr ',' REG ',' '-' 
COMA	 ',' REG '*' expr ',' REG
COMA	 ',' REG '*' expr 
COMA	 ',' REG expr ',' REG ',' '+'
COMA	 ',' REG expr ',' REG ',' '-' 
COMA	 ',' REG expr ',' REG
.sp
COMI	 ',' REG expr
.sp
COMR	 ',' REG '*' expr 
COMR	 ',' REG expr
.sp
COMZ	 REG
.sp
CPSL	 expr
.sp
CPSU	 expr
.sp
DAR	 ',' REG
.sp
EORA	 ',' REG  expr
EORA	 ',' REG '*' expr ',' REG ',' '+' 
EORA	 ',' REG '*' expr ',' REG ',' '-' 
EORA	 ',' REG '*' expr ',' REG
EORA	 ',' REG '*' expr 
EORA	 ',' REG expr ',' REG ',' '+'
EORA	 ',' REG expr ',' REG ',' '-' 
EORA	 ',' REG expr ',' REG
.sp
EORI	 ',' REG expr
.sp
EORR	 ',' REG '*' expr 
EORR	 ',' REG expr
.sp
EORZ	 REG
.sp
HALT	
.sp
IORA	 ',' REG  expr
IORA	 ',' REG '*' expr ',' REG ',' '+' 
IORA	 ',' REG '*' expr ',' REG ',' '-' 
IORA	 ',' REG '*' expr ',' REG
IORA	 ',' REG '*' expr 
IORA	 ',' REG expr ',' REG ',' '+'
IORA	 ',' REG expr ',' REG ',' '-' 
IORA	 ',' REG expr ',' REG
.sp
IORI	 ',' REG expr
.sp
IORR	 ',' REG '*' expr 
IORR	 ',' REG expr
.sp
IORZ	 REG
.sp
LODA	 ',' REG  expr
LODA	 ',' REG '*' expr ',' REG ',' '+' 
LODA	 ',' REG '*' expr ',' REG ',' '-' 
LODA	 ',' REG '*' expr ',' REG
LODA	 ',' REG '*' expr 
LODA	 ',' REG expr ',' REG ',' '+'
LODA	 ',' REG expr ',' REG ',' '-' 
LODA	 ',' REG expr ',' REG
.sp
LODI	 ',' REG expr
.sp
LODR	 ',' REG '*' expr 
LODR	 ',' REG expr
.sp
LODZ	 REG	REG0
LODZ	 REG	REG1
LODZ	 REG	REG2
LODZ	 REG	REG3
.sp
LPSL	
.sp
LPSU	
.sp
NOP	
.sp
PPSL	 expr
.sp
PPSU	 expr
.sp
REDC	 ',' REG
.sp
REDD	 ',' REG
.sp
REDE	 ',' REG expr
.sp
RETC	 ',' CONDITION
.sp
RETE	 ',' CONDITION
.sp
RRL	 ',' REG
.sp
RRR	 ',' REG
.sp
SPSL	
.sp
SPSU	
.sp
STRA	 ',' REG  expr
STRA	 ',' REG '*' expr ',' REG ',' '+' 
STRA	 ',' REG '*' expr ',' REG ',' '-' 
STRA	 ',' REG '*' expr ',' REG
STRA	 ',' REG '*' expr 
STRA	 ',' REG expr ',' REG ',' '+'
STRA	 ',' REG expr ',' REG ',' '-' 
STRA	 ',' REG expr ',' REG
.sp
STRR	 ',' REG '*' expr 
STRR	 ',' REG expr
.sp
STRZ	 REG	REG1
STRZ	 REG	REG2
STRZ	 REG	REG3
.sp
SUBA	 ',' REG  expr
SUBA	 ',' REG '*' expr ',' REG ',' '+' 
SUBA	 ',' REG '*' expr ',' REG ',' '-' 
SUBA	 ',' REG '*' expr ',' REG
SUBA	 ',' REG '*' expr 
SUBA	 ',' REG expr ',' REG ',' '+'
SUBA	 ',' REG expr ',' REG ',' '-' 
SUBA	 ',' REG expr ',' REG
.sp
SUBI	 ',' REG expr
.sp
SUBR	 ',' REG '*' expr 
SUBR	 ',' REG expr
.sp
SUBZ	 REG
.sp
TMI	 ',' REG expr
.sp
TPSL	 expr
.sp
TPSU	 expr
.sp
WRTC	 ',' REG
.sp
WRTD	 ',' REG
.sp
WRTE	 ',' REG expr
.sp
ZBRR	 '*' expr 
ZBRR	 expr
.sp
ZBSR	 '*' expr 
ZBSR	 expr
.TE
.H 3 "Register and Condition Reserved Symbols"
The REG and CONDITION fields in instructions are restricted to only
the values available as reserved symbols. 
These are r0 - r3, or R0 - R3 for registers, and plus, PLUS, minus, MINUS, 
zero, ZERO, gt, GT, lt, LT, eq, EQ, un, UN, always, and ALWAYS for 
conditions.
.H 3 "Destination Register for Indexed Addressing"
If the destination register, the one adjacent to the opcode, is not R0 when
one of the absolute indexed addressing modes is used, an error is issued.
.H 3 "Selection Criteria Keywords"
.VL 10 5 
.LI "REG0 REG1 REG2 REG3"
.SP
Some instructions are restricted to a subset of the registers.
Only those instructions with the specified registers are valid.
.LI "COND0 COND1 COND2 COND3"
.SP
Some instructions are restricted to a subset of the conditions.
Only those instructions with the specified conditions are valid.
.VL 10 0 1
.LI "COND0"
EQ, or ZERO
.LI "COND1
GT, or PLUS
.LI "COND2"
LT, or MINUS
.LI "COND3"
ALWAYS, or UN
.LE
.LE
.H 3 "Apostrophes"
The apostrophes in the syntax field are a notation used for the
parser generator and are not put in the assembler source statement.
.H 2 "Notes"
.H 3 "Location Counter"
The Dollar Sign is used as the location counter symbol in this assembler.
.H 3 "Memory Addressing Error Messages"
.VL 5 0
.LI "ERROR - expression exceeds available field width"
.SP
This message occurs when :
.DL
.LI
The absolute branch address is to an invalid address, one greater than
32767.
.LI
The absolute or relative address was not in the present memory page.
.LI
The relative offset was outside the range that can be represented in 7 bits.
.LE
.LI "ERROR - instruction crosses page boundary"
.SP
The first and last bytes of an instruction are on different sides of an 8k 
page.
.LI "WARNING - Page Boundary"
.SP
The first byte of an instruction is on a 8k page boundry.
.H 3 "Page Wraparound for Relative Addressing"
The wraparound of an effective address, where a relative address from an
instruction near a page boundary accesses memory at the other side of the 
page, is not supported in this assembler and will result in one or more 
error messages.
.P
This does not apply to the ZBRR and ZBSR instructions.  
Memory destinations for these can range from 0 to $3f and $1fc0 to $1fff.
.H 3 "Relational Operators"
The relational operator keywords GT, LT, and EQ are not available.
The '<', '>', and '==' special character representations must be used.
.H 3 "Reserved Symbols"
.H 4 "Machine Dependent Reserved Symbols"
ALWAYS
AND
DEFINED
EQ
GE
GT
HIGH
LE
LOW
LT
MINUS
MOD
NE
NOT
OR
PLUS
R0
R1
R2
R3
SHL
SHR
UN
XOR
ZERO
always
and
defined
eq
ge
gt
high
le
low
lt
minus
mod
ne
not
or
plus
r0
r1
r2
r3
shl
shr
un
xor
zero
.TC 1 1 7