************************************
                    * 8-bit CPU Reassembler package    *
                    * incl. PurePASCAL GEM source code *
                    ************************************

Program author :

Jens Schulz
Rosenstrasse 5
D-25368 Kiebitzreihe
Germany

****************************************************************************

           Reassembler package for these 8-bit CPU processors :
           ----------------------------------------------------

       - INTEL 8051/52/252/535 microcontroller
       - INTEL 8048 microcontroller series
       - Zilog Z-80 CPU
       - Mostek/Rockwell 6502-CPU
       - Motorola 68HC11 microcontroller
       - INTEL 8080/85-CPU

*****************************************************************************

System: ATARI ST/TT/FALCON
        GEM / MultiTOS
        screen resolution independent > 640*400 dots
        requires 1 MB RAM

****************************************************************************

                   These programs are Freeware

You can copy and swap these programs freely without any charge. Sale or
use in any other software for profit is strict forbidden. It's free for
BBS downloading and PD collections.

***************************************************************************

               Special info for Mostek/Rockwell 6502
               -------------------------------------

                      Symbolic reassembling
                      ---------------------

Symbolic reassembling is only supported by the Z-80 and 6502 reassembler.
Z80 and 6502 processor are often used for homecomputers, like C64 or
Amstrad CPC 464.

For these homecomputers exist symbol tables of important ROM and port
addresses.

Main differences between disassembler and reassembler decoding :
----------------------------------------------------------------

 - Disassembler : generates jumps/absolute addresses in hexadecimal
                  terms, like LDA $12AE

 - Standard reassembler : generates jumps/absolute addresses in auto-
                          matic labels, like LDA L12AE. Reassembler
                          outputs are address inpendent for assemblers.

 - Symbolic reassembler : generates jumps/absolute addresses with your
                          symbols, like LDA VALUE_1. You can find
                          important ROM and port addresses much easier.

1. Definition of symbols
------------------------

    - max. 2000 symbols are allowed
    - max. symbol length = 8 characters

All symbols are written with a standard ASCII editor in an ASCII file.
The ASCII file has the file extension .LBI. The symbol addresses must
be specified in hexadecimal form.

    Symbol file example (6502.LBI):
    -------------------------------

    POS_1=203
    LOOP=20D
    LOOP_1=214
    SET_TST=219
    PROC_1=223
    PROC_2=22E
    VALUE_1 = 68
    VALUE_2 = 69

2. Import of ASCII symbols :
----------------------------

   -> Menu Symbols, Import symbols

   Symbol file has the file extension .LBI. The reassembler imports this
   file and sort it by address. Now you can use this symbols for your
   next reassembler run.

3. Generating of a symbol file
------------------------------

After the import of a symbol file, you can generate a compact label
file. This label file stores all symbolic informations in a compact
and sorted form. This label file will be loaded faster than a ASCII
symbol list.

Label symbol files has the file extension .SYM.

4. Load a symbol file
---------------------

The menu entry loads compact label symbol files with the file extension
.SYM.

*****************************************************************************

                      Special keyboard shortcuts
                      --------------------------

     Menu Symbols
     ------------

     Load symbols             Control U
     Import symbols           Control I
     Genaerate symbol file    Control E
     Show symbols             Key F3

*****************************************************************************

                 Standard ORG address of 6502 reassembler
                 ----------------------------------------

The 6502 reassembler uses the address $0200 as standard base address.
All other assemblers uses the address $0000 for start.

The address space $0000 to $01FF is used for the 6502 zeropage and
the stack.

*****************************************************************************

Jens Schulz
18th april 1994