Atari RGB to Composite Video Converter


                   RGB TO COMPOSITE VIDEO CONVERTER DOCUMENTATION
                                  December 27, 1986
                                     version 1.0








          The following document is placed in the public domain.   You  may
          make as many copies of it as you like and transmit it in any form
          you want provided it is not sold commercially,  nor  any  product
          derived from it is sold commercially. The author is not responsi-
          ble for any damage, physical, mental or otherwise caused by  fol-
          lowing  the  instructions  given  below.  Please mail corrections
          and/or suggestions for improvement to the address given below.


                                  Anees Munshi
                                  58 York Road
                                  Weston, Ontario
                                  M9R 3E6
                                  Canada.
                                  (416) 246-0670






























          27 Dec 1986             (C) Anees Munshi                        1






                       Atari RGB to Composite Video Converter


          1.  _I_N_T_R_O_D_U_C_T_I_O_N


               The schematic described in this document converts the analog

          RGB  video  signal  that is output by the ST to an NTSC composite

          signal which can be displayed on a colour or monochrome composite

          monitor,  or on a TV set by adding a modulator. Please be careful

          when building the circuit.  Should anything in the schematics  or

          this documentation seem suspicious, use your better judgement.  A

          certain amount of experience at building electronic circuits will

          be  very  helpful. Also, a good oscilloscope and knowledge of the

          theory of RGB to composite conversion may be necessary  in  order

          to  debug  the circuit (should you have to). I have tried to pro-

          vide some background in this article.



          2.  _A_N__O_V_E_R_V_I_E_W


               The MC1377 RGB to composite video  converter  IC  used  does

          most of the work in converting the red, green and blue signals to

          composite video.  The red, green, blue, horizontal sync and vert-

          ical  sync signals are taken from the ST and fed into the 1377. A

          colour burst carrier (3.579545 Mhz) is fed  in  from  a  separate

          oscillator [1].  The 1377 generates the R-Y,  B-Y  and  luminance

          signals  by  passing  the  red,  green and blue signals through a

          ________
           1.


              The separate oscillator is not really necessary since 1377
              contains a common-collector Colpitts oscillator which can be
              used to generate the colour-burst on-chip. However, I found
              it easier to generate the signal off-chip to make sure the
              thing is indeed oscillating.



          27 Dec 1986             (C) Anees Munshi                        2






                       Atari RGB to Composite Video Converter


          matrix.  Then, the B-Y signal is modulated using the colour-burst

          frequency  carrier,  and  the  R-Y signal is modulated using a 90

          deg. phase shifted carrier.  This results in the  I  and  Q  (in-

          phase  and  quadrature)  components of the chroma signal. The two

          components of the chroma signal are added and amplified and  made

          available  on  pin  13  of the chip. This allows the chroma to be

          band-pass filtered [2] externally and then fed back into pin  10.

          The  band-pass filter should be centered at the colour-burst fre-

          quency and should have a bandwidth of about 1.6 Mhz. Not having a

          very good colour TV to experment with, I chose to do an el-cheapo

          filter since it wouldn't make any difference on  my  set  anyway.

          (Besides,  I  plan to use my board on an old green-screen monitor

          to run an occasional colour-only program). A simple second  order

          LC  filter may be used. Set the resonant frequency of the tank to

          the colour-burst frequency, and choose an appropriate R  so  that

          you get the 1.6 Mhz bandwidth  [3].   Introducing  a  second  (or

          higher  order) BPF to do chroma-filtering will probably result in

          ________
           2.


              If the chroma signal is not band-pass filtered, the low
              frequency components it contains (those components having
              frequency less than 2Mhz or so) will interfere with the
              luminance signal since it is very hard to put the chroma
              specral lines exactly in between the luminance spectral lines
              without any interference between the two.

           3.


              Note Filter bandwidth = Wo/Q, where Wo is the resonant
              frequency in radians/second (Wo=2*PI*3.15 Mhz) and Q is the
              quality factor required. Q=R*sqrt(C/L). A few filters are
              sketched in the Motorola Application Notes if you don't want
              to design one. A reference to these notes is in the appendix.



          27 Dec 1986             (C) Anees Munshi                        3






                       Atari RGB to Composite Video Converter


          a visible delay on  the  chroma-signal.  So,  to  make  sure  the

          colours  are  not  offset  from  the  B&W image (like in sloppily

          coloured comic books), the luminance signal must  be  delayed  an

          equal  amount  so  that the luminance information is not ahead of

          the chrominance information.  To allow this, the luminance signal

          is  looped  out  from  pin-6  to  pin-8. An approprate delay line

          inserted between pin-6 and pin-8 will create the  required  delay

          [4].  The luminance signal does not need any filtering.






          3.  _I_N_T_E_R_F_A_C_I_N_G


               The horizontal and vertical synchs from the  Atari  must  be

          combined  and  fed  into  the  composite  synch input of the 1377

          (pin-2). The HSYNC and VSYNC are taken from the ST's monitor out-

          put,  AND-gated and fed into the comp-sync input. This works fine

          since the syncs are active low, TTL level signals and satisfy the

          (-0.6V, 0.9V) active and (1.7V, 8.2V) inactive threshold levels.


               The colour signals, red, green and blue must be capacitively

          coupled  through  22uF capacitors and attenuated through 2-4 Kohm

          resistors (in series with the input) so as to not interfere  with

          the  chip's bias and satisfy the 1Vp-p signal requirement respec-

          tively. All the three colour signals output  by  the  ST  have  a

          ________
           4.


              The Motorola Application notes show how to hook up a TDK
              delay line if you need one.



          27 Dec 1986             (C) Anees Munshi                        4






                       Atari RGB to Composite Video Converter


          1.8Vp-p range with a 1.2V DC bias. 1377 inputs: Pin 3: red input;

          Pin 4: green input; pin 5: blue input.


               The colour-burst carrier signal is generated as shown in the

          attached schematic and coupled to pin-17 through a 2.2Kohm resis-

          tor and a 0.1uF capacitor in series.


               The colour-burst is added after every sync pulse, (burst  is

          not  suppressed  after VSYNC) approximately 5.5us (micro-seconds)

          after the sync's leading edge and it lasts for approximately  3us

          or  10.7  cycles  of  the  carrier. This timing is done by an R-C

          timer in a fashion similar to an LM555 operating in astable mode.

          A  0.001uF capacitor is connected between pin 1 and ground, and a

          51Kohm resistor is connected between pin 1 and an 8.2V  reference

          (available  at  pin  16).  When  a  sync occurs, the capacitor is

          unclamped from ground and  begins  charging  through  the  51Kohm

          resistor  from  8.2V  DC. When the capacitor voltage reaches 1.0V

          (approx 5.5us after the sync), the colour-burst carrier is  gated

          on.  When the capacitor voltage reaches 1.3V, the colour-burst is

          gated off. The capacitor continues to charge  until  the  voltage

          reaches  5.0V.  At this point, the capacitor is discharged to 0V.

          Clearly, by changing the RC values (and hence the time-constant),

          the burst can be made shorter or longer (8 cycles of colour-burst

          is the NTSC spec, but I don't think a slightly longer period will

          hurt (gives the PLLs in the receiver plenty of time to lock)). If

          the time constant (Time const. = R*C) is increased the burst will

          occur  later  and last for a longer time. The converse is true if

          the time constant is decreased. If the time-constant is made  too



          27 Dec 1986             (C) Anees Munshi                        5






                       Atari RGB to Composite Video Converter


          long,  the  ramp  may not reach 5.0V before the next HSYNC, which

          will result in the some missing bursts (not  too  good).  If  you

          feel  like  it,  put a 50Kohm potentiometer instead of the 51Kohm

          resistor. You may be able to get some cheap special effects while

          calibrating the pot. :-)


               A chroma band-pass filter must be introduced between pins 13

          and  10  as  mentioned  before.   You may use the simple bandpass

          filter shown in the schematic, or to get better results, use  one

          of  the  many  shown in the Application Notes or design one your-

          self.  As mentioned before, if you design your  own,  the  filter

          should  have  a  bandwidth of about 1.6-2.0 Mhz and a center fre-

          quency of 3.58 Mhz. Since most colour TV's have  a  BW  around  3

          Mhz,  the BP filter will help reduce cross-talk between the lumi-

          nance and chroma components (on some TVs, you would never see the

          cross-talk  in all the noise!). If your TV has a comb filter, you

          won't need a fancy BP filter (and the corresponding delay  line);

          in  this  case,  the  simple  bandpass  filter  sketched  in  the

          schematic will do.


               Again, as mentioned before, if you do insert a  fancy  band-

          pass  filter  and  see a noticeable shift between the outlines of

          objects and their colour fill, you will need to put a delay  line

          between  pin 6 and 8.  The Motorola Application Notes should help

          in this department.


               Pin 20 must be grounded to select NTSC operation [5].
          ________
           5.




          27 Dec 1986             (C) Anees Munshi                        6






                       Atari RGB to Composite Video Converter


               Pin 19 provides  the  reference  voltage  for  the  voltage-

          controlled phase shifter (needed for I-Q phase shifting). It must

          be capacitively de-coupled to ground through a  0.01uF  capacitor

          to  provide a stable voltage reference at the pin. By pulling the

          pin up through a resistor to 8.2V, or by pulling it down  through

          a  resistor  to ground, the axes can be tilted to get some colour

          adjustment (about 7 degrees, for a slight effect,  according  the

          application notes).


               A 12V power supply is to be connected to pin 14.  The  power

          supply need not be regulated.


               The 8.2V DC reference voltage appears at pin  16.   A  0.1uF

          cap between pin 16 and ground will provide adequate filtering for

          this reference voltage.


               Pin 15 is the ground connection.


               Pins 11 and 12  are  coupled  through  0.1uF  capacitors  to

          ground.   By sourcing or sinking some current through these pins,

          whites may be made whiter and the blacks blacker (sounds  like  a

          detergent  commercial) by compensating for the balanced modulator

          feedthrough thus.


               Pin 7 is coupled to ground via a 0.01uF capacitor.

          _________________________________________________________________
              If pin-20 is connected to the power supply, PAL operation is
              selected.  For all you PAL hackers: If you replace the 3.58
              Mhz crystal with 4.43 Mhz crystal, and if you have a properly
              serrated vsync, you should be able to use this circuit to get
              PAL composite. If you do hack and get it working, please
              post.  (PAL is the colour system used in England, India and
              some other countries.)



          27 Dec 1986             (C) Anees Munshi                        7






                       Atari RGB to Composite Video Converter


               Pin 9 is the  composite  video  output.  It  has  an  output

          impedance  of about 50ohms. To drive a 75ohm monitor input termi-

          nal, put a 25 ohm resistor in series with pin 9 and a 75 ohm  co-

          axial  cable.  Connect the other end of the co-axial cable to the

          monitor.















































          27 Dec 1986             (C) Anees Munshi                        8






                       Atari RGB to Composite Video Converter


          4.  _C_O_N_S_T_R_U_C_T_I_O_N


               You will need to buy a _c_o_l_o_u_r monitor cable from Atari  [6].

          Start by cutting the cable in half. Then, strip about 2 inches of

          insulation off the end of the cable.  Now  carefully  remove  the

          shielding  without  cutting  the  wires  underneath.  This should

          expose 7 wires. Four of the wires are shielded themselves;  these

          are the red, green, blue and audio out wires. Strip the shielding

          off these wires as well.  The following is a colour-code chart to

          help you find the wires:

                  _c_o_l_o_u_r _o_f _w_i_r_e                  _s_i_g_n_a_l                  _p_i_n#





                  white                           RED output              7

                  red                             GREEN                   6

                  black                           BLUE                    10

                  yellow                          HSYNC                   9

                  blue                            VSYNC                   12

                  green                           AUDIO out               1

                  brown                           ground                  13









          ________
           6.


              If this is not available, you may kludge one up as mentioned
              in the Abacus _I_n_t_e_r_n_a_l_s book.)



          27 Dec 1986             (C) Anees Munshi                        9






                       Atari RGB to Composite Video Converter


                  The pins are labelled as follows (looking at the monitor

                  output plug from outside). Please test the cable with an

                  ohm-meter to see if my colour code is applicable to your

                  cable.


                  pin 4 -> 0 0 0 0 <- pin 1

                           0 0 0 0 <- pin 5

                           0 0 0 0 <- pin 9

                              0 <---- pin 13





               Solder the cable onto the board  you  will  be  using,  then

          solder  or  wire-wrap the circuit as shown in the schematic.  Try

          to keep the construction as clean as possible. Keep  as  much  of

          the  shielded  cables  shielded  as you can. Try to RF shield the

          whole enclosure if you can. All the best.


























          27 Dec 1986             (C) Anees Munshi                       10






                       Atari RGB to Composite Video Converter


          _B_i_b_l_i_o_g_r_a_p_h_y


             o+ Motorola Application Note AN-932


             o+ Motorola Linear Data Book


             o+ _C_o_m_m_u_n_i_c_a_t_i_o_n _S_y_s_t_e_m_s , Simon Haykin, Wiley 1983. pp. 168,

               169.












































          27 Dec 1986             (C) Anees Munshi                       11