ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC   Supplement to TheRef(tm) Drive & Controller Listing ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³   In "publishing" TheRef(tm), I've often been asked the difference ³±
       ³ between the types of drive controllers and recording methods.  I'm ³±
       ³ not going to get into that in this document, as it would require a ³±
       ³ good sized doc. of it's own.  What I have supplied are diagrams of ³±
       ³ the different connectors associated with the technology today.     ³±
       ³                                                                frf ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CABLES ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³            Controller     Drive 2(or none)       Drive 1           ³±
       ³                                                                    ³±
       ³              1ÉÍÍ» ÄÄÄÄÄÄÄÄÄ1ÉÍÍ» ÄÄÄÄstripeÄÄÄÄÄ1ÉÍÍ» Pins 10-16  ³±
       ³ FLOPPY cable  º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º are twisted ³±
       ³ with twist    º::ºðððððððððððºÃ´ºðððððððððððððXXððºÃ´º before the  ³±
       ³ (control &    º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º connector.  ³±
       ³ data, 34 pin) º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º  (7 wires)  ³±
       ³               ÈÍÍ¼           ÈÍÍ¼                 ÈÍÍ¼             ³±
       ³              1ÉÍÍ» ÄÄÄÄÄÄÄÄÄ1ÉÍÍ» ÄÄÄÄstripeÄÄÄÄÄ1ÉÍÍ» Pins 25-29  ³±
       ³ ST412 & ESDI  º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º are twisted ³±
       ³ Hard Drive    º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º before the  ³±
       ³ cable w/twist º::ºðððððððððððºÃ´ºðððððððððððððXXððºÃ´º connector.  ³±
       ³ (control)     º::ºðððððððððððºÃ´ºðððððððððððððððððºÃ´º  (5 wires)  ³±
       ³               ÈÍÍ¼           ÈÍÍ¼                 ÈÍÍ¼             ³±
       ³              1ÉÍÍ» ÄÄÄÄÄÄÄÄÄÄÄstripeÄÄÄÄÄÄÄÄÄÄÄÄÄ1ÉÍÍ» (no twists) ³±
       ³ ST412 & ESDI  º::ºððððððððððððððððððððððððððððððððºÃ´º Each drive  ³±
       ³ Hard Drive    º::ºððððððððððððððððððððððððððððððððºÃ´º has it's    ³±
       ³ (data, 20 pin)º::ºððððððððððððððððððððððððððððððððºÃ´º own data    ³±
       ³               ÈÍÍ¼                                ÈÍÍ¼ cable       ³±
       ³                                                                    ³±
       ³ IMPORTANT NOTE: Pin #1 on any drive cable SHOULD be indicated by a ³±
       ³                 a colored stripe.  If you should find the stripe   ³±
       ³                 by connector pin 34 (or 20), inspect the whole     ³±
       ³                 cable VERY throughly!                              ³±
       ³                                                                    ³±
       ³ DRIVE SELECT  For both Floppy and Hard drives, when the 34 pin     ³±
       ³ JUMPERS:      cable has a twist, the device number should be set   ³±
       ³               to the second position.  Drives numbered 0-3, set to ³±
       ³               1, those numbered 1-4, set to 2.  When cables with-  ³±
       ³               out a twist are used, Floppy "A", and(or) Hard drive ³±
       ³               "C" should be set to 1, and the second Floppy and    ³±
       ³               (or) Hard drive should be set to 2.                  ³±
       ³                                                                    ³±
       ³ TERMINATORS:  When using more than one drive on a cable (ie; 2FDs  ³±
       ³               or 2HDs), the terminating resistor pack should be    ³±
       ³               left on the drive furthest from the controller, and  ³±
       ³               removed from the drive closest to the controller.    ³±
       ³                                                                    ³±
       ³        NOTE:  On SCSI drives, the Host Adapter also has resistors. ³±
       ³               These are needed to terminate both ends of the bus.  ³±
       ³               Since the SCSI bus can have up to 7 devices attached ³±
       ³               to it, only the Host Adapter and the device farthest ³±
       ³               from it will retain the resistors.  All devices in-  ³±
       ³               between should have theirs removed.                  ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

       
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC                                                     2 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CONNECTIONS ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³ FLOPPY DRIVES                                      ÚÄÄÄÄÄ¿         ³±
       ³                                     HI/LO DENSITY >³2   1³ GND     ³±
       ³ The connector on a floppy drive               N/C  ³4 _ 3³  |      ³±
       ³ consists of 34 conductors.  Both              N/C  ³6   5³  |      ³±
       ³ control and data use this same              INDEX <³8   7³  |      ³±
       ³ cable.  Most cables have a twist    MOTOR ENAB. A >³10  9³  |      ³±
       ³ that interchanges pins 10 through    DRIVE SEL. B >³12 11³  |      ³±
       ³ 16 at the end of the cable (on       DRIVE SEL. A >³14 13³  |      ³±
       ³ drive 1).  Most floppy connect-     MOTOR ENAB. B >³16 15³  |      ³±
       ³ ors have a "key" between pins      DIRECTION SEL. >³18 17³  |      ³±
       ³ 4 & 6, and 3 & 5, to prevent the        HEAD STEP >³20 19³  |      ³±
       ³ cable from being reversed.  At         WRITE DATA >³22 21³  |      ³±
       ³ the other end,  the dual row con-      WRITE GATE >³24 23³  |      ³±
       ³ nector that attaches to the con-         TRACK 00 <³26 25³  |      ³±
       ³ troller card will usually have a    WRITE PROTECT <³28 27³  |      ³±
       ³ set of ridges that coincide with        READ DATA <³30 29³  |      ³±
       ³ cutouts in the controller card's      HEAD SELECT >³32 31³  |      ³±
       ³ connector.  Note that old style       DISK CHANGE <³34 33³ GND     ³±
       ³ floppy-only controllers used a                     ÀÄÄÄÄÄÙ         ³±
       ³ card-edge connector just like that        > Input   ( At the       ³±
       ³ of the drive.                             < Output   Drive Conn.)  ³±
       ³                                                                    ³±
       ³ ST506/412 HARD DRIVE  (MFM & RLL)                                  ³±
       ³                                                                    ³±
       ³ This standard drive system uses                    ÚÄÄÄÄÄ¿         ³±
       ³ two cables; a 34 conductor control     HEAD SEL. 8 ³2   1³ GND     ³±
       ³ cable, and a 20 conductor data         HEAD SEL. 4 ³4 _ 3³  |      ³±
       ³ cable.  The control cable contains      WRITE GATE ³6   5³  |      ³±
       ³ a twist of the conductors going to   SEEK COMPLETE ³8   7³  |      ³±
       ³ the farthest drive, which is drive         TRACK 0 ³10  9³  |      ³±
       ³ "C" on most systems.  This twist       WRITE FAULT ³12 11³  |      ³±
       ³ consists of conductors 25 through      HEAD SEL. 1 ³14 13³  |      ³±
       ³ 29.  As with the floppy cable, the        RESERVED ³16 15³  |      ³±
       ³ ST506/412 cables normally have a       HEAD SEL. 2 ³18 17³  |      ³±
       ³ key to prevent reversal, and the             INDEX ³20 19³  |      ³±
       ³ controller end has a pin-type con-           READY ³22 21³  |      ³±
       ³ nector, while the drive end has a             STEP ³24 23³  |      ³±
       ³ card-edge type connector.             DRIVE SEL. 1 ³26 25³  |      ³±
       ³                                       DRIVE SEL. 2 ³28 27³  |      ³±
       ³                   ÚÄÄÄÄÄ¿             DRIVE SEL. 3 ³30 29³  |      ³±
       ³       DRIVE SEL'D ³1   2³ GND         DRIVE SEL. 4 ³32 31³  |      ³±
       ³          RESERVED ³3 _ 4³  |          DIRECTION IN ³34 33³ GND     ³±
       ³             |     ³5   6³  |                       ÀÄÄÄÄÄÙ         ³±
       ³             |     ³7   8³ GND                                      ³±
       ³          RESERVED ³9  10³ RESERVED          Though control signals ³±
       ³               GND ³11 12³ GND               go through a single 34 ³±
       ³     * WRITE DATA+ ³13 14³ * WRITE DATA-     conductor cable, data  ³±
       ³               GND ³15 16³ GND               flows through seperate ³±
       ³      * READ DATA+ ³17 18³ * READ DATA-      20 conductor cables    ³±
       ³               GND ³19 20³ GND               for each drive (C,D).  ³±
       ³ *(MFM or RLL)     ÀÄÄÄÄÄÙ                                          ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

                                                                             
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC                                                     3 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CONNECTIONS ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³ ESDI HARD DRIVES                                      ÚÄÄÄÄÄ¿      ³±
       ³                                           HEAD SEL. 3 ³2   1³ GND  ³±
       ³ Though ESDI and ST506/412 drives          HEAD SEL. 2 ³4 _ 3³  |   ³±
       ³ share similar looking cables,              WRITE GATE ³6   5³  |   ³±
       ³ even to the point of having a        CONFIG/STAT DATA ³8   7³  |   ³±
       ³ twist, the actual data and con-         TRANSFER ACK. ³10  9³  |   ³±
       ³ trol signals are very different.            ATTENTION ³12 11³  |   ³±
       ³ One should never mix components           HEAD SEL. 0 ³14 13³  |   ³±
       ³ from these two drive types.        SECT/ADD.MK. FOUND ³16 15³  |   ³±
       ³ While the ST506/412 interface             HEAD SEL. 1 ³18 17³  |   ³±
       ³ utilizes a standard pulse code                  INDEX ³20 19³  |   ³±
       ³ to transmit data between the                    READY ³22 21³  |   ³±
       ³ drive and controller, ESDI uses         TRANS.REQUEST ³24 23³  |   ³±
       ³ a pulse code that does not require       DRIVE SEL. 1 ³26 25³  |   ³±
       ³ the level to return to zero between      DRIVE SEL. 2 ³28 27³  |   ³±
       ³ pulses.  This format is refered to       DRIVE SEL. 3 ³30 29³  |   ³±
       ³ as NRZ, or Non Return to Zero.  By          READ GATE ³32 31³  |   ³±
       ³ utilizing NRZ, the clock that data       COMMAND DATA ³34 33³ GND  ³±
       ³ is transfered by can be increased,                    ÀÄÄÄÄÄÙ      ³±
       ³ thereby increasing the troughput to                                ³±
       ³ and from the ESDI disk.                                            ³±
       ³                                        ÚÄÄÄÄÄ¿                     ³±
       ³                            DRIVE SEL'D ³1   2³ SECT/ADD.MK. FOUND  ³±
       ³                          SEEK COMPLETE ³3   4³ ADDRESS MARK ENABLE ³±
       ³                   RESV'D FOR STEP MODE ³5   6³ GND                 ³±
       ³                           WRITE CLOCK+ ³7   8³ WRITE CLOCK-        ³±
       ³                      CARTRIDGE CHANGED ³9  10³ READ REF. CLOCK+    ³±
       ³                       READ REF. CLOCK- ³11 12³ GND                 ³±
       ³                        NRZ WRITE DATA+ ³13 14³ NRZ WRITE DATA-     ³±
       ³                                    GND ³15 16³ GND                 ³±
       ³                         NRZ READ DATA+ ³17 18³ NRZ READ DATA-      ³±
       ³                                    GND ³19 20³ GND                 ³±
       ³                                        ÀÄÄÄÄÄÙ                     ³±
       ³                                                                    ³±
       ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ And in this corner... Recording ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³±
       ³                                                                    ³±
       ³     Times were, you had a simple choice for type of disk drive...  ³±
       ³ Any kind, as long as it was ST506/412.  Those were the heydays of  ³±
       ³ MFM drives.  But many manufacturers weren't content with the 17    ³±
       ³ sectors/track that MFM provided.  They devised a newer encoding    ³±
       ³ scheme to pack data tighter, and called it RLL, or Run Length      ³±
       ³ Limited, as opposed to MFM, or Modified Frequency Modulation.  It  ³±
       ³ involves using groups of 16 bits rather than each individual bit,  ³±
       ³ thus achieving a sort of "compression" of the information as it is ³±
       ³ encoded.  Since the same information takes up less space as RLL    ³±
       ³ encoded data, more info can be writen to the disk.  The most com-  ³±
       ³ mon RLL technique, known as 2,7 RLL, can pack roughly 50% more on  ³±
       ³ a disk than MFM.  Of course, there is always a trade-off, and the  ³±
       ³ timing and media required for RLL is it.  RLL requires a higher    ³±
       ³ grade of media because of it's dense bit-packing, and timing is    ³±
       ³ more critical, since the data is flowing at 50% higher rate than   ³±
       ³ an MFM drive.  Also, the mechanics of the drive must have tighter  ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

                                                                              
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
       ³ DIAGRAMS.DOC                                                     4 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³ tolerences because head positioning becomes more critical.  These  ³±
       ³ requirements kept RLL drives at a premium.  It has only been the   ³±
       ³ last two years, that RLL drives have outsold MFM, and have all but ³±
       ³ wiped them from the marketplace.  This turnabout has come from the ³±
       ³ need to increase disk capacity more and more.  Both ESDI, and SCSI ³±
       ³ type drives utilize RLL.(1*) encoding to achieve high capacity and ³±
       ³ transfer rates (from the disk).  And the newest interface, IDE, or ³±
       ³ Integrated Drive Electronics, is also based on this technology.    ³±
       ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³±
       ³                                                  ÚÄÄÄÄÄ¿           ³±
       ³ SCSI HARD DRIVES                           DB0 <>³2   1³ GND    5  ³±
       ³                                            DB1 <>³4   3³  |     0  ³±
       ³ The normal internal cable for SCSI         DB2 <>³6   5³  |        ³±
       ³ is a 50 conductor ribbon, with all         DB3 <>³8   7³  |     P  ³±
       ³ odd numbered conductors grounded.          DB4 <>³10  9³  |     I  ³±
       ³ Two conductors, numbers 25 & 26, are       DB5 <>³12 11³  |     N  ³±
       ³ often left not-connected, as they          DB6 <>³14 13³  |        ³±
       ³ deal with Terminator power, and can        DB7 <>³16 15³  |     D  ³±
       ³ be easily shorted by cable reversals.      DBP <>³18 17³  |     U  ³±
       ³ There are no twists in this cable,         GND   ³20 19³  |     A  ³±
       ³ and it's length may be a maximum of        GND   ³22 21³  |     L  ³±
       ³ 6 meters.  But one is advised to use       GND   ³24 23³  |        ³±
       ³ minimum lengths to improve timing.      TERM PWR ³26 25³  |     R  ³±
       ³ Up to seven drives, or devices may be      GND   ³28 27³  |     O  ³±
       ³ attached to an SCSI cable.  Each is        GND   ³30 29³  |     W  ³±
       ³ daisy-chained on the cable, or, when       ATN  >³32 31³  |        ³±
       ³ a device has two connectors, another       GND   ³34 33³  |     C  ³±
       ³ cable may be "spliced" into the chain      BSY <>³36 35³  |     O  ³±
       ³ starting at the second connector, and      ACK  >³38 37³  |     N  ³±
       ³ continued on.  Care must be taken to       RST <>³40 39³  |     N  ³±
       ³ insure that cables and connectors are      MSG < ³42 41³  |     E  ³±
       ³ not reversed, as this would short pin      SEL <>³44 43³  |     C  ³±
       ³ 26 (TERMPWR) to ground, and likely         C/D < ³46 45³  |     T  ³±
       ³ damage the drive or controller.  Also,     REQ < ³48 47³  |     O  ³±
       ³ as explained earlier, the terminating      I/O < ³50 49³ GND    R  ³±
       ³ resistors should remain only on the              ÀÄÄÄÄÄÙ           ³±
       ³ controller (Host Adapter) and the LAST           ÚÄÄ¿ DB-25F CONN. ³±
       ³ drive on the cable, regardless of it's     GND   ³1 ÀÄÄ¿           ³±
       ³ address.                                   DB1 <>³2  14³<> DB0     ³±
       ³    Most SCSI Host Adapters also have       DB3 <>³3  15³<> DB2     ³±
       ³ a connector for external drives in the     DB5 <>³4  16³<> DB4     ³±
       ³ form of a Centronics(tm) type 50 pin,      DB7 <>³5  17³<> DB6     ³±
       ³ or an "alternate", DB-25F connector.       GND   ³6  18³<> PARITY  ³±
       ³ Only the internal 50-pin, and the          SEL <>³7  19³   GND     ³±
       ³ "alternate" external connector are         GND   ³8  20³<  ATN     ³±
       ³ shown here.  (see also: MORE SCSI)       TMPWR   ³9  21³ > MSG     ³±
       ³    Also, these diagrams refer to the       RST <>³10 22³<  ACK     ³±
       ³ single-ended SCSI connections, since       C/D < ³11 23³<> BSY     ³±
       ³ this is the most common arrangement        I/O < ³12 24³ > REQ     ³±
       ³ for PCs today.  The Differential SCSI      GND   ³13 25³   GND     ³±
       ³ requires balanced lines, and is used             ³  ÚÄÄÙ           ³±
       ³ mostly on high-end workstations.                 ÀÄÄÙ FUTURE DOMAIN³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

                                                                             
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC                                                     5 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CABLES ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³ SCSI (cont.)                                                       ³±
       ³                          (T)                       ÚÄ(DC)¿    (T)  ³±
       ³ On an SCSI cable, the  1ÉÍÍ»ÄstripeÄ1ÉÍÍ»ÄÄ1ÉÍÍ»ÄÄ1ÉÍÍËÍÍ»ÄÄ1ÉÍÍ»  ³±
       ³ terminating resistors   º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ (T) remain at the END   º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ devices on the cable,   º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ even when 2 cables are  º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ "Daisy-Chained" (DC).   º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ Also, the external      º::ºðððððððððº::ºðððº::ºðððº::º::ºðððº::º  ³±
       ³ connector may be used,  ÈÍÍ¼         ÈÍÍ¼   ÈÍÍ¼   ÈÍÍÊÍÍ¼   ÈÍÍ¼  ³±
       ³ requiring the removal    (HA)          Drives 1-7 (in any order)   ³±
       ³ of the Host Adapter's                                              ³±
       ³ internal Term. resistors.                                          ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CONNECTORS ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³ IDE (AT) HARD DRIVES                       (<> AT THE DRIVE CONN)  ³±
       ³                                                  ÚÄÄÄÄÄ¿           ³±
       ³ IDE, or Integrated Drive Electronics       RST  >³1   2³   GND     ³±
       ³ is the most recent drive interface to      SD7 <>³3   4³<> SD8     ³±
       ³ gain popularity.  Often, the control       SD6 <>³5   6³<> SD9     ³±
       ³ circuitry is built into the mother-        SD5 <>³7   8³<> SD10    ³±
       ³ board, eliminating the requirement for     SD4 <>³9  10³<> SD11    ³±
       ³ a seperate Host Adapter.  There are 2      SD3 <>³11 12³<> SD12    ³±
       ³ types of IDE interfaces...those for the    SD2 <>³13 14³<> SD13    ³±
       ³ 8-bit XT bus, and those for the 16-bit     SD1 <>³15 16³<> SD14    ³±
       ³ AT bus (detailed here).  The cable for     SD0 <>³17 18³<> SD15    ³±
       ³ IDE contains 40 conductors and has no      GND   ³19 20³N/C (KEY)  ³±
       ³ twists.  Like an SCSI cable, the IDE      RES.N/C³21 22³   GND     ³±
       ³ cable uses a Dual-row Pin connector for    IOW  >³23 24³   GND     ³±
       ³ both ends.  A single cable may be used     IOR  >³25 26³   GND     ³±
       ³ to connect two drives, or two cables      RES.N/C³27 28³N/C RES.   ³±
       ³ may be Daisy-Chained.  Most IDE Host      RES.N/C³29 30³   GND     ³±
       ³ Adapters will support two hard drives.    IRQ14 <³31 32³> I/O CS16 ³±
       ³ The first drive should be jumpered as      SA1 <>³33 34³<> PDIAG   ³±
       ³ the Master drive, and the second as the    SA0 <>³35 36³<> SA2     ³±
       ³ Slave drive.  Plug-in IDE Host Adapters    CS0  >³37 38³<  CS1     ³±
       ³ are often called Paddle-Boards, and      ACTIVE <³39 40³   GND     ³±
       ³ may contain a floppy controller, and             ÀÄÄÄÄÄÙ           ³±
       ³ serial and parallel ports.                                         ³±
       ³                                                                    ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CABLES ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³ Note:                                                              ³±
       ³                        1ÉÍÍ»ÄÄÄÄstripeÄÄÄÄÄ1ÉÍÍ»ÄÄÄÄÄÄÄÄÄÄÄ1ÉÍÍ»   ³±
       ³ The IDE Host Adapter    º::ºððððððððððððððððº::ºððððððððððððº::º   ³±
       ³ connector may be on     º::ºððððððððððððððððº::ºððððððððððððº::º   ³±
       ³ a plug-in Paddle-Board  º::ºððððððððððððððððº::ºððððððððððððº::º   ³±
       ³ or may be integrated    º::ºððððððððððððððððº::ºððððððððððððº::º   ³±
       ³ on the Motherboard.     º::ºððððððððððððððððº::ºððððððððððððº::º   ³±
       ³                         ÈÍÍ¼                ÈÍÍ¼            ÈÍÍ¼   ³±
       ³                         Host Adapter       Drives 1-2 (any order)  ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³  1*  There ARE some SCSI drives that utilize MFM, but very few.    ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

           
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC                                                     6 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ More on Recording ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³ WRITE PRECOMPENSATION                                              ³±
       ³                                                                    ³±
       ³    OK, so we've all seen it listed, and maybe even had to set it   ³±
       ³ in the CMOS.  So what IS it?  And what does it do?                 ³±
       ³    PreComp. is the way in which the electronics compensates for    ³±
       ³ eventual "drift" of the magnetic domains written on the disk.  A   ³±
       ³ simple explaination is that it allows the head to space bits that  ³±
       ³ would attract each other, further apart, while it puts those that  ³±
       ³ repel each other, closer together.  It does this by analyzing the  ³±
       ³ data stream, and adjusting the timing for each bit, to allow it to ³±
       ³ be recorded earlier or later, if needed.                           ³±
       ³    Not all disks require you to set their PreComp value.  Those    ³±
       ³ that do are asking for a cylinder to start PreComp. at.  Since the ³±
       ³ packing of the bits on a disk increases as you get closer to the   ³±
       ³ center of the disk (higher cylinders), the requirement for PreComp.³±
       ³ increases too.  The PreComp. value specified by the Manufacturer   ³±
       ³ for a disk is his way of insuring your long term data stability.   ³±
       ³                                                                    ³±
       ³         ÄÄ< THE EFFECT OF PRECOMPENSATION OVER TIME >ÄÄ            ³±
       ³                                                                    ³±
       ³    When recorded (w/o PreComp)      When recorded (with PreComp)   ³±
       ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³±
       ³ ³ +-   -+   +-   +-   -+   -+  ³  ³   +-  -+  +-   -+    -+    -+³ ³±
       ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³±
       ³                                                                    ³±
       ³     After time (w/o PreComp)          After time (with PreComp)    ³±
       ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³±
       ³ ³+-    -+    +- +-     -+ -+   ³  ³  +-   -+   +-   -+   -+   -+ ³ ³±
       ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³±
       ³                                                                    ³±
       ³    From the figures above, we can see how a slight amount of Pre-  ³±
       ³ Compensation can insure long term stability.  The disk that didn't ³±
       ³ employ PreComp was eventually unreadable.  Of course, this would   ³±
       ³ take time to happen, but no one can give cold hard specs on how    ³±
       ³ much drift will occure.  (Of course, this example is a gross sim-  ³±
       ³ plification of the process, but, hey, who's counting?)             ³±
       ³                                                                    ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ For Notes & Such ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

        
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ DIAGRAMS.DOC                                                     7 ³±
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´±
       ³ APPLE SCSI                                                         ³±
       ³                                                                    ³±
       ³   Unlike in the PC world, the Apple          APPLE DB-25 SCSI      ³±
       ³ standardized on one drive interface,             ÚÄÄÄÄ¿            ³±
       ³ SCSI.  Also, Apple standardized on         REQ < ³1   À¿           ³±
       ³ a 25 pin connector for external con-       MSG < ³2  14³   GND     ³±
       ³ nections.  However, Apple decided not      I/O < ³3  15³ > C/D     ³±
       ³ to implement the complete ANSI spec.,      RST <>³4  16³   GND     ³±
       ³ so one must be careful that peripherals    ACK  >³5  17³<  ATN     ³±
       ³ used are certified to work with Apple's    BSY <>³6  18³   GND     ³±
       ³ SCSI bus.                                  GND   ³7  19³<> SEL     ³±
       ³   Apple also developed it's own pin-       DB0 <>³8  20³<> PARITY  ³±
       ³ configuration.  The Apple and Future       GND   ³9  21³<> DB1     ³±
       ³ Domain 25-pin SCSI connectors are as       DB3 <>³10 22³<> DB2     ³±
       ³ close to "Standards" as there are in       DB5 <>³11 23³<> DB4     ³±
       ³ the world of PCs.  But the real ANSI       DB6 <>³12 24³   GND     ³±
       ³ Standard called for a 50 pin connector     DB7 <>³13 25³  TMPWR    ³±
       ³ commonly referred to as a "Centronics"           ³    ÚÙ           ³±
       ³ type (made popular by the Centronics             ÀÄÄÄÄÙ            ³±
       ³ printer company).  Instead of the 25                               ³±
       ³ staggered pins of the Apple & Future       50-PIN "CENTRONICS"     ³±
       ³ Domain type connectors, the Centronics         TYPE SCSI           ³±
       ³ type uses 2 parallel rows of 25 pins.            ÚÄÄÄÄÄ¿           ³±
       ³ This arrangement allowed use of extra            ³1  26³           ³±
       ³ grounds for better isolation.                    ³2  27³           ³±
       ³                                                  ³3  28³           ³±
       ³                                                  ³4  29³           ³±
       ³                                                  ³5  30³           ³±
       ³                                                  ³6  31³           ³±
       ³                                                  ³7  32³           ³±
       ³                                                  ³8  33³           ³±
       ³              (WORK IN PROGRESS)                  ³9  34³           ³±
       ³                                                  ³10 35³           ³±
       ³                                                  ³11 36³           ³±
       ³                                                  ³12 37³           ³±
       ³                                                  ³13 38³           ³±
       ³                                                  ³14 39³           ³±
       ³                                                  ³15 40³           ³±
       ³                                                  ³16 41³           ³±
       ³                                                  ³17 42³           ³±
       ³                                                  ³18 43³           ³±
       ³                                                  ³19 44³           ³±
       ³                                                  ³20 45³           ³±
       ³                                                  ³21 46³           ³±
       ³                                                  ³22 47³           ³±
       ³                                                  ³23 48³           ³±
       ³                                                  ³24 49³           ³±
       ³                                                  ³25 50³           ³±
       ³                                                  ÀÄÄÄÄÄÙ           ³±
       ³                                                                    ³±
       ³                                                                    ³±
       ³                          THE END?                                  ³±
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ±
        ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±