CK:  MIDI! 1.0
                                 (ShareWare Version)
                            Copyright 1991 Chris Sorensen
                                All rights reserved.






                                  Table of Contents


          Introduction . . . . . . . . . . . . . . . . . . . . . . . .    3

          What You Need  . . . . . . . . . . . . . . . . . . . . . . .    3

          The CK:  MIDI! Package . . . . . . . . . . . . . . . . . . .    3

          Installing CK:  MIDI!  . . . . . . . . . . . . . . . . . . .    4

          Using CK:  MIDI! . . . . . . . . . . . . . . . . . . . . . .    4

          Button:  About...  . . . . . . . . . . . . . . . . . . . . .    4

          Button:  Display MIDI  . . . . . . . . . . . . . . . . . . .    5

          Button:  Play MIDI . . . . . . . . . . . . . . . . . . . . .    6

          Button:  Test MIDI Cable . . . . . . . . . . . . . . . . . .    6

          Button:  Test MIDI File  . . . . . . . . . . . . . . . . . .    7

          Button:  Exit  . . . . . . . . . . . . . . . . . . . . . . .    7

          The Legal Stuff  . . . . . . . . . . . . . . . . . . . . . .    7

          Correspondence . . . . . . . . . . . . . . . . . . . . . . .    8

          ShareWare  . . . . . . . . . . . . . . . . . . . . . . . . .    8

          Revision History . . . . . . . . . . . . . . . . . . . . . .    8

          Other Programs by
          Chris Sorensen . . . . . . . . . . . . . . . . . . . . . . .    9

          Users Groups . . . . . . . . . . . . . . . . . . . . . . . .   10







          Introduction             Welcome to CK:  MIDI! 1.0.  CK:  MIDI!
                                   is designed to allow a variety of MIDI
                                   tests to be quickly and easily
                                   performed.  With CK:  MIDI!, verifying
                                   your MIDI equipment is a snap.

                                   If you are new to Atari computers, it is
                                   a good idea to read the Owner's Manual
                                   that was included with your Atari
                                   computer.  At the very least, you should
                                   be familiar with the basic operation of
                                   your computer:  using the mouse to
                                   select items and programs for various
                                   purposes and, how to organize and find
                                   files.  You should also be familiar with
                                   the terms associated with using your
                                   computer, such as clicking and dragging. 
                                   Additionally, you should be familiar
                                   with the proper method for linking your
                                   MIDI (Musical Instrument Digital
                                   Interface) equipment with MIDI cables.



          What You Need            You can run CK:  MIDI! on Atari computer
                                   with at least 512K of RAM and TOS in
                                   ROM.  Single or double sided floppy disc
                                   drives may be used, as well as hard
                                   discs.  When running, CK:  MIDI! uses
                                   approximately 15K of RAM.



          The CK:  MIDI!           The CK:  MIDI! package you have received
          Package                  should include the following files: 
                                   CKMIDI.PRG, CKMDI2.RSC, CKMIDI.DOC (the
                                   document file you are currently
                                   reading).  Since CK:  MIDI! is
                                   constantly being updated and improved,
                                   the package may also contain a file
                                   called README.1ST.  The README.1ST file
                                   contains special updates and addendums
                                   to this manual and should be read before
                                   continuing with this manual.  









                                          3






          Installing CK:  MIDI!    Using the GEM desktop, copy the files
                                   CKMIDI.PRG, and CKMDI2.RSC to the
                                   directory folder you'll wish to use. 
                                   CK:  MIDI! does not have any special
                                   requirements as to which folder it is
                                   placed in, so long as all of it's files
                                   are in the same folder.  




          Using CK:  MIDI!         To start CK:  MIDI!, double click on
                                   it's program icon.  After a few moments,
                                   the Main dialog box will be displayed on
                                   the screen.  The Main dialog box
                                   contains a Status box in the center,
                                   which CK:  MIDI! uses to communicate
                                   information to you, and a set of six
                                   command buttons which allow you to
                                   control CK:  MIDI!'s functions.  All
                                   activities, such as starting tests, and
                                   checking MIDI files will be controlled
                                   from this Main dialog box.




          Button:  About...        The About... button provides information
                                   about CK:  MIDI!, as well as various
                                   methods you can use to contact the
                                   author for questions, comments, or
                                   ShareWare contributions.





















                                          4






          Button:  Display MIDI    The Display MIDI button starts the MIDI
                                   receive mode, which displays MIDI
                                   commands as they are received.  The MIDI
                                   commands can originate at a keyboard,
                                   drum machine, sequencer, another
                                   computer, or most any device equipped
                                   with a MIDI Out port.  CK:  MIDI!
                                   recognizes the following MIDI commands: 
                                   Note On, Note Off, Poly Key Pressure,
                                   Control Change, Program Change, Channel
                                   Pressure, Pitch Wheel, System Common
                                   Messages and System Exclusive Messages. 
                                   At this time, System Real-Time Messages
                                   are not displayed, though they are
                                   recognized.

                                   Note On:  This message is generated when
                                   keys are pressed on the (MIDI) keyboard.

                                   Note Off:  This message is generated
                                   when a key is released on a keyboard.  A
                                   Note On message with an attack velocity
                                   of 0 is a synonym for Note Off.

                                   Poly Key Pressure:  This message is
                                   generated to report the amount of
                                   pressure being applied to a key.

                                   Control Change:  This message is
                                   generated whenever the player makes a
                                   change to an instrument's controller(s).

                                   Program Change:  This message is used to
                                   change the preset sound on a MIDI
                                   instrument.  It may also be used to
                                   alter other presets on a MIDI device.

                                   Channel Pressure:  This message is
                                   similar to Poly Key Pressure in that it
                                   is used to report an amount of pressure
                                   being applied.  Unlike Poly Key
                                   Pressure, however, Channel Pressure
                                   affects the entire MIDI channel, rather
                                   than a single key.

                                   Pitch Wheel:  This message is generated
                                   whenever the pitch bend wheel on an
                                   instrument is moved.

                                   System Common Message:  This message is
                                   displayed by CK:  MIDI! whenever any of
                                   the following Sys-Com messages are

                                          5






          Button:  Display MIDI    received:  MIDI Time Code Quarter Frame,
          (Continued)              Song Position Pointer, Song Select, Tune
                                   Request, or End of Exclusive (EOX).

                                   System Exclusive:  These messages allow
                                   special commands, data, and other
                                   information to be transmitted to and
                                   from a specific manufacturer's
                                   equipment.

                                   The MIDI commands are displayed in the
                                   Status box in the center of the Main
                                   dialog.

                                   While in Display MIDI mode, the mouse
                                   will not be active.  Press any key on
                                   the computer keyboard to end the Display
                                   MIDI mode.




          Button:  Play MIDI       This button causes a brief melody to be
                                   played, which can be used to verify that
                                   an instrument is receiving MIDI messages
                                   and processing them.  Only Note On
                                   messages are sent to the connected MIDI
                                   devices.  All other settings on the
                                   connected device(s) remains unchanged.




          Button:  Test MIDI       This button is used to test a MIDI cable
          Cable                    to verify that it is in a condition
                                   suitable to transmit MIDI information. 
                                   To perform this test, first connect one
                                   end of the cable to the MIDI Out port on
                                   the computer.  Next, connect the other
                                   end of the cable to the MIDI In port.
                                   Finally, click on the Test MIDI Cable
                                   button to check the cable.  A Pass or
                                   Fail message will be displayed in the
                                   Status box at the center of the Main
                                   dialog box.  The button may be held down
                                   for a rapid succession of tests, each
                                   showing Pass or Fail.






                                          6






          Button:  Test MIDI       This button allows you to check a file
          File                     to see if it is a MIDI Format File, and,
                                   if it is, determine whether the file is
                                   a format 0, 1, or 2 file.

                                   After clicking on the Test MIDI File
                                   button, an file selector will be
                                   displayed, which you may use to enter
                                   the name of the file to be checked.  The
                                   Status box will display the results of
                                   the test, either indicating that the
                                   file is not a MIDI file, or the format
                                   type.




          Button:  Exit            This button is used to end the current
                                   session of CK:  MIDI!, and returns you
                                   to the desktop, or to the program that
                                   was used to start CK:  MIDI!, such as
                                   AS/X



          The Legal Stuff          This program and its documentation are
                                   provided "AS IS".  Chris Sorensen makes
                                   no warranty of any kind with regard to
                                   this program, including, but not limited
                                   to, the implied warranties of
                                   merchantability or fitness for a
                                   particular purpose.  In no event will
                                   Chris Sorensen be liable for direct,
                                   indirect, special, incidental, or
                                   consequential damages resulting from 
                                   any defect or inaccuracy in this program
                                   or its documentation.


                                   All product names are trademarks or
                                   registered trademarks of their
                                   respective companies or holders.











                                          7






          Correspondence           Questions, comments, suggestions,
                                   ShareWare donations, and other
                                   correspondence may be directed to:

                                   Mail/Post:
                                        Chris Sorensen
                                        3250 W. 53rd Ave
                                        Denver, CO  80221-6564  USA

                                   CompuServe:
                                        73310.761

                                   GEnie:
                                        C.SORENSEN2

                                   InterNet
                                         73310.761@compuserve.com



          ShareWare                This program is ShareWare.  If you keep
                                   this program and use it, please send a
                                   donation to the author.  For a donation
                                   of $15.00 (US) or more, you will become
                                   a registered user of CK:  MIDI! and
                                   recieve the latest ShareWare version of
                                   CK:  MIDI! with laser printed
                                   documentation.  When sending your
                                   donation, please take an extra moment
                                   and send your comments, too!  This
                                   program can only be improved if I know
                                   what additional features users such as
                                   yourself are looking for.  Thank you for
                                   supporting the efforts of ShareWare
                                   authors!



          Revision History         Oct. 22, 1991  1.1 Original ShareWare
                                   release.                  













                                          8






          Other Programs by        Calendar Printer  Print a calendar for
          Chris Sorensen           any month in any year from 1900 through
                                   3000.  Enter and save notes for any
                                   calendar or maintain multiple note files
                                   for the same calendar.  Calendars can be
                                   saved for editing in a word processor or
                                   desktop publishing package.  

                                   AS/X (Application Selector/eXecutive) 
                                   Start any program from any disc or
                                   directory with just a double click on
                                   its name--AS/X handles finding the
                                   program and starting it for you.  No
                                   more searching through windows and
                                   folders!

                                   Scrub ST  Delete files from your discs--
                                   permanently!  Useful to keep deleted
                                   files away from prying eyes--these files
                                   cannot be "revived" with disc utility
                                   packages.

                                   P/ST Graphics  View Portfolio graphics
                                   on the ST.  P/ST Graphics can read,
                                   write, and translate both PGF and PGC
                                   graphic screens.

                                   Attrib G/S  Review, change, or reset ST
                                   file attributes quickly and easily with
                                   Attrib G/S.  Just point, click, and
                                   save.

                                   FormFeed  A handy desk accessory which
                                   ejects partial pages from you printer. 
                                   An excellent tool for use with files
                                   printed from the GEM desktop, and blocks
                                   of text printed inside of programs.

                                   For additional information about these
                                   programs or how to obtain them, please
                                   contact Chris Sorensen.












                                          9






                                   Attention Users Group Librarians:  Do
                                   you have these programs in you group
          Users Groups             library?  If not, send your group's
                                   name, mailing address, telephone number,
                                   president's name, and a copy of the club
                                   newsletter to:

                                   Chris Sorensen
                                   Attn:  Library Disc ST
                                   3250 W 53rd AVE
                                   Denver, CO  80221-6564

                                   I'll send you a disc with my current
                                   ShareWare programs so you can add them
                                   to the group library.  There's no cost
                                   for this service--I just need to know
                                   who and where you are!




































                                         10






                     ShareWare Registration Form--CK:  MIDI! 1.1
                                Please print or type.


          Licensed to:   ____Individual  ____Company



          Name:        ________________________________________________

          Company:     ________________________________________________

          Address:     ________________________________________________

                       ________________________________________________

          City:        __________________  State/Province:  ___________

          Zip/Postal:  __________________  Country:  __________________

          Telephone:   ________________________________________________



          How did you obtain CK:  MIDI!?  _____________________________

          _____________________________________________________________




          Send your check or money order, payable in US funds to:

               Chris Sorensen
               Attn:  Registration
               3250 W 53rd AVE
               Denver, CO  80221-6564

          Anyone registering CK:  MIDI! and making a ShareWare contribution
          of $15.00 (US) or more will receive the most recent version
          ShareWare version of the program with laser printeded
          documentation.



          Comments:    _______________________________________________

          ____________________________________________________________

          ____________________________________________________________

          ____________________________________________________________

          Thank you for using CK:  MIDI!  --Chris Sorensen