Instructions for Atari TT DIS, a 68030/68882 disassembler
  
                      Version 1.01 - 17th Nov 1991
  
  Introduction
  
     DIS is a 68000  disassembler for the Atari TT series computers.   It
  is not in the public domain but can be freely distributed provided that
  this does not involve any direct or indirect profit or an inducement to
  purchase other items (e.g products,  magazines  or  services).  DIS has
  been  derived from an  earlier version on  the Atari ST and this  means
  that the 68000 core has been fairly well tested. However the extensions
  for the 68030 and the 68882 have only  been tested in a limited way and
  there will certainly be bugs in this area.  Please let me know any that
  you come accross.
  
  Operation of DIS
  
     On entry DIS  displays a > prompt and waits for a command line which
  consists of  a letter which may be followed by further parameters which
  are separated from  each other by either commas or blank spaces.  A '?'
  in response to the prompt gives a summary of commands. In the following
  command descriptions 'x1', 'x2' etc. represent numeric parameters which
  are normally in hexadecimal notation.  If a program with a symbol table
  is loaded then x1, x2 etc. can be symbols.
                                                                         
  Command              Function
  
  I  x1 x2             Disassemble Instructions from x1 to x2
  
  B  x1 x2             Disassemble data Bytes  (8 bits) from x1 to x2
  
  W  x1 x2             Disassemble data Words (16 bits) from x1 to x2
  
  L  x1 x2             Disassemble Long words (32 bits) from x1 to x2
  
  C  x1 x2             Disassemble in Character format from x1 to x2
  
  A  x1 x2             Disassemble a table of Addresses from x1 to x2
  
  M  x1 x2 template    Disassemble according to a template. The template
                       is a a sequence of the characters ICBWLANV which
                       represent Instructions, Characters, Bytes, Words,
                       Longs, Addresses, Newlines, & Labels respectively.
                       Each character in the template produces an output
                       of the appropriate type, with the template being
                       repeatedly scanned if more output is required.
                       For example NVCCA would give Labelled blocks with
                       two bytes and an address in each. If the template
                       contains a '/' character this marks the re-scan
                       position rather than the beginning. An optional
                       decimal count can precede any output character
                       (ICBWLA) and then applies to this output.
  
  Ec x1 x2             Output Equates for addresses using range x1 to x2
                       Note that labels external to the range are output
                       as the default but if the character 'c' is present
                       and is 'I', 'E' or 'A' then Internal, External or
                       All labels in the range are output respectively
  
  J  x1 x2             Compile labels from x1 to x2 into the symbol table
  
  Fc x1 x2 xx..        Find positions of the hexadecimal digit sequence
                       xx... between x1 and x2. If 'c' is present and is
                       'E' then only even address matches are output
  
  Fc x1 x2 "cc.."      Find positions of the string "cc..." between x1
                       and x2 . If 'c' is present and is 'E' then only
                       match positions at even addresses are given
  
  K  x1 x2 x3 [x4]     Find positions where address x3 is referenced. If
                       x4 is present then find positions where addresses
                       in the range x3= < address < x4 are referenced
  
  U  x1 x2             Set range limits for disassembly
  
  Uc                   Reset to initial range limits. If 'c' is present
                       and is 'C', 'D', 'B' or 'P' the  the limits  of
                       the Code, the Data, the Bss or the (Code + Data)
                       are set. If 'c' is not present the total program
                       length limits are set
  
  Vc x1                Enter (Make) a symbol at address x1. If 'c' is
                       present and is the character 'E' (or 'e') then
                       the symbol is absolute, otherwise it is program
                       relative (Note that V alone outputs a DIS version
                       number and author information).
  
  X  x1                Set the eXecution address for a program when this
                       is different to the load address (this should not
                       be used on programs loaded with the 'P' command)
  
  Y  x1                SYmbol form control. x1 can be a sum of the values
                       1, 2 and 4 to produce the desired effect:
  
                          x1 = 1: output long labels          (0 = short)
                          x1 = 2: output absolute labels   (0 = relative)
                          x1 = 4: input absolute addresses (0 = relative)
  			  x1 = 8: use old 68000 instruction syntax

  N  x1                Disassembly control. x1 can be a sum of the values
                       1, 2, 4 and 8 to produce the desired effect:
  
                          x1 = 1:   enter labels into the symbol table
                          x1 = 2:    display internal labels in output
                          x1 = 4:    display external labels in output
                          x1 = 8:  use any symbols loaded with program
  
                       Internal and External labels reference addresses
                       inside and outside the program area respectively.
                       Program  symbols will only be available if the
                       program contains a symbol table.
  
  H+  H-               Turn Hexadecimal code output on (+) or off (-)
                       during the disassembly of instructions
  
  D+  D-               Turn character code output on (+) or off (-)
                       during the disassembly of instructions
  
  P prog_name          Load a Program for disassembly
  
  P-                   Unload a Program (or image file)
  
  R file_name x1       Load (Read) a binary image file for disassembly
                       with x1 as the execution address (default = 0)
  
  R-                   Unload a binary image file (or program)
  
  S file_name          Output (Save) disassembly from here onwards to a 
                       specified file
  
  S-                   Turn off saving and close output file
  
  O                    Output file name and range information
  
  Q                    Quit disassembler (safer than ^C !)
  
  T                    Compile auto_disassembly control table (see later)
  
  T-                   Clear auto Table
  
  TD                   Display the contents of the auto control table
  
  TL file_name         Load the auto table contents from specified file 
  
  TS file_name         Save the auto table contents to the specified file 
  
  G                    Run (Go) auto disassembly (see later)
  
  Z                    Delete (Zap) all symbol table entries
  
     When a program or image  file is loaded the relative label forms are
  relative to the start of the file.  Otherwise relative labels take zero
  as a base and are therefore effectively absolute.   Input  values  will
  either be absolute or relative depending on  the  value  set  by  the Y
  command.   In  relative  input  mode an absolute number can be input by
  preceeding it with a '$' sign. If the second number of an input pair is
  preceeded by  a  '+'  sign the value input is added to the value of the
  first parameter to form the  second  parameter.  If  a  '*'  is entered
  instead  of  an  input value then the current  value  of  the  relevant
  parameter is used.   DIS generates address labels by adding a letter in
  front of the lowest six hexadecimal  digits of the address,  the letter
  being determined by the type of access.  Thus a subroutine at $00xxxxxx
  will have a label sxxxx (short) or sxxxxxx (long). Address labels in TT
  RAM are distinguished by  adjusting the top hexadecimal digit by adding
  'k' to it. Thus a subroutine at $012xxxxx has a label smxxx or smxxxxx.
  
     Pressing  the  SPACE  bar  during disassembly will pause the output;
  pressing space again will resume output while any other key will return
  to  command  mode.   Pressing  ESC  during   disassembly   will  return
  immediately  to command mode.  During disassembly the x1  parameter  is
  continuously updated  so  that  a  stopped disassembly can be restarted
  by using a * in the first parameter position.   In number pair commands
  if no second  value  is given then a convenient number of lines will be
  disassembled to the  screen.  A  RETURN  entered  at  the > prompt will
  repeat the previous command.
  
  Automatic Disassembly
  
      The T command allows a table to be  input  in the following form to
  control disassembly:
  
                       c1 x1
                       c2 x2
                       m3 x3 template
                       ...
                       cN xN
  
  where  each Cn is one of the characters (I,C,B,W,L,A,V,M,X) and xN is a
  hexadecimal number as normal.  After a table has been input a G command
  starts disassembly.  Each entry in the table  is processed in turn with
  the  letter  determining  the  type  of  disassembly  and  the  address
  indicating where to start.  The address for  the  next entry determines
  where disassembly finishes and restarts in a new form (an X is used for
  the last entry in the table). An M instruction for template disassembly
  is followed by  a  mask as for the normal M command.  When entering the
  table an entry can be corrected by simply entering a new entry with the
  same address value (or a Z with the same address if the  entry is to be
  removed).  To end table input simply type a  RETURN  in response to the
  prompt.  The table will then be output for you to  confirm  that  it is
  correct. After a table has been input disassembly is initiated with the
  G command (its  output can be saved if required by issuing an S command
  before and after the G command). The symbol table is not cleared before
  an automatic disassembly so you may wish to  do this before issuing a G
  command.
  
  Bug Reports to:
  
                       Brian Gladman
                        8 College Grove
                         Great Malvern
                          Worcs WR14 3HP
                           United Kingdom
  
                       Internet: gladman@ccint1.rsre.mod.uk