Data Compression Details

     Huffman uses variable length codes so that the more commonly 
used  characters  use fewer bits.   Since the  code  is  uniquely 
determined  by  the  frequency counts  for  each  character,  the 
compressed  data  must include a copy of these  frequency  counts 
(which  in this implementation is compressed using  the  adaptive 
arithmetic  method).   This implementation scales  the  frequency 
counts so that the maximum code length is 16 bits.

     The  arithmetic  algorithm is more  efficient  than  Huffman 
since it can use fractional bits.  Consider the entire message as 
a  very large number (billions and billions of bits  long).   One 
can  divide  the  possible  range of  a  number  this  long  into 
segments,  one for each possible character in the character  set.  
The  size of each segment is proportional to the frequency  count 
of  the  corresponding character.   The first character  in  this 
message determines which segment is used. Now divide this segment 
into  segments  corresponding  to the  second  character  in  the 
message, etc.
     In  practice  this  is implemented on 32  bit  registers  by 
shifting  bits out when the leftmost bits are equal for the  high 
and  low  limits  of  the segment.   The  only  losses  from  the 
theoretical  limit are when divisions don't go evenly,  and  when 
the   high  and  low  limits  approach  80000000  and   7FFFFFFF, 
respectively.

     Adaptive  methods  do not  transmit  frequency  counts,  but 
develop them on the fly.  The coding continuously changes as each 
new  character is processed.   Usually this is done  by  starting 
every character with a count of 1 (otherwise there is no code for 
the first occurance of the character).   The problem is that  the 
coding is very inefficient in the early part of the message.  For 
example,  a single character repeated 256 times would take 8 bits 
for the first occurance,  7 bits for the second,  6 bits for  the 
fourth,  5 bits for the sixteenth,  and reach 1 bit at the  256th 
occurence.
     This   particular   implementation  uses  a   special   "new 
character"  code  which  is  followed by  the  new  character  in 
(relatively) uncompressed form.   (Specifically,  if n characters 
have  already  been  sent,  then one need only specify  256  -  n 
segments  for  the new character.   But I  digress.)   The  first 
character takes 8 bits.  The second character takes slightly less 
than  9  bits unless it is the same as the  first  character,  in 
which case it takes 1 bit.  That's pretty fast adaptation!

     LZA is a combination of LZSS and adaptive arithmetic.   (The 
LZ stands for Lempel and Ziv.)
     The  LZ methods look for the longest match between the  next 
few characters and some sequence of characters alrady  processed.  
They then use a pointer to the start of the past sequence and the 
length of the match instead of the characters themselves.   An 11 
bit maximum pointer (the last 2K characters) and a maximum length 
of  31 (actually 33,  since 0 and 1 are never used)  requires  16 
bits,  for a breakeven point of 2 characters.  (The primary limit 
on the size of the pointer is CPU time, not bit length.)
     The  LZ77  code  consisted  of  a  sequence  of   structures 
consisting  of a pointer,  length,  and following  character.   A 
length of zero was used when no match was found.   LZSS,  on  the 
other hand, freely mixed characters and pointer-length structures 
by adding an additional bit to each character and  pointer-length 
structure to distinguish one from the other.
     One  of  the features of variable length coding  methods  is 
that one can easily extend the set of characters to more than 256 
with  relatively little penalty.   For example,  one could add  a 
special  "match  indicator"  character  which  would  always   be 
followed by a pointer-length structure.  If there were exactly as 
many  structures  as  characters,  the resulting  code  for  each 
character  would  be  1 bit longer,  and  the  "match  indicator" 
character  would be coded as 1 bit long,  which is the  same  bit 
penalty as LZSS.   Obviously, any different ratio than one-to-one 
would yeild a lower penalty than LZSS.
     LZA extends the character set to 320: 256 regular characters 
and 64 length characters.   Each length character is followed  by 
a  14 bit (16K) pointer (less for the first  16K  bytes).   Since 
some lengths are much more common than others, this is far better 
than using 6 bits for each length (plus the indicator).
     One   effect  of  using  variable  length  coding  for   the 
characters is that the breakeven point is no longer always at two 
characters.    Instead  it is necessary to compute the  breakeven 
point  for  each  individual match  using  the  frequency  counts 
provided by the adaptive arithmetic algorithm.