FIFO.LIBRARY

			   MANUAL, REVISION 3

	 (c)Copyright 1990, Matthew Dillon, All Rights Reserved


fifo.library/FifoNotes
-
fifo.library/OpenFifo
fifo.library/CloseFifo
fifo.library/ReadFifo
fifo.library/WriteFifo
fifo.library/RequestFifo
fifo.library/BufSizeFifo

fifo.library/FifoNotes				      fifo.library/FifoNotes

    FIFO.LIBRARY is a general fifo library implementation with the following
    features:

	* named fifos
	* support for writing to a fifo from a hardware exception
	* multiple readers on a fifo supported, each get the same data
	  stream
	* efficient reading (no buffer copies on read)
	* automatic or manual (via message passing) flow control

    The uses for this library are limitless.  To use the library, open
    it via OpenLibrary("fifo.library", 0);, the base variable is named:

	FifoBase

    Please refer to the test program for an example of usage.

    LINK LIBRARIES:	fifo.lib    standard amiga (join type) library,
				    large-data model

			fifos.lib   standard amiga (joing type) library,
				    small-data model


fifo.library/OpenFifo				      fifo.library/OpenFifo

    NAME
	OpenFifo - open a rendezvous FIFO by name

    SYNOPSIS
	fifo = OpenFifo(name, bufsize, flags)
	D0		 D0	D1	 A0

	void *fifo;	/*  returned fifo handle		*/
	char *name;	/*  rendezvous name - case sensitive	*/
	long bufsize;	/*  must be a power of 2		*/
	long flags;	/*  open flags				*/

    FUNCTION
	OpenFifo() creates a FIFO if <name> does not exist, else
	references an already existing FIFO named <name>.  OpenFifo()
	returns a fifo handle to be used for further operations.

	bufsize must be a power of 2.  For example, 1024.

	NOTE: two OpenFifo()s openning the same fifo are NOT guarenteed
	to return the same handle, even though they reference the same
	FIFO.

    FLAGS
	FIFOF_READ
	    file handle intended to be used for reading, do not specify
	    unless you read from the handle.

	FIFOF_WRITE
	    file handle intended to be used for writing, do not specify
	    unless you write to the handle.

	    If a previous CloseFifo() activated FIFOF_EOF, then the flag is
	    cleared.

	FIFOF_NORMAL
	    normal (task based) calls to library, else is assumed calls
	    will be made from an interrupt or hardware exception.

	    NOTE: non-normal fifo writes are unable to wake up blocked
	    library calls.  Thus, anybody reading a fifo written to by
	    an interrupt or exception (read: enforcer), must poll the
	    fifo.  Eventually automatic polling will be an option to make
	    operation with non-normal writers transparent to the reader.

	FIFOF_KEEPIFD
	    When this FIFO is eventually closed, do not destroy it if
	    unread data is pending.  Allows a 'writer' to completely finish
	    and exit before a read even has the chance to open the fifo.

	FIFOF_NBIO
	    Specify that ReadFifo() and WriteFifo() calls are not to block.


fifo.library/CloseFifo				      fifo.library/CloseFifo

    NAME
	CloseFifo - close a previously openned FIFO

    SYNOPSIS
	void CloseFifo(fifo, flags)
			D0     D1

	void *fifo;	/*  fifo handle previously returned by OpenFifo() */
	long flags;	/*  see below	*/

    FUNCTION
	CloseFifo() is the reverse of OpenFifo(), dereferencing a Fifo.

	The last close of a shared fifo will result in the deletion of that
	fifo ONLY if all data has been read, allowing unsynchronized
	programs to use the Fifo.

	A future flag will cause the last close of a FIFO to delete the
	fifo and throw away any data.

    FLAGS

	FIFOF_EOF
	    If specified, the FIFO will generate an EOF to readers
	    after the last writer has closed.  This particular handle
	    need not be the last writer.

	    If not specified, any active readers are left hanging
	    (allowing another program to 'take up' where this one left
	    off without the readers knowing)

	    NOTE that any new writer that OpenFifo()s the fifo will
	    clear this flag.

	    NOTE that the EOF condition will be returned only once
	    to a given reader, then cleared (causing the reader to
	    block again).  This is because shells generally ignore
	    EOF and we would otherwise get into an infinite loop.

	    THIS FLAG HAS NO EFFECT IF THE HANDLE WAS NOT ORIGINALLY
	    OPENNED FIFOF_WRITE.

fifo.library/ReadFifo				      fifo.library/ReadFifo

    NAME
	ReadFifo -  read data from a FIFO

    SYNOPSIS
	long ready = ReadFifo(fifo, pptr, skip)
	       D0	       D0    D1   A0

	void *fifo;	/*  fifo handle previously returned by OpenFifo() */
	char **pptr;	/*  address of pointer to store buffer pointer	  */
	long skip;	/*  # of bytes to skip (delete)     */
	long ready;	/*  # of bytes available to read, -1 = EOF    */

    WARNING
	ReadFifo() uses UNCONVENTIONAL ARGUMENTS

    FUNCTION
	ReadFifo() first deletes (skip) bytes from the FIFO, then sets a
	pointer into the fifo's buffer and returns the number of bytes
	immediately available for reading.

	THE DATA POINTER TO MAY NOT BE MODIFIED UNDER ANY CIRCUMSTANCES

	The call is efficient because, in many cases, a buffer copy can be
	completely avoided by the program.  The loop code in the example
	below shows generally how operation works.  For further
	information, refer to the test program (TEST.C).

	The number of bytes available (ready), is independant of the
	number of bytes you threw away (skip).  You get a certain amount
	of lookahead for free, but it should be stressed that the (ready)
	value is not necessarily all the available data.  Data in the
	fifo is not always contiguous and so there may be more data
	available than you can immediately determine.  For example, the
	call might return 1 when in fact 500 bytes are available.  But
	only 1 byte is available contiguously (based at the pointer).
	After processing the 1 byte your next read would return 499.

    NON-BLOCKING IO
	If FIFOF_NBIO was specified on open, this call will return
	immediately and 0 is a valid return.  If 0 is returned there
	is no data ready and the program must poll the fifo.  But
	wait, there is a better way to do it ... instead of polling
	the fifo you can opt to have a message sent to you when data
	becomes available.  see the RequestFifo() function call and
	look at TEST.C

	If FIFOF_NBIO is *not* specified, then 0 will never be returned
	by this call.  Instead, either >0 or -1 (EOF) will be returned.

    MULTIPLE-READERS

	Multiple readers may exist for a given FIFO.  This is completely
	supported.  If you have one writer and two readers, and the
	writer writes "ABC", then both readers will each read "ABC".
	Because the FIFO buffer is shared, readers may NOT modify any
	data returned in (pptr) because this could effect other readers
	(depending on whether they have already read the data or not).

    INTERRUPTS / EXCEPTIONS

	ReadFifo() may not be called from an interrupt or a hardware
	exception.  ReadFifo() may ONLY be called from task or process.

    EXAMPLE

	/*
	 *  dump fifo ff.  FIFO was openned without FIFOF_NBIO.
	 */

	{
	    long i = 0; 	    /*	delete nothing on first loop  */
	    long n;
	    char *ptr;

	    while ((n = ReadFifo(ff, &ptr, i)) > 0) {
		if (n > 64)         /*  can easily limit read-size if you */
		    n = 64;	    /*	want to (optional, obviously)     */
		i = n;		    /*	drain this many on next loop	*/
		write(1, ptr, n);
	    }
	    /*
	     *	note, if you break out of the loop you may need a final
	     *	ReadFifo(ff, &ptr, i); to clear out what you have already
	     *	processed.
	     */
	}


fifo.library/WriteFifo				      fifo.library/WriteFifo

    NAME
	WriteFifo - write data to a FIFO

    SYNOPSIS
	long actual = WriteFifo(fifo, buf, len)
	       D0		D0    D1   A0

	void *fifo;	/*  fifo handle previously returned by OpenFifo() */
	void *buf;	/*  buffer to read data into	*/
	long max;	/*  maximum # of bytes to read	*/

    FUNCTION
	WriteFifo() writes data to a FIFO.  WriteFifo() will either return
	actual = len if the write succeeded, 0 if the FIFO is full, or -1
	if an error occurs.  No intermediate values are currently returned
	(i.e. writes are atomic)

	If two writers attempt to write to the same FIFO at the same time
	and the FIFOF_NORMAL flag was not specified on open (i.e. writer
	writes from an interrupt or exception), then it is possible for
	a collision to occur in which case one of the calls will return
	an error (-1).

    WARNING WARNING
	You may not write blocks larger than 1/2 the fifo buffer size,
	this will generate an immediate error (-2) regardless of how
	much space is actually available.  The reason for this is simply
	that writes are guarenteed to be atomic, and cannot be guarenteed
	if larger blocks are written.  Also, flow control breaks down
	with larger blocks so I figure it is best to nip it in the bud and
	return a formal error.

    NON-BLOCKING-IO (FIFOF_NORMAL fifos only)
	Writes are atomic.  If a write fails and FIFOF_NBIO was specified
	on open, the write will return with a failure code of -1.  You
	may optionally poll or use the RequestFifo() call.

	Note that even if RequestFifo() returns the message, a write may
	fail due to other processes writing to the fifo before you have
	a chance to, in which case you have to RequestFifo() again and
	loop.

	If FIFOF_NBIO was not specified on open, then the write will not
	return until the data has been successfully written, or -2 will
	be returned if you specified too large a buffer.

    INTERRUPTS/EXCEPTIONS
	To write to a fifo from an interrupt or exception you must open the
	fifo WITHOUT the FIFOF_NORMAL flag, and be prepared to handle
	possible collisions with other writers.

	In this case a failure code of -1 could mean either that the FIFO
	is full or that a collision has occured and you were the side that
	lost out.

	WARNING:  any writes via a fifo not openned with the FIFOF_NORMAL
	flag will *NOT* wakeup anybody blocked waiting to read from the
	fifo, whether by RequestFifo() (the message is not returned),
	or via normal opens (without the FIFOF_NBIO flag).  Readers must
	POLL in this case.

fifo.library/RequestFifo			    fifo.library/RequestFifo

    NAME
	RequestFifo - request this message be returned when read data is
		      available or write buffer space is available.


    SYNOPSIS
	RequestFifo(fifo, msg, req)
		     D0   D1	A0

	void *fifo;
	struct Message *msg;	/*  messasge in question    */
	long req;		/*  request		    */

    FUNCTION
	Normally this call is used to queue a message to the fifo.library
	that will be ReplyMsg()d to your task when the specified condition
	occurs.  There are four possible requests.

	FREQ_RPEND
	    Request that the specified message be returned when read data
	    is pending on the fifo.

	    note: if data is immediately available, the message will be
	    immediately replied.  If an EOF condition exists or occurs the
	    message will also be replied.

	FREQ_WAVAIL
	    Request that the specified message be returned when the fifo is
	    more than half empty.  It is possible that an attempt to write
	    after getting your message back will fail due to other writers
	    getting their writes in ahead of you.

	FREQ_ABORT
	    Request that this message, which was previously queued via
	    FREQ_RPEND or FREQ_WAVAIL, be returned immediately.

	    May be called even if message has already been returned but
	    not processed.

	You may queue multiple messages, even several messages all for the
	same thing.  When you queue a message, it's node becomes owned by
	the library until replied.  You CANNOT queue the same message
	multiple times at once.  Generally programmers will queue one
	message for write-avail-space and another message for
	read-data-ready, then poll the fifo when these messages are
	returned and re-queue the message(s).

	ReadFifo() and WriteFifo() call RequestFifo() internally when the
	FIFOF_NBIO flag is NOT used.  This is how they wait for events when
	a call blocks due to lack of data or lack of buffer space.


fifo.library/BufSizeFifo			    fifo.library/BufSizeFifo

    NAME
	BufSizeFifo - return size of fifo's buffer

    SYNOPSIS
	long bytes = BufSizeFifo(fifo)
	       D0		 D0

	void *fifo;

    FUNCTION
	This function returns the size of the specified fifo's buffer.

	Note that you may not make WriteFifo() calls with lengths
	larger than 1/2 the size of the fifo's buffer.  This function
	allows you to determine the fifo's buffer size to properly
	observe this limit.  You cannot depend on the buffer size you
	specified in OpenFifo() because only the first OpenFifo() for
	a given fifo actually sets the buffer size.