Installation Guide to

                                        SKsh

                           A ksh-like Shell for the Amiga

                                     Version 1.6


                               (Copyright) 1989, 1990

                                     Steve Koren

                                   October 4, 1990











































          Installing SKsh

            This  section  descibes how to install SKsh.  It is vitally im-
            portant that all the steps be  performed.   If  they  are  not,
            SKsh  will  not  operate correctly.  In addition, SKsh requires
            version 1.3 of AmigaDos to operate correctly.

            Please  examine this file for each release, as it may change at
            any time.


               1)   First, copy the .skshinit  and  .skshrc  files  to  the
                    's:' directory.  SKsh needs these two  files  to  start
                    correctly.   Their  location can be changed by changing
                    the  SKSH:  device (see below).  Note that ONLY .skshrc
                    IS FOR USER MODIFICATION.  The  .skshinit  file  should
                    be  used  as  supplied and re-installed with  each  new
                    release.


               2)   Edit your startup-sequence and insert:

                         assign SKSH: s:

                    This  controls the location in which SKsh looks for the
                    startup files.


               3)   Copy  the  sksh  binary  itself to  a  location in your
                    AmigaDos search path.  You can be fairly sure the  'c:'
                    directory is in your search path.  If  you  have  modi-
                    fied your path, there may be other  potential locations
                    as well.


               4)   Set the pure bit on the SKsh binary:

                         protect c:sksh rep


               5)   Make sure that 't:' points to  a  fast  device suitable
                    for  storing temporary files.  A sub-directory on a ram
                    disk is best.  For example,

                         makedir ram:tmp
                         assign t: ram:tmp

                    You  will  probably want  to  insert some commands like
                    these into your startup-sequence, if they are  not  al-
                    ready there.  SKsh  uses  temporary files only when ab-
                    solutely  necessary, but some types  of  SKsh  commands
                    will  not  function  properly without them (see command
                    subtitution, for example).



          SKsh Amiga Shell             Page 2           Installation Guide










               6)   SKsh needs a stack size of at least 6000 bytes  in  or-
                    der to run properly.   You  can  manually set the stack
                    size  to  6000  bytes  using the AmigaDos stack command
                    before you run SKsh,  or  you  can  insert 'stack 6000'
                    into  your  startup  sequence (recommended).  If you do
                    not have sufficient stack space, SKsh *will* crash.


               7)   The  following files need  to  be  copied to a location
                    which is in your SKsh search path  (although not neces-
                    sarily in your AmigaDos search path):

                         cat       cmp       cp        crc       cut
                         du        encr      fgrep     find      grep
                         head      indent    join      num       srun
                         strings   tail      tee       view      wc
                         window    xd

                    You can  create a directory called "sys:bin" which con-
                    tains these commands.  The  supplied .skshrc file auto-
                    matically adds this directory to the search path. 


               8)   This  step  is  optional, but recommended.  The default
                    name for the ram disk is "RAM DISK:".  The  space  will
                    make some  things  difficult to do (but not impossible)
                    in SKsh.  I  recommend that you change the default name
                    of the ram disk in your startup-sequence  to  something
                    like the following:

                         relabel ram: RAM_DISK

                    The  only  difference is that the space  has  been  re-
                    placed  by  an  underscore, and it will make your  life
                    much easier.


               9)   Insure  that  your  AmigaDos  ENV:  device  is  set  up
                    properly.  If you are not sure how to do this, see  the
                    AmigaDos manual.


               10)  You must have  arp.library  installed in your system in
                    the LIBS: directory.  If you are not  sure  how  to  do
                    this, see the arp documentation.  arp  is  available on
                    most Amiga BBS systems.  It is best  to  use  the  most
                    recent  available arp.library, since SKsh will not  run
                    correctly with some early versions.







          SKsh Amiga Shell             Page 3           Installation Guide









               11)  The pure bit should be set on all of the SKsh  external
                    commands.   This  can  be  accomplished with either the
                    SKsh  chmod  command or the  AmigaDos  protect command.
                    This  is  necessary if the  external commands are to be
                    made resident.  If all  the  external commands are in a
                    single  directory, and this directory contains no other
                    files, then the SKsh command:

                         chmod +p *

                    will set the  pure  bit  provided that you are cd'ed to
                    the proper directory.

               12)  If the script bit is  not  set  on  the  Check_?.?.sksh
                    file (where ?.? is the version number  of  this  SKsh),
                    set it with "chmod +s Check_?.?.sksh".   Then,  execute
                    this script by cd'ing to the  directory  containing  it
                    and typing the  name.   It  will  prompt  you  for  the
                    locations of your SKsh  files,  and  verify  that  they
                    have been installed correctly.  If not, it  will  print
                    and error message for each offending file.



































          SKsh Amiga Shell             Page 4           Installation Guide