/**********************************************************************/
/*                       This is an 14 bit bomb                       */
/*                 Original doc file by: David Ekholm                 */
/*       Translated from Swedish to English by: Jonas Linqdvist       */
/**********************************************************************/

These four files demonstrates how to get 14 bits sound out of a normal
Amiga with only software manipulation.

Normally the Amiga gives 4 D/A converters with 8 bits converting, but due
to that every channel has its own 6 bits (but analogically) amplutide-
control, its possible to combine the channels two and two to get 14 bits
STerEO sound.

The princips are these: On the disk there are sound in 16 bitformat (due
to CD standardize). This 16 bit data is putted with the high byte then the
low byte and so on. I collect all high bytes and put it to an highbyte
buffer and all the lowbytes into another buffert, the buffer should be placed
in chipmem. Each channel has it's own amplitudecontrol and its own sound-
pointer. I put the highbyte pointer to one channel and set it's volyme to
maximum, and i put the lowbyte pointer to another channel with it's volyme set
to minimum (1), then I start the DMA Output and get 14 bit sound.

Call me at +46-(0)758-15668 if you want a more detailed explination.
David Ekholm is my name.

The files on this disk should be:

14bitsound.doc		-This file in swedish
14bitsoundeng.doc	-This file in english
14bitsound		-Program to be run under CLI
14bitsound.c		-Sourcecode.
Ping44.1KHz16bit	-16bit sound data
Ping44.1KHz8bit		-8bit sound data

Hook up your Amiga to your best STerEO amplifer and push it.

Write "14BitSound ?" from the CLI for instructions. You need a JoyStick
to switch between normal and 14bit sound. You should have atleast 256K of
Chipmem.

The Examplesound is sampled with a VERY low amplitude (look in AudioMaster)
so it should be easy to hear the difference.
The 14bitsound would ofcourse have much better quality if i would have
sampled the sound with an higher input amplitude, but then it wouldn't be
as easy to here the difference at medium amplifiers.

More bits is best needed when the sound amplitude is around zero, because
those extra bits effectly reduces the kvantitizenoise.

With this demoprogram we only reach an output of 28KHz, but with other
technics its possible to get an output speed above 50KHz.

Spread this and try for your own so we together can put a new Amigamusic
standard.