BRINGING UP FASTFLOP ON A NEW SYSTEM

FastFlop achieves its speed by reading the sectors on a track
beginning where the head is likely to be, rather than always starting
with sector 1, thus avoiding the wait for sector 1 to come around under
the head.  Thus, it might read sectors 5-9 followed immediately
by a read of sectors 1-4 of the SAME track.  TOS however
waits for 30 ms before reading each track, so when one attempts to
read sectors 1-4, sector 1 has already passed under the head before
TOS is ready to read it, and the disk make another revolution (200 ms)
before the read begins.  The purpose of this delay
is to allow the head to settle down after moving to a new track, but
unfortunately, TOS inserts the delay even after a seek to the SAME track.

FastFlop overcomes this problem by modifying the floppy disk
driver.  In order to do this, it needs to know about the locations
of particular instructions in TOS, which may vary from country to country
and from version to version of TOS.  FastFlop has a table of
the necessary locations for several versions of TOS.
However, if you want to run FastFlop on a version of TOS that FastFlop
does not know about, you must determine the proper 'magic locations' for
your version of TOS, add them to the FastFlop source code,
and recompile FastFlop.  This document explains how to do that.
You will need a machine-level debugger.

The magic locations needed by FastFlop are stored in the following
structure:

    typedef struct {
        LONG version;   /* The composite version # for this record */
        LONG base_adr;  /* Base address for this version of TOS */
        unsigned length;    /* Length of floppy code */

        int floprd;     /* Location of floprd() */
        int flopwr;     /* Location of flopwr() */
        int flopver;    /* Location of flopver() */
        int patch_place;/* Place to patch in jmp... */

        int ctrack;            /* Place to find CTRACK.w */
        int flop_cmds_offbase; /* Base address for computing flop_cmds() */
    } offset_rec;

They are explained individually below.

1.  The "composite" version number holds the TOS version number in the
upper 16 bits and the TOS date (in GEMDOS format) in the lower 16.
This is used to identify the particular version of TOS you are running.
(We do not know if two different versions of TOS ever have both the
same TOS version number and the same TOS date.)

The version number and date are stored in the OS header which is
at a fixed offset from the location pointed to by the
documented system variable SYSBASE.
The following code obtains the version number for you (using my
special e_osbind.h include file) and builds the composite version
number needed by FastFlop.

    LONG usp;
    LONG version;
        usp = Super(0);
        version = SYSBASE->version;
        version <<= 16;
        version |= SYSBASE->tos_date;
        Super(usp);


2.  base_adr is the starting address of the floppy disk driver
and is the only absolute address needed by FastFlop.  
All other magic values, from floprd to
flop_cmds_offbase, are offsets from base_adr.

The floppy code starts at flopini(), and base_adr should be set 
to its starting address.  Since flopini() has no XBIOS or BIOS calling
sequence, finding it is a little involved.

It is the routine that comes right
before floprd() (generally $48 bytes before), 
which does have an XBIOS calling sequence.
floprd().  
To find the address of floprd() in
memory, in the jump table for the XBIOS trap
handler.  The jump table immediately follows 
the XBIOS trap handler, whose address is generally stored at
location $B8 (XBIOS trap vector).
Some programs, such as TurboST, install
themselves in this trap, obscuring the location of the trap handler in
ROM.  To most easily find the ROM trap handler, de-install all
programs which change the contents of $B8. 

Now, to find the jump table, look directly past the trap handler for a
long string of addresses, or inspect the code of the trap handler
carefully to find where the jump table starts.  In ROM versions, all
addresses stored in the jump table start with $00FC, making it easy to
simply search for a series of longwords of the form $00FCxxxx, 
directly after
the trap handler.  Determine the start of the jump table and then
add 8 longwords (32 bytes) to this to determine the pointer to the
address of floprd().  Look at the code and determine that it matches
the code fragment below, with the arrowed line being the start address of
floprd(). 

    bne
    bsr
    beq
    bra
FLOPRD:
    bsr
    moveq   #~~~,d0
    bsr     ~~~
    bsr     ~~~
    bsr     go2track
    bne

Subtract $48 from the address of FLOPRD(), and you have the start of
the floppy handler.  Store this as the value of base_adr.  Just to make
sure, check its code against the following:

FLOPINI:
    lea     ~~~, A1
    tst.w   0C(A7)
    beq
    lea     ~~~, A1
    move.w  ~~~, 2(A1)
    moveq
    clr.w
    bsr
    bsr
    move.w

3.  'length' should be set to the number of bytes in the floppy disk driver.
To determine the length, look about $780 bytes past
FLOPINI for the following code:

    clr.l     (a0)
    move.w    0x10(a7), ~~~~
    clr.w     0x10(a7)
    rts
    lea       0xECC(a5), a0
    move.b    d0, -(a7)
    move.w    0xA08(a5), d0
    move.b    (a7)+, 0x0(a0,d0)
    rts
    lea       ~~~~, a0
    tst.w     0x4(a7)
    beq       ~~~~
    lea       ~~~~, a0
    move.w    0x2(a0), d0
    move.w    0x6(a7), d1
    cmp.w     #-1, d1
    beq       ~~~~
    move.w    d1, 0x2(a0)
    ext.l     d0
    rts             ; This is the last statement in the floppy code.

Keep in mind that link or unlnk instructions are hallmarks of compiled
code.  The floppy handler was written in assembly code, so it should
(probably) contain no link or unlk instructions.  In my version of
the ROMs, there's a link instruction right after the floppy handler,
making it rather easy to find the end.

If you're not sure where the code ends, it doesn't hurt FastFlop's
functionality to assume that the code is a bit longer than it is.
Guessing too small, on the other hand, could lead to spectacular
crashes at random times. 

All remaining addresses are offsets from the
start of the floppy handler.  You can use the offsets found in 
the FastFlop source code for a close
version of TOS as a starting point in your search.  To compute each
offset, first find the absolute address of the desired location, and
then subtract base_adr from it.

4.  floprd is the offset for the floprd() routine which you found above.
It should be about $48.

5.  flopwr is the offset for flopwr(), the floppy disk write routine.
It is an XBIOS routine and can be found as above by looking in the
XBIOS trap handler's jump table at the entry 9 longwords past the beginning.
The code around it should look as follows:

    bne
    move.w ~~~(A5), D1
    move.w D1, ~~~(A5)
    rts
FLOPWR:
    bsr
    moveq #F6, D0

6.  flopver is the offset for flopver(), the floppy disk verify routine.
It is an XBIOS routine and can be found by looking in the XBIOS trap
handler's jump table at the entry 19 longwords past the beginning.
The code around it should look as follows:

    rts
    move.b D0, (A2)+
    dbf D1, ~~~
    rts
FLOPVER:    
    bsr
    moveq #F5, D0
    bsr
    bsr
    bsr


7.  patchplace, ctrack, and flop_cmds_offbase.  These are all addresses (stored
as offsets from base_adr) into
the middle of the driver routines 'go2track' and 'restore'.  To find
the location of this code, look back at the beginning of the code 
for floprd(), and
notice that the 5th instruction is a 'bsr go2track'.

patchplace and offbase are the addresses shown below.  ctrack is
xctrack - 2.

PATCHPLACE, CTRACK, OFFBASE:
    move.w  #10, D6
    bsr
    bne
    move.w
go2track:
    move.w
    move.w
    move.w
XCTRACK:                 (CTRACK = XCTRACK - 2)
    bsr
    moveq   #14, D6
PATCHPLACE:
    bsr
    bne
    move.w
    and.b
    rts
restore:
    clr.w D6
    bsr
FLOP_CMDS_OFFBASE:
    bne
    btst #02, D7
    eor #04, CCR

That's it!  Put these magic values into a new entry of the 'loc' array,
recompile, and enjoy.

Please, when you make a new version of FastFlop, send the table of
"magic values" and the date and version of your TOS to me (Robert
Fischer).  I will incorperate those changes into a new official
release of FastFlop.

Don't hesitate to call or write if you have trouble.  My address is:

    80 Killdeer Road
    Hamden, CT   06517   (USA)
    (203) 288-9599

    or E-mail c/o Michael Fischer:  <fischer-michael@cs.yale.edu>