CP/M-Z80 EMULATOR

                            OWNER'S MANUAL

               For Use with All ATARI ST[TM] Computers

PLEASE NOTE

Every effort has been made to ensure the accuracy of the product
documentation in this manual.  However, because Atari Corp. is
constantly improving and updating its computer hardware and software,
we are unable to guarantee the accuracy of printed material after the
date of publication and disclaim liability for changes, errors, or
omissions.

ATARI is a registered trademark, and ST and TOS are trademarks of
Atari Corp.

CP/M, CP/M-80, and GEM are trademarks of Digital Research Inc.

WordStar is a trademark or registered trademark of MicroPro
International Corporation.

CP/M-Z80  Emulator was developed by SoftDesign in conjunction with
Atari Corp.


Copyright 1986 Atari Corp.
Sunnyvale, CA 94088
All Rights Reserved.

TABLE OF CONTENTS

INTRODUCTION
   What is CP/M and What Is the CP/M-Z80 Emulator?
   How Well Does the CP/M-Z80 Emulator Perform?
   How to Use This Manual

CHAPTER 1
GETTING STARTED
   Backing Up the CP/M-Z80 Emulator Disk
   Loading the CP/M-Z80 Emulator
   Backing up the CP/M-Z80 Utilities Disk

CHAPTER 2
CP/M AND CP/M-Z80 EMULATOR COMMAND SUMMARY
   How to Enter a CP/M Command
   CP/M File Specifications
   Command Summary Conventions
   CP/M-Z80 Emulator-Specific Command
       @
       CPMTOS
       DDTZ
       DIR
       EDTKEY
       EXIT
       INIT
       READ
       SCOPY
       SETKEY
       TOSCPM
       TOSDIR
   Standard CP/M Commands
      *ASM
      *DDT
       DIR
      *DUMP
      *ED
       ERA
       LOAD
      *PIP
       REN
       SAVE
      *STAT
      *SUBMIT
       TYPE
       USER
       XSUB
   CP/M Control Character Summary
   CP/M Filetypes
   CP/M Messages

CHAPTER 3
CP/M AND CP/M-Z80 EMULATOR TECHNICAL REFERENCE
   Emulator Implementation
   Emulator CCP Implementation
   Emulator BDOS Implementation
   Emulator BIOS Implementation
   Emulator Performance
   Emulator Interface to User I/O
   General Restrictions
   Notes on CP/M-Z80 Emulator I/O DRIVER Conventions
   CP/M BDOS Function Summary

  * Not included with package.
    Copyright Digital Research @1986.

INTRODUCTION

WHAT IS CP/M AND WHAT IS THE CP/M-Z80 EMULATOR?

Every computer requires an operating system.  A computer's operating
system is a set of instructions--a program--that supervises the
running of other programs on the computer.

Your ATARI ST Computer has its own, unique operating system--TOS.  You
load TOS every time you switch on your computer.  Once TOS loads, your
computer is ready to run other programs.  Any program designed to run
on your ST Computer is running under TOS.

CP/M is also an operating system.  It's different from TOS.  A program
designed to run under CP/M will not run under TOS, and vice versa.
However, the CP/M-Z80 Emulator program that you've received on disk
makes TOS "think" and "act like" (i.e., "emulate") a CP/M system.
Without any additional hardware or software, the Emulator program
transforms your ST Computer into a complete CP/M-80 system.

This is a great advantage to you because CP/M has been around for a
long time. As a result, there are literally thousands  of programs
available that run under CP/M, and so will run under the CP/M-Z80
Emulator.


HOW WELL DOES THE EMULATOR PERFORM?

The Emulator is a complete CP/M-80 version 2.2 compatible system
environment.  It provides realtime emulation of all Z80 instructions
over the full 64K addressable range.  The Emulator runs all CP/M-80
compatible programs and accepts all standard CP/M-80 version 2.2
commands.  Some minor errors in version 2.2 of CP/M-80 were corrected,
and some additional system commands were added.

The Emulator runs average CP/M-80 programs with the speed of a 2MHz
Z80 system, but performance will vary according to the particular
program.  One major variable will be the frequency of a program's disk
access.  Programs with heavy disk I/O may run even faster than on
conventional Z80 hardware because the Emulator fully exploits the disk
speed of the ATARI ST Computer.  On the other hand, programs that
perform extensive arithmetic computations will most likely run more
slowly than average.


HOW TO USE THIS MANUAL

This manual is not intended as a CP/M operator's manual.  Rather, it
provides only skeletal information about the CP/M operating system.
You are encouraged, if not already familiar with CP/M, to obtain a
CP/M reference book.  There are many excellent CP/M books on the
market.

The following summarizes the contents of this guide:

Chapter 1, Getting Started, explains how to load the Emulator into
your computer and  have CP/M resident and on screen.  The chapter also
explains how to back up the CP/M-Z80 Emulator and CP/M-Z80 Emulator
Utilities disks you received.

Chapter 2, CP/M and CP/M-Z80 Emulator Command Summary, provides you
with summary explanations of all standard CP/M commands and all
non-standard (CP/M-Z80 Emulator-specific) commands, according to the
CP/M and CP/M-Z80 utility files you received on the CP/M-Z80 Emulator
Utilities disk.  The chapter also provides a summary of CP/M
filetypes, control characters, and messages.

Chapter 3, CP/M and CP/M-Z80 Emulator Technical Reference, presents
some technical information about the Emulator and how it works.  This
chapter is in part geared to CP/M programmers, but non-programmers may
also find much of the information useful.  The chapter ends with a
listing of the standard CP/M BDOS Function Summary.

CHAPTER 1
GETTING STARTED

This chapter explains how to backup both the CP/M-Z80 Emulator and
CP/M-Z80 Emulator Utilities disks you received, and how to load the
Emulator program into your computer.  You will copy the CP/M-Z80
Emulator disk from the GEM Desktop.  But the CP/M-Z80 Emulator
Utilities disk is copied from within the Emulator itself.  Before you
begin, be certain to have two newly formatted disks on hand.


BACKING UP THE CP/M EMULATOR DISK

Before you do anything else, be certain to make a backup copy of the
disk labeled "CP/M-Z80 Emulator."  Since the Emulator is actually a
TOS program, you must make the copy from the GEM Desktop.  If you
haven't done so already, first format a disk, then make the copy
(either by dragging the files from one window to another or by making
a disk-to-disk copy).  Once you've made the copy, always use it as
your working CP/M-Z80 Emulator disk.  Store the original in a safe
place.  By doing this, you will always have at least one usable copy
of the program.

The disk labeled "CP/M-Z80 Emulator Utilities," on the other hand,
must be copied within the Emulator (see the section on Backing Up the
CP/M-Z80 Emulator Utilities Disk).


LOADING THE CP/M-Z80 EMULATOR

The CP/M Emulator is a program like any other program that runs on
your ST Computer.  It needs to be loaded into your computer.

To load the Emulator, follow these steps:

1.  With the GEM Desktop displayed, insert the disk labeled "CP/M-Z80
Emulator" into Drive A (or B, if you have two disk drives).  Obtain a
directory window of the disk, then select and open ("run") the file
CPMZ80.TOS.  Your screen clears and in a moment the CP/M-Z80 Emulator
comes up.


2.  The message on screen instructs you to insert a CP/M-Z80 disk into
your drive.  Remove the CP/M Emulator disk and insert the disk labeled
"CP/M-Z80 Emulator Utilities."  (You may substitute you own CP/M
application disk for the CP/M-Z80 Emulator Utilities disk at this
point.) Now press any key.  In a moment the Emulator's A: (or B:)
prompt appears on screen.  You now have CP/M fully resident and
ready.

Note:  CP/M's classic A> (or B>) prompt is replaced with an A: (or B:)
prompt in the Emulator; the Emulator's A: (or B:) prompt works just
like the CP/M's A> (or B>) prompt.


Now type

       dir

beside the A: (or B:) prompt.  The DIR command returns a directory
listing of the specified drive.


These are the CP/M utilities you received on disk.


BACKING UP THE CP/M-Z80 EMULATOR UTILITIES DISK

It is essential that you make a backup copy of the CP/M-Z80 Emulator
Utilities disk before you do anything else.  To make the copy, follow
these steps:

1.  If you haven't done so already, format a disk under TOS (from the
GEM Desktop), just as you normally do.  If you don't have a blank,
formatted disk available, then you'll have to exit the Emulator (type
EXIT beside the A: or B: prompt), format a disk from the GEM Desktop,
then run the Emulator.

2.  If you have one disk drive and with the Emulator's A: prompt
displayed, write-protect and insert the disk labeled "CP/M-Z80
Emulator Utilities" in Drive A, then type

SCOPY *.* <cr>

The program prompts you to swap the utilities (source) disk for your
newly formatted (destination) disk, displaying the name of each file
as it's copied.

If you have two disk drives and with the Emulator's A: prompt
displayed, write-protect and insert the disk labeled "CP/M-Z80
Emulator Utilities" into Drive A and your newly formatted disk in
Drive B, then type

NSWP207

Pressing '?' will display all of the commands that NSWP207
understands.
To copy ALL files from Drive A to Drive B, press 'T' for TAG to mark
each file.  After marking each file for transfer, press 'M' to perform
the mass file copy.

You will be prompted for a destination.

Type     B:

to send the files to the B drive.

The program proceeds to copy all files in Drive A to Drive B,
displaying the name of each file as it's copied.

3.  With your new copy of the utilities disk in Drive A (or B), type

     dir <cr>

beside the A: (or B:) prompt, just to be certain that the duplication
procedure was a success.

4.  Now type

     INIT A: <cr>

This initializes your copy of the CP/M-Z80 Emulator Utilities disk.
For an explanation of disk-initialization, see INIT in Chapter 2.

Now that you've made the copy, always use it as your working CP/M-Z80
Emulator Utilities disk.  Store the original in a safe place.  By
doing this, you will always have at least one usable copy of the
utilities disk, should anything ever happen to any one copy.

CHAPTER 2


CP/M AND CP/M-Z80 EMULATOR COMMAND SUMMARY


HOW TO ENTER A CP/M COMMAND

To enter a CP/M command, you must type a complete command line in
response to the CP/M system prompt.  A CP/M  command line consists of
a command keyword, an optional command tail, and a carriage return
([cr]).  The command keyword identifies a command (program) to be
executed.  The optional command tail consists of a file specification
and options or parameters.  To complete the command, add a carriage
return by pressing the [Return] key on the ST computer keyboard.


CP/M FILE SPECIFICATIONS

CP/M identifies every file by its unique file specification.  A file
specification is composed of three parts: a drive specification, a
primary filename, and a filetype.  The term "filespec" is an
abbreviation for file specification, and indicates any valid
combination of the drive specification, the filename, and the
filetype.  The following symbols are used to designate the parts of a
filespec:

D:          Represents the optional drive specification,
            which must be a single alphabetical character
            in the range A through P, followed by a colon.

filename    Represents the required primary filename which
            can be 1 to 8 alphabetic or numeric characters.

.typ        Represents the optional filetype, which can be 0
            to 3 alphabetic or numeric characters separated
            from the primary filename by a period.

Valid combinations of the elements of a filespec are shown below:

  filename
  D:filename
  filename.typ
  D:filename.typ

Certain CP/M commands can select and process several files when
wildcard characters are included in the primary filename or filetype.
The two wildcard characters are ?, which matches any single letter in
the same position, and *, which matches any character at the position
and any other characters remaining in the filename or filetype.  The
command summary indicates which commands can accept wildcard
characters (* or ?) in a filename or filetype.


COMMAND SUMMARY CONVENTIONS

The command summary lists CP/M commands in alphabetical order, using
the following special symbols to define command syntax:

[]        Indicate an optional item within DDT and ED.
          Also indicate the optional parts of a command
          line.
|         Separates choices.
N         Indicates a number.
[cr]      Indicates a carriage return keystroke.
 or CTRL  Indicates a control keystroke
O         Indicates an option or option list.
R/W       Means Read-Write.
R/O       Means Read-Only.
SYS       Means System attribute.
DIR       Means Directory attribute.
...       Preceding element can be repeated as many
          times desired.
*         Wildcard; replaces all or part of a filename
          and/or filetype.
?         Wildcard; replaces any single character in the
          same position.


CP/M-Z80 EMULATOR-SPECIFIC COMMANDS

@

Syntax:

     @
     @/
     @/ <command lines>
     @/ <filename> <parameters>

Purpose:

The @ command invokes the @.COM utility.  The @.COM utility lets you
interactively design and use SUBMIT files.

Examples:

     @
     @/
     @/NSWP207

CPMTOS

Syntax:

     CPMTOS <CP/M-Z80 filename> <TOS filename>

Purpose:

The CPMTOS command lets you convert a CP/M-Z80 file to a TOS file.
Note however, that CP/M programs will not run under TOS, even though
they are converted.   An unambiguous CP/M-Z80 file as source and a
destination drive or unambiguous TOS destination filename must be
specified on the command line.  Source and destination drive cannot be
the same.  CPMTOS allows you to change disks and prompts you to start
the conversion by pressing [Return].  To abort the conversion, press
[Esc] or [Control] [C].

Examples:

     CPMTOS A:HAPPY.TXT B:
     CPMTOS ORDERS.DAT B:ORDERS.DTA


DDTZ

Syntax:

     DDTZ
     DDTZ filespec

Purpose:

The DDTZ command works quite like DDT, save that it invokes the
CP/M-Z80 debugging utility.

Examples:

     A: DDTZ
     A: DDTZ PROGRAM.COM


DDTZ commands

>  @                              Examine [and substitute]
                                  the displacement
                                  register @.
>  A [startaddress]               Assemble.
>  B                              Display all Breakpoints.
>  B breakp [breakp..][:count]    Set Breakpoints.
   BX                             Clear all Breakpoints.
   BX address [address]           Clear Breakpoints.
>> C[N][J][number of commands]    Trace over Calls
                                  [no list][jumps only].
   C[N][J] W expression           ..while..
   C[N][J] U expression           ..until..
>>D [startaddr][endaddr]          Display memory in hex
                                  and ascii.
> F commandline                   Specify Filename and
                                  command line.
> G [startaddr][;breakpoint..]    Go [to start][temporary
                                  breakpoints]
> H                               Display High and maximal
                                  size of files.
> H expression                    Compute hex and other
                                  expressions.
  H expression expression         Hex and other sum and
                                  difference.
>>I [port]                        Input a byte from port.
>>L [startaddr][endaddr]          List disassembled code.
> M[V] startadr endadr targetadr  Move memory [and verify].
>>O [byte][port]                  Output a byte to port.
> Q[J] startaddr endaddr bytes    Query memory for byte
                                  string [justified].
> R [displacement]                Read binary or hex file
                                  [add dislacement].
> S Startaddr                     Substitute memory.
>>T[N][J][number of commands]     Trace [no list]
                                  [Jumps only].
  T[N][J] W expression            ..while..
  T[N][J] U expression            ..until..
> V startaddr endaddr targetaddr  Verify (compare) two
                                  memory areas.
> W startaddr endaddr             Write a file to disk.
> X                               Examine all cpu registers.
  X register                      Examine [and substitute]
                                  a register.
> Y                               Examine all Y variables.
  Y number between 0 and 9        Examine [and substitute]
                                  a Y variable.
> Z startaddr endaddr bytes       Zap (fill) memory with a
                                  byte string.



DDTZ: Names of Registers

A , F , B , C , D , E , H , L , BC , DE , HL
A', F', B', C', D', E', H', L', BC', DE', HL'
IX or X, IY or Y, SP or S, PC or P, I

DDTZ: Flags of Registers F and F':

S       Sign
Z       Zero
H       Half carry             Carry of bit 3 to bit 4.
V       Overflow/parity        Overflow/even parity.
N       Negation               NEG, DEC, SUB or the like
                               executed.
C       Carry                  Carry of bit 7.
E       Interrupt Enabled      The Interrupt flag is handled
                               in DDTZ like a flag of the
                               F-Register.

DDTZ: Constants and Variables

L       Low            Start of user-memory.
H       High           Highest address of files last loaded.
M       Max            Highest address of all files loaded.
T       Top            Top of user memory.
@                      Displacement Register.
$                      Start address when assembling
                       otherwise = PC.
Y0 ... Y9              Free usable variables.
^register              Content of register.
(address)              Content of a memory cell (byte).
(address)              Content of a memory cell (word).

Calling DDTZ:

        DDTZ
        DDTZ d:filename.ext

If DDTZ was called together with a filename, then DDTZ loads the file
into the memory.  When the '>' sign appears, DDTZ is ready.

General remarks for the use of DDTZ.

In all situations, where numbers can be entered, 'expressions' can be
entered too.  Expressions are structured as follows:

<arithmetic expression>
        or
<arithmetic expression> <relational operator> <arithmetic expression>

Relation operators are: = , <> , < , > , >= , <=

If the relation is true, the expression has the value -1, otherwise it
is 0.

e.g.: the expression 1 + 2 = 3 has the value -1.

An arithmetic expression has the general structure:

<factor><arithmetic operator><factor><arith... ... <factor>

Arithmetic operators are:

+ , - , * , / , %        plus, minus, multiplication, division,
modulo.
& , ! , #                AND, OR, XOR (bit oriented).

Factors are:

[expression]             Expression in brackets.
+factor
-factor                  Negation.
~factor                  NOT (bit oriented).
'a'                      Value of ASCII-character.
'a'.                     Bit 7 on.
'ab'                     Value of two ASCII characters.
'ab'.                    Bit 7 on in low byte.
(expression)             Byte in memory.
(expression)             Word in memory.
variable                 arbitrary variable mentioned above.
hhhh[H]                  Hex-number.
dddd.                    Decimal-number.
bbbbbbbb"bbbbbbbb"       Binary number.

If an expression contains a relational operator, first both arithmetic
expressions are calculated and then the relation.  An arithmetic
expression will be calculated from the left to the right without
regard to algebraic rules.  However, the order can be changed with
brackets.  Expressions must not contain blanks.

Commands start with one of the characters '@' to 'Z', optionally
followed by other characters or arguments.  If the start address is
omitted, the address where the command ended before is used instead.
If the end address is omitted, the command (e.g. L or D) will be
repeated until one screen is filled.  If one argument is omitted and
other arguments follow, it has to be replaced by a comma.  Between two
arguments, a blank, a tab, or a comma must be put.

Commands which need a starting address and an ending address can use
the character 'S', followed by an offset.

For example:

   D 1000 S 100 resp. D1000S100
       means the same as:
   D1000 10FF resp. D1000,10FF


DIR

Syntax:

     DIR filename

Purpose:

The DIR command displays the names of all files with "system
indicator" set on the specified disk.

Examples:

     DIR A:
     DIR B:


EDTKEY

Syntax:

     EDTKEY <keyboard definition file>

Purpose:

The EDTKEY command lets you edit a CP/M-Z80 keyboard definition file.
A keyboard definition file contains information about the nationality
and character strings for the function keys.  You can choose from one
of five national keyboard layouts:  American, English, French, German,
and German/American.  German/American is a special German layout for
programmers.  Each of the ten function keys [F1]--[F10] on the top row
of the keyboard and all the eight keys in the cursor block, both
unshifted and shifted, may be assigned an ASCII string of up to eight
characters.  This provides you with a total of 36 configurable
function keys.

EDTKEY displays the current keyboard nationality and function key
definitions, and shows a menu of possible entries.  To abort without
making any changes, and return to the CP/M-Z80 Emulator, press [Esc].
To change the keyboard nationality, which is displayed in the top
right corner of the EDTKEY screen, press [Space Bar].  To save the
current definition to disk, press [Enter] (on the numeric keypad);
EDTKEY then terminates automatically.  To edit the string assigned to
a function key, just press the desired function key, unshifted or
shifted.  Correct a definition with [Backspace] and terminate editing
with [Enter].  All ASCII characters except Backspace (08H) may be used
in function key strings.  Control characters are shown in arrow
notation.

EDTKEY is a versatile tool that can adapt the CP/M-Z80 environment to
your changing needs.  You may assign function keys various commands
used in CP/M applications programs, and so tailor the ST keyboard to
the specific needs of an application program.  You can create as many
keyboard definition files as you want.  EDTKEY displays or changes an
existing keyboard definition or creates a new keyboard definition
file, if the specified file cannot be found.  A new definition is
filled with default values at startup.  The default file type for
keyboard definition files is .KEY and may be omitted from the file
specification.  A predefined keyboard definition must be activated
with the SETKEY utility.

Note:  The DEFAULT.KEY file on disk is the default keyboard definition
file.  The WS.KEY file configures the keyboard for use with WordStar.

Examples:

     EDTKEY DEFAULT
     EDTKEY


EXIT

Syntax:

     EXIT

Purpose:

The EXIT command allows you to exit the Emulator and return control to
TOS and the GEM Desktop.

Examples:

     A: EXIT
     B: EXIT


INIT

Syntax:

     INIT <drive specifier>

Purpose:

The INIT command initializes a formatted TOS disk for use under the
CP/M-Z80 Emulator.  Disks used with the Emulator must be formatted
under TOS first, then initialized with the INIT utility running under
the Emulator.  The drive containing the disk to initialize must be
specified on the command line, and the INIT.COM file must be on the
specified disk.  The INIT command zeros the TOS directory so that you
can recognize CP/M-Z80 disks from the GEM Desktop.  When you display a
initialized CP/M-Z80 disk directory on the GEM Desktop, only the one
item (CPMZ80.APP) appears in the directory window, and (falsely) shows
999999 bytes used in that one item.

Examples:

     INIT A:
     INIT B:

READ

Syntax:

     READ
     PIP PUN: = A: <filename> [0], eof: eof: eof: eof eof:

Purpose:

The READ command invokes the READ communications utility.  The READ
communications utility is a self-relocating receiver routine for
serial data transmission via the CP/M reader channel.  This allows for
the conversion from one CP/M computer to another.  The READ.ASM file
(on disk) provides you with the READ utility's source code.

Examples:

     A: READ PROG
     A: READ PROG.BBX
     A: READ b:PROG.bzz


SCOPY

Syntax:

    SCOPY <ambiguous CP/M-Z80 filename>

Purpose:

The SCOPY command allows you to copy CP/M-Z80 files on a single drive
system.  You may select a file or group of files to copy, according to
your file parameter.  The utility informs you to swap source and
destination disks, and echoes the name of each copied file.

Examples:

     SCOPY *.*
     SCOPY *.PAS
     SCOPY DU.COM


SETKEY

Syntax:

     SETKEY <keyboard definition file>

Purpose:

The SETKEY command activates an existing keyboard definition file
(created  with EDTKEY).  The default file type for keyboard definition
is .KEY and may be omitted from the file specification.

Note:  The DEFAULT.KEY file on disk is the default keyboard definition
file.  The WS.KEY file configures the keyboard for use with WordStar.


Examples:

     SETKEY MP
     SETKEY B:MBAS


TOSCPM

Syntax:

     TOSCPM <TOS file> <CP/M-Z80 file>

Purpose:

The TOSCPM utility lets you convert a TOS file to a CP/M-Z80 file.
Note that TOS programs will not run under CP/M-Z80.  An unambiguous
TOS file as source and a destination drive or unambiguous CP/M-Z80
destination filename must be specified on the command line.  Source
and destination drive cannot be the same.  TOSCPM allows you to change
disks and prompts you to start the conversion by pressing [Return].
To abort the conversion, press [Esc] or [Control] [C].

Examples:

     TOSCPM A:README.TXT B:
     TOSCPM TURN11.DAT B:T11.DTA


TOSDIR

Syntax:

     TOSDIR <ambiguous file specification>

Purpose:

The TOSDIR utility displays the directory of a TOS disk.  An ambiguous
file specification may be specified.  If no drive is specified, the
utility displays the directory of the current default drive.  If you
give no file specification, the utility lists all files in the
directory.

Examples:

     TOSDIR
     TOSDIR A:
     TOSDIR *.PRG

STANDARD CP/M COMMANDS


ASM                        NOT INCLUDED IN PACKAGE
                        FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     ASM [filename]
     ASM [filename.ABC]

Purpose:

ASM assembles assembly language statements, producing an output file
in Intel [tm] hexadecimal format and a print file.  The source
filetype must be ASM.  Character A indicates source file drive, B
indicates HEX file destination, and C indicates PRN file destination.
If you put a Z in position B or C, the HEX file or PRN file is
suppressed.  An X in position C sends the print file to the console.

ASM Error Messages

D   Data Error: Data statement element cannot be placed in
    specified data area.
E   Expression Error: Expression cannot be evaluated during
    assembly.
L   Label Error: Label cannot appear in this context (might
    be duplicate label).
N   Not Implemented: Unimplemented features, such as macros,
    are trapped.
O   Overflow: Expression is too complex to evaluate.
P   Phase Error: Label value changes on two passes through
    assembly.
R   Register Error: The value specified as a register is
    incompatible with the code.
S   Syntax Error: Improperly formed expression.
U   Undefined Label: Label used does not exist.
V   Value Error: Improperly formed operand encountered in an
    expression.

Examples:

     A:ASM PROG
     A:ASM PROG.BBX
     A:ASM B:PROG.BZZ

DDT                           NOT INCLUDED IN PACKAGE
                           FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     DDT [filespec]

Purpose:

DDT is used in debugging 8080 programs.  If you specify DDT without a
filespec, DDT loads into the TPA and prompts for a command.  The
command character can be followed by one or more arguments:
hexadecimal values, file specifications, or other information,
depending on the command.  Arguments are separated from each other by
commas or spaces.  No spaces are allowed between the command character
and the first argument.  Optional parts of the command are enclosed in
square brackets ([]).

Examples:

     A:DDT
     A:DDT PROGRAM.COM


DDT Command Summary

As               Assemble: Enter assembly language
                 statements.
D[s[f]]          Display: Display memory in Hex and ASCII.
Fs,f,bc          Fill: Fill memory block - byte.
G[s][,b1[,b2]]   Go: Begin execution.
Hc1,c2           Hex: Hexadecimal sum and difference.
Ifilespec        Input: Set up input command line for R or W
                 commands.
L[[,f]]          List: List memory in mnemonic form.
Ms,f,d           Move: Move memory block.
R[o]             Read: Read disk file to memory.
Ss               Set: Set memory values.
T[n]             Trace: Trace program execution.
U[n]             Untrace: Monitor execution without trace.
X[r]             Examine: Examine and modify CPU registers.

Symbol           Meaning

bc               byte constant
b1               breakpoint one
b2               breakpoint two
c1               byte or word constant one
c2               byte or word constant two
d                destination data
f                final address
n                number of instructions to execute
o                offset to load address
r                8080 CPU register or flag name
s                starting address


DIR

Syntax:

     DIR [d:filename.typ]

Purpose:

DIR displays names of files on the specified disk.  DIR does not
display files set to SYS.

Examples:

     A:DIR
     A:DIR B:
     A:DIR B:MYFILE.TEX
     A:DIR A*.ASM
     A:DIR PROG???.PRN
     A:DIR PROGRAM.*


DUMP                         NOT INCLUDED IN PACKAGE
                          FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     DUMP filespec

Purpose:

The DUMP command lets you display the contents of a file in hex.  The
DUMP.ASM file (on disk) provides you with the DUMP utility's source
code.

Example:

     A: DUMP ASM.COM


ED                        NOT INCLUDED IN PACKAGE
                       FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     ED [d:filename.typ]

Purpose:

ED is the CP/M line editor.  Using the ED commands, you can create or
alter your files.  Optional parts of the commands are enclosed in
square brackets ([]).

Example:

     A:ED TEST.DAT

In ED, the [Control] key appears an an up arrow ( ).

L           Logical [cr][lf] within strings.
X           Line delete.
Z           String terminator/separator, exit insert mode.
Backspace   Delete character.
C           Stop function.


ED Command Summary

Command         Action

nA              Append n lines from original file to memory
                buffer.
0A              Append file until buffer is half full.
#A              Append file until buffer is full (or end of
                file).
B,-B            Move CP to beginning (B) or bottom (-B) of
                buffer.
nC,-nC          Move CP n characters forward (C) or backward
                (-C) through buffer.
nD,-nD          Delete n characters before (-D) or after (D)
                the CP.
E               Save new file and return to CP/M.
Fstring[Z]      Find character string.
H               Save the new file, then reedit, using the
                new file as the original.
I               Enter insert mode; use Z to exit insert
                mode.
Istring[Z]      Insert string at CP.
J[search str]Z  Juxtapose strings.
 [insert str]Z
 [delete to str]Z
nK,-nK          Delete n lines from the CP.
nL,-nL,0L       Move CP n lines.
nMcommands      Execute commands n times.
n,-n            Move CP n lines and display that line.
n:              Move to line n.
cncommand       Execute command through line n.
Nstring[Z]      Extended find string.
O               Return to original file.
nP,-nP          Move CP n lines forward or backward and
                display n lines at console.
Q               Abandon new file; return to CP/M.
R               Read X$$$$$$$.LIB file into buffer.
Rfilespec       Read filename.LIB into buffer
Sdelete str Zinsert
str[Z           Substitute string.
nT,-nT,0T       Type n lines
U,-U            Upper-case translation.
V,-V,0V         Line numbering on/off; display free buffer
                space.
nW              Write n lines to new file.
nX              Write n lines to temporary LIB file.
QX              Delete file X$$$$$$$.LIB
nZ              Wait n seconds.


ERA

Syntax:

     ERA [d:filename.typ]

Purpose:

ERA erases a file or group of files.  ERA accepts wildcard filenames.

Note:  In the Emulator, the ERA command displays the name of each file
as it is deleted.

Examples:

     A:ERA PROGRAM.BAS
     A:ERA B:LETTER.DAT
     A:ERA A:LETTER.*
     A:ERA *.BAK
     A:ERA B:*.*


LOAD                       NOT INCLUDED IN PACKAGE
                        FOR DOCUMENTATION PURPOSES ONLY

Syntax:

      LOAD filespec

Purpose:

The LOAD command invokes the LOAD utility.  The LOAD utility converts
.HEX (Intel format) program files created with ASM to executable .COM
machine-code files.  Since .HEX is the default extension, there's no
need to include it in the filespec.

Example:

     A: LOAD DUMP


PIP                        NOT INCLUDED IN PACKAGE
                        FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     Destination = Source

     PIP [d: |filespec = filespec][options]
     PIP [filespec = d:][options]
     PIP [d:filename.type = filespec1,filespec2,...]
     PIP [filespec|device: =
         filespec][options][|device:][options]
     PIP

Purpose:

PIP copies files, combine files, and transfers files between
peripheral devices.  The first filespec is the destination; the second
filespec is the source.  Source filespec with options can be repeated,
separated by commas, to combine two or more files into one
concatenated file.  The source or destination can be any CP/M logical
device.  PIP entered with no command tail displays a * prompt and
awaits your series of commands, entered and executed one line at a
time.

Examples:

     Copies from One Disk to Another
     A:PIP B: = A:DRAFT.TEX
     A:PIP B:DRAFT.TEX = A:

     Copy and File
     A:PIP B:NEWDRAFT.TEX = A:OLDDRAFT.TEX
     A:PIP NEWDRAFT.TEX = OLDDRAFT.TEX

     Copy Multiple Files
     A:PIP[cr]
     A:PIP B: = *.TEX[AV]
     A:B: = *.COM[RW]
     A:PIP B: = C:DRAFT.*
     A:PIP B: = *.*
     A:PIP B: = C:*.*


     Combine Multiple Files
     A:PIP B:NEW.DAT = FILE1.DAT,FILE2.DAT

     Copy, Rename, and Get from User 1
     A:PIP NEWDRAFT.TEX = OLDDRAFT.TEX[G1]

     Copy to/from Logical Devices
     A:PIP B:FUNFILE.SUE = CON:
     A:PIP LST: = CON:
     A:PIP LST: = B:DRAFT.TEX[T8]
     A:PIP PRN: = B:DRAFT.TEX

PIP Options:

Option      Description

A           Archive: Copy only modified files.
Dn          Delete any characters past column n.
E           Echo transfer to console.
F           Filter form-feeds from source data.
Gn          Get file from user number n.
H           Test for valid Hex format.
I           Ignore :00 Hex data records, test for valid
            Hex format.
L           Translate upper-case to lower-case.
N           Number the output lines, incrementing by 1
            starting at 1. Object file transfer, Z ignored.
Pn          Set page length to n (default n = 60).
Qs Z        Quit copying from source at string s.
R           Read files that have been set to SYS (system).
Ss Z        Start copying from the source at string s.
Tn          Expand tabs to n spaces.
U           Translate lower-case to upper-case.
V           Verify that data has been written correctly.
W           Write over files that have been set to
            Read-Only.
Z           Zero the parity bit.


PIP Logical Devices

The following four devices are mapped in the IOBYTE using STAT and
must be defined in BIOS:

CON:        Console device.
LST:        List device.
PUN:        Punch device.
RDR:        Reader device.

Additional device names that can be used in PIP commands are:

INP:        Patched character input.
OUT:        Pathced character output.
PRN:        Like LST; tabs on 8th character, page breaks on
            60th line; numbers lines.
EOF:        Generates CTRL-Z (end of file).
NUL:        Generates 40 nulls for PUN device.


PIP Physical Devices

TTY:        Console, terminal, reader, punch,
            teletypewriter.
CRT:        Console, terminal, CRT device.
PTR:        Paper tape or card reader.
PTP:        Paper tape or card punch.
LPT:        List device, line printer.
UC1:        User-defined console.
UR1:        User-defined reader.
UR2:        User-defined reader.
UP1:        User-defined punch.
UP2:        User-defined punch.
UL1:        User-defined listing device.


REN

Syntax:

     REN [d:newfile.typ = oldfile.typ]

Purpose:

REN changes the name of the existing file (oldfile) to the name
specified by newfile.

Note: In the Emulator, the REN command allows you to omit one drive
specification.

Examples:

     A:REN NEWFILE.DAT = OLDFILE.INP
     A:REN B:NEWFILE.DAT = OLDFILE.DAT
     B:REN NEWLIST = OLDLIST


SAVE

Syntax:

     SAVE n[d:filename.typ]

Purpose:

SAVE copies to a disk file the contents of the Transient Program Area
(TPA) starting at location 100 Hex and continuing to the page
indicated by n in the command tail.  SAVE assigns the filename and
filetype specified in the command tail.  Wildcard characters are not
accepted.  The number of pages to save can be calculated using DDT.

Examples:

     A:SAVE 3 EXTRA.COM
     A:SAVE 40 QUICK
     A:SAVE 4 X.Y
     A:SAVE 10 B:ZOT.COM


STAT                    NOT INCLUDED IN PACKAGE
                     FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     Display Status
     STAT
     STAT [d:]
     STAT [filespec]
     STAT [d:DSK:]
     STAT [DEV:|VAL:|USR:]

     Change Status:
     STAT [d: = R/O]
     STAT [filespec $R/O|R/W|SYS|DIR]
     STAT [filespec $S]

Purpose:

STAT returns information about files, disk drives, and other
peripheral devices attached to the computer.  STAT changes attributes
of drives and files.  STAT with no command tail returns free storage
space in kilobytes for the current drive, and also tells if the drive
is Read-Only )R/O) or Read-Write (R/W).  Use STAT to set the drive to
R/O and [Control][C] to reset it to R/W.  STAT filespec returns the
number of kilobytes used by a file, and the attributes of that file.
STAT filespec can, with an option, set a file or files to R/O, R/W,
SYS, or DIR.  STAT displays files set to SYS in parentheses.  STAT
DSK: shows the characteristics of the default or specified drive.
STAT USR: shows which user numbers contain files on a given disk.
STAT VAL: shows the possible commands and the external devices that
can be assigned to your computer.  STAT DEV: displays the current
logical device assignments.  STAT accepts wildcards in the command
tail.

Examples:

     A:STAT
     A:STAT [myfile.txt]
     A:STAT [C:letter.bak]
     A:STAT [genledgr.dat] = $R/O]
     A:STAT [*.com = $R/O]
     A:STAT [*.bak]
     A:STAT [B:*.*]

Options

R/W         Read-Write.
R/O         Read-Only.
SYS         System attribute.
DIR         No system attribute.
S           Display the size of the file or files based
            on last record numbers.
USR:        Display USER numbers containing files.
DSK:        Display characteristic of the drive.
VAL:        Display possible STAT commands and devices.
DEV:        Display current logical device assignments.

SUBMIT                       NOT INCLUDED IN PACKAGE
                          FOR DOCUMENTATION PURPOSES ONLY

Syntax:

     SUBMIT [filename][parameters]

Purpose:

SUBMIT starts execution of a file of CP/M commands, one command per
line in the file.  The SUBMIT file must have a filetype of .SUB.  Any
optional parameters following the file specification in the command
line, such as a drive or file specification, are substituted for their
corresponding formal parameters ($1,$2,...) in the SUBMIT file.

Note:  In the Emulator, command lines beginning with a semicolon (;)
are ignored in order to support command lines within SUBMIT files.
Also SUBMIT processing may be initiated from any drive.

Examples:

     A:SUBMIT START
     A:SUBMIT B:START
     A:SUBMIT START C:LETTER

In the preceding examples, START.SUB is the SUBMIT file.  The command
lines in START.SUB are not displayed here.  In the second example,
START.SUB is on Drive B.  In the last example, the actual parameters
C: and LETTER follow the SUBMIT filename.  SUBMIT>COM creates a
temporary file and substitutes the actual parameters in the command
line for the formal parameters ($1, $2,...) appearing in the SUBMIT
file START.SUB.  C: is substituted for any $1 parameters that appear
in the SUBMIT file.  START.SUB LETTER is substituted for any $2
parameters that appear in the START.SUB SUBMIT file.


TYPE

Syntax:

     TYPE [d:filename.typ]

Purpose:

TYPE displays the contents of an ASCII file on screen.  Press any key
to stop the display.  TYPE does not accept wildcard filespecs.
Entering a [Control][P] before the type command causes the output to
be echoed to the printer; another [Control][P] stops the printing.

Examples:

     A:TYPE [letter.dat]
     B:TYPE [a.document.law]
     B:TYPE [program.bas]
     a:TYPE [B:reader.asm]


USER

Syntax:

     USER n

Purpose:

USER with a number from 0 to 15 changes the current user number to the
number specified by n.  CP/M assumes a default user number of 0.  STAT
USR displays current and active users.

Note: In the Emulator, command files not found under the current user
are additionally searched under user 0.

Examples:

     B:USER 2
     A:USER 7


XSUB


Syntax:

     XSUB

Purpose:

XSUB, when used within a SUBMIT file, allows most programs to accept
input from command lines in the SUBMIT file rather than from the
console.  The XSUB command must appear before the command line that
invokes the program requiring console input.

Example:

     A:TYPE SAVER.SUB
     XSUB
     DDT
     |$1.HEX
     R
     GO
     SAVE 1 $2.COM

CP/M CONTROL CHARACTER SUMMARY

KEYSTROKE         ACTION

[CTRL][C]         Aborts the current program and performs a
                  warm start.
[CTRL][E]         Forces a physical carriage return, but
                  does not sent command to CP/M.
[CTRL][H]         Same as [Backspace].
[CTRL][J]         Line-feed; terminates input at the
                  console.
[CTRL][M]         Same as carriage return.
[CTRL][P]         Echoes all console activity at the
                  printer; a second [CTRL][P] ends printer
                  echo.
[CTRL][S]         Stops console listing temporarily;
                  [CTRL][S] resumes the listing.
[CTRL][X]         Deletes all characters in the command
                  line.
[CTRL][Z]         String or field separator.
[Backspace]       Moves cursor back one space; erases
                  previous character.
[DEL]             Same as [Backspace].
[Return]          Carriage return.

Note: In the Emulator, changed disks are automatically detected and
newly logged in.  [CTRL][C] is no longer necessary to log in new
disks.

CP/M FILETYPES

CP/M identifies every file by a unique file specification, which
consists of a drive specification, a filename, and a filetype.  The
filetype is an optional three character ending separated from the
filename by a period.  The filetype generally indicates a special kind
of file.  Common filetypes and their meanings follow.

FILETYPE    MEANING

ASM         Assembly language source file; the CP/M
            assembler, ASM, assembles or translates
            an .ASM file into machine language.

BAK         Back-up file created by text editor; the editor
            renames the source file with this filetype to
            indicate that the original file has been
            processed.  The original file stays on disk
            as the back-up file, so you can refer to it.

BAS         CBASIC (tm) program source file.

COM         8080 executable file.

HEX         Program file in Intel hexadecimal format.

INT         CBASIC program intermediate language file.

IRL         Indexed REL file produced by LIB.

LIB         Used by MAC (tm) and RMAC (tm) for macro
            libraries. The ED R command reads files of
            type LIB.  The ED X command writes files of
            type LIB.  Printable file displayable on
            console or printer.

OVL         Program overlay file.  PL/I-80 (tm) compiler
            overlays files; you can create overlay files
            with LINK-80 (tm).

PLI         PL/I-80 source program filetype.

PRN         Printable file displayable on console or
            printer.

REL         Relocatable file produced by RMAC and PL/I-80
            that can be linked by LINK-80.

SUB         Filetype required for submit file containing one
            or more CP/M commands.  The SUBMIT program
            executes commands in files of type SUB,
            providing a batch execution mode for CP/M.

SYM         Symbol table file.  MAC, RMAC, and LINK-80
            output files of type SYM.  SID (tm) and ZSID
            (tm) read files of type SYM.

TEX         Source file for TEX-80, the Digital Research
            text formatter.

XRF         Cross-reference file produced by XREF.

$$$         Temporary file.

CP/M MESSAGES

? (DDT Error Message)

DDT.  This message appears when DDT does not understand the assembly
language instruction, the file cannot be opened, a checksum error
occurred in a .HEX file, or the assembler/disassembler was overlayed.


ABORTED

PIP.  You stopped a PIP operation by pressing a key.


ASM ERROR MESSAGES

D      Data Error:  Data statement element cannot be placed
       in specified data area.

E      Expression Error:  Expression cannot be evaluated
       during assembly.

L      Label Error:  Label cannot appear in this context
       (might be duplicate label).

N      Not implemented:  Unimplemented features such as
       macros are trapped.

O      Overflow:  Expression is too complex to evaluate.

P      Phase Error:  Label value changes on two passes
       through assembly.

R      Register Error:  Value specified as a register is
       incompatible with the code.

S      Syntax Error:  Improperly formed expression.

U      Undefined Label:  Label used does not exist.

V      Value Error:  Improperly formed operand encountered
       in an expression.


BAD DELIMITER

STAT.  Check command line for typing errors.


BAD LOAD

CCP error message, or SAVE error message.


BDOS ERR ON D:

Basic Disk Operating System (BDOS) Error on the designated drive.
CP/M replaces d: with the drive specification of the drive where the
rror occurred.  This message is followed by one of the four phrases in
the situations that follow.

Note:  The Basic Input/Output System (BIOS) passes codes to the BDOS.
These codes detrmine which messages the BDOS prints.  The BIOS is
dependent on the hardware and varies among computers.  Therefore, the
specific cause of these BDOS error messages can vary.


BREAK "x" AT C

ED. "x" is one of the symbols described below and C is the command
letter being executed when the error occurred.

#      Search failure.  ED cannot find the string specified
       in an F, S, or N command.

?      Unrecognized command letter c.  ED does not recognize
       the indicated command letter, or an E, H, Q, or O
       command is not alone on its command line.

O      The file specified in an R command cannot be found.

       Buffer full.  ED cannot put any more characters in
       the memory buffer, or the string specified in an F,
       N, or S command is too long.

E      Command aborted.  A keystroke at the console aborted
       command execution.

F      Disk or directory full.  This error is followed by
       either the disk or directory-full message.  Refer
       to the recovery procedures listed under these
       messages.


CHECKSUM ERROR

PIP.  A Hex record checksum error was encountered.  The HEX record
that produced the error must be corrected, probably by recreating the
.HEX file.

CHECKSUM ERROR
LOAD ADDRESS hhhh
ERROR ADDRESS hhhh
BYTES READ:
hhhh:

LOAD:  File contains incorrect data.  Regenerate .HEX file from the
source.


COMMAND BUFFER OVERFLOW

SUBMIT.  The SUBMIT buffer allows up to 2048 characters in the input
file.


[COMMAND TEXT FOLLOWED BY]?

CP/M receives a command specifying a nonexistent drive.  CP/M
terminates the current program as soon as you press any key.  Press
[Return] or [Control][C] to recover.


COMMAND TOO LONG

SUBMIT.  A command in the SUBMIT file cannot exceed 125 characters.



CORRECT ERROR, TYPE RETURN OR CTRL-Z

PIP. A Hex record checksum was encountered during the transfer of a
.HEX file.  The .HEX file with the checksum error should be corrected,
probably by recreating the .HEX file.



CPMZ80 ERROR ON DRIVE D: BAD SECTOR

This message appears when CP/M finds no disk in the drive, the disk is
improperly formatted or power to the drive is off.  Check for one of
these situations and try again.  This message can also indicate a
hardware problem or a worn or improperly formatted disk.  Press
[Control][C] to terminate the program and return to CP/M, or press
[Return] to ignore the error.


CPMZ80 ERROR ON DRIVE D: BAD SECTOR

CP/M cannot write to the file.  This usually occurs because the disk
is write-protected.

ASM. An output file cannot be closed.  This is a fatal error that
terminates ASM execution.  Check to see that the disk is in the drive
and that the disk is not write-protected.

DDT. The disk file written by a W command cannot be closed.  This is a
fatal error that terminates DDT execution.  Check that the correct
disk is in the dirve, and that the disk is not write-protected.

SUBMIT.  This error can occur during SUBMIT file processing.  Check
that the correct system disk is in Drive A, and that the disk is not
write-protected.  The SUBMIT job can be restarted after rebooting
CP/M.


CPMZ80 ERROR ON DRIVE D: BAD SECTOR

PIP.  PIP cannot read the specified source.  Reader cannot be
implemented.


CPMZ80 ERROR ON DRIVE D: BAD SECTOR

PIP.  The destination specified in the PIP command is illegal.  You
probably specified an input device as a destination.


CPMZ80 ERROR ON DRIVE D: BAD SECTOR

PIP.  The input disk file specified in a PIP command cannot be read
properly.  This is usually the result of an unexpected end-of-file.
Correct the problem in your file.


CPMZ80 ERROR ON DRIVE D: BAD SECTOR

ASM.  You specified a write-protected disk as the destination for the
.PRN and .HEX files, or the disk has no space left.  Correct the
problem before assembling your program.


CPMZ80 ERROR ON DRIVE D: FILE IS READ-ONLY

You tried to erase, rename, or set file attributes on a Read-Only
file.  The file should first be set to Read/Write (R/W) with the
command: STAT filespec $R/W.


CPMZ80 ERROR ON DRIVE #: SELECT FAILED

ED.  you typed the ED command without a filename.  Reenter the ED
command, followed by the name of the file you want to edit or create.


CPMZ80 ERROR ON DRIVE #: SELECT FAILED

CP/M received a command line specifying a nonexistent drive, or the
disk in the drive is improperly formatted.  CP/M terminates the
current program as soon as you press any key.


CPMZ80 ERROR ON DRIVE D: SELECT FAILED

ASM.  The assembler cannot find the file you specified.  Either you
mistyped the file specification in your command line, or the filetype
is not ASM.


DESTINATION IS R/O, DELETE (Y/N)?

PIP.  The destination file specified in a PIP command already exists,
and is Read-Only.  If you type Y, the destination file is deleted
before the file copy is done.


DIRECTORY FULL

ED.  There is not enough directory space for the file being written to
the destination disk.  you can use the OXfilespec command to erase any
unnecessary files on the disk without leaving the editor.

SUBMIT.  There is not enough directory space to write the $$$.SUB file
on Drive A, which is used for processng SUBMITs.  Erase some files or
use a new disk and retry.


DISK FULL

ED.  There is not enough disk space for the output file.  This error
can occur on the W,E,H, or X commands.  If it occurs with an X
command, you can repeat the command, prefixing the filename with a
different drive.


DISK WRITE ERROR - [FILESPEC]

DDT.  A disk-write operation cannot be successfully performed during a
W command, probably due to a full disk.  You should either erase some
unnecessary files or use another disk with more space.

PIP.  A disk-write operation cannot be successfully performed during a
PIP command, probably due to a full disk.  You should either erase
some unnecessary files or use another disk with more space and execute
PIP again.

SUBMIT.  The SUBMIT program cannot write the $$$.SUB file to the disk.
Erase some files or use a new disk and try again.


ERROR: CANNOT OPEN SOURCE,
LOAD ADDRESS hhhh

LOAD.  Caused by an error code returned by a BDOS function call.  Disk
might be write-protected.


ERROR: CANNOT OPEN SOURCE,
LOAD ADDRESS hhhh

LOAD.  Cannot find source file.  Check disk directory.


ERROR: DISK READ, LOAD ADDRESS hhhh

LOAD.  Caused by an error code returned by a BDOS function call.


ERROR: DISK WRITE, LOAD ADDRESS hhhh

LOAD.  Destination disk is full.


ERROR: INVERTED LOAD ADDRESS,
LOAD ADDRESS hhhh

LOAD.  The address of a record was too far from the address of the
previously processed record.  This is an internal limitation of LOAD,
but it can be circumvented.  Use DDT to read the .HEX file into
memory, then use a SAVE command to store the memory image file on
disk.


ERROR: NO MORE DIRECTORY SPACE,
LOAD ADDRESS hhhh

LOAD.  Disk directory is full.


ERROR ON LINE nnn MESSAGE

SUBMIT.  The SUBMIT program displays its messages in the format shown
above, where nnn represents the line number of the SUBMIT file.  Refer
to the message following the line number (messages will vary).

FILE ERROR

ED.  Disk or directory is full, and ED cannot write anything more on
the disk.  This is a fatal error, so make sure there is enough space
on the disk to hold a second copy of the file before invoking ED.


FILE EXISTS

You asked CP/M to create or rename a file using a file specification
that is already assigned to another file.  Either delete the existing
file or use another file specification.

REN.  The new name specified is the name of a file that already
exists.  You cannot rename a file with the name of an existing file.
If you want to replace an existing file with a newer version of the
same file, either rename or erase the existing file, or use the PIP
utility.


FILE EXISTS, ERASE IT

ED.  The destination filename already exists when you are placing the
destination file on a different disk than the source.  It should be
erased, or another disk selected to receive the output file.


** FILE IS READ/ONLY **

ED.  The file specified in the command to invoke ED is Read-Only.  ED
can read the file so that you can examine it, but ED cannot change a
Read-Only file.


FILE NOT FOUND

CP/M cannot find the specified file.  Check that you have entered the
correct drive specification and that you have the correct disk in the
drive.

ED.  ED cannot find the specified file.  Check that you have entered
the correct drive specification and that you have the correct disk in
the drive.

STAT.  STAT cannot find the specified file.  The message might appear
if you omit the drive specification.  Check that the correct disk is
in the drive.

hhhh?? = dd

DDT.  The ?? indicates DDT does not know how to represent the
hexadecimal value dd encountered at address hhhh in 8080 assembly
language.  dd is not an 8080 machine instruction opcode.


INSUFFICIENT MEMORY

DDT.  There is not enought memory to load the file specified in an R
or E command.


INVALID CONTROL CHARACTER

SUBMIT.  The only valid control characters in the SUBMIT file of type
SUB are A through Z.  Note that in a SUBMIT file, the control
character is represented by typing the circumflex, not by pressing the
[Control] key.


INVALID DIGIT: STRING

PIP.  An invalid hex digit has been encountered while reading a .HEX
file.  The hex file with the invalid .HEX digit should be corrected,
probably by recreating the .HEX file.


INVALID DISK ASSIGNMENT

STAT.  You specified an invalid drive or file assignment, or
misspelled a device name.  This error message might be followed by a
list of the valid file assignments that can follow a filename.  If an
invalid drive assignment was attempted, the message "Use: d: = RO" is
displayed showing the proper syntax for drive assignments.


INVALID DISK ASSIGNMENT

STAT.  Might appear if you follow the drive specification with
anything except = R/O.


INVALID DRIVE NAME (USE A, B, C, OR D)

SYSGEN.  SYSGEN recognizes only drives A, B, C, and D as valid
destinations for system generation.


INVALID FILE INDICATOR

STAT.  Appears if you do not specify RO, RW, DIR, or SYS.


INVALID FORMAT: [FILESPEC]

PIP.  The format of your PIP command is illegal.  See the description
of the PIP command.


INVALID FORMAT: [FORMAT STRING]

PIP.  You have placed an invalid character for a separator between two
input filenames.

INVALID FORMAT: SYNTAX

PIP.  You entered an illegal parameter in a PIP command.  Retype the
entry correctly.


INVALID HEX DIGIT
LOAD ADDRESS hhhh
ERROR ADDRESS hhhh
BYTES READ:
hhhh


INVALID MEMORY SIZE

MOVCPM.  Specify a value less than 64K or your computer's actual
memory size.


N?

LOAD.  File contains incorrect .HEX digit.

USER.  You specified a number greater than 15 for a user area number.
For example, if you type USER 16[cr], the screen displays 16?.


NO DIRECTORY SPACE

ASM.  The disk directory is full.  Erase some files to make room for
.PRN and .HEX files.  The directory can usually hold only 64
filenames.


NO DIRECTORY SPACE - [FILESPEC]

PIP.  There is not enough directory space for the output file.  you
should either erase some unnecessary file or get another disk with
more directory space and execute PIP again.


NO FILE: = [FILESPEC]

DIR, ERA, REN, PIP.  CP/M cannot find the specified file, or no files
exist.

ASM.  The indicated source or include file cannot be found on the
disk.

DDT.  The file specified in an R or E command cannot be found on the
disk.


NO FILE: = [FILESPEC]

PIP.  An input file that you have specified does not exist.


NO INPUT FILE PRESENT ON DISK

DUMP.  The file you requested does not exist.


NO MEMORY

There is not enough memory available for loading the program
specified.


NO SUB FILE PRESENT

SUBMIT.  For SUBMIT to operate properly, you must create a file with
filetype of SUB.  The SUB file contains usual CP/M commands.  Use one
command per line.


NOT FOUND: [FILESPEC,#]

PIP.  You have specified a user number greater than 15.  User numbers
are in the range of 0 to 15.


** NOT DELETED **

PIP.  PIP did not delete the file, which might have had the R/O
attribute.


PARAMETER ERROR

SUBMIT.  Within the SUBMIT file of type SUB, valid parameters are $0
through $9.


QUIT NOT FOUND: - [FILESPEC]

PIP.  The string argument to a Q parameter was not found in your input
file.


READ ERROR

TYPE.  An error occurred when reading the file specified in the type
command.  Check the disk and try again.  The STAT filespec command can
diagnose trouble.


READER STOPPING

PIP.  Reader operation interrupted.


RECORD TOO LONG

PIP.  PIP cannot process a record longer than 128 bytes.


SOURCE FILE NAME ERROR

ASM.  When you assemble a file, you cannot use the wildcard characters
* and ? in the filename.  Only one file can be assembled at a time.


START NOT FOUND = [FILESPEC]

PIP.  The string argument to an S parameter cannot be found in the
source file.


CHAPTER 3
CP/M AND CP/M-Z80 EMULATOR TECHNICAL REFERENCE

EMULATOR IMPLEMENTATION

The Emulator is completely written in assembly language and maximally
uses the large register frame of the MC 68000.

Z80 I/0 opcodes are supported by a built-in interface of user-supplied
drivers.


NOTES ON CPM-Z80 EMULATOR CCP IMPLEMENTATION

The Console Command Processor (CCP) is CP/M 2.2 upward compatible but
enhanced in many respects.

User Memory (TPA) is 58K ("63K CP/M").


EMULATOR BDOS IMPLEMENTATION

The BDOS system interface is totally compatible with CP/M 2.2.  Full
implementation of the BIOS interface permits application programs to
use direct BIOS access (even disk related).

Changed disks are automatically detected and newly logged in.  The
[Control] [C] command is no longer necessary.

With disk read and write errors, the user can optionally abort, retry,
or ignore the error.


EMULATOR BIOS IMPLEMENTATION

The BIOS functions are directed to 68000 routines which use the TOS
BIOS.

All physical I/O devices implemented under TOS are accessible under
the CPM-Z80 Emulator.  The printer port is mapped to the CPM-Z80 LST:
device; the TTY device corresponds to the modem port; the floppy
drives act as A: and B: drives under the Emulator; and the CON: device
accesses the keyboard and screen of the ATARI ST Computer.

A fully implemented CP/M 2.2 compatible I/O byte allows the user to
change the logical to physical I/O device-mapping.


EMULATOR PERFORMANCE

The time ratio (Emulator/Z80) between the Emulator on an 8MHz 68000
system and a 4MHz Z80 system was measured for some CP/M 2.2 programs:

Extreme Values:  0.6 and 6.0
Average:         2.0


EMULATOR INTERFACE TO USER I/O

A special interface is provided to line 68000 hardware I/O to Z80
programs. A user-supplied I/O driver can optionally be activated.
When you boot the Emulator, it looks for the file EMUIO.PRG.  The
Emulator tries to open this file and loads it.  If the file was loaded
successfully, the I/O driver is activated and the Emulator displays
the message:

Emulator I/O driver installed.

If a hardware I/O driver cannot be found, Z80 I/0 opcodes in emulated
programs lead to the message:

Emulator error =>  Illegal opcode : XX XX  at address : XXXX

and the Emulator is aborted.


GENERAL RESTRICTIONS

The Emulator does not support any undocumented Z80 opcodes or
hardware-dependant opcodes such as interrupt control.  If the Emulator
finds such opcodes in emulated programs, it aborts with the message

Emulator error =>  Illegal opcode : XX XX  at address : XXXX


EMULATOR I/O DRIVER CONVENTIONS

If a user-driver is activated, the Z80 I/O opcodes are directed into
this driver.  The driver has to be a user-coded 68000 program with the
following conventions:

The driver code must begin with two jump instructions.  The first jump
is used by all input requests and the second by all output requests.
These jumps lead to the user input and output service routines.  These
routines terminate with a Return To Subroutine (RTS) instruction.

The input routine receives the Z80 port number in the low byte of
register D0, and must return the input value in the low byte of D0.

The output routine receives the Z80 port number in the low byte of
register D0, and the output value in the low byte of D1.

All registers may be used within the user-driver.  The user-driver
must be supplied as a TOS ".PRG" file.  The following is a user I/O
driver example:

This simple 68000 code example shows how to access 16 contiguous I/0
ports from startaddress $FFFF81 through $FFFF9F on odd addresses.  For
example, the Z80 instruction IN A,(07H) in an emulated program would
read a byte from 68000 address $FFFF8F.

              .TEXT

    IOBASE:   .EQU    $FFFF80

    IO:       JMP     INPUT
              JMP     OUTPUT

    INPUT:    MOVE.L  #IOBASE,A0
              AND.W   #$000F,D0
              ADD.W   D0,D0
              MOVE.B  1(A0,D0.W),D0
              RTS

    OUTPUT:   MOVE.L  #IOBASE,A0
              AND.W   #$000F,D0
              ADD.W   D0,D0
              MOVE.B  D1,1(A0,D0.W)
              RTS

             .END

CP/M BDOS FUNCTION SUMMARY>

No.  Hex   Function Name        Input         Output

 0   00H   Sys Reset            None          None
 1   01H   Con Input            None          A=char
 2   02H   Con Output           E=char        None
 3   03H   Reader Input         None          A=char
 4   04H   Punch Output         E=char        None
 5   05H   List Output          E=char        None
 6   06H   Direct Con I/O *     E=0FEH inpt   A=0 or Char
                                0FEH stat     0 or nonzero
                                Char outpt    No value
 7   07H   Get I/O Byte         None          A=IOBYTE
 8   08H   Set I/O Byte         E=IOBYTE      None
 9   09H   Print String         DE=.Buffer    None
10   0AH   Read Con Buf         DE=.Buffer    Chars in Buf
11   0BH   Get Con Status       None          A=00/nonzero
12   0CH   Rtn Version #        None          HL=Vers **
13   0DH   Reset Disk Sys       None          None
14   0EH   Select Disk          E=Disk Num    None
15   0FH   Open File            DE=.FCB       A=Dir Code
                                              A=FF if
                                              not found
16   10H   Close File           DE=.FCB       A=Dir Code
                                              A=FF if
                                              not found
17   11H   Search for First     DE=.FCB       A=Dir Code
                                              A=FF if
                                              not found
18   12H   Search for Next      None          A=Dir Code
                                              A=FF if
                                              not found
19   13H   Delete File          DE=FCB        A=Dir Code
                                              A=FF if code
                                              not found
20   14H   Read Seq             DE=FCB        A=0 if ok
                                              A=Err Code
21   15H   Write Seq            DE=FCB        A=0 if ok
                                              A=Err Code
22   16H   Make File            DE=FCB        A=Dir Code
                                              A=FF if no
                                              Dir space
23   17H   Rename File          DE=FCB        A=Dir Code
                                              A=FF if
                                              not found
24   18H   Rtn Login Vect       None          HL= Login
                                              Vect **
25   19H   Rtn Cur Disk         None          A=Cur Disk #
26   1AH   Set DMA Addr         DE=DMA        None
27   1BH   Get Addr(Alloc)      None          HL=Login
28   1CH   Write Prot Disk      None          None
29   1DH   Get R/O Vect         None          HL=R/O Vect **
30   1EH   Set File Attrib      DE=FCB        None
31   1FH   Get Addr
           (dsk parm)
32   20H   Set/Get Usr Code     E=0FFH GET    User #
                                E=0-0FH SET
33   21H   Read Ran             DE=FCB        A=Err Code
34   22H   Write Ran            DE=FCB        A=Err Code
35   23H   Compute File Size    DE=FCB        r0,r1,r2
36   24H   Set Ran Rec          DE=FCB        r0,r1,r2
37   25H   Reset Drive  ***     DE=drv vect   A=0
40   28H   Write Ran w/Fill     DE=FCB        A=Err Code

  *Note that function 6 must be used with functions
   1,2,9, or 11
 **Note that A=L and B=H upon return
***Default drive cannot be reset.

The preceding table used these abbreviations

Addr      =        Address
Alloc     =        Allocation
Attrib    =        Attribute
Buf       =        Buffer
Char      =        ASCII Character
Con       =        Console
Cur       =        Current
Dir       =        Directory
Dsk       =        Disk
Err       =        Error
Parm      =        Parameter
Prot      =        Protect
Ran       =        Random
Rec       =        Record
Rtn       =        Return
Seq       =        Sequential
Stat      =        Status
Sys       =        System
Usr       =        User
Vect      =        Vector
Vers      =        Version


*END OF MANUAL*