MUSIC IN THE KEY OF C

                                           By Mark Lewis Baldwin

*****************************************************************************
                                 NOTICE

This article and the attached program and code are Copyright (c) 1986 by
Mark Lewis Baldwin.  It is realeased as shareware.  It may be copied and
distributed freely so long as this notice and the copyright remain
intact.

If you feel that the article/program is of value, please send me a
pricely sum of $1 for its use.  If the code (or a substatial part
thereof) is used in a commercial product, I ask that a sum of $100 be
sent to me for licensed use of the code.  My mailing address is:

    Mark Baldwin
    Beacon Technical Services
    7711 S Curtice Way, #E
    Littleton, CO 80120

I can also be reached through GEnie at M.L.BALDWIN and through
Compuserve at 73637,3032.

I hope that you find the article of value.  Enjoy.

Mark Baldwin

*****************************************************************************

    Over the past months, there have been many articles about using the
MIDI for music on the Atari ST.  But the ST has an internal sound chip
as well capable of a wide range of sound and music.  Lets have a look at
this sound chip and figure out how to make beautiful music with it. 
What I'm going to do is describe the sound chip and how to talk to it. 
Then we'll look at a program I wrote for the chip which allows us to use
three independent voices and even describe instrument ADSR envelopes. 
Before I talk about the program, let us look at the sound chip itself. 

                    The Chip and Its Registers

    The ST sound chip is a General Instruments AY-3-8910 programmable
sound generator.  It has three tone generators and a noise generator
which can be mixed and matched on three output channels (or voices).  It
communicates with 16 registers, each an 8 bit word in length, from which
the user can communicate with the chip.  These registers are numbered 0
through 15.  We are actually only interested in the first 14 registers
(0-13) since the last two are used to communicate with the I/O port. 
Each of the first 14 registers has a specific purpose which are
described below:

Register 0 and 1 - These registers control the frequency (or tone) of
the first voice (Channel A) of the sound chip.  A 12 bit word is
necessary to define the frequency, therefore the lower 8 bits of the
word are stored in register 0 and the upper 4 bits of the word are
stored in the lower half of register 1.  See the next section to find
out how to convert musical notes to the proper frequency. 

Register 2 and 3 - These registers control the frequency of the second
voice (Channel B). 

Register 4 and 5 - These registers control the frequency of the third
voice (Channel C). 

Register 6 - The frequency of the noise generator is controlled through
this register.  Only the first 5 bits are used so acceptable values are
between 0 and 31. 

Register 7 - This register is actually 8 on/off flags used to control
mixing of the tone and noise generator plus control of the I/O ports
(registers 14 and 15).  Bits 0 through 2 control mixing the tone signals
for channels A, B and C respectively.  A 1 in the bit position will turn
the tone for that channel off while a 0 will turn it on.  Bits 3 through
5 do the same thing for the noise generator.  Note that by turning on
both tone and noise, you can mix both signals together.  This may be a
little confusing, so let's try an example.  Lets say we want to turn the
tone on for Channel A and B plus merge the noise signal as well on
Channel B and leave Channel C off.  As a result, we need bits 0, 1, and
4 to be 0 while 2, 3 and 5 should be set to 1.  Or in binary it looks
like this 101100 (the right most bit is bit 0).  101100 in binary
converts to 44 decimal which we would place in register 7. 

Register 8 through 10 - These registers control the volume for channels
A, B and C after mixing.  Values of 0 through 15 are acceptable with 0
being no sound and 15 being the loudest.  However, if bit 4 is set (i.e. 
a value of 16), the volume is calculated from the sound envelope data
described in registers 11 through 13. 

Register 11 through 13 - These registers describe a wave form that can
be used to control the volume of a voice should the voices respective
volume register be set to 16.  Registers 11 and 12 contain a two byte
word (lower byte in register 11) describing the length of the wave form. 
This is calculated by taking the incoming clock frequency (2 Megahertz),
dividing by 256, and then dividing that result by the contents in
registers 11 and 12.  Register 13 describes the shape of the wave form
as shown in Figure 1. 

Register 14 and 15 - As mention before, these registers have nothing to
do with producing sound but are used for the I/O ports of the ST so let
us leave them alone. 

                  Converting Musical Notes For The Registers  

    Any musical note can be calculated as follows:

                period = 284.0909091 * ( 1.059462 ** index )
                
    After rounding 'period' to an integer, the lower byte would be
stored in the first register (i.e.  registers 0, 2, or 4) while the
upper byte would be stored in the second register (i.e.  1, 3, or 5). 
The value of index is determined by counting the number of notes there
are between the desired note and a 440hz "A".  When counting, higher
notes are negative.  Remember that there are 12 notes to an octave, not
7 because of the sharps.  Therefore a "C" in the same octave as "A"
would have an index of 9 (with register values of 222 and 1) while a "B"
would be -2 (with register values of 253 and 1).  If you look in the
attached program listing, the note_f and note_c arrays contain register
data for 5 octaves around middle "A". 

                    Talking to the Sound Chip

    Now that we know what makes our chip sing (or at least croak), how
do we get the data into the chip registers.  Atari has solve that for us
by giving us two routines to communicate with the sound chip. 
    The simpler of the two routines is 'Giaccess'.  The C form is

                     char Giaccess( data, register )
                     char data
                     int register

This routine allows us to read or write to any single register in the
sound chip.  If you wish to write to a register (like putting in the
volume for a channel), 'data' would contain the value you wish to write
and 'register' would contain the register number plus 128.  The added
128 (which turns on bit 7) tells the routine that this is a write and
not a read action.  If you wish to read a register, just use the
register number itself, and the value will be returned. 
    The second routine for accessing the sound chip is 'Dosound'.  This
routine actually allows you to send an array of byte commands to the
chip and then forget about it.  Therefore, it is a little more complex. 
The C call is of the form:

                                Dosound( ptr )
                                char *ptr

where *ptr points to a byte array containing the sound commands.  The
following commands are allowed for the byte array:

Commands 0 - 15 ($00-$0F): These commands are perceived as register
numbers in which the next byte will be inserted as data.  Therefore the
sequence 8 10 would put the value 10 in register 8. 

Command 128 ($80): This command loads the next byte into a temporary
register. 

Command 129 ($81): This command uses the next three bytes as data.  The
first byte is the number of the register in which the contents of the
temporary register will be loaded.  The second byte is a 2's compliment
value to be added to the temporary register.  The third byte is the
termination value.  The sound register will be loaded once each cycle
until the temporary register equals the termination value. 

Command 130-255 ($82-$FF): The byte following this command either
terminates the byte array (with a 0) or defines the number of 50HZ
cycles before the next update. 

    The example program includes an example of using 'Dosound'.

                        Entering the Score

    Now that we know how to produce sound out of the sound chip, how can
we turn that into music.  That's what the attached example program is
for.  I designed this program to play a three voice score using multiply
designed instruments.  You can use the program just as it is or include
it in you own programming projects.  Let's go through it step by step
and see how we use it to make the sound chip sing. 
    Since we want to be able to include music easily, I had to invent a
simple language to describe the musical score.  Two scores are included
named 'interstel' and 'spake'.  'interstel' is the theme for software
produced by The Interstel Company while 'spake' is "Thus Spake
Zarathustra" by Richard Strauss.  I used these two songs because I
previously used them in Star Fleet I for the ST and had the scores lying
around.  Note that although the Interstel Theme is copyright, you are
welcome to use it for your personal use with this program.  Each song is
an integer array where each value has a meaning to the score processor. 
To make things simple, I've defined all of the parameters we need to
construct the score at the start of the program.  The following score
instructions are available:

SPEED n, - Change the song speed to n.  The larger the number, the
slower the song.  Start the score with a SPEED value, and insert it
again if you need to change speed part way through the song.  Remember
to put a comma after the number n. 

<instrument> - There are three instruments defined in the program being
ORGAN, HORN and SNARE.  They indicate that all note entries following
will be played with that instrument until a new instrument is used.  A
little later I'll show you how to define your own instrument. 

<note duration> - The following durations are available, WH, HF, QU, EI,
SX and TH representing WHole, HalF, QUarter, EIghth, SiXteenth and
THirty second.  They indicate that all note entries following will be of
the designated length until a new length is defined.  The length values
can be modified for dotted and tripleted notes by adding a D or T to the
end of the duration (i.e.  EID means eighth note dotted). 

<note> - Five octaves have been defined.  Two above and two below the
middle octave.  A note is designated by the note (C,D,E,F,G,A or B), a
optional S for sharp, and the octave (2-6) where 4 is the middle octave. 
Therefore FS3 would be F sharp below middle C.  The note will use the
currently active instrument for the currently active note duration. 

REST - Rest (no sound) for the current note duration.

P - Play the current notes you've defined since the last P.

VU - Increase the volume of all following notes by one.  

VD - Decrease the volume of all following notes by one.

VN - Return the notes to normal volume.

DO n, - Repeat the following music until the ENDDO n times.  
Remember to put a comma after the n.

END - Terminate the music. 

All you have to do to create a score is to build a data array using the
above defined parameters. 

                         The Instruments

    We also have a capability of defining instruments to a limited
extent in the program.  We can define the ADSR envelope for each
instrument.  ADSR stand for Attack, Decay, Sustain and Release and are a
means of defining a sound envelope for the instrument.  See figure 2. 
The magnitude of each phase of the envelope is contained in the array
'inst_mag'.  Values of 0 to 15 are allowable.  These correspond to the
volume levels allowed on the sound chip.  The array 'inst_tim' describes
the time allowed for each phase.  Values of 1 to 15 are allowed here
with one exception.  If a value of 16 is used for the sustain phase (3rd
value), the program will calculate the length of the sustain based on
the length of the note being played.  Therefore, long notes will be
drawn out while short notes will be cut short.  Go ahead and play with
the values or add as many more instruments as you wish. 
    Since we can also mix the noise generator with the tone generator,
two more arrays have been defined.  The first is 'inst_tone'.  A value
of TRUE mixes in the tone generator.  Secondly, we have 'inst_noise'
which will mix in the noise generator if TRUE.  Note that either one can
be turned on or even both of them at once as I did for the SNARE
instrument. 

                            The Code  

    The program first calls 'init_music' to initialize some
precalculations and clear the sound chip.  It then starts a song by
entering 'play_music' passing a pointer to the song array.  'play_music'
actually processes the song array separating out the notes, durations,
instruments, etc.  When it's ready to play some notes, it calls
'inst_sound' with arrays containing the note(s) it wishes to play, the
instrument assigned to each note, the duration of each note, and the
time 'inst_sound' should play until returning to 'play_music'.  Note
that if less than three notes are passed and 'inst_sound' still has some
of a note left over from a previous call, it will continue to play the
old note as well as the new ones. 
    'inst_sound' actually builds the data array that we are going to
pass to the sound chip through 'Dosound'.  The function 'sound_build'
takes the register and value data and places them in 's_array' which is
our data array.  The function 'calc_s_vol' used toward the bottom of
'inst_sound' is the routine which actually calculates where we are in
the ADSR envelope for each of our voices, and returns a volume level. 
Finally, 'sound_go' takes the sound array and passes it to 'Dosound'. 

                        Play It Again, Sam

     I hope that now that you've been exposed to the Atari sound chip,
you'll see that there are a great deal of possibilities for it.  The
program will play it's two songs as much as you wish, but I hope you dig
into the program yourself and add more songs or instruments.  Or even
improved on the processing code itself.  I can already think of half a
dozen ways to improve upon the program.  If you come up with any
improvements, I'd love to see them, so drop me a line.  Until then,
happy sounds to you.